## Slide 1
Challenge Gravitational Wave Measurement with a Novel Mössbauer Spectrometer
Huaqiao ZHANG (IHEP)
张华桥 （高能所）
collaborate with Yu Gao(IHEP), Wei Xu (IHEP)
Science Bulletin 2024; 69(18): 2795-2798
10.1016/j.scib.2024.07.038

## Slide 2: Gravitational Wave
阿里
国内实验
太极，天琴
原初黑洞…
GW： a new way to explore our universe
PTA
(Fast)
Thickness of a paper over the diameter of solar system
微波背景涨落
计数频率变化
激光干涉
原子干涉

## Slide 3: Mössbauer effect
"for his researches concerning the resonance absorption of gamma radiation and his discovery in this connection of the effect which bears his name"
1961
Recoil-less emission and resonant absorption of nuclear transition photons
  Mössbauer active nucleus bound to solid state lattice
  Thermal vibration(~1013 Hz) much faster than nuclear transitions (lifetime ~>10-7 s)
    Effect averages to zero, no 1st Doppler broadening
    Recoil to the whole crystallite(>1014 atom)
    Without phonon excitations recoil free
Fine tune
recoil
Solid, liquid, gas

## Slide 4: Doppler shift
Sound
Photon： E=hv
Red shift
Notes: 精密移动探针，来测量极小的能量变化

## Slide 5: “Traditional” Mössbauer Spectrometer
Change the recoil-less emission and absorption overlap with doppler effects
Strength of recoilless nuclear resonant absorption as determined by the “overlap” of emission and absorption lines when the emission line is shifted by Doppler modulation
High accuracy of the resonant absorption width w.r.t. photon energy
Widely used in material analysis
Ex: mars
Notes: 穆斯堡尔谱仪原理
源，吸收体，计数探测器，运动控制： 简单可靠，精度高，灵敏度高

## Slide 6: Relativity test with Mössbauer effect
Gravitational redshift test with Mössbauer effect
Pound, Rebka & Snyder (1960-1965)
Observation of a height-induced frequency shift
Notes: 非常高精度测量：
QED 目前也只是在13个数量级中检验了其精度

## Slide 7: Mössbauer for Gradational Wave
Idea since 1970
  Photon frequency varies when it propagates in an un-even space-time background.
Gave way to clock-based experiments in later tests of “static” gravity.
  See K. Hentschel, Annals of Science 53, 269–295 (1996)

## Slide 8: Issues in traditional Mössbauer Gravity tests
A cryogenic 65Zn measurement
of the local g-value (Potzel et.al. 1992)
Differential measurement of the resonance with a sinusoidal oscillator
  Resonance is achieved
  g-value is off, possibly due to various line-shifts
“such solid-state effects might be difficult …… there might exist two exceptions. The first are null redshift experiments,
in particular measurements with stationary source and absorber”.
Can be improved with a stationary scheme

## Slide 9: Idea of the stationary measurement
Doppler shift ==> Gravitational shift
  V=1mm/s  ~10-12 h = 1mm  ~10-19
  Improve on sensitivity to energy shift
h
h<<r

## Slide 10: Design of a gravitational shift Mössbauer Spectrometer
Replace Doppler shift with gravitational shift
Parallel readout the resonant absorption shape
Time dependent of resonance’s height-shift instead of absolute height
Radioactive source (intensity RS)
0
-h
h
distance (d)
Photon counters with proper Z resolution
¼ cut view
x
Z
Resonance peak(s)
Energy loss ER is compensated by a slight height difference between absorber and source: can be calibrated in advance. --- the absolute height of resonance (Z0) is affected by large systematics: 2nd Doppler, chemical composition, etc. --- but its time-dependent shift under GW is not affected.
horizontal→
absorption layer

## Slide 11: The transmission integral
Photon emission at source
  Fractional recoil-less : fs,
  Fractional recoiled:1-fs
Photon absorption at absorber
  Mass attenuation effect: all photons
  Resonant absorption: only resonant emitted photons
The transmission integral (textbook)
  Replaced the doppler shift with gravitational shift

## Slide 12: The simplified resonance line-shape
Flux reduction due to res. absorption
C()
w/o res.
Recoil-free photons
Recoiled photons
( parameters exaggerated for illustration )

## Slide 13: The choice of isotope source: 109Ag
Mössbauer database (DICP, CAS)
Long parent nuclei lifetime: 461 days allow for sufficient operation time
Narrow 88 keV linewidth: O(10-22) sensitivity
Workable ΔZ ~ 10μm under terrestrial (1 g) gravity field for
The quest of the 109Ag resonance:
, (W. Wildner and U. Gonser, 1979)
Improved resonance resolution, w broadening factors down to 16 (US) R. D. Taylor and G. R. Hoy, SPIE 875, 126 (1988).
S.RezaieSerej, G. R. Hoy, and R. D. Taylor, Laser Phys. 5, 240 (1995). Russian group: improvements with Grav. Effects V. G. Alpatov, et.al. Laser Physics 17, 1067–1072 (2007).
Yu. D. Bayukov, et.al. JETP Letters 90, 499–503 (2009).

## Slide 14: Accuracy from Pseudo experiments
Pseudo experiment simulation with reasonable parameter
  Ex: z-position resolution 10 μm, detection efficiency ~100%
  Readout frequency ~10 fGW
Sensitivity extracted by fitting the resonance absorption peak
Accuracy compatible to the accuracy needed for GW strain
Silver alloy/compound with higher TdeBye helps improve fS e.g. AgB2 has a higher TdeBye and fS =0.2 (@ 4K)
Parallel measure of resonance absorption shape: fast enough for GW

## Slide 15: The GW signal: frequency shift
Consider a plain-wave strain perturbation
A particle’s 4-momentum response to GW strain after one-way propagation:
Estabrook and Wahlquist, Gen. Relat. Gravit. 6, 439–447 (1975);
Hellings, Phys. Rev. D 23, 832–843 (1981).
(figure from Hellings paper)
Energy diff. between and
Frequency shift due to different space-time matrix for photon emission and absorption

## Slide 16
When the baseline distance approaches to the GW’s wavelength scale, a particle starts to see the strain difference.
Non-trivial angular pattern with the incident GW direction: Low GW freq: max. at 90. High GW freq: modulated btw
* Requires a perpen- dicular h component. * Extra complication w baseline at high freq.
* Vanishes when (anti) parallel to GW direction
Spin-2
“blind directions”
Multiple directions can compensate for others’ insensitive directions.
(optimal angle)
Maximal shift with GW frequency:
at high frequency, with multiple maxima. Angular patterns becomes very complicated for Angular pattern allows for GW direction reconstruction At low-freq, freq. shift decreases linearly with

## Slide 17: Stationary Mössbauer GW setup
Absorber+detectors are in the resonance plane around source
  At least two perpendicular directions relative to any GW incident θ angle.
  Enhance acceptance of resonances photons

## Slide 18: Hypothetical GW signal “seen” by our experiment
Modulation of resonance peak shifts in the ring
  Allow direction and polarization reconstruction

## Slide 19: Benchmark scenarios
An estimate on the required source intensity:
Beware: pars on the 2nd line do not scale independently.
Source intensity scales linearly with baseline length and inversely with the local gravitational acceleration.
Need to balance between resonance shift length, detector size, and practical sources.
Non-isotropic source / focusing would immensely enhance efficiency.
Coherently repeated signals can boost statistics: N90 -> N90*Q
(RS for an isotropic source)
Benchmarks: A: table-top experiment. B: 10-meter radius in low-g
No IC included

## Slide 20: Expected sensitive on GWs
A, A’ & B: single period AC: 106 periods
Coherent GWs from NS, SR, PBHs, see N.Aggarwal et al., Living Rev. Rel. 24, 4 (2021) Inverse Gentsenshtein: also see: 2305.00877
Science Bulletin 2024; 69(18): 2795-2798
Max Freq. Reach: cutoffs at:
*3σ peak with ,
*
1011 Bq.,1m
1013 Bq., 5m
1011 Bq. 1m
1014 Bq., 10m

## Slide 21: Summary
Conceptual design use Mössbauer effect for GW measurement:
  Stationary scheme （from table size to multi-kilometers）
    Measure the spatial resonance absorption peak shift.
    Allow direction and polarization reconstruction.
    Relatively small-scale setup (meter – 10 meter)
    109Ag source gives 10-22 strain sensitivity, long lived mother particle.
    Multiband sensitivity（Sensitive to fGW > kHz）
  Possible extension on sensitivity
    low-g, focusing of photons(Laue lens)…
  Larger diameter between source and absorber:
    Aiming for lower frequency GWs
Ground based experiment
Moon based experiment?
Lagrangian point based experiment？