## Slide 1
CEPC injection and extraction system EDR progresses
(including the kickers replacing electro-magnetic separators)
Jinhui Chen
On behalf of the CEPC injection & extraction team
27. Sep. 2024, CEPC Day

## Slide 2: Content
Injection & extraction system EDR progress
  Septum magnet
  Half-sine wave kicker pulser
Alternative scheme of RF region beam separating system
  Ferrite-core kicker with CW square-wave power supply
  RF resonance kicker system
Summary

## Slide 3
Lambertson Septum
Injection & extraction system EDR progress

## Slide 4
Type and quantity of septum magnets
No | Hardware | Type | Typical parameters |  |  |  | Unit | Number | Unit price (10,000 CNY) | Total Price (10,000 CNY)
 |  |  | Length | B | Septum | Clearance |  |  |  | 
1 | thin septa | In-vac LSM | 1.75m | 0.8T | 2mm | 20*20mm | set | 28 | 58 | 1624
2 | thick septa1 | In-air LSM | 1.75m | 0.8T | 6mm | 20*20mm | set | 148 | 25.8 | 3818.4
3 | thick septa2 | In-air LSM | 1.2m | 0.8T | 5.5mm | 50*50mm | set | 2 | 22.8 | 45.6
4 | thick septa3 | In-air LSM | 0.5m | 0.8T | 3.5mm | 30*30mm | set | 2 | 20.8 | 41.6
 |  |  |  |  |  | Total Number: | set | 180 | Total price: | 5529.6
Lambertson magnet (LSM)with DC exciting was adopted in CEPC inj.&ext. system due to its higher reliability.
The total number of LSM is 180 sets.

## Slide 5
Two types of Lambertson magnets for TDR
To realize thinner septum as possible, 2 novel structures of magnet were proposed:
Injected bunch
Stored bunch
Magnet pole
Installation margin
Yoke
Injected bunch
Magnet pole
Installation margin
Yoke
Stored bunch
Injected bunch
Magnet pole
Installation margin
Installation margin
Yoke
Stored bunch
SS
Iron or
VP(FeCoV，1J22)
Traditional LSM
SS
Half in-vacuum
in-air
Septum
thickness
Wall of stored beam pipe
+
Wall of injected beam pipe
+
Iron septum
+
installation margins
=
  half-in-vacuum
  (for septum of 2mm)
  embedded thin-wall vacuum chamber
  (for septum≥3.5mm)
Thin septum
(IN-VAC)
Thick septum
(IN-AIR)
Quantity:152 sets
Quantity:28 sets

## Slide 6: LSM design considerations in EDR phase
What experiences and lessons can be learned from HEPS?
How to reduce the cost of magnets?
How to reduce the difficulty of magnet manufacturing, assembly and magnetic field measurement?
How to make magnets longer to decrease the magnet quantity?
  1.75m -> 4m？
  Vacuum achievement？
  Iron-core manufacturing？
  Magnetic-field measurement？

## Slide 7
IN-Air LSM
Research status：final magnets for HEPS BST injection was applied in beam commissioning successfully last year.
BST injection LSM
BST extraction LSM

## Slide 8: Experience and Lessons of in-air LSM for HEPS
FeCoV alloy（1J22）is hard to machine, the magnetic shielding blocks must segmented processing by EDM . And that, the embedded thin wall vacuum chamber for stored beam is needed.
It is difficult to control the deformation of the FeCoV blocks after 1000℃ annealing.
The seam between two materials on the magnet pole has an impact on the quality of the main field distribution and increase the leakage field.
Magnetic field measurement is difficult for the magnet with small aperture.

## Slide 9: BS1LSM main field vertical field uniformity
  2D model analysis: the real reason is that upper and bottom polar surface width is not symmetrical
Chart: 垂直场分布
有孔：2.75E-03
无孔：2.67E-03
Chart: 水平场均匀度
有孔：1.19E-05
无孔：4.73E-05
D
W
Chart: 间隙中心垂直场均匀度
| -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
error | -0.00044011 | -0.00030781 | -0.00019295 | -0.00011083 | -5.1257e-05 | -7.5141e-06 | 2.4421e-05 | 3.596e-05 | 3.757e-05 | 2.2811e-05 | 0 | -3.4618e-05 | -7.7824e-05 | -0.00012801 | -0.00018141 | -0.00023884 | -0.00029868 | -0.00035772 | -0.00042267 | -0.00048761 | -0.00054531
ERROR:
5.83E-04
Chart: 间隙中心水平场均匀度
| -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5
error | 0.00024957 | 0.00012371 | 3.8107e-05 | -2.4152e-06 | -1.6638e-05 | 0 | 4.9915e-05 | 0.00014196 | 0.00025333 | 0.00040737 | 0.00059093
ERROR:
6.07E-04

## Slide 10: BS3LSM main field horizontal field uniformity
  Measurement data display: the bad data is location at the region which injection beam track across the slot between DT4 and 1J22 block.
Horizontal field uniformity is bad
  2D model analysis: If the overlap part is horizontal field distribution is narrow, the vertical slot between DT4 and 1J22 could significant impact the field distribution in horizontal.
0.5mm slot
Explore 25mm
0.5mm slot
Chart: 
Chart: 

## Slide 11
IN-Vacuum LSM
FeCoV
Cu
2mm
DT4
Research status：final magnets for HEPS SR was applied in beam commissioning successfully in July this year.
SR injection straight section（R03）
SR extraction LSM
SR extraction straight section（R48）
Full A:HxV=10.5mmx5mm

## Slide 12: Experience and Lessons of in-vacuum LSM for HEPS
There are also difficulties in processing FeCoV alloy and magnetic field measurement
Other difficulties:
  Processing, welding, and assembly of the rectangle vacuum chamber and the transition section.
  Alignment of magnet in the vacuum
  Rectangle flange vacuum sealing with knife-edge because of flange deformation.
Copper washer
Silver wire
一度成为HEPS的关键路线

## Slide 13: New explore：4-meter In-air LSM for LHC
4-meter Laminated iron core magnet
Magnetic shielding vacuum tube: Mumetal (domestic brand:1j77) + NEG coating
Need cooperation with vacuum system

## Slide 14
Kickers and Pulsers
Injection & extraction system EDR progress

## Slide 15: Type and quantity of kicker and pulser
No | Hardware | Type | Typical parameters | Unit | Number | Unit price (10,000 CNY) | Total Price (10,000 CNY)
1 | kicker1 | delay-line dipole kicker | in-air delay-line dipole kicker, horizontal, 0.1mrad, 0.04T·m, L=1m, B=0.04T(H), inc. ion pump | set | 24 | 50 | 1200
2 | kicker pulser1 | trapezoidal wave pulser | PFN, solid-state,440~2400ns, inc. cable | set | 24 | 100 | 2400
3 | kicker2 | ferrite-core dipole kicker | in-air ferrite-core dipole kicker, horizontal,0.2mrad,0.08T·m, L=1m, B=0.04T(H)， inc. ion pump | set | 6 | 33 | 198
4 | kicker pulser2 | half-sine wave pulser | LC, solid-state,1360ns, halfsine, inc. cable | set | 6 | 31 | 186
5 | kicker3 | strip-line kicker | Strip-line kicker, vertical, 46ns, L=1m, inc. ion pump | set | 6 | 28 | 168
6 | kicker pulser3 | DSRD pulser | 46ns, ±12.5kV,DSRD pulser, inc. cable | set | 6 | 67 | 402
7 | kicker4 | slotted-pipe kicker | Slotted-pipe kicker,vertical,250ns,L=0.25m, DR beam pipe φ=30mm, inc. ion pump | set | 2 | 23 | 46
8 | kicker pulser4 | trapezoidal wave pulser | solid-state,inductive adder, 250ns, inc. cable | set | 2 | 40 | 80
9 | dilution kicker | CW full-sine | CW full-sine，L=2m，150Gauss，T=25us, total length=10m | set | 10 | 30 | 300
10 | dilution kicker pulser | CW full-sine | CW full-sine，T=25us | set | 10 | 30 | 300
11 | NLK | NLK | in-air Nonlinear kicker or pulsed sextupole, horizontal, 0.1mrad, 0.04T·m, L=1m, inc. ion pump | set | 2 | 38 | 76
12 | NLK pulser | half-sine wave pulser | LC, solid-state,0.3ms, halfsine, inc. cable | set | 2 | 15 | 30
 |  |  | Total Number: | set | 100 | Total price: | 5386
In CEPC inj.&ext. System, there are 6 kinds of kicker and its pulser.
The total quantity of kicker and its pulser in CEPC is 100 sets, and the delay-line kicker and trapezoidal wave pulser account for largest proportion.

## Slide 16: Design parameters of ferrite core kickers for CEPC
parameter | Unit | BST-EXT-kicker1/CR-inj-kicker1/dump （for CR off-axis inj.） | BST-EXT-kicker2/CR-inj-kicker2 （for CR on-axis inj.）
Type | - | In-air delay-line dipole kicker | In-air lumped parameter dipole kicker
Deflect direction | - | Horizontal | Horizontal
Beam Energy | GeV | 120 | 120
Deflect angle | mrad | 0.1 | 0.2
Magnetic effective length | m | 1 | 1+1
Magnetic strength | T | 0.04 | 0.04
Integral magnetic strength | T·m | 0.04 | 0.08
Clearance region(H×V) | mm | 56×56 | 56×56
Good field region(H×V) | mm | 50×50 | 50×50
Field uniformity in good field region | - | ±1.5% | ±1.5%
Repetition rate | Hz | 1k | 1k
Amplitude repeatability | - | ±0.5% | ±0.5%
Pulse jitter | ns | ≤5 | ≤5
Bottom width of pulse(5%-5%) | ns | Trapezoid：440~2420 | Half-sine：1360
Tr/Tf(5%-95%) | ns | <200 | <680
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
There are 2 kinds of kicker with ferrite core for trapezoid wave and half-sine wave pulsed system.

## Slide 17: Trapezoid wave kicker system（No new progress）
200ns
40~2000ns
200ns
1kHz
Delay-line dipole kicker and pulser Parameter | Value
Aperture of magnet (mm) | 100 × 80
Longitudinal length of magnet cell (mm) | 36
Cell number of magnet | 26
Differential impedance of magnet (Ω) | 12.5
Length of magnet (mm) | 942
Total mechanical Length of magnet (mm) | 1018
Inductance of magnet cell (nH) | 56.6
Total inductance of magnet (nH) | 1471.6
Capacitance of magnet cell (pF) | 362
Total capacitance of magnet (nF) | 9.412
Magnetic strength (Gs) | 425
Exciting current of magnet (A) | 2703
Differential voltage of magnet (V) | +/-16895.5
Pulse waveform | trapezoid
Rise/fall time (ns) | 200
Flat-top width of pulse (ns) | 40~2000 adjustable
Filling time of magnet (ns) | 117.728
Rise/fall time of pulser (ns) | 80
Repetition rate (kHz) | 1
Research status：
A delay-line kicker (NLK) prototype was done. But magnet characteristic impedance is a little high and volume is Large; Beam impedance issue of ceramic vacuum chamber with Ti coating is not clear
A solid-state pulser prototype based on SiC MOSFET was done. But the pulse HV dose not meet CEPC requirement yet.
18-stage@800V：14.2kV into 10Ω
Voltage is lower

## Slide 18: Half-sine wave kicker system
Research status：
  A novel solid-state pulser circuit is proposed. (LC resonance discharge with inductive-adder based on IGBT and SiC-SBD) .
  The IGBT module(FZ600R12KS4: 1.2kV/1200A) is adopted for its higher performance-cost ratio.
Lumped dipole kicker Parameter | Value
Magnetic field B (T) | 0.04
Inner aperture of ceramic vacuum chamber (mm×mm) | 56×56
Ceramic vacuum chamber outer aperture (mm×mm) | 85×66
Magnet aperture w × h (mm×mm) | 100×80
Length of magnet l (m) | 1
Inductance of magnet L (μH) | 1.6
Magnet exercitation current I (kA) | 2.6
Impedance Z (Ω) | 3.7
Voltage of magnet U (kV) | 9.62
Pules bottom width τ (ns) | 1360
Repetition rate（Hz） | 1000
<1360ns,1kHz

## Slide 19: New half-sine wave kicker pulser
Principle verify circuit in condition of 5 stages was test
Load=1.3uH（Z=1.18Ω）
DC=750V
Ip=616A
Pw=715ns
Load=90nH（z=0.44Ω）
DC=1000V
Ip=2340A
Pw=250ns
f=1kHz（CW）
P=1kW

## Slide 20
Alternative scheme of RF region beam separating system

## Slide 21: Alternative scheme of RF region beam separating system
k1
k2
k4
k3
165us
165us
k1
k2
k3
k4
165us
CW=3.03kHz, 50%
Motivations：The adverse issues of DC HV as high as hundred kV and beam impedance of the electrostatic separator are inevitable
The alternative scheme was proposed first in 2019. Similar idea was found in ILC head-on-collision option scheme*（EPAC2006，TESLA-scheme is electrostatic-separator）.
In Higgs mode，e- /e+ beams only fill half ring respectively. So, it is possible to separate beams by kickers.
Compared with static-electrical separator, kicker magnet is stronger and contributes lower beam impedance.
4 sets of kicker locate at both sides of RF region, K1 and k4 applied for e+ beam,K2 and K3 applied for e- beam;
The waveform of kicker pulsers is square wave with duty cycle of 50%, pulse width of 165 us and frequency of 3.03 kHz;
The phase difference between K1 (K3) and K2(K4) is π.
RFC
RFC
K2
K1
 | Kicker | Septa
Integrated strength BL [T*m] | 0.1624 | 1.4
Strength B [Guass] | 203 | 1000
Effective length Leff [m] | 8 | 14
Half width of good field region Hgf/Vgf [mm] | 10.1/3.8 @ 5E-4 | 18.9/3.8 @ 5E-4
Half width of beam stay clear Hbsc/Vbsc [mm] | 9.6/3.6 | 9.2/3.6
Septum width width [mm] | - | 10
kickers
DC septas
Last e+ Bunch
First e- Bunch
k1
Top view
Yiwei Wang

## Slide 22: Ferrite-core kicker with CW square-wave power supply
Parameters | Kicker
Integrated strength BL [T*m] | 0.1624
Strength B [Guass] | 203
Total effective length Leff [m] | 8
Size of core window w×h [mm] | 90×70
Length of a piece of magnet [mm] | 1000
Exciting current [A] | 1131
Inductance of magnet of a piece of magnet [μH] | 1.6
Width of pulse[μs] | 165
Frequency[Hz] | 3.03k
Rise/fall time of [μs] | 1
Voltage of coil [kV] | 1.8
Flatness of pulse flat-top | ?
Long term stability of amplitude of square-wave | ? 40ppm
The bandwidth of fast corrector power supply for HEPS is 1kHz
CW HF（3kHz） square-wave power supply
  Circuit topology：Multi-level technology
  Feedback control：digital control
  Kicker magnet preliminary design：ferrite core，in-air，ceramic vacuum chamber with metallic coating

## Slide 23: Resonance kicker scheme
680ns
165us
165us
Swiss FEL beam separating system

## Slide 24: Resonance kicker system preliminary design
Frequency of CEPCRF system:650MHz
Bunch spacing in Higgs mode: 680ns
Kicker system fundamental frequency: 1.5MHz+3.3KHz
Resonance frequency: 15MHz (650MHz/43.3, 1.5MHz*10, to ensure that every bunches receive the same kick angle)
Power source: Solid-state amplifier based on MOSFET
Low-level control: to achieve amplitude and phase stability controlling
165us
(242bunch)
680ns，1.5MHz，duty cycle:50%
680ns
165us
165us
L=0.5uH
C=225pF
Z=Ω

## Slide 25
Summary
This year, the injection team was mainly dedicated to HEPS and BIIU projects, and the R&D of CEPC EDR has just started.
Some key technologies have been validated on HEPS successfully and the experiences and lessons can be learned from HEPS.
The design of LHC septum magnet has important reference significance for CEPC.
Good results were obtained from new half-sine wave kicker pulser circuit test.
The preliminary designs of ferrite core kicker with square-wave power supply and resonance kicker system for RF region beam separating system has been initiated.

## Slide 26
Thank you for attentions!
END

## Slide 27
Backup

## Slide 28: List of all type of hardware
No | Hardware | Type | Typical parameters | Unit | Number | Unit price (10,000 CNY) | Total Price (10,000 CNY)
1 | kicker1 | delay-line dipole kicker | in-air delay-line dipole kicker, horizontal, 0.1mrad, 0.04T·m, L=1m, B=0.04T(H), inc. ion pump | set | 24 | 50 | 1200
2 | kicker pulser1 | trapezoidal wave pulser | PFN, solid-state,440~2400ns, inc. cable | set | 24 | 100 | 2400
3 | kicker2 | ferrite-core dipole kicker | in-air ferrite-core dipole kicker, horizontal,0.2mrad,0.08T·m, L=1m, B=0.04T(H)， inc. ion pump | set | 6 | 33 | 198
4 | kicker pulser2 | half-sine wave pulser | LC, solid-state,1360ns, halfsine, inc. cable | set | 6 | 31 | 186
5 | kicker3 | strip-line kicker | Strip-line kicker, vertical, 46ns, L=1m, inc. ion pump | set | 6 | 28 | 168
6 | kicker pulser3 | DSRD pulser | 46ns, ±12.5kV,DSRD pulser, inc. cable | set | 6 | 67 | 402
7 | kicker4 | slotted-pipe kicker | Slotted-pipe kicker,vertical,250ns,L=0.25m, DR beam pipe φ=30mm, inc. ion pump | set | 2 | 23 | 46
8 | kicker pulser4 | trapezoidal wave pulser | solid-state,inductive adder, 250ns, inc. cable | set | 2 | 40 | 80
9 | dilution kicker | CW full-sine | CW full-sine，L=2m，150Gauss，T=25us, total length=10m | set | 10 | 30 | 300
10 | dilution kicker pulser | CW full-sine | CW full-sine，T=25us | set | 10 | 30 | 300
11 | NLK | NLK | in-air Nonlinear kicker or pulsed sextupole, horizontal, 0.1mrad, 0.04T·m, L=1m, inc. ion pump | set | 2 | 38 | 76
12 | NLK pulser | half-sine wave pulser | LC, solid-state,0.3ms, halfsine, inc. cable | set | 2 | 15 | 30
13 | thin septa | In-vacuum Lambertson | Lambertson,vertical,DC,L=1.75m,B=0.8T,Septum=2mm, mainfield clearance=20*20mm, 13mrad, 5.22T·m,inc. ion pump | set | 28 | 58 | 1624
14 | thick septa1 | In-air Lambertson | Lambertson,vertical,DC,L=1.75m,B=0.8T,Septum=6mm, mainfield clearance=20*20mm, 13mrad, 5.22T·m,inc. ion pump | set | 148 | 25.8 | 3818.4
15 | thick septa2 | In-air Lambertson | Lambertson,horizontal,DC,L=1.2m, B=0.8T, Septum=5.5mm, mainfield clearance=50*50mm, 45mrad, 0.92T-m,inc. ion pump | set | 2 | 22.8 | 45.6
16 | thick septa3 | In-air Lambertson | Lambertson,horizontal,DC,L=0.5m,Septum=3.5mm, DR beam pipe φ=30mm,inc. ion pump | set | 2 | 20.8 | 41.6
17 | septa power supply | DC power supply | DC switch power supply, inc. cable | set | 28 | 12.5 | 350
18 | local control system1 |  | PLC，touch screen，oscilloscope | set | 16 | 10 | 160
19 | local control system2 |  | PLC，touch screen，oscilloscope | set | 2 | 5 | 10
20 | Field measurement devices1 | hall | Hall point measurement system for Lambertson | set | 2 | 160 | 320
21 | Field measurement devices2 | inductive coil measurement | inductive coil measurement system for kicker | set | 1 | 10 | 10
 |  |  |  |  |  | Total cost： | 11765.6
 |  |  |  |  |  | Toal cost with installation fee(3%)： | 12118.568

## Slide 29: 谐振腔式kicker方案

## Slide 30: 谐振kicker磁铁方案
RESONANT KICKER SYSTEM FOR HEAD-ON-COLLISION OPTION OF LINEAR COLLIDER*

## Slide 31: 高重复频率窄脉冲kicker电源方案
自由电子激光的束流分配系统上有类似的kicker电源设计。
优点：效率更高，脉冲电源的充能元件体积更小。匹配放电电路，按照10ns/10kV/50Ω计算，终端电阻上的平均功率是：16.7kW. 谐振放电电路，能量可以回收
特点：重复频率高达1.5MHz，商业的半导体开关器件MOSFET和特殊DSRD开关工作频率已达到这个量级。为HEPS研发的strip-line kicker10ns快脉冲电源测试结果显示，可以工作在1MHz。
难点：高重复频率下如何解决脉冲幅度一致性和稳定性的问题。需要研究快速充电技术和补偿控制技术。
165us
(242bunch)
680ns，1.5MHz，占空比50%
242,1.5MHz
165us
165us
165us
CW=3.03kHz,50%
实际波形：
理想波形：

## Slide 32: 商业谐振式高频电源

## Slide 33
Manpower and funding requirements

## Slide 34
Research Team
Team member in TDR phase : 11 persons
  Researcher: Jinhui Chen
  Associate-researcher: Lei Wang, Lihua Huo, Yuwen Wu, Hua Shi
  Engineer: Guanwen Wang, Peng Liu, Xiaolei Shi
  Post-doctor: Guanjian Wu, Zilin Chen
  Doctoral-graduate-student: Xinzhe Zhai
Chart: HR
Researcher | 1
associate | 4
engineer | 3
Post-doctor | 2
Doctor | 1
Problems：
Team members are from several groups
All people is part-time: HEPS (first half of this year), BEPCII-U(second half of this year), CSNSII
Some people are leaving
Need at least 25 FTEs in future construction phase

## Slide 35
Funding and manpower requirements
R&D item | Budget (X10000CNY) | Man power（FTEs）
Lambertson magnet | 45 | 1 （霍丽华、吴官健、吴煜文）
Delay-line Kicker | 45 | 2 （王磊、吴官健）
Kicker pulser | 80 | 2（翟心哲、王冠文、陈锦晖）
Resonance kicker | 80 | 2（王磊、吴官健、霍丽华、施华）
Resonance power supply | 80 | 2（陈锦晖、翟心哲、王冠文、刘鹏）
Bumper magnet（6kHz） | 20 | 1（霍丽华）
Continue square wave power supply | 30 | 2（刘鹏、？）
total | 380 | 12