## Slide 1: Material Budget Caculation

## Slide 2: Method
Radiation length (X0)
Could quantify material budget with xxx% of X0
B: material budget (fraction of X0)
L: thickness
X0: radiation length of certain material
Total material budget could be simply calculated with:

## Slide 3: Results for normal case
Layer | Material | Radiation length(mm) | thickness(mm) | Material Budget(X0)
ASIC | Silicon | 93.6 | 3 | 0.03205
PCB | FR-4 | 174 | 1.6 | 0.009195
AC-LGAD | Silicon | 93.6 | 0.5 | 0.005342
Carbon fiber board | Carbon fiber | 237 | 0.2 | 0.000844
Total |  |  |  | 0.047432

## Slide 4: Results with heat sink(copper)
Layer | Material | Radiation length(mm) | thickness(mm) | Material Budget(X0)
ASIC | Silicon | 93.6 | 3 | 0.03205
Heat sink | Copper | 14.36 | 1.6 | 0.11142
AC-LGAD | Silicon | 93.6 | 0.5 | 0.005342
Carbon fiber board | Carbon fiber | 237 | 0.2 | 0.000844
Total |  |  |  | 0.149658

## Slide 5: Results with heat sink(aluminum)
Layer | Material | Radiation length(mm) | thickness(mm) | Material Budget(X0)
ASIC | Silicon | 93.6 | 3 | 0.03205
Heat sink | Aluminum | 88.9 | 1.6 | 0.017998
AC-LGAD | Silicon | 93.6 | 0.5 | 0.005342
Carbon fiber board | Carbon fiber | 237 | 0.2 | 0.000844
Total |  |  |  | 0.056235