## Slide 1
Critical Current Measurement of Superconductors
Chunyan Li, Fan Ren
Institute of High Energy Physics, CAS
High Field Superconducting Magnet Group
Hands-on Training 2

## Slide 2: What is Superconductor（超导体）?
Zero resistance （零电阻）
Meissner effect （迈斯纳效应）
Superconductivity discovered in 1911 by Onnes:
Zero resistance of mercury (Hg) wire at 4.2 K
Perfect diamagnetism (完全抗磁性）
Below its critical temperature (Tc), a superconductor exhibits the expulsion of magnetic fields.
Below its critical temperature (Tc),
a superconductor’s resistance drops to zero.

## Slide 3: Application Fields
Magnetic Levitation Train
Wind Turbine Generator
Particle Accelerator
Nuclear Fusion
Magnetic Resonance Imaging
Power Transmission

## Slide 4: Circular Particle Accelerator
Next generation super-high energy accelerator rely on high field (16-24 T) dipole magnet.
Circumference环的周长
Magnetic Field
磁场强度
Energy
质心能量
The energy of an accelerator is proportional to the magnetic field strength of the dipole magnets and the circumference of the ring.

## Slide 5: Superconducting Dipole Magnet-超导二极磁体
Dipole Magnet
Electromatic and mechanical
design of superconducting
dipole magnet
Fabrication of racetrack coils
Dipole magnet assembly
Nb3Sn coils
LTS + HTS
B[T ]

## Slide 6: Superconductors (SCs)
Low temperature superconductor (LTS)
NbTi (铌钛), Nb3Sn (铌三锡) superconductors
Wires with single superconducting filament to tens of thousands of ultra fine filaments.
Rutherford cable
Luwata
High temperature superconductor (HTS)
SST 上海超导
HTS tape - REBCO
Conductor on Round Core (CORC) cable
HTS can be used in liquid hydrogen (77 K)
LTS is used in liquid Helium (4.2 K)

## Slide 7: Critical Parameters of SCs
The critical temperature (Tc) 临界温度
Above Tc, the superconductor reverts to normal (non-superconducting) state.
Nb3Sn (Tc =18 K); REBCO (Tc =92 K);
The critical current (Ic) 临界电流
The maximum current the superconductor carries without losing its superconducting property.
Je = Ic / (cross sectional area of the superconductor)
The critical field (Hc2) 临界磁场
Above Hc2, the superconductor reverts to normal (non-superconducting) state.
Nb3Sn (Hc2 , 4.2K = 25 T); REBCO (Hc2, 4.2K ＞100 T);
High Ic / Je
High central field in magnet

## Slide 8: Measurement of critical current (Ic)
The Four Probe Method:
Current Leads: two outer probes supply a DC current (I).
Voltage Leads: two inner probes measure the voltage .
Steps of the Ic measurement:
Sample preparation
Cooling
Current ramping (Power supply)
Voltage monitoring
Quench protection
Data analysis (V-I curve)
1 µV/cm
Quench criteria for Ic determination:
Ic is the current producing 1 µV per cm between two voltage probes.

## Slide 9
Thank You for Your Attention !