## Slide 1: Hands-on training 6
HEPS Cryogenic Hall
Mar. 24th-29th, 2025
Keyu Zhu & Changcheng Ma

## Slide 2: OUTLINE
1
Cryogenics
2
3
Insulation support
Hands-on training

## Slide 3: Cryogenics in HEPS
Refrigeration Room
Cryogenic Hall
106# Conference Room

## Slide 4: Cryogenics
Cryogenics is a branch of physics that studies what happens to things at low temperatures.
Temperature range is bellow 123 K= -150 oC
Room temperature
0 oC=273K

## Slide 5: OUTLINE
1
Cryogenics
2
3
Insulation support
Hands-on training

## Slide 6: Insulation support
Insulation support is a common component in cryogenic equipment, which plays a role in bearing weight load and reducing heat transfer. Choose materials carefully:
Good Mechanical properties for room temperatures & cryogenic temperatures
Low heat leak

## Slide 7: Mechanical properties
Young’s Modulus E
E=
σ is the stress (Pa ), representing the force per unit area.
ε is the strain ( dimensionless ), which represents the relative deformation of the material in the direction of force.
It reflects the stiffness of the material. The larger the Young 's modulus, the smaller the deformation of the material under stress.
Yield Stress
Yield stress is used to describe the critical stress value of plastic deformation (broken) ( permanent deformation ) when the material is subjected to external force. Specifically, when the stress on the material reaches the yield stress, the material will enter the plastic deformation stage from the elastic deformation stage.

## Slide 8: Solid Material
Cu
304
At low temperature, the yield stress of metal usually increases.
Metal
Good toughness at low temperature.
1000 psi
Yield stress of metal
1psi=6.89kPa

## Slide 9: Three Ways to Transfer Heat
Conduction
  Heat transfer through solid material
Convection
  Heat transfer via a moving fluid
    Natural or free convection – motion caused by gravity (i.e. density changes)
    Forced – motion caused by external force such as a pump
Radiation
  Heat transferred by electromagnetic radiation/photons
There is no such thing as a perfect insulator – though we can design systems with very small heat leaks
All matter above 0 K radiate heat
  Remember we can’t get to 0 K – 3rd Law of Thermodynamics though we can get vanishingly close

## Slide 10: Thermal Conductivity
From Lakeshore Cryotronics
Copper
Stainless steel
G-10/PTFE
Compound glass fibre

## Slide 11: Structural Support of cryostat 1
1 Can support up to 50 kN
2 Total Heat Leak (conduction & radiation)
  70 K - 10.5 W
  5 K - 0.9 W
  2 K - 0.03 W
300 K
70 K
4 K
2 K
G-10
316L SS

## Slide 12: Structural Support of cryostat 1
Support from 300 K to 2K
Cavity assemblies tied to 300 mm pipe backbone
All other connections to 300 K have flex line.
1.3G SRF cavity Cryomodule is designed by IHEP
Support
300 K
2 K

## Slide 13: Structural Support of cryostat 2
IHEP---CSNS II Spoke cavity Cryomodule : All components are tied to space frame which rolls into the vacuum vessel. Connections to 300 K done via flex lines and bellow.
16 flex lines from 300K to 2K
Biphasic pipe
Supports
Spoke Cavity 2K

## Slide 14: OUTLINE
1
Cryogenics
2
3
Insulation support
Hands-on training

## Slide 15: Training 1
  Different materials in Liquid Nitrogen
304L tube
G10 bar
Rubber gloves
Plastic tube
Carbon fiber rod
Liquid Nitrogen Tank
Be careful

## Slide 16: Training 2
Power
Cryogenic
Dewar
Support
Tension
Serisor
Guide
rod
Ø260
Goal：Tests of Mechanical properties of materials at low temperature.
Unit: Power part, High precision sensor: tension sensor and displacement sensor, Cryostat, support.
Function: Maximum force 100kN~0.5%FS.
Power: Hydraulic cylinder
High force in a small package size
Linear displacement and power load
Cryostat : Temperature —80K~300K

## Slide 17: Training 2
Liquid Nitrogen
Control Carbine
Experimental Installation

## Slide 18: Training 2
Speed setting
Displacement setting
Pressure setting
Control Interface