## Slide 1
CEPC Polarization EDR Progress
Zhe Duan
On behalf of the CEPC Polarization Working Group
27 Nov 2024, CEPC Day, email: duanz@ihep.ac.cn
Circular Electron Positron Collider

## Slide 2: Outline
Key technology R&D Progress
  Polarized electron source
  Compton Polarimeter
  HTS solenoid
Summary

## Slide 3: Polarized electron source R&D (李小平等)
高量子效率（QE）、高极化度（ESP）光阴极研发
  提高QE和ESP需要长期的工艺优化、测试，反复迭代
  主要vendor已经退出市场
  EIC: BNL/JLab/Old Dominon Univ恢复美国本土生产
  苏州焜原2019年曾向BNL供货应变超晶格光阴极
陈意桥：
2017之前在美国SVT公司，负责极化阴极生产工艺
2017至今，苏州焜原董事长/上海微系统所研究员，实验室主任
刘伟：
2015-2023，JLab博士/BNL博后，负责极化阴极测试
2023至今，重庆大学，极化电镜研发
建立极化光阴极的国内合作研发

## Slide 4: Polarized electron source R&D (李小平等)
“光阴极材料实验和测试平台”，苏州焜原光电，350万元，已启动采购流程
    苏州焜原负责阴极生长，同高能所合作搭建测试平台（刘伟在焜原兼职）
    测试平台可直接测量阴极的量子效率、极化度（同mini-Mott对接）
    测试平台可同MBE系统对接，为阴极生产工艺的快速迭代优化奠定基础
    最终提供可用于PAPS极化电子源的阴极材料，满足量子效率 > 0.8%，极化度> 85%
mini-Mott 极化仪： Specs公司售价260万元，决定高能所自研（预计100万元以内）
mini-Mott polarimeter
极化阴极生产MBE系统
光阴极材料测试平台

## Slide 5: Polarized electron source R&D (李小平等)
V. Tyukin 第二次PIFI来访两个月
完成第一版束线改造布局设计（ V. Tyukin、王建力），正在进行物理方案设计评估（孟才、张澍）
完成极化翻转器、Mott极化仪等核心部件的初步设计（V. Tyukin、王海静、刘劲东、王建力、梁志均等）
同德国美因茨大学核物理所签订合作备忘录， 美因茨大学和苏州焜原在商讨阴极采购、测试事宜

## Slide 6: Polarized electron source R&D (李小平等)
束线物理设计
极化阴极测试平台
自旋旋转器研制
极化阴极生产
束线工程设计
Mott polarimeter研制
mini-Mott研制
束线安装、调试、调束
阴极生产和测试
电子枪load-lock改造
激光系统研制
电子枪
极化电子测试束线
2025
2026
2027
2028
束线元件研制
Milestone2: 测试平台实现对阴极性能的测试
Milestone1: 极化阴极在美因茨大学进行首次测试
Milestone3: 极化电子束线出束

## Slide 7: Compton polarimeter @ BEPCII
完成4W2束线的第一轮改造
开展激光传输实验，为对撞调试奠定基础
A. Martens（IJCLab）12月3-4日来访，推进合作研究
准备25年暑期的第二轮束线改造，25年秋季进行首次极化测量实验
已安装的自研激光定标靶
祝德充，王建力，周宁闯等
激光光路传输实验
苏梦雨
麻中惠、雷革、马新朋
同步定时设计
4W2束线第一轮改造示意图

## Slide 8: Compton polarimeter @ BEPCII
第二轮束线改造
激光采购和调试
极化测量调试
共振退极化能量测量
2025
2026
2027
Milestone1: 首次极化测量
Milestone2: 首次能量标定
2028
极化度优化实验
潜在扩展: 纵向极化测量、正电子环极化测量，为BES物理研究提供关键输入； 河南环的极化精确测量
梁羽铁等

## Slide 9: 12T传导冷却高温超导螺线管研制进展（赵玲等）
线圈结构优化：线圈采用10+80+10的多饼结构，共计100个双饼YBCO线圈，实现10.26T.m的轴向积分场。
针对拟解决的两个关键问题，开展实验验证：
    采用传导冷却的多饼YBCO线圈温度一致性问题
    YBCO线圈不同工况下的稳定性问题
导冷结构测试示意图
线圈稳定性测试平台结构图
80 Double-winding（4.8mm宽）
10 Double-winding（12mm宽）
10 Double-winding（12mm宽）
 | 具体内容 | 进展 | 预计完成时间
1. | 多饼线圈轴向导冷结构测试 | 进行中 | 2024.12
2. | HTS线圈径向导冷结构测试 | 进行中 | 2024.12
3. | 屏蔽电流对HTS线圈稳定性的影响 | 进行中 | 2024.12
4. | 绕线张力对线圈应力的影响 | 已完成 | 2024.10
5. | 绕制方式对线圈稳定性的影响（不锈钢并绕or无绝缘绕制） | 待完成 | 2024.12
6 | 电流引线优化设计及工作电流的选择 | 进行中 | 2024.11
测试线圈组装示意图

## Slide 10: Summary
Major progress in polarized electron source R&D
Other R&D items are under way
Thank you for your attention!

## Slide 12: IARC recommendations on polarization
CEPC Linac
  The polarized-beam option was not described at this stage. In the future, the polarization option would need to be designed in a coherent way with the ring design. It is necessary to investigate the proper distribution of the workload for this option.
  Decide on the polarization option and assign the appropriate human resources.
CEPC booster and damping ring
  Beam polarization is being studied, but there are beam dynamics issues for the polarization and to keep the polarization during ramping. These study will continue next year, they are mandatory if the polarization option is to become a standard feature for CEPC.
CEPC collider ring beam dynamics
  The polarization of the electron beam, both transverse for energy calibration and longitudinal for physics is being explored. To provide longitudinally polarized electron at the IP for the Z running, the ring layout needs to be able to accommodate one spin rotator cell at both sides of the IR. This option, which would benefit the physics capabilities, and would be a unique feature of CEPC, should be carefully studied since of course the machine layout cannot be changed.
  Review the electron-ring layout to be able to install spin rotators for longitudinal polarization in the future, without disruption of the machine design
评估对直线加速器设计的影响
增强器lattice需优化设计
对撞环为spin rotator预留空间

## Slide 13: Status of beam polarization design
Prospects
Injecting pre-polarized beams
  Polarized e– source
  Polarized e+ ring @ ~2.0 GeV
Beam energy calibration @ Z & W
~70% longitudinal polarization for e- @ Z
CEPC TDR-Accelerator, arXiv:2312.14363
Radiat. Det. Tech. Meth. 6:490 (2022).
Phys. Rev. Accel. Beams, 26, 051003 (2023).
Phys. Rev. Accel. Beams, 26, 091001 (2023).
positron polarizing ring
Topics to study
Useful polarization level @ Higgs
Longitudinal polarization w/ pol e+, at higher energies
  Polarized e+ source
    flux requirement ~ 1/60 of ILC
    revisit of the Compton Ring scheme under way (Li Xiaoping, in contact with IJCLab for collaboration )
  Spin rotators at higher energies

## Slide 14: Potential modification to e- Linac (Meng Cai)
Add a polarized electron source at the position of the electron source.
  local adjustments are made at the electron source
  no influence to the overall layout of the Linac

## Slide 15: Potential modification to e+ linac (Meng Cai)
The energy of damping ring is increased from 1.1 GeV to ~2.0GeV
Linac
  The energy of EBTL is increased from 1.1 GeV to 2.0 GeV (Magnet & Power supply)
  Add 5 sets of S-band power source to replace 8 sets of C-band power source
    8 C-band klystron (50MW)  5 S-band klystron (80MW)
    16 C-band accelerating structure (1.8m)  20 S-band accelerating structure (3m)
    The length will be increased by 30m

## Slide 16: Updates on booster (Wang Dou, Ji Daheng)
Optimization for better polarization transmission
  Vertical betatron tune changed by ~ -11 units
  W/o change of layout & beam emittance
  Promising for Z &W
  Optimization for Higgs is under way
30 GeV
injection energy
45.6 GeV
80 GeV
120 GeV
TDR lattice
New lattice
 | TDR lattice | New lattice
νy | 116.83 | 105.18
νB/ηarc | 79 | 50
Polarization transmission to Z | ~50% | ~99%
Polarization transmission to W | ~50% | ~95%
Polarization transmission to H | ~20% | ~0%

## Slide 17: R&D Plan in EDR Phase
 | 物理设计 | 极化电子源 | Compton极化测量 | 自旋旋转器
2024年下半年 | 注入器极化保持设计优化 | 束线物理设计，Wien filter物理设计 | 前端区改造，开展激光传输实验 | 超导线圈优化、应力控制研究
2025年上半年 | 自旋旋转器加入lattice | Mott仪方案设计，第一批光阴极试制 | 棚屋改造，搭建调试激光光学平台 | 超导磁体样机设计
2025年下半年 | 更高能量的极化束获取和保持研究 | 搭建光学平台，束线工程设计 | 加速器真空、定时改造，首次束流实验 | 线圈制造工艺研究
2026年上半年 |  | 光阴极激活实验，Mott仪研制 | 提高极化测量精度，开展共振退极化能量测量 | 超导线圈制造
2026年下半年 | 极化物理方案的工程设计，LPA-Ring极化束实验方案设计 | 束线设备安装调试，具备实验条件 |  | 超导磁体加工及组装
2027年上半年 |  | 开展束流实验和极化测量实验 | 束流极化度提高实验研究 | 超导磁体测试
2027年下半年 |  |  |  | 准备LPA-Ring束流实验

## Slide 18: MoU between IHEP & INP, JGU Mainz
Joint efforts in polarized electron beam generation, manipulation and measurements
  Design of spin rotation system, Mott-polarimeter suitable for facilities at IHEP & JGU
Signed by IHEP director, in due process @ JGU
Wien filter
Mott polarimeter
PAPS polarized electron TF @IHEP
400kV DC gun
@JGU Mainz