## Slide 1: Possibility studies of 3T solenoid detector field for CEPC Z pole operation
Yiwei Wang
CEPC day, Nov 27, 2024, IHEP

## Slide 2: Outline
Solenoid field compensation in CEPC TDR
Possibility studies of 3T solenoid detector field for CEPC Z pole operation
  Local, non-local scheme
Work to be done and summary

## Slide 3
  Solenoid field compensation in CEPC TDR
The detector solenoid are compensated locally with anti-solenoids
From IP to the entrance of Q1A (0 to 1.9m):
  ∫Bzdz cancled between the IP and the entrance of final quadrupole with strong anti-solenoid field in 1.1m to 1.9m.
  Field configuration optimized to get emittance minimum and iterate with anti-solenoid technical constraints
From the entrance of Q1A to Q3(1.9m to 10.55m)
  Bz keep fully cancellation along this region
From the Q3 to the last bend (farer than 10.55m)
  ∫Bzdz from detector only < 0.5 T*m.
  Along beam line (not z), fully cancelation in Q3 and pre-cancelation in some extension region (with length of 1m) for the long tail of the detector solenoid field
Compensated solenoid field from IP to the entrance of Q1A (same with TDR for combined field)
Emittance contribution from the from IP to the entrance of Q1A
Z scaled to 2T
Version | Ttbar (3T) | Higgs (3T) | W (3T) | Z (2T)
(pm) | 4.7 | 1.3 | 1.7 | 1.4
op. design (pm) | 0.03 | 0.26 | 0.85 | 0.67
tech. design v6 (pm) | 0.04 | 0.41 | 1.35 | 1.07
tech. design V7 (pm) | 0.04 | 0.36 | 1.20 | 0.95
Version | Ttbar (3T) | Higgs (3T) | W (3T) | Z (2T)
 | 4.7 | 1.3 | 1.7 | 1.4
 | 0.03 | 0.26 | 0.85 | 0.67
 | 0.04 | 0.41 | 1.35 | 1.07
 | 0.04 | 0.36 | 1.20 | 0.95
Updated detector solenoid field @ W/Higgs/ttbar
(Scaled to 2T at IP @ Z)
Chart: Z(m)
Data from Feipeng Ning
tentative, to be optimized with the evolution of the detector design
Z(m)

## Slide 4: Possibility studies of 3T solenoid detector field for CEPC Z pole operation
If keep local compensation scheme
  Bz0 2 T=>3 T
  vertical emittance 0.95pm => 7.2pm, possible to reduced to 5.1 pm (excluded other region) by optimize the technical design
Compensated solenoid field from IP to the entrance of Q1A (same with TDR for combined field)
Emittance contribution from the from IP to the entrance of Q1A
Version | Ttbar (3T) | Higgs (3T) | W (3T) | Z (2T)
(pm) | 4.7 | 1.3 | 1.7 | 1.4
op. design (pm) | 0.03 | 0.26 | 0.85 | 0.67
tech. design v6 (pm) | 0.04 | 0.41 | 1.35 | 1.07
tech. design V7 (pm) | 0.04 | 0.36 | 1.20 | 0.95
Version | Ttbar (3T) | Higgs (3T) | W (3T) | Z (2T)
 | 4.7 | 1.3 | 1.7 | 1.4
 | 0.03 | 0.26 | 0.85 | 0.67
 | 0.04 | 0.41 | 1.35 | 1.07
 | 0.04 | 0.36 | 1.20 | 0.95
Lumi may be a bit lower due to coupling in other regions
Para table by D. Wang, Nov 2024
Z scaled to 2T
Highl lumi Z: 115*10^34/cm^2/s

## Slide 5: Possibility studies of 3T solenoid detector field for CEPC Z pole operation
If non-local compensation scheme
  Bz0 2 T=>3 T
  asumming same length of anti-solenoid in front of the final quadrupoles, dBz 5.7 T => 3 T, vertical emittance 0.95pm => 0.04pm
  effect on Beam dynamics : Peak luminosity will not be limited by the vertical emittance, but the residual orbit and dispersion will disturb the beam dynamics: beam lifetime, polarization
  effect on MDI: Ani-solenoid Bzmax 5.7 T => 3 T, synchrotron radiation power will be reduced with 1/Bzmax^2

## Slide 6: FCCee local vs. non-local compensation A. Ciarma, H. Burkhardt, P. Raimondi et al
Emittance reduced 0.195 pm to 0.002 pm
SR power reduced from 80 kW to 12 kW/IP
local
Non-local
A. Ciarma et al, IPAC24

## Slide 7: FCCee local vs. non-local compensation K. Oide
Emittance reduced 0.43 pm to 0.24 pm
The vertical emittance of type F still looks larger than Burkhardt/Ciarma’s, but it is already enough small.
  The recent required lattice vertical emittance is 1.0 pm
• The type F with seems usable, except for the polarization.
  • A polarization tuning such as vertical bump in the arc is necessary
local
Non-local
K. Oide, 11 Nov 2024

## Slide 8: FCCee local vs. non-local compensation (cont.) K. Oide
The type F with seems usable, except for the polarization.
  • A polarization tuning such as vertical bump in the arc is necessary

## Slide 9: Beam-Beam with solenoid (local scheme)
Beam lost

## Slide 10: Summary
Possibility studies of 3T solenoid detector field for CEPC Z pole operation
  With local compensation scheme: 115 => 26E34/cm^2/s
  With non-local compensation scheme
    effect on Beam dynamics : Peak luminosity will not be limited by the vertical emittance, but the residual orbit and dispersion will disturb the beam dynamics: beam lifetime, polarization (to be checked)
    effect on MDI: Ani-solenoid Bzmax 5.7 T => 3 T, synchrotron radiation power will be reduced with 1/Bzmax^2

## Slide 11: backup

## Slide 12
CEPC Design Parameters
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch Spacing (ns) | 576.9 | 23.1 | 253.8 | 4523.1
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 317/317 | 317/317 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.0/1.7 | 1.05/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (min) | 18 | 77 | 22 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch Spacing (ns) | 576.9 | 23.1 | 253.8 | 4523.1
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 317/317 | 317/317 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.0/1.7 | 1.05/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (min) | 18 | 77 | 22 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
𝛽y∗ and emittance chosen for luminosity
adequate bunch population Ne for the luminosity and the achievable energy acceptance for lattice design
Number of bunches Nb is adjusted to keep the beam current
Updated bunch spacing for the requirement from detector (D. Wang, Aug 2024, CEPC day)
Ref: CEPC TDR; Radiation Detection Technology and Methods (2024) 8:1–1105, https://doi.org/10.1007/s41605-024-00463-y;