## Slide 1
RPC-Scintillator Hybrid Detection System for
Muon Scattering Experiments at HIAF-HIRIBL
Jinning Li on behalf of collaborators
2025/5/17

## Slide 2
Outline
Muon Scattering Experiment on Beamline
Detector Design
-First Stage: ToF-dE PID of Beam Particles
-Multilayer PID System in Higher-momentum Case
Experimental Progress
Summary & Outlook

## Slide 3
Muon Scattering Experiment on Beamline
Muongraphy:
-Archaeology
-Geology
-Nuclear safety
muSR:
-Heavy fermion
-Superconductivity
-Quantum spin liquid
Muonic X-ray:
-Elemental analysis
-Tomography
Fundamental particle physics:
-Muon g-2
-Muon EDM
-Muon CLFV
-…
Muon g-2
Muons play a vital role in both fundamental physics and applied research:
Experiments on muon scattering for new physics are relatively rare internationally.
(NA64mu, MuonE, PKMu…)

## Slide 4
Multi-purpose platform detecting muon scattering on target for cosmic muon or muon beam:
Dark matter
Dark boson
CLFV
Quantum entanglement
Muon-nuclear interaction
Muongraphy
Muon Scattering Experiment on Beamline
Preliminary simulation researches for muon beam experiments:
μ dark matter:
μ DM -> μ DM
Angle distribution
Dark boson:
μ e -> μ e Z’
E loss caused by Z’
Free lepton quantum
entanglement:
μ e -> μ e
Angle and momentum
[1] Phys. Rev. D 110, 016017
[2] arXiv: 2410.20323
[3] arXiv: 2411.12518
[4] arXiv: 2502.20915
[5] arXiv: 2503.22956
Scattering angle distribution of 1GeV muons on dark matter
Sensitivity to dark bosons
PKMu--Probing and Knocking with Muons

## Slide 5
HIAF-HIRIBL is one of the world's earliest high-energy muon beams.
It separates muon\pion generated by projectile-nucleus reaction via magnetic rigidity:
Momentum: 500MeV/c~7.5GeV/c
Flux: 106~107 mu/s
Beam spot size: 10cm*10cm
High-energy muon source with higher momentum purity and brightness.
Muon Scattering Experiment on Beamline
Refers to The Feasibility Study of the GeV-Energy Muon Source Based on HIAF, Yu Xu (IMP)

## Slide 6
First Stage: ToF-dE PID of Beam Particles
By the end of 2025：
A prototype detection system will be implemented on HIRIBL for muon beam condition monitoring, detector testing, and preliminary experiments (scattering on samples, tomography)
Measurement objective
- Beam profile and divergence
- Beam particle identification
Decay; magnetic rigidity selection:
Muon\pion\electron\proton at the same momentum (GeV/c)…
PID basis:
-> Mass difference: ToF, dE
-> Different physical processes: dE

## Slide 7
First Stage: ToF-dE PID of Beam Particles
For 1.2GeV/c μ+ beam, 0.2ns time resolution, 2% Edep resolution:
Electron(positron)--dE、ToF
Proton—ToF、dE
Muons and pions have similar masses;
Muons decay from pions.
Muons and a major part of pions distribute closely on the spectrum.
1cm Plastic Scintillator
+
10cm CsI Scintillator
+
30cm CsI Scintillator
Simulation:
ToF start detector is a thin plastic scintillator in G4BL beamline simulator.
ToF stop detector (~155m to the start counter) and two Edep detectors are simulated in Geant4.

## Slide 8
First Stage: ToF-dE PID of Beam Particles
Positron
Muon
Pion
Pz / (MeV/c)
ToF / ns
ToF-dE: Muons' tail of ToF mixes with pions.
Detailed identification of L-shaped Pz-ToF spectrum of muons:
- Muons decay from pions midway, which might causes ToF of muons distributes in a wide range.
- The momentum tail of muons generated late can be excluded together with pions via ToF cut.
Effective exclusion of pi, p, e, and the momentum tail of muons in relatively low-momentum beam via ToF-dE.

## Slide 9
Multilayer PID System in Higher-momentum Case
ToF-based PID is less effective (ineffective) for higher energy muon\pion or secondary particles.
Differences in energy deposition and scattering in heavy matters (scattering angle\track residual...) will be more significant.
PID system attached to the tracker:
Multilayer Pb and position detectors: Scattering behavior
End scintillator: Energy deposition
ToF detectors before tracker are remained
9
Muon\pion:
ToF difference for 155m length is less than 10ps at 3GeV/c;
Ionization energy losses are very close; Pions can interact via strong force.
Secondaries:
Generated inside the detection system;
Complex composition;
Electrons, gamma, and ions readily deposit energy.

## Slide 10
Multilayer PID System in Higher-momentum Case
3 GeV/c muons and pions (simplified simulation: 4% momentum spread; equal numbers of muons and pions):
ToF / energy deposition / square residual of linear track:
10
Plastic scintillators
10cm-thick Pb
RPC: 2mm gas gap as sensitive detector; hit positions averaged (weighted by ionization energy loss)
Simulation study of higher-momentum muon\pion identification:

## Slide 11
Multilayer PID System in Higher-momentum Case
PID based on the product of likelihoods of 3 variables:
(ToF / energy deposition / square residual of linear track)
Lμ>0.7 |  | 
\ | True Muon | True Pion
Identified Muon | 30756 | 4815
Identified Muon | 12778 | 13321
Likelihood analysis + Pb scatters and absorbs more pions;
Over 70% muon\pion efficiency at 3 GeV/c in this preliminary version.
Upgrade: detailed simulation, delicate detectors (ECal/RICH…)
Study on secondary particle identification is ongoing…
Accumulate spectrums of measurable variable X by simulation as P(X|α) & P(X|β) distributions;
For a certain event with measured value X0, the likelihood values of different initial particles are L(α|X0)=P(X0|α) & L(β|X0)=P(X0|β).
α
β

## Slide 12
PKMu Experimental Progress
4-RPC detection system:
Timing and X-Y position with delay-line readout method.
Accumulating cosmic-ray data for composition analysis and muon-DM scattering searching…
Tracker prototype for further experiments.
Monday 19/05:

## Slide 13
Experimental Progress
New RPC:
Less matter over sensitive area;
2-D strip read-out on a single PCB.
Detector commission with Scintillators: Cosmic-ray test of plastic scintillator bar based on new RPC
Correlation between hit positions measured by RPCs and scintillator

## Slide 14
Summary & Outlook
Muon scattering experiments on HIAF-HIRIBL beamline proposed by PKMu
- DM search, dark boson, quantum entanglement…
The scintillator-RPC hybrid detector for first-stage experiments on HIRIBL
- 1cm plastic+10cm CsI+30cm CsI ToF-dE detection
- Exclude p\e\pi and the tail of muon momentum in reletively low energy beam
Multilayer system for higher momentum beam\secondaries identification
- Multiple Pb-RPCs and the end scintillator layer
- Identification based on likelihood (energy deposition, square residual, ToF…)
- To be upgraded: efficiency optimization and secondary particle identification
Development of the new RPC and detector commission with scintillators are ongoing…