## Slide 1: Operation mode vs Higgs, LowLumi Z & HighLumi Z from Electronics
Vertex
  Higgs & Low LumiZ
    Data rate: ~2Gbps per RSU/chip innermost @triggerless
    Given the power limit of 40mW/cm2，the chip capability is reaching the limit
    Long distance transmission on stitching, or Flex Cable material, are challenging, however there are possible solutions
  High LumiZ
    Data rate: ~4Gbps per chip innermost @CDR MDI @25μm pixel @triggerless
      Even higher in current TDR MDI calculation, needs further optimization from MDI design
      Even higher with 16μm pixel (x 2.5times)
    Estimated power ~110mW/cm2, by using TJ65
      Even higher with 16μm pixel (x 2.5times)
      Not possible with current Stitching Technology for power distribution, only possible by normal Ladder
      Major issue for cooling of conventional CMOS Ladder for innermost
    Not achievable for the compatible design at current technology
  TID
    ~2.1Mrad/y, with 10year operation reaching the limit of a MAPS, a replacement is necessary
  Strategy:
    A replaceable design for Vertex
    First 10 years of Higgs + LowLumi Z @triggerless
    A critical upgrade expected (~15years from now), new technology for HighZ@triggerless, or HighZ@Fast trigger

## Slide 2: Operation mode vs Higgs, LowLumi Z & HighLumi Z from Electronics
ITK
  No general issue for Higgs & Low LumiZ
  Waiting for MDI Bkgrd rate for High LumiZ, total data rate on module may need MTX fiber channels
    However compatible with current design
Pixel TPC
  Higgs & Low LumiZ @ 2T
  To prove the compatibility @ High LumiZ with 3T from the detector side
OTK
  No general issue for Higgs, Low LumiZ & High LumiZ
  However, OTK is fully fixed on TPC
Strategy:
  If Pixel TPC should be replaced or changed to Drift Chamber, the full Tracker also seems to be upgraded
  Otherwise can be stood in HighZ

## Slide 3: Operation mode vs Higgs, LowLumi Z & HighLumi Z from Electronics
ECAL & HCAL & Muon cannot be replaceable due to the total cost
Main issue related to Higgs, Low Z & High Z comes from ECAL Bkgrd rate
  Maximum rate 1 (230 kHz) vs. mean rate 2 (13 kHz) for barrel @Higgs
    The count rate w/ 1Mev threshold is do-able for electronics
      If higher rate, a continues ADC should be considered, results in large power
      Higher rate also impacts a lot on detector’s energy resolution
    But the Bkgrd rate w/o threshold had a big impact on crystal’s rad damage
  Rate too high from current HighZ estimation, needs MDI optimization
    Similar as the vertex for HighZ
Strategy:
  Electronics currently has enough headroom for the readout on module
  The optimization of MDI Bkgrd rate is a must for High Lumi Z
    Matters for crystal radiation damage
    Matters for detector energy resolution
    Matters on electronics FEE scheme (low power FEE or continuous ADC)