## Slide 1: Overview of the muon facility MLF J-PARC MUSE (Muon Science Establishment)
2nd WS of Muon Science Technology and Industry, 10/Jan/’25
Muon Sci. Sec. MLF Div. J-PARC Naritoshi Kawamura

## Slide 2: Ｊ－ＰＡＲＣ
400 MeV linac
3GeV synchrotron (RCS)
30GeV synchrotron (MR)
Materials and Life Science Facility
Hadron facility
Neutrino facility
Nuclear transmutation research
(under design)
4 facilities
3 accelerators

## Slide 3: Requirements of a muon facility
A high-power proton driver with an energy of more than
  Practically, more than 500 MeV accelerators
A pion production target that can be operated safely and stably under high heat deposition and high radiation field
A beamline with high transmission efficiency.
  Particle physics: only a beamline for a specific purpose COMET@J-PARC Hadron, MU2E@Fermi, g-2@Fermi
  Material science/General science: as much as a variety of beamlines to answer a variety of users’ demands
“Specialties” characterizing the facility

## Slide 4: Meson factories in the world
PSI (CW)
TRIUMF (CW)
J-PARC
(Pulse)
ISIS
(Pulse)
MuSIC (CW)
Country | Japan |  | The U.K. | Switzerland | Canada
Facility | J-PARC MUSE | RCNP MuSIC | RAL ISIS | PSI | TRIUMF
proton energy [GeV] | 3.0 | 0.39 | 0.8 | 0.59 | 0.52
proton intensity [MW] | 1.0 | 0.0004 | 0.16 | 1.4 | 0.05
m+ [/s] (surface) | 3108 (U line) | 2104 (50MeV/c) | 6105 | 6108 (mE4) | 2105
m- [/s] | 1107 | 104 | 7104 | 2107 | (5104)
CW / Pulse | Pulse (25Hz) | CW | Pulse (50Hz) | CW | CW

## Slide 5: Time Structure - Pulse and CW
Pulse beam （Synchrotron; J-PARC, ISIS）
  Good S/N under high BG
  Long-time observation (relaxation >10 ms)
  Particle identify
  Low time reso. around (Muonium rotation)
CW beam (Cyclotron; PSI, TRIUMF)
  Practical limit in the beam int. due to pile up events. （MORE in PSI was solved.）
gate
time
20µs
20ms
pulsed muon beam
time
CW muon beam
continus b.g.
A highly segmented spectrometer is required

## Slide 6: Materials and Life Science Facility
RCS (3GeV333mA)
MLF
Beam transport tunnel
Exp. Hall #1
Exp. Hall #2
Muon target
Spallation neutron target
Exp. Hall #1
Exp. Hall #2
100%
>90%
graphite
mercury
m
n
Cascade target
4 kW
21015 p/s @1MW

## Slide 7: The chronicle of the construction
11/May/06
28/Jun/06
29/May/07
13/Jul/07
guide shields
target chamber
BT-line magnets
M-line magnets
Vacuum parts (duct, pillow seal, and so on)
air circulator
roof-shield hatch
FY2004 | FY2005 | FY2006 | FY2007
buried iron block
4/Nov/04
buried iron blocks
21/Oct/05
base plates
base plate
alignment plate
guide shield
target chamber
BT magnet
BT shield
vacuum parts
cask
M magnet
air circulator
cask
CW pipe, cabling
roof shield hatch
system commissioning
★MTAC

## Slide 8: History of facility extension
2008
2011
2013
2015
2016
2020
2022

## Slide 9: H line construction history
2022.1.27 official approval of operation
2022.1.25 inspection by NRA
2022.1.15 test beam
2020～2021 cabling/piping work
magnets in the downstream
2017～2019 electric sub-station
J-PARC center started to secure the extra budget to proceed with the H line construction.
2016 Radiation shield in the exp. hall
2014 Remaining devices in the M2 tunnel
2012 Frontend magnet
2010～ Conceptual design
2012
2014
2016

## Slide 10: Muon Facility in MLF, MUSE
Decay and surface muon （100 keV - 50 MeV） to answer a variety of users’ demands with mSR spectrometer (D1) general purpose (D2)
Ultra slow muon （0.1 - 30 keV） surface/sub-surface /interface sciences (U1A) Test-bench for TmM (U1B)
D-line
U-line
µ+
Surface muon （4 MeV）
dedicated to bulk µSR in 4 experimental areas w/ various sample env:
ultra-low temperature
high magnetic field
pulsed excitations etc.
S-line
µ+
High-intensity surface and high-energy cloud muon （<4 - 50 MeV） for general purpose “fundamental physics”
requiring high precision, high sensitivity
H-line
µ+/µ-
µ+/µ-
General Use
4 areas Simultaneous use
High Intensity General Use
Ultra Slow Muon
Surface/Interface

## Slide 11
Two Scrapers (proton collimator)
Scrape the scattered protons by the target
Renewed in 2015.
Heat deposit：20 kW＠No1
Water cooling
Thermocouple thermometers
Rotating target
To prolong the lifetime of the target against DPA, operation started. #1: 2014-2019 #2: 2019-
Heat deposit：4 kW
Graphite disk: rad. cooling Bearing, jacket: water cooling
Monitors: motor torque, vacuum level, Q-mass for outgas. IR-Radiation thermometer is going to be operated.
Vacuum vessel
In service since 2008
Hea deposit：10 kW
Water (>90%) and air cooling
Thermocouple thermometers
p
m
m
Muon Production Target

## Slide 12: D-line: A decay/surface muon beamline
to D1
to D2
600 ns
100 ns
S.C. Solenoid magnet replaced in FY2015
Kicker magnet
p
m
Double pulse structure due to accelerator bunch
Each pulse is distributed to D1 and D2 areas with a kicker magnet.
Septum magnet
D2: General purpose (open space) area
D1: mSR
mSR spectrometer
elemental-analysis chamber

## Slide 13: U-line: The highest intensity beamline for USM
NC large aperture capture solenoid
SC curved solenoid
SC focusing solenoid w/ wien filters
All beamline magnets are axial focusing
The world strongest pulsed muon: 2108 m+/s, 1107 m-/s
proton

## Slide 14: U-line: Generation of Ultra slow muon (USM)
W(2000C)
USM is generated by the laser resonant ionization method synchronized with the muon beam pulse.

## Slide 15
S-line: A surface muon beamline
Pulse mSR: Highly segmented spectrometer is necessary to avoid the distortion of time spectrum due to pileup.
Cf. 5-T magnet needs 3008-ch
S line is dedicated to transport surface muon beam. By using two kicker system, S line provides muon beams to all 4 areas simultaneously. At present two experimental areas, S1 and S2, were completed.
In the S1 area, a mSR spectrometer was placed.
The S1 area is one of the busiest ones, and users are switching every few days.
The S2 area is partially funded by Okayama-univ. group to perform high-precision measurement of the Mu 1s-2s level.
S1
S2
S3
S4
The 1st spectrum of 5-T magnet
S1
S2
Kicker
Kicker
A. Koda’s presentation

## Slide 16: H-line: Generic-purpose High-intensity beamline
Capture solenoid (HS1)
Bending magnet (HB1)
Gate valve (HGV1)
Transport solenoid
(HS2 and HS3)
↑beam transport tunnel
Kicker magnets and/or wien filers are installable
Septum or bending magnet (HB2)
Experimental area #2 and #3
+B
-B
Conceptual design was proposed by J. Doornbos, TRIUMF.
Adopting a new beamline concept which is confirmed by a particle tracking simulation, the H line is designed to provide a high-intensity beam with a wide-range momentum tunability to each of several areas.
The muon beamline of MLF-TS2 inherited this concept.
Experimental area #1
3GeV proton
Instrument specification of H1
Beam Intensity: 1108 m+(surface)/s 2106 m-(28 MeV/c cloud)/s
2107 m-(40 MeV/c cloud)/s
4107 m-(>50 MeV/c cloud)/s
Beam spot size:
30-35 mm

## Slide 17
Accumulation
H line bldg. （plan）
g-2/EDM exp. Searching for BSM.
ＭＬＦ bldg.
H line
H2
H1
Transmission Muon Microscope
Observation of whole living cell owing to high transmittance capability of muon
H-line: feature prospects (the world’s first muon acc.)
Ｈ line bldg.
Ｈ1
Ｈ line
Acceleration
Cooling
The studies in the H1 area
DeeMe:
muon-to-electron conversion search
MuSEUM:
High-precision measurement of muonium

## Slide 18: MLF Target Station2
Muon:：
10 (target) x 5~10 (Muon capture solenoid)  50 ~100 times gain of flux
Neutron:
10 (target) x 2 (device)  20 times gain of brightness
Moderator & reflector
Neutron Focusing Devices
Neutron Detectors
Proton beam
Rotating tungsten target
Muon Capture Solenoid
Integrated neutron and muon target
6e+14
5e+14
4e+14
3e+14
2e+14
1e+14
0
0 2000 4000
Emission time (ms)
Brightness (n/cm2/sr/Å/s)
SNS TS2
ESS
J-PARC
TS1
SNS
J-PARC
TS2
Neutron Brightness
TS1
3GeV RCS
J-PARC TS2
TS2
Integration of neutron and muon sources (world's first)
J-PARC proton accelerator intensity (1 MW) increased to 1.5 MW
1 MW (17 Hz) for TS1 and 0.5 MW (8 Hz) for TS2
Brightness of MLF TS2 will be the world's highest compared to the next plan of overseas facilities
Chart: Energy [MeV]
This project was selected as one of “The Medium- to the Long Term Academic Research Strategy” by the Science Council of Japan although the budget has not been guaranteed yet.

## Slide 19: Summary
The world’s highest-intensity pulsed muon facility, MUSE, coexists with the neutron facility J-PARC.
In MUSE, we have 4 unique beamlines to answer a demand of various muon sciences; material science, atomic and molecular physics, particle physics, industrial application, elemental analysis, heritage science, etc.
The biggest disadvantage in muon science is there are only 5 facilities in the world. This loses a lot of users’ chances. We welcome a new facility in China.
Thank you. 謝謝