## Slide 1
Progress in the overall mechanical design of CEPC detectors
Ji Quan
(On behalf of the CEPC Mechanics Working Group)
Jan 24, 2025

## Slide 2
Outline
1. General Drawing
2. Connection of the detectors
3. Installation of the detectors
4. Experimental Hall
5. Summary

## Slide 3
TDR Version
1. General Drawing --- Size distribution of Overall Detectors
Continue to optimize :
Pipeline arrangement

## Slide 4
1. General Drawing --- Retrospect the Journey of the General drawing
2019年6月29日
2020年3月31日

## Slide 5
1. General Drawing --- Detectors Mechanical Layout
From outmost to innermost
Yoke
(Muon)
Magnet
HCAL
ECAL
TPC
(OTK)
ITK
Beam pipe
(VTX LumiCal)
Barrel(7)
Endcap(3)
Yoke
(Muon)
HCAL
ECAL
(OTK)
MDI(1)
ACC component
Total weight :
≈ 5,120 t

## Slide 6
1. General Drawing --- Open Range of the End Yokes
Muon
Side Maintenance
Main
maintenance path
Factors considered :
1. Maintenance and replacement
2. Saving floor space

## Slide 7
1. General Drawing --- Pre-assembly Installation
TDR Version

## Slide 8
2. Connection of sub detectors
Barrel Yoke : Fixed on the ground Base
Magnet : Fixed on the Barrel Yoke
Barrel HCAL : Fixed on the Barrel Yoke
Barrel ECAL : Fixed on the Barrel HCAL
TPC+OTK : Fixed on the Barrel ECAL
ITK : Fixed on the TPC
Beampipe(Vertex and LumiCal) : Fixed on the ITK
End-cap ECAL+OTK : Fixed on the Barrel HCAL
End-cap HCAL : Fixed on the Barrel HCAL
(Auxiliary ring or Flange)
End Yoke : Fixed on the ground Base
1. The connection structure should be proximity
2. The connection structure should be adjustable (Remote automatic)
Design Requirements
Base
Continue to optimize :
Connection Structure

## Slide 9
2. Connection of sub detectors --- Magnet
“T” Shape Connection Structure
Weight :
≈ 1560(Yoke) + 290(Magnet) t

## Slide 10
2. Connection of sub detectors --- Barrel HCAL
Half connection rings Structure
Weight :
≈ 960 t

## Slide 11
2. Connection of sub detectors --- Barrel ECAL
“Z” Shape Suspended Structure
Weight :
≈ 150 t

## Slide 12
2. Connection of sub detectors --- TPC
ECAL
TPC
ITK
OTK
Eight-point
suspension structure
Weight :
≈ 2 t

## Slide 13
2. Connection of sub detectors --- TPC + OTK
OTK
Weight :
≈ 1.5 t

## Slide 14
2. Connection of sub detectors --- ITK
Beampipe
Weight :
≈ 80 kg

## Slide 15
2. Connection of sub detectors --- Beampipe
BPM
LumiCAL
Vertex
Pillow Seal
Weight :
≈ 10 kg

## Slide 16
2. Connection of sub detectors --- End ECAL + End OTK
End ECAL
L Connection Ring
Weight :
≈ 25X2 t

## Slide 17
2. Connection of sub detectors --- End HCAL
Eight pairs Adjustable Pad Irons
End HCAL
Weight :
≈ 350X2 t

## Slide 18
3. Installation of the Detectors
Step 1 Alternating installation : Yoke and Magnet (3) --- Barrel and End Yoke, Magnet
Step 2 Core shaft installation : Barrel HCAL and Barrel ECAL (2) --- Barrel Detectors
Step 3 Cantilever installation : TPC(OTK) ITK + Beampipe(Vertex + LumiCal) (3) --- Barrel Detectors
End HCAL and End ECAL (2) --- End Detectors
Step 4 Move the detectors from the Pre-assembly point to the Collision point
Push the accelerator vacuum component into the center of the detector and connect it with the Be beampipe

## Slide 19
3. Installation of the Detectors
Step 1 Alternating installation : Yoke and Magnet (3) --- Barrel and End Yoke, Magnet

## Slide 20
3. Installation of the Detectors
Step 2 Core shaft method installation : HCAL and ECAL (2) --- Barrel Detectors
Continue to optimize :
Merge Animation

## Slide 21
3. Installation of the Detectors
Step 3 Cantilever installation : TPC(OTK) ITK + Beampipe(Vertex + LumiCal) (3) --- Barrel Detectors
End HCAL and End ECAL (2) --- End Detectors
Pre-assembly between of the ITK and Beampipe
Installing
TPC
ITK
Beampipe
End ECAL
End HCAL
Optimize : Display the installation process in animation

## Slide 22
3. Installation of the Detectors
Step 3 Cantilever installation : TPC(OTK) ITK + Beampipe(Vertex + LumiCal) (3) --- Barrel Detectors
End HCAL and End ECAL (2) --- End Detectors
Pipeline path

## Slide 23
3. Installation of the Detectors
Step 4 Move the detectors from the Pre-assembly point to the Collision point

## Slide 24
4. Experimental Hall
Overall layout
Overall layout
Auxiliary facilities
1. Water-cooling system
ECAL
HCAL
TPC
Beampipe
Inlet temperature
15℃
2. Air-cooling system
Vertex
ITK
OTK
5℃
5℃
4. Cryogenic system
Magnet(Det. and ACC.)
3. Gas System
TPC (Ground)
5. Electronics Cabinet
Power Cabinet
ambient temperature : 25 ℃
ambient humidity : ＜60%

## Slide 25
4. Experimental Hall --- Water cooling and Air cooling system
Hall
Design Features :
1. Two for use and one for backup
2. Energy conservation
3. integrated design

## Slide 26
4. Experimental Hall --- Water cooling and Air cooling system
郑州轻工业大学 吴学红(热能与动力学院 院长)
严琪, 李刚, 祁辉荣, ……

## Slide 27
4. Experimental Hall --- Cryogenic system
宁飞鹏, 朱应顺, 杨啸辰, 张祥镇, 陈兵, 王海静, 石澔玙, ……
Total power : Collecting and confirming

## Slide 28
4. Experimental Hall --- Electronics Cabinet and Power Cabinet
Minimum crates from current MDI
110 data crates, 237 power crates, 91 Det-HV crates, 20 Trigger crates
Minimum racks from current MDI
37 data racks, 24 power racks, 23 Det-HV racks, 10 trigger racks (94 in total)
More 2 racks for AC-DC power for all the above racks
96 racks in total
王铮, 魏微, 黄金书, ……

## Slide 29
5. Summary
The design content of the Ref TDR report is basically completed
Suggestion :
Mechanical design must undergo in-depth research and provide feasible solutions
If there are modification requirements, I hope all sub detectors can be modified together

## Slide 30
Thank you for your attention!