## Slide 1
Acceleration of CGEM Digitizer

## Slide 2
Introduction
3 layer Cylindrical GEM
Geant4
Digitization
Particle type, charge,
momentum,
trajectory
Index of fired strips, T & Q
Ionization
Drift and Avalanche
Induction
Electronics Measurement
Cathode
GEM1
GEM2
GEM3
Anode
Time Consuming
Each layer composed by 3 gem foils, a cathode and an anode
Simulation procedure
CGEM cluster

## Slide 3
Drift and Avalanche
Induction
Problem:
Too many electrons!  Too many sampling!
Solution:
Pre-generate random numbers in memory in initialing, using them rather than generating random numbers in real time
Modify the code to improve code spatial locality to fully utilize CPU cache
Take advantage of compiler
Problem:
Many time bins in induction
Solution:
Reduce the numbers of time bins from 2000 to 1200

## Slide 4
Per CGEM cluster
Real-time: using G4Gassian() to generate one random number when needed in real time
Single Acquisition: Pre-generated random numbers in memory in initialing, get one random number when needed & time bins reduction
Batch Acquisition: Pre-generated random numbers in memory in initialing , get a batch of random numbers when needed & time bins reduction
Batch Acquisition & Compiler Optimizations: Batch Acquisition with (g++ -ffast-math -mavx2)
(-ffast-math: complier flag for floating-point number
-mavx2: hardware-related, avaliable after 2013 for Intel and after 2017 for AMD)
4 times faster!
p (0.02 ~ 1.4) GeV/c, (-1,1), (0,)

## Slide 5
Per Track (Only CGEM)
p (0.02 ~ 1.4) GeV/c, (-1,1), (0,)

## Slide 6
T, Q distribution comparison
consistent

## Slide 7
consistent

## Slide 8
Summary
Acceleration of CGEM digitizer has been primarily completed
  4 times faster
  consistent results of CGEM digits with original digitization

## Slide 9
Improving cache hit rate can enhance the execution speed of the code.

## Slide 10
Fitted parameters: Amplitude = 2456.3387436007806,
Mean = 2.8461761092549596, Stddev = 0.8799734127274031
9倍
~10倍
2.85/0.36 = 8倍
Exclude events whose time > 20s
~10倍
All events
Time distribution of full sim
Time distribution of Toy cluster