## Slide 1
Roberto Santorelli
CIEMAT – Madrid
24/Oct/2025
Scaling Up TPCs for Rare Event Searches:
Space Charge and Pile-Up Effects
LIDINE2025 – Hong Kong

## Slide 2
Signal vs Background

## Slide 3: Strategy for rare event research:
Lower background
Bigger detector

## Slide 5: What we need to explore the WIMP parameter space:
Better radiopurity
Bigger detector

## Slide 6
LAr-TPCs have been extremely successful over the last 20 years.
Well proven technology: such types of particle detectors have been used in different fields, spanning 7-8 orders of magnitude difference in energy.
There is currently a strong effort to extend this technology to extreme levels. There are plans for 10 kton-scale detectors with drift length of more than 10 meters.
A successful technology

## Slide 7
Scaling up
’00s kg-scale
’10s ton-scale
’20s tens of ton

## Slide 8
Have we investigated everything about this technology?
A successful story

## Slide 9
Have we investigated everything about this technology?
Is it possible that instrumental effects, negligible at a small scale, become relevant at a “giant” detector?
A successful story

## Slide 10
Frontiers
Signal reconstruction
Charge drift
Light emission

## Slide 11
Frontiers
Signal reconstruction
Charge drift
Light emission

## Slide 12
Reconciling S2 and S1
Conceptual example
time

## Slide 13
Pile-up problems
S1
S1
S2
S2
Max drift time
time

## Slide 14
Pile-up problem
TPCs are “slow” detectors
@ Ed ~0.1 kV/cm)
time

## Slide 15
Pile-up probability
50%
10%
This widely limits the maximum allowed interaction rate in a TPC  setting very stringent limits on the material contamination (gamma)
Pile-up limits the max drift distances (i.e. size of the detector)
Possible mitigation strategies based on M.L.

## Slide 16: Equilibrium in the U-238 chain
Very little mass needed
Relatively fast
Digestion
Destructive
Only U-238 (Th-232)
ICPMS
Larger mass needed
Slow
Non-destructive
Gamma activity (40K+...)
HPGe
Radiochemical
Little mass needed
Relatively fast
Digestion
Destructive
Only Po-210 (Pb-210)

## Slide 17
Back-of-the envelope calculation
Future DM detector: ~100 m2 sensor coverage
Sensor radioactivity ~1 mBq/cm2
1 kHz event rate in the detector

## Slide 19
Frontiers
Signal reconstruction
Charge drift
Light emission

## Slide 20
Charge signal in a TPC

## Slide 21
how about the positive charges?
Charge signal in a TPC

## Slide 22
Space charge
The electron drift in a positively charged volume (neutral target only when the field is off)
Ions have drift velocity which is five to six orders of magnitude lower than the el.
Without taking into account the liquid motion:
(T.H. Dey , T.J. Lewis , J. Phys. D: Appl. Phys. 1 (8) - 1968)
  (M. Torti , Proceedings of the Fourth International Conference on New Frontiers in Physics - 2015 )
  At =1 kV/cm, / to be compared to /
Depending on drift field, ionization rate,
(+liquid motion ...etc)
The electrons drift to the anode, the ions stay!
The space charge can locally modify the electric field, the drift lines and the velocity of electrons

## Slide 23
Space charge
depends on:
Amount of ionization (event energy and rate)
Total drift length
Ion velocity ( and mobility)
/ (to be compared to for =1 kV/cm)
Drift velocity:
…up to 12 m !
Drift distance:
Underground:
“Dominant” contribution from 39Ar (~1 Bq/kg or ~1.4 kBq/m3)
Q-value of 565 keV, 1/3 mean energy, One decay 8e3 pairs,
Mean deposited energy 263 MeV/m3/s, h0 ~ 1.1e7 pairs/m3/s
Surface:
Dominant contribution from muons (168 muons/m2/s)
Minimum ionizing energy:
Mean deposited energy  35 GeV/m3/s, h0  1.5e9 pairs/m3/s
“Ion yield”:

## Slide 24
We can determine the recombination rate in LAr knowing the currents and the drift field.
In a stationary state the density variation is null at any l:
=0 =h
=0 =-h
Electron and ion fluxes as
The recombination rate is given by 
At the same time the variation of the drift field is determined by
the charge density:  >>
These are three coupled differential equations with three functions () and a variable l
Boundary conditions
Mathematical framework - I
(h constant ionization rate)
2
d
d
d
Astropart.Phys. 92 (2017) 11-20

## Slide 25
A
The field variation is a function of l
The cathode voltage necessary to obtain a given field can be calculated integrating the drift field
The field is minimum at 0 () and maximum at the cathode
The secondary recombination probability is equal to the fraction of the surface S(l) spanned the filed lines ending on the anode with respect to the total anode (cathode) area.
Field variation, cathode voltage and secondary recombination probability can be calculated knowing the constant ionization rate, the field at the anode and ion gain
A
Mathematical framework - I

## Slide 26
COMSOL Multiphysics Electrostatics and Transport of Diluted Species modules 1 × 1 × 1 m3 box filled with liquid Argon, 100 kV between the top and the bottom surface.
Finite element analysis
JINST 13 (2018) 04, C04015

## Slide 27
Ed
A
K
Free ion
Free electron
Field distortion, “Secondary”recombination and volume light emission
1 kV/cm
=1 kV/cm
 transverse area (far enough) whose crossing field lines end on one ion (all the lines emerging from the ion cross that section)
=
l=0
l=L
l
Displacement of the reconstructed position
“Uncorrelated” light emission due to “secondary recombination”

## Slide 28
Underground case L=12 m
Astropart.Phys. 92 (2017) 11-20

## Slide 29
HV and electric field
Detector with 12 m drift UG
Dominant contribution from 39Ar
(h0 ~ 1.1e7 pairs/m3/s)
L=12 m
Detector with 6 m drift UG
Dominant contribution from 39Ar
(h0 ~ 1.1e7 pairs/m3/s)
L=6 m

## Slide 30
ArIon: Experimental setup

## Slide 31
  Warm gas
  Cold gas
  Liquid + gas
Field lines from the tip of the needle
COMSOL
Universe 8 (2022) 2, 134,

## Slide 32
Summary & conclusions
LAr-TPCs: a proven, versatile technology! Now scaling up to unprecedented sizes.
Rare event searches need very large exposures, and extraordinary background mitigation/rejection.
Ongoing worldwide R&D (materials radiopurity, UAr, GADMC) trying to address these challenges.
Key open issues: pile-up, space charge effects, light emission.
Roberto Santorelli - LIDINE25, 24/Oct/25 32

## Slide 33
谢谢大家！

## Slide 34
Bonus Slides