## Slide 1
CEPC Detector Magnet
Feipeng Ning
On behalf of Detector magnet team
April 14, 2025, CEPC Detector Review

## Slide 2: Content
Requirements
Physical design of the magnet
Conductor and dummy coil development
Cryogenic system
Mechanical design of the magnet
R&D in the future
Cost estimation
Research team
Summary

## Slide 3: Requirements
This report is about the design and development of the detector magnet for the Ref-TDR. It is related to Chapter 10.

## Slide 4: Requirements
Position and size
Magnetic field
Inner diameter | 7070 mm
Thickness | 700 mm
Outer diameter | 8470 mm
Length | 9050 mm
Energy | t | Higgs | W | Z
Magnetic field | 3T | 3T | 3T | 2T/3T
Energy |  | Higgs | W | Z
Magnetic field | 3T | 3T | 3T | 2T/3T
Magnet
Magnet

## Slide 5
Physical design of the solenoid magnet
Design of the magnet
5
Central magnetic field | 3 T
Inner diameter | 7070 mm
Outer diameter | 8470 mm
Thickness | 700 mm
Length | 9050 mm
Cold mass | 185 tons
Yoke weight | 2960 tons
Magnet weight | 290 tons
Magnet parameters:
Yoke + Muon
Solenoid magnet
HCal

## Slide 6
Physical design of the solenoid magnet
Physical design of the magnet
6
Central magnetic field | 3 T
Inner diameter | 7300 mm
Operating current | 17 kA
Cable length | 33 km
Inductance | 11 H
Stored Energy | 1.54 GJ
Coil parameters:
Magnetic field distribution on the axis
2D Magnetic field simulation
3D Magnetic field simulation
3D Magnetic field simulation

## Slide 7
Physical design of the solenoid magnet
Stress analysis
7
Material | Von Mises stress (MPa)
Coil at 4.2 K | 
Aluminum stabilizer | 4.4-86.1
SC cable | 174-243
Al alloy support | 4.6-36.2
Coil at 4.2 K, energized | 
Aluminum stabilizer | 41.5-95.9
SC cable | 54.9-221
Al alloy support | 43.2-87.4
Coil structure
Cable structure
We will update the coil design in real-time based on the development of high strength aluminum stabilizer and aluminum stabilized superconducting cable.
High strength and High RRR Al stabilizer
NbTi Rutherford cable

## Slide 8: Physical design of the solenoid magnet
Coil Stress analysis
The maximum von mise stress on the aluminum stabilizer (96MPa) is close to the yield strength of the material (105MPa). The safety margin is less than 1/3 of 0.2% yield strength.
The maximum stress on the aluminum stabilizer is only in a very small local area, near the Rutherford cable, with the majority of the region within the stress 70-80 MPa, indicating that the coil can operate safely.
We are still doing the R&D of aluminum stabilizers, aiming to achieve higher strength by combining the required RRR values for quench simulations.

## Slide 9
Physical design of the solenoid magnet
Quench protection
9
Fast dump discharge
50mΩ
The coil protection system is based on a 50 mΩ dump resistor. The maximum voltage and temperature rise of the coil after quench have been controlled within a safe range.
No breakers opening delay

## Slide 10
Physical design of the solenoid magnet
Yoke
10
Yoke parameters：
In order to reduce the detection dead zone of the muon detector, the barrel yoke is designed as a spiral structure.
Barrel yoke: 1560 tons
Single module of the barrel yoke
130 tons
End yoke
700 tons
Barrel yoke (ton) | 1560
Each End yoke (ton) | 700
Total Yoke (ton) | 2960
Diameter(m) & length (m) | 10.37&11.75

## Slide 11
Conductor and dummy coil development
Conductors
  Conductor is the foundation of the magnet development. Most of the detector magnets used or will use the Aluminum-stabilized Nb-Ti/Cu conductors.
11
The IHEP and Toly company have jointly established an aluminum coated conductor production line in 2015.
Rutherford Cable
Aluminum stabilized NbTi/Cu conductor
Extrusion machine
NbTi Rutherford cable
High strength and High RRR Al stabilizer

## Slide 12
Conductor and dummy coil development
Al-stabilized Conductors
12
1.5 km
100 m
LTS: Aluminum stabilized NbTi Rutherford cable
HTS: Aluminum stabilized Stacked REBCO Tape Cable
Aluminum coated conductor production line

## Slide 13
Conductor and dummy coil development
R&D of High Strength and High RRR Aluminum- Stabilizer for Superconducting Cable
13
Yield strength > 100 MPa@4.2K, 74 MPa at room temperature, RRR value > 400
By doping Ni-0.025% Be-0.025.
The Al-0.025%Ni-0.025%Be alloy prepared from 4N8-aluminum achieved high 0.2% yield strength of 75MPa (R.T.) with RRR of 417.
Poisson’s ratio | 0.33/0.34
Young modulus | See the curve
Thermal expansivity | 14.23×10-6 K-1
4.2KRp0.25 | 105MPa
We are still doing the R&D on high-strength pure aluminum to improve its yield strength and solve the problems encountered in mass production.

## Slide 14
Conductor and dummy coil development
Dummy coil development
14
Large scale superconducting coil winding platform
φ7.2m dummy coil
Coil winding, vacuum leak detection, epoxy impregnation curing.
Coil winding
Dummy coil
4 layers*10 turns
The manufacturing accuracy is controlled within ± 1mm

## Slide 15
Cryogenic system
Cooling methods: Thermal siphon
15
Uniform temperature distribution;
High heat transfer efficiency, not limited by source pressure and pressure drop;
Low cost. No need for liquid helium circulation pump
Cooling process diagram
Cooling structure
The verification experiment are being design.
 | Thermosyphon | Force flow
Difference | Need more space to install the phase separator | A liquid helium circulating pump is required
heat exchange capability | 1200 W/(K·m2) | 412.1 W/(K·m2)
Coil maximum temperature | 4.982 K | 5.383 K
Coil average temperature | 4.591 K | 4.972 K
Inner diameter of Liquid helium pipes | Φ15 mm | Φ 20 mm

## Slide 16: Cryogenic system
Coil temperature distribution:
Thermal shield temperature distribution:
Boundary Conditions and Temperature Contour of the coil
Boundary Conditions and Temperature Contour of the thermal shield

## Slide 17: Cryogenic system
Cryogenic System Flowchart

## Slide 18
Mechanical design
2D
Completed the design of the 2D chain and the space occupied by each component.
3D
Completed the design of the 3D structure, added suspension system, cooling pipes, and connection structure.
coil
Thermal shield
suspension rod

## Slide 19
Mechanical design
Suspension system
Thermal shield suspension system:
6 radial rods each end
Material: titanium alloy
Coil suspension system (185 tons):
8 axial rods each end
6 radial rods each end
Material: titanium alloy
Forces and torques resulting from axial and radial offset, and from angular tilt of the coil.
Axial displacement (cm) | 1 | 3 | 10
Axial force (kN) | 484 | 1498 | 5034
Radial displacement (cm) | 1 | 3 | 10
Radial force (kN) | 34.3 | 236 | 656
Angular tilt (angle) | 1/407.5 =0.14° | 3/407.5 =0.42° | 10/407.5 =1.41°
Torque (kN.m) | 1965 | 6170 | 19935
 | Diameter | Length | amount
Axial rods | 30 mm | 3530 mm | 16
Radial rods | 40 mm | 1700 mm | 8
Main pull rods | 48 mm | 1650 mm | 4

## Slide 20: R&D in the future
High strength and high RRR value aluminum stabilizer research.
Full size Aluminum stabilized superconducting cable development.
Detailed design of mechanical system. Optimize the thickness design of magnet.

## Slide 21
Cost estimation
Cost of the detector magnet

## Slide 22
IHEP: staff 13; engineer 5; post doctor 1; students 3
Cooperative institutes and Universities: SJTU, SWJTU, NCEPU, TSINGHUA, IEE, IPC, IPP and so on.
Cooperative companies: Wuxi Toly (aluminum stabilized conductors), Hefei Keye ( coil winding platform and dummy coil development), Xinjiang Zhonghe ( Aluminum stabilizer), WST ( LTS wires), SSCT ( HTS tapes), and so on.
Welcome international cooperation.
Research Team

## Slide 23
Experience: BES III detector magnet
Research Team
Design, processing, manufacturing, and assembly experience of BES III detector magnet;
Safe, stable, and accident free operation for nearly 20 years.

## Slide 24
Experiences: 12T Dipole Magnet
Research Team
12T Dipole Magnet
Development of the LPF1 NbTi+Nb3Sn dual-aperture model dipole magnet from 2017.
Dipole field reached 12 T in 2*Φ14 mm apertures in May 2021 and 12.47 T in July after a thermal cycle.

## Slide 25
Experience: Aluminum stabilized superconducting conductors
Research Team
Dimensions: 15*10 mm2
Number of tapes ：14
Materiel: Al 1100
Complete time: 2023.12
Length: 100 m
HTS: ReBCO cable
Aluminum stabilized Stacked REBCO Tape Cable
100 m
Dimensions: 15*4.7mm2
Number of strands ：14
Materiel : Al(99.99% purity)
Complete time:2017.8
Shear strength (COPPER &Al) > 35MPa
Length: 1.5 km
1.5 km
LTS: NbTi cable
Aluminum stabilized NbTi Rutherford cable
This is the only aluminum coated superconducting cable production line in the world at present.

## Slide 26: Summary
1. We carried out the physical design, mechanical design, and cryogenic system design of the magnet.
2. We have completed the writing of Ref-TDR and will continue to optimize the plan, develop cables, and validate the project in the future.
3. The research team has a lot of experience in developing superconducting magnets, and is confident in the implementation of the project.

## Slide 27
Thank you for your attention!
April 14, 2025, CEPC Detector Review