## Slide 1
Review of accelerator activities in INFN-Frascati
Alessandro Gallo
INFN - LNF
CEPC workshop 2025,
November 6-10 2025
Dongfang Hotel, Guangzhou, China

## Slide 2: INFN-LNF Frascati Labs
Frascati is worldwide known for its historical heritage, gorgeous renaissance villas, viticulture landscapes and wine production.
Since late 50’s it is also well known for hosting LNF, the largest INFN laboratory.
LNF is the fatherland of accelerator in Italy
Long tradition in accelerators for fundamental physics experiments (like ADONE and DAFNE), it hosts a lively particle physics community also participating to many int. experiments
Many accelerator breakthroughs were achieved here :
  Two beam colliders (Touschek heritage)
  Pioneeristic work on Sinchrotron light, undulator, FEL…
  Crabbed waist collision scheme in circular colliders
  Particle driven plasma acceleration
  …
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
2
A. Gallo: Review of accelerator activities in INFN-Frascati

## Slide 3
Electro-synchrotron, 1959
ADA, 1961
Particle accelerators have always been at the core of the INFN Frascati Labs!
ADONE, 1969
DAFNE, 1998
LISA, 1989
EuPRAXIA@SPARC_Lab, 2030
SPARCLAB, 2005
ELI-NP, 2013
CNAO, 2010
EUAPS, 2025
STAR-HE, 2025
SSRIP, 2026
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
3
A. Gallo: Review of accelerator activities in INFN-Frascati

## Slide 4
SUMMARY
Accelerator based internal facilities
  DAFNE complex
  SPARCLab area
The INFN-Frascati flagship project EuPRAXIA@SPARCLab
Collaboration to FCC_ee activities
Construction of accelerators outside LNF as contractor
  STAR ICS source at University of Calabria
  SSRIP radioactive beam source at IFIN-HH Magurele (Ro)
Conclusions
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
4
A. Gallo: Review of accelerator activities in INFN-Frascati

## Slide 5
Internal Infrastructures: the DAFNE Complex
BTF #1/2
DAΦNE Light
The collider is presently in stand-by, after completion of the SIDDHARTA- 2 program, an experiment devoted to production and decay study of exotic atoms
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
5
A. Gallo: Review of accelerator activities in INFN-Frascati

## Slide 6
DAFNE: the Frascati F-factory collider
performance summary over time
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
6
A. Gallo: Review of accelerator activities in INFN-Frascati

## Slide 7
DAFNE: the Siddharta-2 Run
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
7
A. Gallo: Review of accelerator activities in INFN-Frascati
Signal to noise ratio was 3 times higher wrt the one measured in 2009.
The fraction of high-quality data increased significantly along the time thank to collider adiabatic tuning, and machine studies.

## Slide 8
DAFNE future: requests from the users
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
8
A. Gallo: Review of accelerator activities in INFN-Frascati
EXtensive
Kaonic
Atoms research: from
LIthium and
Beryllium to
URanium
EXKALIBUR – A future plan beyond SIDDHARTA-2
EXKALIBUR proposes to conduct a series of unique kaonic atom measurements with a total integrated luminosity ranging from approximately 600 (but also 400) pb to 1500 pb. It is a feasible, comprehensive scientific program that can be executed modularly (i.e., over a few months each year) in the next 2-3 years, becoming a global reference for research on strangeness.
To be underlined that the program is elastic, and one can extend it from 400 pb to more than 1000, in various runs periods
https://news.stanford.edu/stories/2025/01/sodium-ion-batteries-need-breakthroughs-to-compete
Measurements at the sodium and magnesium K edge for new batteries can be performed at the DAFNE-Light soft X-ray beamline. Due to the shortage of the lithium element potential alternatives can be sodium ion batteries (SIB) and magnesium ion batteries (MIB).
100 mm
Very thin sections of paintings needed to achieve information on the the very complex multi-layered structure of paintings need to be studied using FTIR and SR.
as collider:
as synchrotron light source:

## Slide 9
DAFNE future: a Test Facility for the next colliders
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
9
A. Gallo: Review of accelerator activities in INFN-Frascati
COLLIDER MODE
Collision dedicated
  Collision monochromatization, study the possibility to use PM steering magnets.
  Interplay between Beam - Beam and FBK systems by using a calibrated and tunable source of noise
Collision time-sharing
  Validation of eCloud and Ion Trapping code
  Mitigation of eCloud
  Background simulation code
STORAGE RING MODE
Dedicated beam
  (with additional equipment/diagnostics):
  Longitudinal injection
  Crystal collimation with leptons
Additional options:
  Photo-electron emission measurements
  Dust injection to test SBL check dust injector
The idea of using DAFNE as a Test Facility for future collider, eventually in combination with an extension of the operation for fundamental physics users has been considered since long time
see https://agenda.infn.it/event/16334/page/2177-program-timetable
The LNF collider physics team is preparing a structured comprehensive measurement plan.

## Slide 10
Consolidation: electron accelerators of the DAFNE era
DAFNE has represented the backbone of LNF activity for a quarter of century and today is a well exploited scientific investment.
Most of the lepton accelerators of the DAFNE era (colliders or synchrotron radiation sources) have been either stopped or renewed for lifetime extension.
Only one B-factory survived (SUPERKEKB), a new tau-charm factory project (SCTF) is waiting for approval in China, the Russian colliders at lower energy are still in operation.
Essentially all synchrotron radiation sources are moving from 3rd to 4th generation (ESRF was the first one to complete the transition).
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
10
A. Gallo: Review of accelerator activities in INFN-Frascati

## Slide 11
DAFNE consolidation plan - minimal needs for an operation extension of ≈5 years
SYSTEM | COST | MANPOWER
MAGNETS | 2200 k€ | 40 FTE*month
CONTROLS | 310 k€ | 36 FTE*month
BEAM DIAGNOSTICS (only Critical items) | 520 k€ | 22 FTE*month
RF | 710 k€ | 24 FTE*month
VACUUM | 690 k€ | 8 FTE*month
LINAC (only pulsed magnet PS) | 170 k€ | 5 FTE*month
COOLING (Tech. Division) | 1350 k€ | 
ELECTRIC POWER (Tech. Division) | 450 k€ | 
TOTAL | 6400 | 135 FTE*month (DA only)
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
11
A. Gallo: Review of accelerator activities in INFN-Frascati
Expected total budgetary costs are 6.4 M€. The associated impact on manpower workload is especially worrying since the consolidation program would rely essentially on the DA/DT staff, already heavily committed (beyond 100 %) on the operation of the other Lab facilities and construction of the new EuPRAXIA@SPARCLAB infrastructure. Availability of extra resources from external collaborations should be explored at the highest priority for this task.
DAFNE is an aged machine. Most of the lepton accelerators of the DAFNE era have been either stopped or renewed for lifetime extension;
Many DAFNE components are at end of life, or obsolete, or unmaintainable, representing single-points-of-failure. A credible/reliable scientific medium-term program must be based on a consolidation/mitigation plan to remove the weak points and reduce the machine vulnerability
A generic, minimal consolidation plan to extend the collider lifetime for ≈5 years has been elaborated. Neither upgrades nor performance improvements (only preserved in the best case) have been considered, just reduction of the risk of fatal events with minimal effort. Machine modifications eventually required by the collider physics measurements plan could not be included.
Final decisions have not been taken yet

## Slide 12
THE DAFNE LINAC
S band LINear Accelerator
≈ 60 m long
Termoionic gun
4x45 MW klystrons + SLEDs
15 2/3π sections SLAC type 3m long
Upgrade pulse width: ~ 300 ns
 | Design | Operational
Electron beam final energy | 800 MeV | 510 MeV
Positron beam final energy | 550 MeV | 510 MeV
RF frequency | 2856 MHz | 
Positron conversion energy | 250 MeV | 220 MeV
Beam pulse rep. rate | 1 to 50 Hz | 1 to 50 Hz
Beam macropulse length | 10 nsec | 1.4 to 300 nsec
Gun current | 8 A | 8 A
Beam spot on positron converter | 1 mm | 1 mm
norm. Emittance (mm. mrad) | 1 (electron) 10 (positron) | < 1.5
rms Energy spread | 0.5% (electron) 1.0% (positron) | 0.5% (electron) 1.0% (positron)
electron current on positron converter | 5 A | 5.2 A
Max output electron current | >150 mA | 500 mA
Max output positron current | 36 mA | 85 mA
Trasport efficiency from capture section to linac end | 90% | 90%
Accelerating structure | SLAC-type, CG, 2π/3 | 
RF source | 4 x 45 MWp sledded klystrons TH2128C | 
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
12
A. Gallo: Review of accelerator activities in INFN-Frascati

## Slide 13
13
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
A. Gallo: Review of accelerator activities in INFN-Frascati
BEAM TEST FACILITY – LINES 1-2

## Slide 14: PADME experiment at LNF Beam Test Facility
More recently PADME has been focused on the existence verification of a new particle named X17 with a mass of approx. 17 MeV/c2, already proposed to explain anomalies observed in the ATOMKI laboratory in Debrecen, Hungary.
PADME Experiment presently installed in BTF1 hall
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
14
A. Gallo: Review of accelerator activities in INFN-Frascati
In April 2025 it was announced that the analysis of data collected at LNF BTF in 2022 during PADME run III presents a promising result in the search for the hypothetical particle known as X17, an excess with statistical significance of 2σ in correspondence of the mass of 17 MeV indicated by the ATOMKI (Debrecen, Hungary) experiment.
Work in progress (PADME run IV) to shed light …
Since 2018 BTF1 hall is permanently occupied by the detector of PADME, an experiment searching for “dark photons” by colliding e+ beams from BTF with atomic e- of a fixed target.

## Slide 15
Internal Infrastructures: SPARCLAB
In the new century many accelerator centers needed to revise their mission, SLAC and DESY as the major examples, moving from HEP to science based on state-of-the-art radiation sources (both synchrotrons and FEL) for a different, wider and more articulated and interdisciplinary user community.
The SPARC_Lab facility, active since 2005, has given us the opportunity to enter and in the field of advanced study and applications of high brightness electron beam.
We could run an FEL experiment (not for users) and more recently we tested experimentally plasma wave acceleration in the particle-driven modality, with extremely promising results.
In the same complex we also run the sub-PW laser system FLAME for stand-alone experiments or in combinations with the SPARC linac electrons.
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
15

## Slide 16
Internal Infrastructures: SPARCLAB
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
16
Electron beam parameters of the
SPARC photo-injector
RF Gun
S-Band structure
(with solenoids)
C-Band structure
Plasma chamber
EUAPS
THz undulators
(SABINA)
Photocathode
laser
beam
diagnostics line
LINAC:
  RF Gun (clamped, INFN design)
  2 x S-band structures (SLAC-type)
  1 x C-band structure (INFN)
  1 x S-band RF deflector (INFN)
PLASMA CHAMBER
Main Undulator Line
THz Undulator line
Beam Diagnostisc Line (previously dedicated to ICS)

## Slide 17
SPARCLAB
from advanced test facility to EuPRAXIA incubator and THz source for users
Since the beginning of its operation SPARC has been an advanced test facility devoted to particle accelerator R&D and studies, including:
High brightness electron beams
FEL radiation production (SASE, seeded, high harmonics, …)
Advanced beam diagnostics (phase space tomography, EOS, fs synchronization, …)
THz radiation production
Electron-Photon Inverse Compton scattering
At present SPARCLAB has been destinated to two main missions:
Plasma acceleration experiments and, more generally, all the experimental activities to prepare and consolidate the physics and technology required by the EuPRAXIA@SPARCLAB project;
Set-up a FEL THZ radiation user facility (the SABINA project)
SPARC photoinjector
SABINA THz
undulators
FEL THz radiation line to user hutch
The SABINA (Source of Advanced Beam Imaging for Novel Applications) project, co-funded by Regione Lazio, has been recently completed. It consisted in a consolidation of the SPARC electron source and construction of a THz FEL radiation user facility including innovative undulators (Apple-X type), transport line and experimental hutch.
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
17

## Slide 18
SPARCLAB
from advanced test facility to EuPRAXIA incubator and THz source for users
A sample of the many SPARCLAB achievements in Plasma Acceleration physics and technology
increased to 36 MeV (1.2 GV/m) with 500 pC driver
Particle-driven Plasma Acceleration (PWFA)
FEL radiation production
Active Plasma bending
Active Plasma lenses
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
18

## Slide 19
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
19
EUAPS: Eupraxia Advanced Photon Source
a new user facility under installation in the SPARCLAB bunker
A very important characteristic of the electron bunch produced in such interactions is its fs duration. The radiation pulse generated by the electron beam will have equivalent tens of fs duration and this has important implications for time resolved pump–probe experiments.
The radiation will be emitted from a small focal spot, in the order of few micrometers, thus ensuring highly coherent X-rays.
Given these important properties some of the possible and promising applications are surely X-ray phase contrast imaging (XPCI), X-ray absorption (XAS) and emission (XES) spectroscopies.
The ponderomotive force produced by a short and intense laser pulse focused inside a plasma completely expels the plasma electrons away from the region around its propagation front, forming an ion bubble in the wake of the pulse. Electrons trapped at the back of this structure are accelerated and wiggled to produce broadband, synchrotron-like radiation in the keV energy range.
The novel user facility EUPAS based on this concept has been funded by the Italian Government through the Next Generation EU program and is presently in the final installation phase prior to the source commissioning expected in early 2026.
The EUAPS project also includes development of ultra-high-power lasers (INFN LNS) and high rep rate power lasers (INO-CNR, PISA)

## Slide 20
Plasma source for particle acceleration
The Plasma_Lab is devoted to research and technological development activities for designing and characterizing plasma sources needed to implement particle accelerators based on plasma technology
Vacuum chamber to test plasma devices
Plasma modue to create and confine plasmas
Plasma_Lab current activity
  Plasma formation techniques
    based on High-voltage discharges
    based on Laser-pulse ionization
  Plasma source design and characterization
    Study on source shapes to optimize the plasma formation
    Plasma density measurements
Plasma_Lab future activity
  Plasma sources for EuPRAXIA project
    Long sources design (High-voltage or laser methods)
    High repetition rate plasma sources (up to 400 Hz)
    Studies on vacuum systems for high rep rate sources
    New materials for producing stronger plasma sources
PLASMA LAB – an advanced facility for plasma source studies
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
20

## Slide 21
TEX has been co-funded by INFN and Lazio regional government in the framework of the LATINO project (Laboratory in Advanced Technologies for INnOvation) to enhance collaboration with SME. It has been recently upgraded to include C-band (5.7 GHz) with the installation of a new RF power plant partially funded by a next-gen EU project (PNRR Rome Technopole).
It is not only a facility for accelerating structures but also R&D for RF components, LLRF systems, Beam Diagnostics, Vacuum and Control System. Presently we are waiting for the final permission from National Radioprotection Authority to fully operate the facility up to the highest peak-power and rep rate.
TEX – TEst stand for X-band at Frascati
Concrete Bunker and Modulator Cage with the RF Source
Building 7 at LNF
Rack room
Control room
The TEst-stand for X-band (TEX) is a facility conceived for R&D on high gradient X-band (12 GHz) accelerating structures and waveguide components in view of Eupraxia@SPARC_LAB project. TEX is located in bld. 7, the LNF accelerator technology hub.
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
21

## Slide 22
The European project EuPRAXIA
an opportunity to draw a new mission for the INFN Frascati Labs future
The Eupraxia Design Study is a 4-year concluded project within the Horizon 2020 framework programme, culminated with the delivery of a Conceptual Design Report (CDR) in 2019.
The project objective was the design of a first high energy plasma-based accelerator to provide high-quality beam usable in different areas. The study was conceived and organized as a global effort involving a large numbers of research institutes and universities worldwide.
The projects represents a fundamental step bridging the gap between proof-of-principle test experiments and future ultra-compact accelerators for the energy frontier, having already the potentiality to serve a wide community in applied science, industry, medicine.
Thanks to the SPARC_Lab paving activity INFN Frascati Lab has been recognized since the very beginning as a natural and credible candidate to host one of the two construction sites foreseen in the project.
All this finally led to the EuPRAXIA@SPARC_Lab project proposal, where for the first time a user facility will be built based on plasma acceleration. In particular LNF will be the pillar devoted to the implementation of Particle Wake-Field acceleration PWFA technique.
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
22

## Slide 23: The Italian Pillar: EuPRAXIA@SPARC_LAB User Facility
The purpose of the EuPRAXIA@SPARC_LAB User Facility is to establish a research infrastructure that pioneers the use of plasma wakefield acceleration (PWFA) for driving a high-brightness Free-Electron Laser (FEL) in the soft X-ray regime. Its first user beamline, AQUA, will deliver ultrashort femtosecond soft X-ray pulses within the biologically relevant “water window” spectrum, enabling real-time imaging, advanced materials development and investigation of chemical processes with unprecedented spatial and temporal resolution.
•Moderate Energy with High Impact: Operating at around 1 GeV, will deliver Soft X-rays radiation in the “water window”.
•Compact Design: With an accelerating length shorter than 50 meters, it is the most compact facility in the soft X-rays list, at least by a factor 3.
•Technology Demonstrator: it will be also a strategic testbed for integrating advanced acceleration schemes and short period undulators into user-oriented FELs marking a paradigm shift toward compact and cost-effective light sources.
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
23
The EuPRAXIA@SPARCLAB user facility
The facility aims to operate in two modes: a full-RF mode for initial commissioning, and a hybrid RF+PWFA mode that serves as a demonstrator for plasma-driven FELs user operation. Full-RF mode user operation is also possible.

## Slide 24
EuPRAXIA@SPARC_LAB
S-band Injector
X-band Linac
Plasma module
Undulators
AQUA Beamline
ARIA Beamline
Photon beamlines
17.5 m
33.5 m
9 m
28.5 m
54 m
Plasma chamber: 3.5 m
Plasma capillary: 0.6 m
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
24
The EuPRAXIA@SPARCLAB user facility

## Slide 25: X-band linac structures
Describe the X-band accelerating module we want to implement in terms of:
  RF structure design and parameters (electromagnetic design, cooling, etc.)
  Waveguide components (DC, pumping, etc.)
  Expected performance (RF, vacuum, etc.)
  Supports
  Parameters of the power sources (with reference to the dedicated chapter)
Magnetic chicane layout and main parameters.
Quadrupoles and diagnostics
D. Alesini, X-Band LINAC, 9° EUPRAXIA@SPARC_LAB TDR Review meeting, LNF 16-18 June 2025
EuPRAXIA@SPARC_LAB
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
25
X-band Linac structures

## Slide 26
EuPRAXIA@SPARC_LAB
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
26
Plasma Accelerating Module

## Slide 27
EuPRAXIA@SPARC_LAB
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
27
Plasma Accelerating Module

## Slide 28
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
10 Apple X undulators for SASE FEL in the water window with variable polarization
EuPRAXIA@SPARC_LAB
28
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
28
AQUA beamline: Undulators

## Slide 29
GDM
Mirror
Aperture
Spectrometer
Filters
Radial ion. chamber area
Monochromator area
Split & delay line area
Gas absorber
K-B mirrors
Exp. Chamber area
BPM
GDM
BPM
GDM
Filters
29
EuPRAXIA@SPARC_LAB
29
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
29
AQUA Beamline: Photon Beamline

## Slide 30
The expected power consumption for the AQUA operation at 100 Hz repetition rate, delivering up to 1.0 GeV electron beams is 1.1 MW
Electrical loads | kW | %
RF Modulators | 575 | 52
Magnet PSU | 300 | 27
Laser | 15 | 1.3
Experimental users | 10 | 1
Vacuum, electronics and controls | 30 | 2.7
Cooling magnet + RF | 45 | 4.1
HVAC | 120 | 11
Total Expected power consumption | 1095 | 
  Start of the tender procedure for the awarding of the works
30
EuPRAXIA@SPARC_LAB
30
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
30
The Building

## Slide 31
As expected, the cost of the Plasma Module is significantly lower than that of the High Energy Line, almost one fifth, despite delivering the same energy gain, underscoring the economic advantage of plasma-based acceleration technologies in comparison to conventional radio-frequency systems.
The implementation timeline targets 2029 for building readiness and 2031 for minimum operational status, aligned with ESFRI Landmark designation requirements. EuAPS is expected to run as User Facility from 2026
31
EuPRAXIA@SPARC_LAB
31
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
31
Project cost and Timeline

## Slide 32
Sub - systems | TRL | Comments |  |  |  |  |  |  | 
Injector | 9 | S-Band injectors are widely used in many facilities including SPARC_LAB. S-Band technology is fully available in the market. |  |  |  |  |  |  | 
X-Band Linac | 6 | X-Band Linacs are relatively new. Impressive progress has been made and the final testing of the acc. section full prototype will upscale the corresponding TRL level in the upcoming months. |  |  |  |  |  |  | 
Plasma Module | 5 | Extensive R&D has been made to validate the plasma capillary technology and solid results have proved the validity of the technical choice. A full system proven in a real environment is expected to be done in the next year |  |  |  |  |  |  | 
AQUA Undulators | 7 | Technology demonstrated in other facilities (FERMI, SwissFEL, etc.) |  |  |  |  |  |  | 
FEL Beamline | 8 | Most of the components of the photon beamline are implemented at other facilities are commercially available, few systems (needed only for a subset of possible experiments) are still in development |  |  |  |  |  |  | 
RF power system | 8 | X-Band RF power system has been already tested and operated in normal condition in the test-stand. The final operational test will prove the validity and reproducibility of the technical choices in the real setting |  |  |  |  |  |  | 
Laser system | 9 | Photocathode laser is now a proven technology tested in real facilities (including SPARC_LAB). The systems are full available in the market almost as off-the shelf products |  |  |  |  |  |  | 
General elements | 9 | Other elements (Control, mechanics etc) are based on standardized components daily used in other facilities and in other context (e.g. industrial context) |  |  |  |  |  |  | 
TRL LEVEL | TRL Description
TRL 1 | Basic principles observed – Scientific research begins to be translated into applied research and development (R&D).
TRL 2 | Technology concept formulated – The basic principles are explored and practical applications are identified.
TRL 3 | Experimental proof of concept – Active R&D is initiated, including analytical and laboratory studies to validate predictions.
TRL 4 | Technology validated in lab – Basic technological components are integrated to establish that they work together.
TRL 5 | Technology validated in relevant environment – The technology is tested in a simulated or relevant environment
TRL 6 | Technology demonstrated in relevant environment – A prototype system is tested in an environment similar to the operational one.
TRL 7 | System prototype demonstration in operational environment – A working prototype is demonstrated in a real operational setting.
TRL 8 | System complete and qualified – The technology is proven to work in its final form and under expected conditions.
TRL 9 | Actual system proven in operational environment – The technology is fully commercialized and operational in its intended setting.
Risk Mitigation: Two dedicated test facilities, SPARC_LAB and PLASMA_LAB, are actively supporting the development and validation of plasma acceleration concepts, while the TeX facility is dedicated to high power testing of X-band performance. Achieving a Technology Readiness Level (TRL) above 7 for these subsystems will only be possible following the successful operation of the EuPRAXIA@SPARC_LAB facility.
32
EuPRAXIA@SPARC_LAB
32
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
32
Technological Readiness Level

## Slide 33
INFN-LNF contribution to FCC-ee studies | CERN-INFN MoU Addenda
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
33
FCC
INFN Frascati is part of the collaboration contributing to the studies for the CERN Future Circular Collider. In particular LNF team is involved in two main distinct sectors:
Design of the Damping Ring and Transfer Lines as part of the collider injector system
  Includes low impedance design of the DR vacuum chamber
Design and optimizazion of the Machine-Detector Interface (MDI)
  Interaction Region (IR) mechanical design
  Background studies
  Experimental activities on full-scale IR mechanical prototype (IR mock-up)

## Slide 34
FCC-ee Damping Ring/TL design
Present Injector Layout Baseline
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
34
RF system
injection e-
extraction e+
injection e+
extraction e-
  3 WIGGLER insertion h = h’ =0 in the arcs to enhance damping
Positron linac
Electron linac
Electron transfer line
HE linac
e+
e-
e+
e-
20 GeV
2.86 GeV
BC
EC
Design constrains
Available footprint space (≈120x120 m2)
Dipoles Field < 1T (normal conducting)
Wiggler Field < 1.9 T (normal conducting)
Quadrupole Gradient kQ < 50 T/m
Sextupole strength kS< 1700 T/m2
Minimal element spacing Ld > 8 cm
Element length: LQUA > 20 cm, LSXP (LOCT/LKCK/...)> 10 cm

## Slide 35
FCC-ee MDI activities
Non-local Solenoid Compensation Scheme
Alternative scheme inspired by DAFNE rotating frame method
Lower SR and coupling, easier spatial constraints
IR Mechanical Model
Engineered design of beam pipe, cooling system and support
Material budget and structural optimization
Assembly strategy for innermost detectors
Background Simulations
Estimation of beam losses in the MDI region
Halo collimation scheme and SR maskings
Beam-gas and Touschek scattering
Dedicated interface tool for single beam background studies
Occupancy calculation in the subdetectors
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
35

## Slide 36
FCC-ee IR Mockup
@INFN-LNF
1:1 Aluminium model of the Central Chamber beam pipe, cooled with liquid paraffin (n-decane)
Thermal and hydraulic characterization of the cooling system under expected heat load from impedence
Elliptoconical chambers in final stage of manifacture (EBW)
Carbon fibre support tube for innermost subdetectors to be manifactured
VXD integration tests with INFN-Pisa
Funded with ESPP_A_FCCMDI
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
36

## Slide 37
“Off-shore” accelerator construction: STAR-HE at UniCal
Sept. 26, 2025
The STAR Project (Southern Europe Thomson Back-Scattering Source for Applied Research) is a Thomson Back-Scattering (TBS) X-ray Source located at the University of Calabria campus. It will provide monochromatic, polarized, and tunable hard X-ray in the range 30 keV to 140 keV as investigative tools for matter science.
INFN has recently completed and put in operation the linear accelerator driving the source as UNICAL contractor.
First beam: September 2025
Inauguration: October 28th 2025 !!!
Still some commissioning work left
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
37

## Slide 38
“Off-shore” accelerator construction: SSRIP at IFIN-HH (Ro)
The radioactive beam facility project SSRIP (Scalable System for Radio Isotopes Production) is an electron LINAC for irradiation under construction by INFN Frascati at IFIN-HH site of Magurele (Ro). It will integrate all the component formerly delivered for ELI-NP stage I by the Eurogammas consortium (of which the INFN was part). For this realization INFN is an IFIN-HH contractor.
Installation proceeding fairly smoothly
Project ends scheduled at end of 2026 with beam demonstration
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
38

## Slide 39
9 Technical Services
1 Scientific Staff unit
1 Secretariat Office
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
39

## Slide 40
This is a very busy but exciting period for our Lab, we have extreme challenging enterprises ahead, the realization of a new and advanced research infrastructure together with the completion of various initiatives (included those funded by the next generation EU recovery plan) and the ordinary run and maintenance of the existing facilities.
Conclusion: future accelerator landscape at INFN-LNF
Besides the iconic image of the Frascati collider dome the profile of a new building will appear, a major change in the Lab landscape and mission. "The Lab’s ambition is to sit at the forefront of a novel, revolutionary paradigm for particle accelerators: the utilization of plasma waves to routinely run facilities at multi-GeV/m gradients.
Nevertheless, the tradition and expertise of the Lab in the lepton storage ring physics is expected to last and survive. While the future program of our collider DAFNE and the required consolidation plan are still under discussion, the collaboration with existing colliders and the participation in the preparation of future ones such as FCCee are crucial opportunities to renew and keep alive our heritage.
A. Gallo: Review of accelerator activities in INFN-Frascati
CEPC workshop 2025, November 6-10 2025 , Dongfang Hotel, Guangzhou, China
40