## Slide 1
CEPC vacuum system EDR plan and status
Yongsheng Ma
Vacuum group, IHEP,CAS
Nov 7th 2025

## Slide 2: Content
Preview of CEPC vacuum system
Discussion on vacuum chamber with photon absorber of collider ring
MDI vacuum progress
Production line development of NEG coating/ Spray for heating film in EDR
Possibility of AL alloy vacuum chamber in use of collider ring
Summary

## Slide 3: Preview of CEPC vacuum system
Accelerator | length/m
LINAC | 1,601+335
Damping ring | 147
Booster | 100,000
Collider | 200,000
Transport line | 4,680
Total length/m | 306,763
 | E | I | ρ
 | Gev | A | m
Higgs | 120 | 0.0167 | 10700
W | 80 | 0.084 | 10700
Z | 45.5 | 0.803 | 10700
tt | 180 | 0.0033 | 10700
Machine and Vacuum Parameters
Technical developments in TDR
Those prototypes have a good application in HEPS.

## Slide 4: Vacuum requirements and configuration
 | Energy | Material | Cross Section/mm | Length/m | Dynamic pressure /Torr
LINAC | 30 GeV | Stainless steel, copper | Φ20~30 | 1,601+ 335 (BTL) | Acc <2×10-7 E-gun<2×10-8
Damping ring | 1.1 GeV | Extruded aluminum 6061 | Φ30/Al 6061, 2mm | 147 | <2×10-8
Booster | 30 to 180 GeV | Extruded aluminum 6061 | Φ56/thickness of 2mm | 100,000 | <3×10-8 tt<4×10-8
Collider | 45.5~180 GeV | Extruded copper, NEG film SEY<1.2 | Φ56/thickness of 2mm | 100,000×2 | Z<8×10-10 tt<1×10-8
MDI | 45.5~180 GeV | Copper/tungsten alloy, NEG film | Φ20 | 12 | <3×10-9
LTB | 30 GeV | Stainless steel | Φ56 | 3,000 | <1×10-7
BTC(CTB) | 6 GeV | Stainless steel | Φ56 | 240×6 | <1×10-7
DL | 1.1 GeV | Stainless steel | Φ30 | 240 | <1×10-7

## Slide 5: Discussion on vacuum chamber with photon absorber
The round vacuum chamber convert to antechamber;
Absorber will be welded together with vacuum chamber;
Colling pipe is necessary: the total heat load due to the resistive wall for collider single ring is about 2MW under 50 MW mode; SR reflection from absorber.
The structure of vacuum chamber will be more complex.
NEG coating , spraying heating layer will be more complex.
Changes to vacuum chamber
56
A.9.2 Recommendations 1. A thorough comparison of the advantages and disadvantages of the proposed distributed approach versus the photon stopper approach is necessary for effective management of synchrotron radiation;
First CEPC IARC EDR Review Report
VC with photon absorber

## Slide 6
There will be 2 or 3 absorbers in one vacuum chamber, if its length is still ~11meters.
The manufacture of absorber is very challenge;
The complex internal geometry of the SRAs calls for the use of additive manufacturing technology; (FCC)
Conventional dematerializing manufacturing (mechanical processing)
Structure of vacuum chamber with absorbers
Lots risks of vacuum chamber with Absorbers due to the welding between beam pipe and absorbers
The risk of leakage has increased due to the large number of welding seals.(焊缝漏的风险)
Extra impedance due to mechanical Dimension error；
More outgassing due to outer welding;(外焊接带来夹气)
Prototypes should be taken out to test feasibility.

## Slide 7: Mechanical adaption with magnets
[1]GAO J. CEPC Technical Design Report: Accelerator [J]. Radiation Detection Technology and Methods, 2024, 8(1): 1-1105.

## Slide 8: Preliminary design of absorbers power and distribution
No. | SR Power (W) | Power density (W/mm2) | Distance(mm)
ABS_01 | 4311.53 | 101.31 | 
ABS_02 | 4204.12 | 95.17 | 5893
ABS_03 | 4403.59 | 96.33 | 5697
ABS_04 | 4280.84 | 107.48 | 6100
ABS_05 | 4265.50 | 101.40 | 6675
ABS_06 | 3912.60 | 99.13 | 5247
ABS_07 | 4173.44 | 93.85 | 5793
ABS_08 | 4326.87 | 94.98 | 5547
ABS_09 | 4127.41 | 101.96 | 6334
ABS_10 | 4234.81 | 99.77 | 6093
ABS_11 | 4265.50 | 98.00 | 5686
ABS_12 | 4158.09 | 91.23 | 5693
ABS_13 | 4188.78 | 90.27 | 5590
ABS_14 | 4250.15 | 101.10 | 6601
ABS_15 | 4188.78 | 93.87 | 6688
ABS_16 | 4142.75 | 87.60 | 6263
ABS_17 | 4112.06 | 83.30 | 6128
ABS_18 | 4219.47 | 103.88 | 6674
ABS_19 | 4188.78 | 97.48 | 6993
ABS_20 | 4219.47 | 95.64 | 5646
ABS_21 | 4142.75 | 90.71 | 5693
The distance of absorbers is about 5.2~7m, corresponding deposited power varies from 3.9~ 4.4kw.
Qi Li

## Slide 9: Design of Absorber
Dipole magnet n+i
Dipole magnet n
Absorbers bear high power density synchronous light deposition, requiring good machining and installation accuracy.
The layout of vacuum devices will be more complex.
SR power from dipole magnet | Power density | Area of absorber | Length of absorber
W | W/mm2 | mm2 | mm
4071.01 | 15 | 271.4 | 407.10
The manufacture of absorbers is very challenging.
SR power 3660W
Heat exchange coefficient 10000W/m2-℃
Max temperature 206 ℃
Cooling surface temperature 128 ℃（ cooling water 22 ℃ ）

## Slide 10: Impedance of absorbers
Main contribution to the ring impedance
  Resistive wall impedance  no significant change between circular and antechamber
  Longitudinal geometrical impedance
  Horizontal geometrical impedance
Number per ring: 12217
Distance to the beam: 29.5mm
Length of top flat: 30mm
Taper angle upstream: 1/5
Taper angle downstream: 1/3
 Mainly broadband, no narrowband resonances
Wang Na

## Slide 11: Impedance of absorbers
Main contribution to the ring impedance
  Resistive wall impedance  no significant change between circular and antechamber
  Longitudinal geometrical impedance
  Horizontal geometrical impedance
With bunch length of 3 mm, the broadband impedance contributions:
  Kloss=1.16E-3 V/pC
  ZL=4.1E-8 Ohm
  Kx=0.223 V/pC/m
 | Z¦¦/n [m] | kloss [V/pC] | kx [kV/pC/m]
Absorbers | 0.5 | 14.2 | 3.4
Total | 16.5 | 819.8 | 65.5
Occupation | 3% | 2% | 5%
Evaluate @z=3mm
The impedance increase due to the absorbers are less than 5% of the total budget  acceptable from the instabilities
Na Wang

## Slide 12
MDI vacuum progress
The total length of MDI vacuum system is about 14m, mainly composed of vacuum chamber, NEG coating, water cooling system, support system, etc.
The energy, beam life, and pressure indicators of the vacuum system at MDI are as the same as collider ring;
Crotch chamber
Z: 783~855mm
Φ20 chamber
Z: 855~4438mm
Φ30 chamber
Z: 4653~7000mm
Φ20-30 chamber
Z: 4438~4653mm
      The length of MDI vacuum chamber is about 14m.
      Central beam pipe：-700~700mm；
      RVC：700-783mm；
      Chamber：783-7000mm.

## Slide 13
The structure of beam chamber
      The vacuum chamber is made of CuCrZr (C18150), with a cooling water pipe welded on the outer side. The cross-section of the circular pipe with a diameter of 20 is shown in the figure.
      Inner diameter φ20mm；
      Outer diameter φ26mm；
      Width 29mm；
      Multi-layer heating film：0.5mm.
      The length of MDI vacuum chamber is about 14m.
      Central beam pipe：-700~700mm；
      RVC：700-783mm；
      Chamber：783-7000mm.
35
R10
15
Notes: Secondary Electron Yield

## Slide 14
Thermal simulation
      Thermal analyses of chamber at cryostat @Higgs, 50MW. The highest temperature at crotch part is 42.9 ℃; The highest temperature at Masks is 38.5 ℃.
      Material ：C18150
      Cooling medium: water
      Inlet temperature：22℃
      Inlet velocity：1.5-2m/s (14.7-19.6 L/min)
Lei Zhang
Notes: Secondary Electron Yield

## Slide 15
      The central beam pipe and luminal cannot be NEG-coated or baked.
      The worst vacuum pressure is 7.8E-9mbar. Most other part of vacuum chambers are better than 2E-9mbar.
      Sticking factor is 0.003；
      The out gassing rate of baked chamber is 1E-12 mabr·L/(s·cm2) , no baked part is 1E-11 mabr·L/(s·cm2) .
Vacuum pressure simulation
7.2m, Mask-2
1.9m, Mask-1
Central chamber without NEG coating.No baking.
Lei Zhang
Notes: Secondary Electron Yield

## Slide 16: Preview of NEG coating/ Spray for heating film production line
Items | Specifications
Dimension | L 11400-d56-D62
Weight | 50~100kg
NEG coating | Thickness：200nm±30% SEY<1.1 S、Q、life-times
Spraying heating | Thickness<0.5mm Heating temperature <300℃
Requirement
Due to the difference in length, two production lines will be used to complete the production of vacuum chambers for the CEPC collider. The quantity of NEG coating and spraying facilities for the two lines varies to match the production speed.
The full quantity of vacuum chambers for the collider will be manufactured within five years, utilizing two production lines operating at a combined capacity of 4,500 units per year.
Advantages
More stable process, less manpower, less NEG coating facility, more adaptive capacity in production, etc.
Heating layer spraying
NEG coating
Cleaning

## Slide 17: Critical Step in the Production Line
Important nodes and progresses
Technical scheme review
Procurement bidding
Process Review prior to Manufacturing
Most of components have been manufactured 2025.11
The production line will be conditioned 2026.3
2024.10
2024.12
2025.6
Process Review prior to Manufacturing
Project kicker off
Manufacturer visit

## Slide 18: Production line composition
Classification | Sub-devices | Parameters | Note
Electron-beam welder | Electron-beam gun Power supply Vacuum chamber | Meets the Length of 11.4m vacuum chamber 6 working position | Design and manufacturing
Brazing | Mechanical holder Power supply | 350℃ 11.4m long | Low temperature brazing in air by conductivity heating, expecting stead by double hole copper tube
Heating film spraying facility | Electron-beam gun Power supply Controller Mechanical Structure | Meets the Length of 11.4m vacuum chamber Multilayer Spray Ceramic and conductivity layer | R&D
NEG coating tower | Pumping system Vacuum measurement Power supply Vacuum chambers Discharge Gas Cathode、controller | Meets the Length of 11.4m vacuum chamber 6 working position Background vacuum <5e-7Pa Baking temperature 200℃ | Developing to be more fitted the production line
Measurement and testing | Dimension measurement Leakage testing | Dimension measurement 11.5m/0.1mm Leakage testing 1e-10 mbar·L/s | Design and manufacturing
Cleaning | rinsing | deionized water rinsing | Design and manufacturing
Production line auxiliary equipment | Moving band robot arm system controller | Meets the Length of 11.4m vacuum chamber | Design and manufacturing

## Slide 19: Procedure of NEG coating & spraying of production line
Spraying (Air plasma spraying)
Sandblasting
Spraying_Isolation_layer
Spraying_Conductivity-layer
Spraying_Isolation-layer
Spraying_Contactor-layer
Cleaning
Outside
Inside
NEG coating
vacuum chambers, cathodes assembling by mechanical arms (flanges sealing).
Leakage testing.
Deliver the assembles to vacuum oven/ baking/ NEG coating;
Disassembly the vacuum chambers
Function | Materials | Thichness/um
Transition-layer | MCrAlY alloy | 50~100
Isolation-layer | Al2O3 cermic | ~200
Conductivity-layer | NiCr alloy | 50~100
Isolation-layer | Al2O3 cermic | ~200
Contactor-layer | Copper | ~50
Notes: Atmosphere plasma spray

## Slide 20
NEG coating, VC assembly and disassembly with automatic robot arms.
Cathodes driven
Cathodes
VC assembly
Vacuum oven
Layout & composition of NEG coating facility
Kr+
磁环
Inside magnet
DCMS for NEG coating

## Slide 21
Vacuum chamber automatic assembly
X
z
Sealing gasket installation
Flanges fastening

## Slide 22
VC inserted into the oven
VC & cathode support
UHV system for NEG coating
Vacuum chamber automatic assembly
Safety insurence
Due to the diameter of CEPC is D56, we plan to replace the cathode wire with a magnetron sputtering cathode
Permanent magnet instead of the solenoid which supplies magnetic field for DCMS;
By combining the low vacuum chamber outside of the vacuum chambers to be coated with NEG, the high vacuum process is simplified;

## Slide 23: Prototype of cathode for NEG coating
23000mm(23 meters)
Magnetron Cathode
~12000mm(12 meters)
After testing and conditioning, the cathode achieves a stable DCMS plasma discharge under 367 V and 1.1 A.
Motor for magnets driven
23

## Slide 24: Manufacturing progress of production line
The 12-meter cathode prototype for NEG coating is under manufacturing.
The oven for NEG coating, which provides a low vacuum environment and baking capabilities, is under manufacturing.

## Slide 25: Manufacturing progress of production line
The main components of vacuum oven for NEG coating have been manufactured and under are now being assembled.

## Slide 26: VC baking & Why spray heating film
Necessity:
In order to meet the ultra-high vacuum requirement of achieving a dynamic vacuum level of 3.0E-10 mbar.
NEG coating reactivation
The baking is the most crucial procedure in achieving ultra-high vacuum
N2
O2
H2
H2O
CO2
N2
H2
H2O
CO2
CO
O2
Heat
High
vacuum
or
inert gas
MO
MC
O
C
Too thick
Lifetime is very short under SR of CEPC

## Slide 27: Spraying for heating film
Conductivity layer
Ceramic layer
Ceramic layer
Cu/ceramic transition layer
Vacuum chamber
I
Conduction
Convection
Radiation
Multilayer heating film will be coated outside of the vacuum chamber which composited by ceramic and conductivity layer
The heating temperature could reach 250℃
Heating layer
Thickness： 0.5mm
solution
Plasma spraying
Processing of spray
Cu/Ag NW
Electric heating circuit
De-icing for airplane
Related commercial products

## Slide 28: Plasma Spraying system
Sandblasting room
Plasma Spraying
& Laser etching room
The vacuum chamber will be transferred by motorized conveyance to the coating station, where a robotic arm will execute multi-layer deposition using an automated spray gun.
Notes: Reciprocating motion

## Slide 29: Heating coating spraying
项目 | 参数
驱动方式 | 旋转气缸驱动
遮蔽材质 | 不锈钢
轴向可调节范围 | 100mm
Etching by laser
Sandblasting
Plasma Spraying
The processing step for the heating coating spraying

## Slide 30: Length of 1.5m prototype of Spraying
Sandblasting
Spraying_Isolation_layer
Spraying_Conductivity-layer
Spraying_Isolation-layer
Installation
Spraying
A 1.5-meter prototype has been developed to validate key process steps that will be implemented in the production line.

## Slide 31: Elements and thickness testing
Conductivity layer
Ceramic layer
Ceramic layer
Cu/ceramic transition layer
Vacuum chamber
I
Conduction
Convection
Radiation
Al2O3
NiCr
Function | Materials | Thichness/um
Transition-layer | NiCr alloy | 47.6
Isolation-layer | Al2O3 cermic | 224
Conductivity-layer | NiCr alloy | 65.5
Isolation-layer | Al2O3 cermic | 174

## Slide 32: Prototype spraying of a heating coating and tests
Dimension: L1500*D60 Substrate: copper
Reheating test more than 12 times
Adhesion test in ultrasonic resining
Dimension: L400*D24 Substrate: copper
Due to the strong natural convection formed inside the pipeline, the highest temperature point deviates from the center, and the temperature drop at both ends is significant.

## Slide 33: Plasma spraying devices
The spraying system is similar to the system detailed in the following pictures.

## Slide 34: All metal gate valve development with company
Under the demand traction of CEPC, two enterprises simultaneously carried out technological research and development, and the opened/closed times of CF63 gate valve are more than 2000 times.
日扬电子科技（上海）有限公司（HTC）
上海真空阀门制造有限公司（SHZK）
Gate Valve Evaluation Meeting 2025.2.20

## Slide 35: Possibility of AL alloy vacuum chamber in use of collider ring
AL alloy (6000 series) vacuum chamber have been used in lots of accelerators, such as BEPCII, LEP, superKEKB (e+), and insertion devices of light source, under conditions where baking temperature is lower than180℃. However, their use is limited in NEG-coated vacuum chambers because the yield strength of the material undergoes a sharp decline when the baking temperature exceeds 180°C.
The 7000 series alloy exhibits superior high-temperature mechanical properties, with a yield strength of 200 MPa at 250°C compared to 150 MPa for the 6000 series—a 33% increase.

## Slide 36: Conclusion
The impedance increase due to the absorbers are less than 5% of the total budget;
Lots risks of vacuum chamber with absorbers due to the welding between beam pipe and absorbers; The structure of vacuum chamber will be more complex, bad to NEG coating process;
Prototypes of absorbers should be taken out to access its feasibility.
Production line of vacuum chambers NEG coating and spraying heating has been carried out;
Prototype of Spraying heating film and tests have been carried out;
Feasibility study of AL alloy 7000 vacuum chamber in use of collider ring in next step;
NEG coating optimization for low impedance film will be carried out.

## Slide 37
Thanks for your attention!