## Slide 1
Radiation in the tunnel and its mitigation for CEPC EDR
Guangyi Tang
On behalf of CEPC RP Group
The 2025 International Workshop on the CEPC, Nov. 6, 2025, Guangzhou.

## Slide 2: Content
Introduction
CEPC TDR shielding scheme
  Prompt dose level in the tunnel for TDR scheme
  Protection of radiation-sensitive equipment
    Cables, electronics, optical fiber …
  Induced dose level in the tunnel for TDR scheme
Conclusion

## Slide 3: Upper limit of absorber dose for electronics
Radiation-sensitive equipment: electronics, optical fibers and cables/insulations.
In the collider tunnel, the radiation level is much higher than in the linac/transport line/damping ring. Electronics in the collider tunnel without shielding may be broken soon.
  First priority to design shielding in collider tunnel.
Use absorbed dose, 1MeV-equivalent neutron fluence and high energy hadron fluence to assess the radiation exposure levels.
For electronics:
  High Energy hadron fluence <
  Absorbed dose < 20 Gy/y
  1MeV equivalent neutron fluence <
CAS - CERN Accelerator School: Power Converters, 245-263
We set upper limits here.
Notes: Upper limits changed to red color.

## Slide 4: Upper limit of absorber dose for optical fiber and cable
Radiation-sensitive equipment: electronics, optical fibers and cables/insulations.
In the collider tunnel, the radiation level is much higher than in the linac/transport line/damping ring. Electronics in the collider tunnel without shielding may be broken soon.
  First priority to design shielding in collider tunnel.
Use absorbed dose, 1MeV-equivalent neutron fluence and high energy hadron fluence to assess the radiation exposure levels.
For optical fibers:
  Accumulated absorbed dose < 10 ~ 100 Gy for ordinary optical fiber
  Accumulated absorbed dose < 10 kGy for radiation-resistant optical fiber
For cables/insulations:
  Absorbed dose < 1 MGy considered for polyethylene, PVC, etc.
RADIATION PROBLEMS IN THE DESIGN OF THE LARGE ELECTRON - POSITRON COLLIDER (LEP). (1984)
2025 European Edition of the International Workshop on the Circular Electron-Positron Collider (CEPC), Barcelona, Spain: CEPC large scale and precision control system study in EDR (remotely) · IFAE Indico
Total dose:
354Gy@HCF，268Gy@RRF，195Gy@G652
Radiation Induced Attenuation (dB)

## Slide 5: CEPC TDR scheme: collider tunnel and auxiliary tunnel maze
5.8m
2.5m
3.5m
2.5m
3.5m
2.5m
0.5m
0.5m
0.5m
The dose level in the tunnel is so high that would damage cables, fibers and electronics in the tunnel without shielding.
Add lead/concrete block to protect the cables on the cable trays. The cable trays are located in the inner wall.
Auxiliary tunnels with mazes are designed to contain all electronics.
collider
booster
Lead/concrete block
support
internal
external
cable trays
6m
5m
Auxiliary tunnel
booster
collider
collider
internal
external
internal
external

## Slide 6: CEPC dipole, quadrupole and sextupole in CAD
Dipole typical length: 5m; quadrupole typical length: 3m; sextupole typical length: 1.5m;

## Slide 7: CEPC TDR scheme simulation setup: a typical collider arc region
According to mechanical arrangement, a beamline shows below
Dipoles with bellows and pumps -> Correctors -> Quadrupole -> BPMs -> Sextopoles -> Dipoles with bellows and pumps

## Slide 8: Lead in dipole and around vacuum chamber
dipole：2.5cm thick, 6.6cm high;
epoxy resin coil lead
Lead area: 66
Vacuum chamber：2.5cm thick, 11~17cm wide
Lead area: 70
2.5cm
2.5cm
2.5cm
2.5cm
6.6cm
17cm
11cm
16cm
12cm

## Slide 9: Lead in quadrupole and sextupole
Quadrupole: 2.5cm thick
epoxy resin coil lead
Lead area: 97
Sextupole: 2.5cm thick
Lead area: 152
2.5cm
2.5cm
2.5cm
2.5cm
2.5cm
2.5cm
2.5cm
2.5cm

## Slide 10: Lead shielding at the end of magnet
At dipole end: transvers area73cm x 20cm, 3~5cm thick
The volume and weight of lead used for the collider can be obtained, 996 (10916 tons)
  FCC: 11360 tons Pb94Sb6
dipole
dipole
Lead at the end of dipole
Pump and bellow
At quadrupole end: transvers area 65cm x 62cm, 5cm thick
At sextupole end: transvers area 34cm x 36cm, 5cm thick
sextupole
quadrupole
Lead at the end of quadrupole and sextupole
BPM
 | Dipole | Quadrupole | Sextupole | Other | total
Lead in each component | 446.0 | 89.3 | 49.3 | 41.4 | 965.8
Lead at the end of each component | 141.4 | 129.4 | 58.2 | 10.8 | 
 | Dipole | Quadrupole | Sextupole | Other | total
Lead in each component |  |  |  |  | 
Lead at the end of each component |  |  |  |  | 
From FCC Week 2025 talk

## Slide 11: Prompt dose level for CEPC TDR scheme
Dose level caused by beam loss is much lower than that caused by SR. Dose rate @Z/WW can also be negligible.
@Higgs SR
  Internal wall: 180kGy/y, external wall: 60kGy/y
  Internal wall 30kGy/y,
After 18 years operation (10H+2Z+1W+5ttbar), the cumulative absorbed dose to the outer wall cable, 950 kGy, remains below the upper limit (1 MGy). By the lead/concrete shielding, the cumulative absorbed dose to the inner wall cables decrease from 4.8MGy to 550 kGy, lower than 1 MGy upper limit, so that the cables near inner wall and outter wall are both safe.
@ttbar SR
  Internal wall: 600kGy/y, external wall: 70kGy/y
  Internal wall:50kGy/y,
Without lead/concrete shielding
With lead/concrete shielding
internal
external
external
internal

## Slide 12: Radiation protection for cable insulation for CEPC TDR scheme
The cables next to quadrupoles and sextopoles are safe since the magnet cores are good shielding block.
  Accumulated absorbed dose < 800 kGy, around quadrupoles < 8 MGy, around sextopoles
  Safe for polyethylene or epoxy resin insulations, respectively.
And, cables next to other equipment needs radiation hardening.
  Cables/connectors with SiO2/ceramic insulation
  Multilayer insulations with wire meshing
Cost: assume 10k CNY per 10m radiation-hardening cable, 78160 cables signify 790M CNY
Plan to test the feasibility of cables.

## Slide 13: Radiation protection for electronics for CEPC TDR scheme
For electronics
With a 3-leg maze, radiation in the auxiliary tunnel decreases to a safe level
  Number of electronics (power supply): ~ 26000 for magnets, ~ 30000 for vacuum system, ~ 12000 for BPM
  198 auxiliary tunnels supply enough space to contain all electronics.
Alternatively, by shielding with 15cm lead and 15cm concrete, radiation in gaps between supports decreases to a safe level.
 | Upper limit | 3-leg maze with 0.5m-thick concrete wall | between supports 15-cm lead + 15-cm concrete
High energy hadron fluence ( |  |  | 
Absorbed dose (Gy/y) | 20 | (1m far from entrance) | <20
1MeV equivalent neutron fluence ( |  |  | 
 | Upper limit | 3-leg maze with 0.5m-thick concrete wall | between supports 15-cm lead + 15-cm concrete
Absorbed dose (Gy/y) | 20 |  | <20

## Slide 14: Radiation protection for fiber/cables for CEPC TDR scheme
Upper limit for ordinary optical fiber: accumulated absorbed dose < 10 ~ 100 Gy Upper limit for radiation-resistant optical fiber: accumulated absorbed dose < 10 kGy
  Radiation-resistant optical fibers are safe in the inner trench with 30cm concrete cover and in the outer trench with 10cm concrete cover.
  Ordinary optical fibers are safe in outer trench with 30cm concrete cover.
For cable insulations (polyethylene, etc.) on the cable trays: accumulated absorbed dose <1 MGy
  Use 2cm-thick 2m-high lead sheet, or 10cm-thick 2m-high concrete block to shield radiation. Cost: 830M CNY for lead, or 30M CNY for concrete
  Cable aging test: polyethylene, SiO2, PEEK, etc.
 |  | Trench with 10-cm concrete cover | Trench with 30-cm concrete cover
Accumulated absorbed dose after 18y operation | internal trench | <72 kGy | <140 Gy
 | external trench | <7 kGy | <27 Gy
@Higgs
@ttbar
external
internal

## Slide 15: Induced dose-eq for CEPC TDR scheme, 10min after shutdown
For 4 operations (120/45.5/80/180 GeV), simulate the induced dose-eq caused by SR and random beam losses.
The dose-eq after 1-year running and 10-min shutdown is shown below
@Higgs operation：1m away from equipment <1 uSv/h，surface of equipment ~10 uSv/h
  SR random beam loss
Similar radiation level @the end of BEPCII Linac (~10 uSv/h). Safe to work 500h per year

## Slide 16: Induced dose-eq for CEPC TDR scheme, 10min after shutdown
@Z operation: 1m away from equipment <2 uSv/h， surface of equipment ~ 20 uSv/h
  SR can be negligible
A little higher than radiation level around the end of BEPCII Linac (~10 uSv/h). Safe to work ~100h per year.
@ WW operation: 1m away from equipment <1 uSv/h， surface of equipment ~10 uSv/h
  SR can be negligible

## Slide 17: Induced dose-eq for CEPC TDR scheme, 10min after shutdown
@ttbar operation： 1m away from equipment <20 uSv/h， surface of equipment >100 uSv/h
  SR random beam loss
Higher than the radiation level around BEPCII positron target. Considering 5mSv/y as the upper limit for workers, a short time (~10h per year) stay is permitted.

## Slide 18: Induced dose-eq for CEPC TDR scheme, 1day after shutdown
@ttbar operation: 1m away from equipment <5 uSv/h, surface of equipment >10 uSv/h
  SR
Considering 5mSv/y as the upper limit for workers, a long time (~100h per year) stay is permitted. So the induced radiation levels for all operations are acceptable.
Slightly higher than the dose-eq @Z/WW operation.

## Slide 19: Conclusion
The induced dose-eq levels are safe for a long-time work in the tunnel, except the short-cooling-after-ttbar-operation case in which it is safe for a short-time work (10h).
Radiation level in the auxiliary tunnel is safe for electronics, radiation level around inner wall with shielding is safe for cables, radiation level in the trench is safe for optical fiber.
Further study on feasibility, shielding performance, operational complexity and maintainability. The engineering design for the lead fixing, cooling and cable tray shielding (aligns with our EDR plan).
Cable aging test, lead cooling test.
Thank you

## Slide 20: backup

## Slide 22: Random Beam Loss @50MW
Booster (transport efficiency 90%)
Collider
Assuming beam losses are uniformly distributed along beampipe.
  For collider, , then .
  For booster,
Beam losses from collider (1st row) and booster (2nd row)
 | Higgs | Z | WW | ttbar
Beam energy (GeV) | 120 | 45.5 | 80 | 180
Ne () | 13446 | 21.413104 | 13.52162 | 2058
Current (mA) | 27.8 | 1340.9 | 140.2 | 5.5
Life time (min) | 20 | 81 | 25 | 18
 | Higgs | Z | WW | ttbar
Beam energy (GeV) | 120 | 45.5 | 80 | 180
Current (mA) | 27.8 | 1340.9 | 140.2 | 5.5
Life time (min) | 20 | 81 | 25 | 18
 | Higgs | Z | WW | ttbar
Current (mA) | 0.98 | 14.4 | 2.85 | 0.11
Time with beams (s) | 23.4 | 125.7 | 33.3 | 15.0
Injection interval (s) | 38.0 | 153.5 | 155.0 | 65.0
 |  | Higgs | Z | WW | ttbar
(mA/s) | Collider | 0.023 | 0.276 | 0.093 | 0.005
 |  | 0.003 | 0.009 | 0.002 | 0.0002
 |  | Higgs | Z | WW | ttbar
 | Collider | 0.023 | 0.276 | 0.093 | 0.005
 |  | 0.003 | 0.009 | 0.002 | 0.0002
Prompt dose caused by beam loss is negligible, compared with prompt dose caused by SR.

## Slide 23: SR @50MW
Booster (transport efficiency 90%)
Ramping simulation: example @Higgs
  More smooth ramping simulation than TDR.
Collider
With bending radius of 10.7km, SR can be simulated using parameters above in FLUKA.
SR photon spectrum
30 GeV
120 GeV
30 GeV
120 GeV
Ramping scheme simulated
In TDR
Now
 | Higgs | Z | WW | ttbar
Current(mA) | 0.98 | 14.4 | 2.85 | 0.11
Time with beams(s) | 23.4 | 125.7 | 33.3 | 15.0
Injection interval(s) | 38.0 | 153.5 | 155.0 | 65.0
 | Higgs | Z | WW | ttbar
Beam energy (GeV) | 120 | 45.5 | 80 | 180
Ne () | 13446 | 21.413104 | 13.52162 | 2058
Current (mA) | 27.8 | 1340.9 | 140.2 | 5.5
Critical energy (KeV) | 357.5 | 19.5 | 105.9 | 1208.9
 | Higgs | Z | WW | ttbar
Beam energy (GeV) | 120 | 45.5 | 80 | 180
Current (mA) | 27.8 | 1340.9 | 140.2 | 5.5
Critical energy (KeV) | 357.5 | 19.5 | 105.9 | 1208.9

## Slide 24: Radiation Protection for Fiber between TDR Scheme and Photon Absorber Scheme
For TDR scheme, ignoring dose decrease by1m-air, the dose under 30cm cover is 15Gy/y @ttbar. For photon absorber scheme, the dose under 30cm cover is 20Gy/y @ttbar.
Accumulated dose after 18y operation ~ 15Gy/y * 9 year (10y higgs ~ 4y ttbar, Z/WW negligible)
  For TDR scheme, 135Gy; For photon absorber scheme, 180Gy.
10cm cover
1m air
20cm concrete
30cm cover
1m air