## Slide 1
CEPC impedance budget update in EDR (including collimators) and limitation to luminosity
CEPC workshop, 5-10 November 2025, Guangzhou
Circular Electron Positron Collider
Na Wang
Institute of High Energy physics
Contributors:
Yuan Zhang, YuDong Liu, ZhiYuan Li , Haisheng Xu , Saike Tian, Jintao Li

## Slide 2: Outline
EDR plane on impedance and collective effects
Main progress on impedance development
Limitation to luminosities
Summary and outlook

## Slide 3: EDR plane on collective effects (collider rings)
Develop the impedance model with more realistic hardware designs, along with possible impedance mitigations
Contributions from the missing elements  increase the impedance budget  Limitations to the Luminosity
  Inj./ext. elements, feedback kickers, absorbers, masks and collimators outside the IR region are not included.
Influence of the High Order Modes (HOMs) should be further identified
  IR Chambers, Electro-separators, Collimators…
Influence of updated impedance on beam instabilities, along with mitigations
  Beam current threshold
  Luminosity

## Slide 4: Main progress
Continued impedance modeling and optimizations
HOMs in the electro-separator is investigated and mitigation strategies are proposed
Instability studies are updated with the new impedance model
Influence of impedance on beam-beam interaction is checked

## Slide 5: CEPC beam parameters (30MW)
Parameter [unit] | Higgs | Z | W | tt
Beam energy Ek [GeV] | 120 | 45.5 | 80 | 180
Lmax/IP (1034cm-2s-1) | 5 | 115 | 16 | 0.5
Emittance (H/V) [nm/pm] | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Beam current [mA] | 16.7 | 803.5 | 84.1 | 3.3
Bunch number | 268 | 11934 | 1297 | 35
Bunch Population [1010] | 13 | 14 | 13.5 | 20
Momentum compaction p [10-5] | 0.71 | 1.43 | 1.43 | 0.71
Bunch length z (natural/total) [mm] | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) [10-4] | 10/17 | 4/13 | 7/14 | 15/20
Betatron tune x/y | 445.10/445.22 | 317.10/317.22 | 317.10/317.22 | 445.10/445.22
Synchrotron tune | 0.049 | 0.035 | 0.062 | 0.078
Radiation damping [ms] | 44/44/22 | 816/816/408 | 150/150/75 | 14/14/7
Design queries
Small p
Short natural z
Slow damping at low Ek

## Slide 6: Impedance modeling
Impedance modeling of the key vacuum components has been evolving, some of the components, such as the collimators, electrostatic-separators, injection and extraction components are still under optimization and development
  Resistive wall, collimators, RF cavities, flanges, BPMs, bellows, gate valves, pumping ports, masks, IP chambers, electrostatic-separators, feedback kickers, taper transitions
Resistive wall impedance
  Considering different type of vacuum chambers: main vacuum chamber with NEG coating, IP chamber, collimators and stainless steel chamber  Contribution from the main vacuum chamber dominates both the longitudinal and transverse RW impedance (>80%)
Components | Z¦¦/n, mΩ | kloss, V/pC | ky, kV/pC/m
Main chamber | 6.1 | 355.7 | 11.3
SS chamber | 0.7 | 73.4 | 1.7
IP chamber | 6.9E-3 | 0.7 | 0.2
Collimators | 1.4E-2 | 1.4 | 0.6
RW Total | 6.8 | 431.2 | 13.8
Ring Total | 12.2 | 739.5 | 48.2
Broadband effective impedance @z=3mm
ReZL
ReZy
RW takes ~50% of the total Z||/n and the total kloss, ~30% of the total ky @z=3mm
Heat load deposition on the main chamber: ~15W/m @z=8.7mm (PSR=30MW/beam)

## Slide 7: Impedance suppression of collimators
Collimator impedance optimizations
  Reducing taper angle
  Select appropriate beta function to reduce the impedance contribution
Reducing the number of collimators from the perspective of optimizing the collimation system design
Horizontal/Vertical:
SuperKEKB type collimator:
flattop=40mm
Half aperture=6~8mm
Taper angle=0.06
Sliding fingers for the RF shielding
Transverse impedance occupation for different elements (@rms bunch length of 3mm)
Preliminary design of the collimation system has 58 collimators for both background reduction in the detectors and machine protection from beam losses  Dominant contribution to the transverse impedance.

## Slide 8: Dependence of the impedance on the taper angles
Circular collimator
  By decreasing the taper angle, the impedance of circular collimator can be reduced by 20%
taper angle
Current case
Evaluate with rms bunch length of 3mm

## Slide 9: Dependence of impedance on beta function
Collimation design usually chose location with high  to have large beam size and high collimation efficiency  Roughly, if we take  Lower impedance & high beta function weighting
 We have betatron weighted kick factor kykV-2.2 -2.2 -0.1
 Further impedance reduction by choosing proper  function may not easy.
Aperture [mm] | kV [V/pC/m] | kH [V/pC/m]
2.2 | 290.5 | 43.7
3 | 136.2 | 21.6
4 | 85.2 | 15.9
6 | 33.1 | 8.4
Evaluate with rms bunch length of 3mm
kH and kV are not weighted by beta function
kV: kick factor in the direction of jaws
Impedance without  weighting:

## Slide 10: Impedance suppression of the collimator
Optimization of the collimation system provides the iterative version with total of 34 collimators
The transverse impedance contribution from the collimators is decreased by ~40%
The transverse impedance of the whole ring reduced by ~20%
Impedance budget | 
ky,coll, kV/pC/m | 34.5
ky,total, kV/pC/m | 64.2
Impedance budget | 
ky,coll, kV/pC/m | 21.1
ky,total, kV/pC/m | 50.8
Previous design
Current design with reduced num. of colls
Evaluate with rms bunch length of 3mm

## Slide 11: Collimator impedance contributions

## Slide 12: Collimator impedance contributions
Dominant contributors to vertical impedance:
Vertical/circular collimators with high vertical beta function
Use nonlinear collimators as proposed in SuperKEKB is another candidate solution to further reduce the collimator impedance.
The collimation system design is currently undergoing continuous development and refinement.

## Slide 13: Flanges
Adopted in BEPCII
One cylindrical gap:
width = 1mm
depth = 1mm
Previous model
Current model
Impedance is mainly contributed by the construction or mounting errors.
Imaginary part of longitudinal impedance
With the previous model, the flanges show the dominate contribution to the total longitudinal broadband impedance (nearly 1/3), due to the large quantity (~38k).
The dependence of impedance on the extent of construction or mounting errors are studied  The current model effectively reduces impedance with error tolerance constrained to <0.3 mm.
The edge of the flange facing the gasket need to be flat, to avoid bump or cavity structures at the connection.
Effective impedance with offset of the gasket
Cylindrical

## Slide 14: Electrostatic-separator
Supporting parts and HV feedthroughs are included
Actual materials are considered
Electrostatic separators have been used extensively in the days when the e- and e+ sharing the vacuum chamber, because their ability to generate opposite beam deflections depending on the charge of the beam.
They are essential components for the CEPC, enabling the two beams to share the RF cavities.
The shearing scheme utilize both electrostatic-separator and bending magnets to deflect beams in the RF regions.
Key impedance aspects:
Rich of HOMs  could induce CBI  Further investigations and mitigations are needed.
High beam power loss  Water cooling is implemented in the design

## Slide 15: HOM damping with absorbing materials
Absorbing material:
  r ~ 1 (Less influence to the magnetic field)
  High r (high absorbing efficiency)
Location of absorbing material
  Different cases: around the feedthroughs or ceramic support, replace the ceramic support material
Supporting rods
electrodes
feedthroughs
Primary studies show that the modes can be well damped by adding absorbers at the supporting rods or replace the support with SiC.
Considering the complexity of the terminal load, further bench impedance measurement is planned to verify the impedance suppression effect.

## Slide 16: Summary on impedance budget
Components | Number | Z¦¦/n, mΩ | L, nH | kloss, V/pC | ky, kV/pC/m
Resistive wall | - | 6.8 | 361.0 | 431.2 | 13.8
RF cavities | 60 | 0.5 | 24.8 | 101.2 | 0.5
Flanges | 37714 | 0.9 | 44.6 | 9.2 | 2.6
BPMs | 1808 | 0.04 | 2.0 | 9.5 | 0.2
Bellows | 15949 | 2.9 | 154.6 | 87.4 | 3.9
Gate Valves | 520 | 0.2 | 11.4 | 14.5 | 0.4
Pumping ports | 5316 | 0.3 | 18.4 | 2.3 | 0.2
Collimators | 34 | 0.1 | 6.9 | 22.2 | 21.1
Masks | 17757 | 0.5 | 24.6 | 19.5 | 0.8
Feedback kickers | 8 | -0.04 | -1.9 | 5.2 | 0.1
IP chambers | 2 | 0.004 | 0.2 | 0.3 | 2.9
Electro-separators | 20 | -0.1 | -5.4 | 34.5 | 0.1
Taper transitions | 48 | 0.04 | 2.3 | 2.5 | 0.09
Total |  | 12.2 | 643.4 | 739.5 | 48.2
Longitudinal impedance:
Effective impedance evaluated with z=3mm
ReZL
ImZL

## Slide 17: Summary on impedance budget
Components | Number | Z¦¦/n, mΩ | L, nH | kloss, V/pC | ky, kV/pC/m
Resistive wall | - | 6.8 | 361.0 | 431.2 | 13.8
RF cavities | 60 | 0.5 | 24.8 | 101.2 | 0.5
Flanges | 37714 | 0.9 | 44.6 | 9.2 | 2.6
BPMs | 1808 | 0.04 | 2.0 | 9.5 | 0.2
Bellows | 15949 | 2.9 | 154.6 | 87.4 | 3.9
Gate Valves | 520 | 0.2 | 11.4 | 14.5 | 0.4
Pumping ports | 5316 | 0.3 | 18.4 | 2.3 | 0.2
Collimators | 34 | 0.1 | 6.9 | 22.2 | 21.1
Masks | 17757 | 0.5 | 24.6 | 19.5 | 0.8
Feedback kickers | 8 | -0.04 | -1.9 | 5.2 | 0.1
IP chambers | 2 | 0.004 | 0.2 | 0.3 | 2.9
Electro-separators | 20 | -0.1 | -5.4 | 34.5 | 0.1
Taper transitions | 48 | 0.04 | 2.3 | 2.5 | 0.09
Total |  | 12.2 | 643.4 | 739.5 | 48.2
Transverse impedance:
Effective impedance evaluated with z=3mm
ReZy
ImZy

## Slide 18: Impedance evolution
Evaluate with rms bunch length of 3mm
2018
2021
2023_V1
Elliptical cross section (CDR)
Circular cross section
More contributors included (TDR)
More detailed chamber material, collimator (no.=18) updated,  weighing
The longitudinal impedance is about stable, however, the transverse impedance varies mainly with the development of the collimation system.
We will keep tracking and control the impedance along with the hardware development.
2023_V2
Collimators for machine protection (no.=58), masks and feedback kickers included
2024_V1
More detailed collimator design (no.=58), RW and Electrostatic-separator updated
Chart: Normalized by V2018
| Z/n | kloss | ky
2018 | 1 | 1 | 1
2021 | 1.3421 | 0.8452 | 1.099
2023_V1 | 1.3947 | 0.9423 | 1.6733
2023_V2 | 1.4354 | 1.0296 | 2.8989
2024_V1 | 1.4491 | 1.0419 | 3.1782
2024_V2 | 1.0702 | 0.81774 | 2.3861
2024_V2
Collimator (no.=34) and flange updated

## Slide 19: Rough estimations on single beam instabilities
Broadband imp.  beam distortion/centroid oscillation  bunch current threshold
Narrowband imp.  coupled bunch oscillation  restrict total beam current
luminosity
(beam energy loss heat load）
Impedance budget | 
Z¦¦/n, mΩ | 12.2
ky, kV/pC/m | 48.2
 | Higgs | W | Z | ttbar
Single bunch threshold (Long) Z¦¦/n [m] | 6.5 | 4.1 | 0.7 | 14.4
Single bunch threshold (Trans) ky [kV/pC/m] | 69.7 | 40.2 | 12.4 | 109.8
TMCI unstable
Longitudinal distortion
Luminosity limitations
In the following, the instability studies are mainly focused on the Z energy.
 | Higgs | W | Z | ttbar
Multi-bunch SR threshold (Long) [GHzG] | 4.5 | 0.1 | 6.5E-4 | 171.2
Multi-bunch SR threshold (Trans) [G/m] | 3.0 | 0.08 | 8.9E-4 | 72.7
 | Higgs | W | Z | ttbar
 | 4.5 | 0.1 | 6.5E-4 | 171.2
 | 3.0 | 0.08 | 8.9E-4 | 72.7
Tight narrowband impedance requirements for Z (at least ~two orders higher for the other energies)
Evaluate with rms bunch length of 3mm

## Slide 20: Single bunch instabilities with reduced impedance
The TMCI for Z is investigated with simulations
  The bunch charge is restricted to 5 nC (much lower than the design value of 22.4 nC)
  Need high chromaticity and feedback damping, and further impedance mitigation.
Transverse oscillation modes vs. bunch charge
Transmission rate vs. bunch charge
Courtesy of H.S. Xu

## Slide 21: Mitigation with chromaticity and FB
Two bunch charge cases are tested: Ne=5E10, 14E10(22.4nC), theoretical studies underway.
1) Only chromaticity Qy’~5 (half ring)
2) Only chromaticity Qy’~10 (half ring)
Courtesy of Z.Y. Li, Y. Zhang

## Slide 22: Mitigation with chromaticity and FB
3) With B-by-B feedback (damp rate ~0.05)
4) With B-by-B feedback (damp rate ~0.05) and Qy’~5 (half ring)
Courtesy of Z.Y. Li, Y. Zhang

## Slide 23: Influence of impedance on Beam-beam interaction
Multiparticle tracking simulations are performed with IBB
  Strong-strong beam-beam interaction
  Linear Arc Map with SR radiation, localized beam-beam kick
  Support large Piwinski angle collision, beamstrahlung effect, multiple bunches/multiple IPs
  Longitudinal +transverse impedance
Eigen mode analysis
  Beam-Beam cross wake
  Discretization of longitudinal phase space distribution with PWD
  Synchrotron-betatron motion described by transfer matrix
  Linear eigenvalue issue
Horizontal plane:
  Coherent X-Z instability due to large Piwinski angle.
  Influenced by Horizontal impedance and potential well distortion from longitudinal impedance
Vertical plane:
  Transverse mode coupling instability, enhanced with combination of impedance and beam-beam
Y. Zhang et al., PRST-AB, 8, 074402 (2005)
K. Ohmi et al., PRL 119, 134801 (2017)
Y. Zhang et al., PRAB 23, 104402 (2020)
Y. Zhang et al., PRAB 26, 064401 (2023)
C.T. Lin et al., PRAB 25, 011001 (2022)

## Slide 24: Update simulations with reduced impedance (Z)
With design bunch intensity (Ne=14E10)
  Only feedback can not stabilize the beam.
  Only Qy’~10, the beam will dynamically stable at luminosity around 0.8x1036cm-2s-1.
  Beam-beam stable at 1x1036cm-2s-1 with FB and Qy’~5.
  Further impedance reduction is preferred (~20% lower, collimator optimizations, nonlinear collimator, …).
Courtesy of Z.Y. Li, Y. Zhang
Impedance 2024-V2
Impedance 2024-V2
Impedance 2023-V1
Evaluate with rms bunch length of 3mm

## Slide 25: Summary and outlook
The impedance model is updated considering the impedance contribution from the collimators and possible mitigations strategies. Their influence to the beam instabilities and luminosity is checked.
The design luminosity for Higgs could be achieved.
The design luminosity for Z could only be reached with strong FB and chromaticity:
    For single beam, the single bunch current is restricted by TMCI (); the total beam current is restricted by resistive wall instability and HOMs from ES; Mitigation strategies: bunch-by-bunch feedback, chromaticity, HOM dampers.
    Considering beam-beam interaction, the design luminosity could be achieved in the pure beam-beam simulation, when include impedance, the mitigation strategies (feedback + chromaticity) are necessary to realize beam-beam stable.
The impedance model will be continuously updated along with the development of the hardware designs (collimators, injection & extraction components).
Further studies are needed to confirm the reliability of the mitigation strategies (more realistic modeling, lab bench measurements …).

## Slide 26: Thank you for your attention!