## Slide 1
CEPC machine protection with collimators and transport line systems
Cui Xiaohao (IHEP)
on behalf of CEPC machine protection team
Guangzhou, Nov 5-10, The 2025 international workshop on the high energy Circular Electron Positron Collider

## Slide 2: Content
  Introduction
  Collimator Setting
  Simulation results
  4. Summary & Outlook

## Slide 3
1. Introduction
  The energy stored in the beam at CEPC is very high, and the machine protection system is needed to mitigate beam damage to critical machine components.
  In Z mode, the beam energy in the ring is maximum. So in our study, we primarily considered the Z mode while also referencing the Higgs mode
  In our study, we used TDR parameters and 30MW SR power.

## Slide 4: 1. Introduction
Active Protection System
Consists of:
  Beam loss monitors
  Signal control system
  Beam dump system (kicker + dump line)
Advantage: Beam is extracted from ring → no internal damage
Disadvantage: Slower response (~3 turns):
  Detection + transmission + processing + extraction time
~ 500 us
~330 us

## Slide 5: 1. Introduction
Passive Protection System
Includes: collimators, masks, shielding
Advantage:
  Always present, can block beam losses
  Reduces detector background
Disadvantage:
  Beam lost inside ring → secondary particles
  May not block 100% of losses
  Collimators may be damaged
x
horizontal collimator
y
x
vertical collimator
y
z
x
Two types: horizontal/vertical collimator
  Aperture: 3~4 mm
Material: Molybdenum – Carbon composite

## Slide 6
2. Collimator Setting
Functions:
  Reduce detector backgrounds
  Protect accelerator components from beam losses
  Improve beam stability and lifetime
Types of Collimators in CEPC:
  BG Collimators: Reduce beam background at detectors
  SR Masks: Located ~1.9 m from IP, block synchrotron radiation
  Machine Protection Collimators: Protect accelerator components

## Slide 7
2. Collimator Setting
BG collimators:
  10 horizontal BG collimators in one ring
  12 vertical BG collimators in one ring
  2 SR mask in one ring
Types of Collimators in CEPC:
  4 horizontal MP collimators in a ring
  4 vertical MP collimators in one ring
  4 Momentum collimators in one ring (horizontal collimator located at position with large dispersion)
The number and positions may have slight variations as the collimator settings are still in the optimization process.

## Slide 8
2. Collimator Setting
The collimators are designed with movable jaws, so that we can change the apertures at different operating modes.
Collimators | Half Aperture in simulation (mm)
Horizontal MP collimators | 3
Momentum MP collimators | 3
Vertical MP collimators | 2.5
Horizontal BG collimators | 4
Vertical BG collimators | 3

## Slide 9: 2. Collimator Setting- BG collimators
Collimators were implemented to reduce IR loss caused by single beam.
  22 sets of collimators were implemented for MDI purpose with updated position. The parameters of the collimators is keeping optimizing.
  2 SR mask, may also hit by single BGs.
With the implementation of collimators, multi-turn beamstrahlung and radiative Bhabha loss particles have been effectively shielded outside of the IR.
Current Settings on TDR Lattice w/o SOL
By Shi Haoyu

## Slide 10: 2. Collimator Setting-BG collimators
Single beam only, bare lattice with beam-beam.
Loss rate reduced ~66%-99% at Higgs mode
  The single beam BG can be effectively mitigated by optimizing the collimators in bare lattice.
  The SR mask considered in SAD tracking and detector simulation.
Beam Way
With MDI Collimators
Acceptable
with Collimators
SR Mask
By Shi Haoyu

## Slide 11: 2. Collimator Setting- MP collimator design
Currently, focus on 4 beam loss scenarios:
  Superconducting RF cavity quenching
  Final focus quadrupole quenching
  Dipole power supply failure
  Quadrupole power failure
The bottom line of the passive protection system is to ensure that in the beam loss situations the IRs are not damaged and to protect equipment in the ring except the collimators:
  Particles hit in IR should be very low
  The temperature rise should be low enough

## Slide 12: 3. Particle loss simulation
Tool: SAD tracking code
Features:
  Synchrotron radiation included
  Vacuum pipe aperture: 28 mm radius
  Collimator aperture set by real geometry
Parameters: Beam energy 45 GeV (Z) and 120 GeV (Higgs)

## Slide 13: 3. Particle loss simulation– Particle loss simulation-RF (Z)
RF cavity voltage drops exponentially: V(t) = V₀·e^(−t/τ), τ = 773 µs
  Beam loss starts ~15 turns particle distributions hit on several collimators

## Slide 14
1/8 dipole in the ring powered in series. After power failure, magnetic field drops exponentially:B(t) = B₀·e^(−t/τ), τ = 10 ms. Tracked the beam for 50 turns, only a small portion get lost
3. Particle loss simulation– Particle loss simulation-Dipole (Z)
  Get lost after 20 turns, and only a small portion get lost in 50 turns

## Slide 15
Assuming 9 or 10 quadrupole magnets in the accelerator experiences power loss, the magnetic field of the quadrupole magnet decays exponentially B(t) = B₀·e^(−t/τ), τ = 10 ms.
3. Particle loss simulation– Particle loss simulation-Q (Z)
  Get lost after several turns

## Slide 16
In Final focus SC quadrupole magnets quench case, the magnetic field of the SCQ is assumed to drop linearly, and get to 0 at 200 ms
3. Particle loss simulation– Particle loss simulation-SCQ (Z)
  Get lost in the second turn

## Slide 17
Simulations were also conducted at Higgs energy levels. The results were similar to that of Z mode.
3. Particle loss simulation– Particle loss simulation-Higgs
  1. Particle lost every turn for Dipole failure 2. Particle lost every turn for SCQ failure

## Slide 18
Different scenarios can be set in SAD simulation.
Beam losses along beam pipe/collimators will be record.
All processes that beam losses hitting collimators would pass to FLUKA simulations, then secondaries send back to SAD.
What’s new: the kicker and septum for the extraction line to collider dump are added in the SAD simulation to study the extraction efficiency.
3. Particle loss simulation– SAD-Fluka Simulation
By Tang Guangyi

## Slide 19
One-power-supply-breakdown case: beams begin to loss after tens of turns.
  Have enough time to extract beams
Superconducting-RF-cavities-quenching case: beams begin to loss after 12 turns.
  Have enough time to extract beams, too
Superconducting-magnets-quenching case: beams begin to loss at the first turn.
  Extract nothing even though the response time of extraction line is set to be 1 turn.
For Higgs/WW/ttbar operations, the similar simulations will be finished soon.
3. Particle loss simulation– SAD-Fluka Simulation
By Tang Guangyi

## Slide 20: 4. Summary & outlook
The CEPC stores extremely high beam energy; a robust Machine Protection System (MPS) is essential.
Passive protection: >40 collimators (BG/MP/momentum) + 2 SR masks in one ring have been optimized, effectively suppressing backgrounds and protecting the IR and ring equipment.
Active protection: a beam-dump system has been included. For most power-failure scenarios (RF, dipole, quadrupole) the beam can be fully extracted, but the super-conducting final-focus quadrupole (SCQ) quench loses beam within 2 turns—faster response or secondary collimators are under study.
Next steps: complete loss-map studies, couple FLUKA hotspot-temperature calculations, further optimize collimator numbers/positions, and evaluate downstream secondary collimators to finalize the protection scheme for the EDR.
  Ongoing SAD-FLUKA coupling is refining hotspot temperature calculations.

## Slide 21: Thank You