## Slide 1
Luminosity monitoring at SuperKEKB
lessons learned
Philip Bambade IJCLab – Orsay
Acknowledgements: Yoshihiro Funakoshi, Mika Masuzawa, Hiroyuki Nakayama, Yukiyoshi Ohnishi, Sadaharu Uehara, Kenta Uno (KEK – Tsukuba)
Yunyun Fan (IHEP – Beijing), Sandry Wallon (IJCLab – Orsay)
Meng Li, Qiming Li (IHEP – Beijing) ; Shishuan Tang (Fudan – Shanghai)
D. El Khechen (2013-2016), V. Kubytskyi (2016-2017), C.-G. Pang (2016-2019), S. Di Carlo (2017-2019),…
CEPC 2025 International Workshop November 5-10, 2025 Guangzhou - China

## Slide 2: The SuperKEKB/Belle II project
Damping Ring
Injector Linac
Main Ring
Belle-II
 | Electron | Positron
Energy (GeV) | 7 | 4
Current (A) | 3.6 | 2.6
Belle II (General purpose detector) Vertex detectors: Pixel Vertex Detector (PXD), Silicon strip Vertex Detector (SVD) Tracking: Central Drift Chamber (CDC) Calorimeter: Electromagnetic CaLorimeter (ECL) Particle ID: Aerogel Ring Image CHerenkov detector (ARICH) K-Long and Muon detector (KLM) Time-Of-Propagation counter (TOP)
SuperKEKB (Electron-Positron Collider) C.M.S. Energy: √s = 10.58 GeV Luminosity: L  8 x 1035 cm– 2s–1 （Luminosity Frontier Machine）
Achieved in 2024 : L = 5.1 x 1034 cm-2 s-1

## Slide 3
KEKB ↔ SuperKEKB parameters
× 1/20 βy
× 2-3 beam currents
 up to × 40 peak luminosity
σy ≈ 50-60 nm
(similar as ILC/ATF2)
similar beam-beam strength
(tune-shift)

## Slide 4: Fast & slow beam position variations at IP require feedback corrections
Beam-beam deflection for fast vertical motion
Luminosity feedback by “dithering” for slower horizontal motion
Dy at IP=  5nm  1/10sy*
BPM
IP
BPM
Dy at BPM=  1.3mm
x
Luminosity
Vertical vibration  25-100 Hz
Sampling (BPMs)  32 kHz
Horizontal motion  few Hz
Modulation freq. f0  79 Hz
Sampling (lumi. meas.)  1 kHz
- minimize f0 output component
- dithering  lumi. signal  phase


2f0
f0
LUMINOSITY
DITHERING
Dithering coil x 12

## Slide 5: Fast luminosity monitoring specifications
“Dithering” feedback
Bunch by bunch luminosity diagnostic
IP vertical beam size measurement + tuning at very low currents
Correct for few Hz horizontal motion
79 Hz orbit “dithering” + luminosity sampling @ 1 kHz  reconstruct baseline freq. + 2nd harmonic
Efficient separation from other “slow” variations
1% relative precision @ 1 kHz sufficient (cf. C.-G. Pang et al., J.Phys.Conf.Ser. 1067 (2018) no.7, 072023)
Provide analog signal as input to lock-in amplifier
Nominally 4 ns bunch separation  need short signal pulses, ideally < 4 ns
1% or better relative precision @ 1 Hz
Single beam orbit + optics corrections in two rings
Vertical e+ and e- beam size optical tuning  suppress local aberrations in nanobeam final focus
Control of beam-beam blowup  find best spot in tune diagram
Very low current  avoid confusion from beam-beam induced blowup
Dynamic range L ≈ 1032  1036 cm-2 s-1
Non luminosity scaling contamination < 1% (e.g. beam gas bremsstrahlung and Touschek losses)
Manage radiation damage at highest luminosity
Notes: LGSO (Lu2-xGdxSiO5)

## Slide 6: Luminosity related observables
1) Bhabha scattering measured in very forward Belle II calorimeter
- cross section precisely known + detector calibration  absolute measurement
- statistical precision needs averaging
2) Single bremsstrahlung ↔ radiative Bhabha process at zero scattering angle
- cross section not precisely computed
 effective photon approximation
- beam size and collision offset dependencies
 QED large impact parameter effects
 experimental acceptance distorted by beam-beam deflections : pre- and post-scattering
- very high cross section (0.15-0.2 barn)  OK for fast / high precision monitoring
3) Beamstrahlung
- optical detection at large angles (SuperKEKB)
- high photon rate detection (SLC, FCCee, CEPC)
- rates / asymmetries / polarization dependences on beam sizes  indirect reconstruction
Notes: LGSO (Lu2-xGdxSiO5)

## Slide 7
Large cross section for
    1) 𝑒+ rate in LER 10 m after IP (part of energy spectrum near E(𝑒+) ≈ 3.5 GeV after large bend)
    2) 𝛾 rate in HER 30 m after IP (part of 0.1-0.3 mrad IP beam angular spread due to geometry)
Bhabha process at vanishing scattering angle
a.k.a. Single Bremsstrahlung
𝑒+
𝛾
Only relative luminosity  with certain conditions…
Acceptance depends on choice of sensor / location
Also some variation with beam parameters…
𝜎Bhabha@zero-degree not precisely computed in QED
 OK for usage on “short” enough time-scales
 care for beam parameter dependence
Dima El Khechen et al., PRAB 22, 062801 (2019)
Notes: LGSO (Lu2-xGdxSiO5)

## Slide 8
Optimal position found at 10 m behind IP using SAD
Over-bent Bhabha positrons  vacuum chamber
Special beam pipe with window + Tungsten radiator
Start-to-end simulation (GuineaPig++, SAD, GEANT4)
POSITRON RING (measure e+)
IP
X(m)
0
28 m
Photon ray-tracing in detailed vacuum chamber geometry + GEANT4
Original position at 30 m (2018)
New optimal position found at 28 m with ≈ 10 times higher rate
ELECTRON RING (measure )
IP
0.4
Implementation in LER and HER
Cheng Guo Pang et al., Nucl.Instrum.Meth. A931 (2019) 225-235
loss position distribution
Notes: Radiation length of Tungsten is 0.3504 cm

## Slide 9: Two complementary techniques for fast luminosity measurements - compare / collaborate / mutually supporting - share simulation, mechanics, some data… - since 2012
LumiBelle2 / IJCLab
ZDLM (Zero Degree Luminosity Monitor) / KEK
single crystal CVD diamond sensors
Fast charge/current amplifiers
Digital electronics and processing
Cherenkov and scintillator detectors
LGSO non-organic scintillator and ES-crystal (quartz)
Photomultipliers
Analog & digital processing
Notes: LGSO (Lu2-xGdxSiO5)

## Slide 10
Yunyun FAN
Qiming LI
Xiang LI

## Slide 11
ADC Channels
HER
LER
CH1
CH2
CH3
CH4
IP
140 μm diamond + current amp 2 GHz
500 μm diamond + charge amp 10 ns
latest setup
2025/11
LGAD 16/25 pixel + current amp 2 GHz

## Slide 12
LumiBelle2 fast luminosity monitor in 2024
Install LGAD sensors in LumiBelle2 -> radiation hard version from IHEP-Beijing used in Atlas/HGTD (Yunyun Fan et al.)
LGAD sensor from IHEP with C2HV0235 and RF splitter / inverter
500μm diamond herd42 with C2HV0235
Trigger level -20mV
Trigger level 13.8mV
sensitivity@500um diamond
Data analysis to estimate diamond sensor performance (Meng Li)
- Internal data handling/archiving software instability
- Sensor sensitivity drift in one diamond detector
In 2024, LumiBelle2 was operated successfully at KEK
Observed variation of B-by-B lifetimes -> B-by-B luminosity data for machine tuning required by SuperKEKB group

## Slide 13: Setting up and optimizing beam collision with LumiBelle2
Initial scanning of IP beam offset to enable Regularly optimizing IP beam offset
collisions at very beginning of the run… to maximize luminosity…

## Slide 14: Minimising electron and positron IP beam sizes with LumiBelle2…
 Machine learning effort for optimizing tuning process…

## Slide 15
Concluding remarks
Continuously measure IP beam size & offsets  essential at SuperKEKB, FCCee, CEPC,…
LumiBelle2 and ZDLM used daily  maximize SuperKEKB performance
Bunch-by-bunch on-line monitor prepared at KEK by Junxi Cui
Design challenges  minimize unwanted beam parameter dependences
- unbiased extraction of scattered particle
- beam-beam deflections pre- & post-scattering
 issue of radiation
- LGAD sensors with Carbon implantation from IHEP/Atlas/HGTD
- amplifier placed 50 cm from sensor
 dynamic range and precision
- specifications
- combine redundant channels with different sensitivities
R&D activity ↔ long term operational sustainability
- LumiBelle2 has been operated by IJCLab partly remotely and with local help at KEK
- recent prospect of strong CERN & IHEP interest in collaborating on LumiBelle2
- opt for professional / commercial DAQ & electronics rather than in-house designs
Lessons learned