## Slide 1
Mechanical Design of CEPC HCAL
Apr. 14, 2025, CEPC IDRC Review for CEPC Reference Detector TDR
Pei Yatian
On behalf of CEPC HCAL group
2025.11.08

## Slide 2: Outline
Overview of HCAL structure
HCAL mechanics design
Barrel HCAL mechanics
Endcap HCAL mechanics
HCAL Cooling scheme
HCAL prototype and GS test structure

## Slide 3: Overview of HCAL structure
Barrel HCAL
Endcap HCAL
8

## Slide 4: HCAL mechanics design
Layout for all the HCAL components
Barrel HCAL
Endcap HCAL
Support rings
Endcap HCAL
The support structure zone is as lower as possible.
The maximum stress of different materials need to be lower than their allowable stress level.
The deformation of different materials need to be controlled so that there will be no broken parts under different conditions.
Outer contour dimension tolerance need to be 0mm to -5mm and inner contour dimension tolerance need to be 0mm to +5mm.
Requirements:
General structure information:
The cross section of barrel HCAL is a regular hexdecagon
Total weight is 1679 tons and there are totally 5224960 glass scintillator

## Slide 5: Barrel HCAL mechanics
 | Cell | Box | Layer | Wedge
Quantities | 3212800 | 27840 | 48*16=768 | 16
Main Structure
Integration of barrel HCAL structure
1 Wedge dimension
Total weight: 955 tons

## Slide 6: Barrel HCAL mechanics
One box structure
Cable routing scheme

## Slide 7: Barrel HCAL mechanics
Connection within one box
Connection between box and absorber layer
Connection between neighbor layers
Connection between two wedges
Edge sealings
Connection between Barrel HCAL and support rings
Connection between Barrel HCAL and Barrel ECAL

## Slide 8: Barrel HCAL mechanics
Stress and deformation of barrel HCAL under different conditions
Parameter | Stress | Deformation
One wedge assembling condition | 24.7MPa | 0.33mm
16 wedges assembling condition | 190MPa | 0.66mm
Barrel ECAL connection condition
FEA result of barrel HCAL
Boundary condition
1.26mm
371.1MPa
Changing the trapezoid beam from stainless steel to titanium alloy
Active layer space analysis
The deformation of all 48 layers at the same X
The deformation difference between 48 layer is lower than 0.2mm
The difference between the lowest point to highest point is 0.5mm
Deformation within one layer
GS analysis
0.5mm
20MPa

## Slide 9: Endcap HCAL mechanics
 | Cell | Box | Layer | Wedge
Quantities | 1006080*2 | 3072*2 | 48*16*2 | 16*2
Main Structure
Boxes in one layer
4 types boxes
Total weight: 362*2=724 tons
One box structure
4 kinds of abnormal shape GS

## Slide 10: Endcap HCAL mechanics
Cable routing scheme
5 cables in one box
Cable diameter 2mm
1
2
3
4
Connection within one box
Structure between neighbor wedges
Connection between layers
Connection between end HCAL and support rings

## Slide 11: Endcap ECAL mechanics
The max principal stress of GS is 32MPa which is lower than its allowable stress 60MPa
FEA result
0.075mm
25.3MPa
Absorber structure during self-gravity condition
GS in one box
Connection parts are made of SS (18Mn18Cr)
1.5 safety factor

## Slide 12: HCAL cooling system
Cooling scheme definition
FEA result of thermal performance of natural convection
FEA result of thermal performance of air-cooling
The excessively narrow interlayer gaps significantly reduce the efficiency of natural convection and air cooling, thereby failing to address the thermal management demands.
It is imperative to adopt liquid cooling technology to ensure efficient heat dissipation and temperature uniformity.
The temperature error of different SiPM need to be controlled less than ±1.5℃
Cooling structure of barrel and end cap HCAL
4 pipes in each layer in parallel
8 layers gather in one pipe in parallel
One end is inlet and another end is outlet
1 pipe in each layer for one wedge
5 layers gather in one pipe in parallel for one wedge
There is one inlet and outlet for each region.

## Slide 13: HCAL cooling system
FEA simulation of cooling system
Temperature distribution of the HCAL through liquid cooling
Inlet temperature is 15 ℃ with a flow rate of 0.005 kg/s (corresponding to an inlet velocity of 0.1 m/s).
Effectively maintaining the temperature rise below 0.6 °C.
The maximum temperature variations of chips under the same modules were under 0.1 °C
Eight-in-one design of flow pipe
(b) Flow velocity distribution across different layers
Achieving a uniform flow velocity distribution across different layers
The pipe resistance and length of endcap HCAL is smaller than barrel HCAL, so the same scheme can also meet our requirement

## Slide 14: HCAL prototype and GS test structure
Beam test for two HCAL prototypes
Different SiPM suppliers
Beam test for GS
7 GS with same dimension
Beam goes through different position for each GS
1st GS chain
2nd GS chain
6 GS with different dimensions
Beam goes through the center of each GS

## Slide 15: HCAL prototype and GS test structure
SiPM read out
LED read out
Electronics board
Box
Absorber
plate
Cooling fins
Bottom plate
One box
7 Boxes in one prototype
Lower cover plate
GS with reflective coating
SiPM
LED
Gasket
PCB plate
Upper cover plate
Bolts
9 GS in one box
HCAL prototypes
Real prototype and beam test
@CERN

## Slide 16: Thanks