## Slide 1
The overall readout electronics for the reference detector at CEPC
Zheng Wang
On behalf of the CEPC electronics group
November 8th, 2025 - CEPC Workshop 2025, Guangzhou

## Slide 2: Outline
Requirements for the electronics
Global framework of the electronics system
Common electronics design & frontend ASICs
Research team and working plan
Summary

## Slide 3: The Reference Detector
The electronic system is to readout tens of millions of detector channel in real time.

## Slide 4: Requirements for the electronics
This talk will focus on electronics baseline design
Future upgrade possibility considered

## Slide 5: Critical Input from Sub-Det & MDI
Safety factor of 2 used for background rate estimation from MDI study
Endcap detectors have the highest hit rate, mostly from the beam background
Time window and data rate for TDAQ system
Max data rate for the detector:
1040 Gbps (for Higgs)
1771 Gbps (for LowLumZ)

## Slide 6: Do we need hardware trigger ?
Two main frameworks for the electronics-TDAQ can be simply categorized as full data transmission (FEE-Triggerless readout) & readout with hardware trigger.
 | Full data transmission | Hardware Trigger
Where to acquire trigger info | On BEE | On FEE
Trigger latency tolerance | Medium-to-long | Short
Compatibility on Trigger Strategy | Hardware / software | Hardware only
FEE-ASIC complexity on Trigger | Simple | Complex on algorithm
Upgrade possibility on new trigger | High | Limited
FEE data throughput | Large | Small
Maturity | Mature but relatively new | Very mature
Resources needed for calculation | High | Low
Representative experiments | CMS, LHCb, … | ATLAS, BELLE2, BESIII, …

## Slide 7: Global framework of the CEPC Electronics
Common subsystems (data buffering, aggregation, transmission; powering)
A common BEE hardware, configurable for individual subsystems.
TDAQ interface is only on BEE
Det-ASIC
Det-ASIC
Det-ASIC
Det-ASIC
Data Aggregation & Data Buffering （FEDA）
Data Interface
（FEDI）
Optical Module
（OAT）
DC-DC - LV
1.2/2.5V
（PAL-LV）
DC-DC - MV
12/48 V
(PAL-MV）
Customized frontend
BEE
Comm-Brd
Trigger
Comm-Brd
DAQ
Fiber
(Only)
Power Cable
Trg. Info.
Backend: Common Platform
Slow Ctrl
Radiation tolerant
Non Rad-tol
Data Link, Clock & Ctrl
Power Management
Figure 11.2

## Slide 8: Backup scheme of the framework
The proposed framework was based on the estimated background rate of all sub-det.
Background rate indicated the data link capability can manage the Phase I operation of Higgs & LowLumiZ for first ten years.
For high LumiZ, the detector will upgrade
  VTX, ITK.. (replaceable) can be upgraded with new chips
  ECAL, HCAL (unreplaceable) will have more fiber channels
The hardware trigger scheme can serve as a backup plan, with sufficient on-detector data buffering and reasonable trigger latency.

## Slide 9: Key Electronics Components
Frontend ASICs for sub-detectors
Common Data Link
Common Powering
Common Backend Electronics
Alternative Scheme based on Wireless Communication

## Slide 10: Vertex Detector Baseline layout
  Baseline :4 single layer of bent MAPS + 1 double layer ladders
  Inner layer: Use single bent MAPS for Inner layer (~0.15m2)
    Low material budget 0.06%X0 per layer
    Different rotation angle in each layer to reduce dead area
  Outer layer: Double layer Ladder (~0.28% X0 per layer)
Long barrel layout covering cos θ<=0.991
See Ying Zhang’s talk (11:30)

## Slide 11: ITK Design with HV-CMOS Pixels

## Slide 12: OTK Design Based on AC-LGAD Strip Sensor

## Slide 13: Readout Electronics framework for TRK
See Xiongbo yan ’s talk (11:50)

## Slide 14: TPC electronics
On detector: readout modules
  Double-mesh Micromegas with high granularity readout (500μm × 500μm pad size)
  FEE board: a readout ASIC chip array. Interposer connection between pads and ASIC chis
  Readout board: data interface and data concentrator
Off detector:
  High-speed optical links
  Off-detector BEE
  Data Acquisition (DAQ) system
See Zhi Deng’s talk (12:10)

## Slide 15: ECAL electronics
Main Structure
Module Integration
See Jinfan Chang’s talk (14:00)
See Huaishen Li’s talk (14:30)

## Slide 16: HCAL electronics
Front-End boards in HCAL cell Box
  thickness limited: 3.2mm = PCB 1.2mm + ASIC 2mm
  SiPMs, ASICs and Data Aggregation
  PCB dimensions: flexible in different positions
SiPM-readout ASIC
  customized for CEPC calorimeter system
  functionality: energy and time measurements
  power consumption: 15mW/ch
Aggregation board at the end of barrel, cable connection
FEE
Energy Measurement: ASIC for ECAL & HCAL
Data transmission: common
Trigger mode: FEE triggerless readout
See Jinfan Chang’s talk (14:00)

## Slide 17: Muon electronics
FEB
MB
New
New
See Jie Zhang’s talk (14:15)
According to the R&D results and required performance: ,
Use the same chip designed for calorimeter, but customize the FEB based on ASIC according to the constraints in detector modules.
Three stages for readout
  SiPM tile: SiPM on PCB
  FEB: Front-End Electronics Board, 32 channel, mini HV generator integrated.
  MB: Management Board, central node for multiple functions.

## Slide 18: An overview of the sub-detector electronics
All sub-det readout electronics were proposed based on this unified framework, maximizing common design, easy for production and maintenance.
VTX
TPC
TRK
ECAL
HCAL

## Slide 19: Technical Survey on Data Transmission
GBT Project:
  The lpGBT & VTRx chip series, developed by CERN, are widely used by LHC.
  Core components:
    GBTx: Bidirectional Serdes ASIC
    GBLD: Laser driver
    GBTIA: Transimpedance amplifier
    Customized Optical Module
  However the base clock frequency of CEPC 43.3MHz is not compatible with lpGBT system
Our choice:
  Build a GBT-like universal bidirectional data transmission system
  Take the lpGBT as a reference, the protocol can be a minimum & necessary set for the readout, clocking & control
lpGBTx
Uplink: 10.24Gbps
Downlink: 2.56 Gbps
GBLD (LDQ10)
10.24 Gbps x 4ch
GBTIA
2.56 Gbps
VTRx+
4Tx + 1Rx
Array Optical Module
GBT Architecture Developed by CERN
Ref. P. Moreira, The GBT Project, 2007
GBT Series ASICs and optical module
Ref. P. Moreira, GBT Chipset Status and Production Plans, 2013

## Slide 20: Detailed design on Data Transmission Structure
Pre-Aggregation ASIC (FEDA): Intend to fit with different front-end detector (different data rates/channels)
GBTx-like Data Link ASIC (FEDI): Bidirectional serdes ASIC including ser/des, PLL, CDR, code/decode …
Array Laser Driver ASIC (ALDD) + TIA ASIC (ATIA) + Customized Optical module (OAT)
FEDA
FEDI
OAT
See Xiaomin Wei’s talk (15:10)
See Guoxiang Zhang’s talk (16:00)
First version ASICs submitted October, 2025

## Slide 21: Technology Survey and Scheme on Powering
On powering distribution
  Serial Powering is superior in many aspects (material, cabling and installation…) than Parallel Powering, especially on VTX & TRK
  It is also a hot area with a lot of focused R&D
  However, due to the common substrate at negative voltage for the stitching sensor in VTX, serial powering is not feasible
Our choice
  As a general platform, we chose (conventional) Parallel Powering as the baseline scheme, while to keep pace on R&D of Serial Powering as the backup scheme
Ref. Malte Backhaus, 2018
Serial Powering
Parallel Powering
 | Serial Power | Parallel Power
Material | Much less | 
Cabling | Much less | 
Installation | Much easier | 
Maturity | New | Very mature
System Reliability | Potential issue | Very robust

## Slide 22: R&D efforts preliminary design on powering
Design spec summarized from Sub-Det
Preliminary rad-tol. of COTS GaN verified
PAL Series
Figure 11.52
 | Nominal | Range
Input V | 48V | 36V-48V
Output V | 1.2V | 1.2V、3.3V
Output Current | 10A | 
Output ripple | 10mVpp | 
Efficiency | 85% | 80%-85%-80%（light-nom -heavy）
Dimension | 50mmX20mmX6.7mm | Including cooling & shielding
TID | 5 Mrad（Si） | 
Magnet | 3T | 
See Jia Wang’s talk (16:55)
Proposed design of BUCK DC-DC convertor

## Slide 23: Related R&D and experience on BEE
The back-end box for the JUNO experiment
located between trigger system and front-end electronics,
Collects the incoming trigger request for trigger system,
Fanout the synchronized clock and the trigger decisions to front-end electronics.
Red box: The base board provides the power supply,
Blue box: Trigger and Time Interface Mezzanine (TTIM) with WR node,
Green box: The extenders interface with ethernet cables coming from underwater front-end boxes.

## Slide 24: Detailed design on common BEE
Routing data from front-end optical link to highspeed network to DAQ.
receives clock, global control from TTC, and synchronized and fanout to front-end.
Real-time data processing, such as trigger algorithm and data assembly.
On-board storage for data buffering.
Xilinx Kintex UltraScale series preferable, cost-effective/availability.
Interface：SFP+ 10 Gbps✖️12 + QSFP 40 Gbps ✖️ 3
FPGA based machine learning for clustering, hit point searching, and tracking algorithms
 | KC705 (XC7K325T-2FFG900C) | KCU105 (XCKU040-2FFVA1156E) | VC709 (XC7VX690T-2FFG1761C) | VCU108 (XCVU095-2FFVA2104E) | XCKU115
Logic Cells(k) | 326 | 530 | 693 | 1,176 | 1451
DSP Slices | 840 | 1920 | 3,600 | 768 | 5520
Memory(Kbits) | 16,020 | 21,100 | 52,920 | 60,800 | 75,900
Transceivers | 16(12.5Gb/s) | 20(16.3Gb/s) | 80(13.1Gb/s) | 32(16.3Gb/s) and 32(30.5Gb/s) | 64(16.3Gb/s)
I/O Pins | 500 | 520 | 1,000 | 832 | 832
Cost | 2748 (650) | 3882(1500) | 8094 | 7770 | 
Data aggregation and processing board Prototype for Vertex detector
The back-end Card structure
See Jun Hu’s talk (17:10)

## Slide 25: Alternative scheme based on wireless communication
Radial readout with mm-wave
  12- 24 cm distance
  Data rate : < 30Mbps
Axial readout to endcap
  Only at the outermost layer or dedicated aggregation layer.
Wireless communication based readout scheme was proposed to mitigate the cabling problem, as a backup scheme.
WiFi (2.4GHz, 5GHz)
    large antenna volume, high power consumption, narrow frequency band, and high interference
Millimeter Wave (24GHz，45GHz，60GHz，77GHz)
Optical wireless communication (OWC) / Free Space Optical (FSO)
Z [mm]
R [mm]
Radial readout
Axial readout
Silicon Inner Tracker

## Slide 26: Recent progress on mm-wave transmission
Single-channel MMW RX/TX verified
  Max distance: 1.25Gbps @ 67.5cm
  Max line rate: 6.6Gbps @ 22.5cm
Multi-channel Millimeter-Wave transmission prototype in development
  Millimeter-wave modules mass produced and tested
  TX/RX flex PCBs and adapter boards produced, assembly in progress
  FPGA data source board produced and tested
  Repeater design: double-sided PCB, in progress
  Focus: Multi-channel crosstalk validation
Multi-channel Millimeter-Wave transmission prototype
Dummy Flex with MMW
MMW transmission module
FPGA data source board

## Slide 27: Electronics interface to the counting room
Fibers：12,628
Power cables: 11,346
Total power consumption: 450 kW
Data Link, Fibers & BEE
On-detector LV, HV & cables

## Slide 28: Research team
Electronics working group was founded: IHEP + universities, ~50 staffs (not full time) + 60 posdoc/student. We are looking for more collaborators.
IHEP joined DRD7 collaboration in July 2025.
Overall electronics and BEE: IHEP(5)
Sub-detector readout electronics: IHEP(11), Tsinghua(5), CCNU(3), NPU(7), SDU(4), NJU(3)
Data link: CCNU(3), IHEP(3), USTC(2), NPU(4)
Powering: NPU(3), IHEP(2), USTC(2)

## Slide 29: ASIC development & teams
Chip | Application | Functional | Foundry & technology | Similar chips | Leading person | Development team | Staff | Students
Taichu | VTX | VTX-Stitching | Towerjazz 180nm / 65nm | MOSAIX | Wei Wei (IHEP) | NPU, CCNU, SDU, NJU | 10 | 8
TEPIX | TPC | Pixel TPC | TSMC 180nm (SMIC 55nm) | Timepix3/4 | Zhi Deng (THU) | IHEP | 1 | 4
COFFEE | ITK | HVCMOS | SMIC 55nm HV | MightyPix | Yiming Li (IHEP) | ZJU, NPU, DMU，SDU, NJU | 8 | 12
LATRIC | OTK | LGAD-TOF | SMIC 55nm | ALTIROC | Xiongbo Yan (IHEP) | CCNU, WTU, HPU | 9 | 10
SIPAC | SiPM ASIC | ECAL, HCAL, Muon | SMIC 55nm | HGCROC、SPIROC | Huaishen Li (IHEP) | CCNU, NPU | 5 | 6
FEDI | Common Elec | Data Link | SMIC 55nm | lpGBT | Di Guo (CCNU) | IHEP, NPU, USTC, WTU, HPU | 9 | 16
OAT | Common Elec | Optical | SMIC 55nm | VTRx+ | Di Guo (CCNU) | IPAS, IHEP | 3 | 3
FEDA | Common Elec | Data Aggregation | SMIC 55nm | lpGBT | Di Guo (CCNU) | IHEP, NPU | 2 | 4
PAL | Common Elec | DC-DC | SMIC 180nm HV | bPolx | Jia Wang (NPU) | IHEP, USTC, TECHORILUX | 7 | 3

## Slide 30: ASIC Development Schedule
Elec TDR Draft1
Towards final CEPC detectors
GaN Selection
PAL func module prototype
Module on detector test
2024.11
2026.12
2027.12
Power & DC-DC
(PAL)
Rad-tol & Mag proof PAL prototype
2029.12
Protocol define
1st tapeout
Chip set
Rad-tol FEDI DataLink prototype
2024.10
2025.10
2029.12
Data Link
(FEDA, FEDI & OAT)
Overall Electronics system
2024.12
2027.12
VTX STCH
(Taichu-Stitching)
Preliminary scheme for Stitching
TJ65 single chip design
TJ65 wafer-level
Stitching detector prototype
2024.12
2026.12
2029.12
Prototype beamtest
Chip Finalization
2025.6
2029.12
Preliminary scheme
AC-LGAD detector co-test
Chip Finalization & detector co-test
2024.12
2027.10
2029.12
Spec finalization & device selection
HCAL module prototype
2025.1
2027.12
2027.12
ECAL/HCAL/Muon
SiPM ASIC
(SIPAC)
OTK
AC-LGAD
(LATRIC)
PIX TPC
(TEPIX)
2029.12
Final Design Review
Production Readiness Review
2025.1
DC-DC Controller schematic design
2028.12
Rad enhancement & Inductor design
2026.12
FEDI & OAT func prototype
2027.12
FEDI & OAT on detector test
Rad enhancement & FEDA development
2028.12
Taichu-stitching-180 development
2025.1
1st design of wafer-level stitch onTJ180
2025.12
TJ65 single chip prototype
2027.12
wafer-level stitching mechanical prototype
Optimized Prototype beamtest
2027.12
2026.12
Chip optim for optimized TPC
2025.12
FPMROC prototype test (for FASTPMT)
OTK detector optimization
2026.6
ASIC-128chn
tapeout
2025.12
1st SiPM ASIC
test
2026.12
Existing chip based modification
SiPM ASIC optimization
Chip Finalization
Y
N
TJ65 design kit finalization
Scheme define
2025.1
1st tapeout
2025.4
1st tapeout
2025.4
1st tapeout
2025.4
FPMROC chip test (for FASTPMT)

## Slide 31: Working plan
Most chips’ development followed the schedule.
Toward end of 2025:
  Submitted October MPW tapeout
    1st full chip tapeout for FEDI, core chip of the data interface
    2nd ver chips fixed bugs founded
  Thorough test after chips come back.
Longer term:
  develop with detector group for the first prototypes, with available sister chips or newly developed chips.

## Slide 32: Summary
The CEPC Reference TDR electronics design has been completed, incorporating full data transmission and a backend trigger scheme while preserving the potential for future upgrades.
ASIC development is progressing with a dedicated team; the first version of the ASIC designs have been submitted, and fully functional chips are expected within 2–4 years.
Collaborations are very welcome.

## Slide 33
Thank you for your attention!
November 8th, 2025 - CEPC Workshop 2025, Guangzhou

## Slide 34
Backups
November 8th, 2025 - CEPC Workshop 2025, Guangzhou

## Slide 35: Manpower for electronics system
 | Overall | BEE | VTX | TPC | ITK+OTK (LATRIC) | CAL (SiPM) | Muon | Data Link | Power | Wireless
Staff | 5 | 1 | 10 | 1 | 9 | 5 | 1 | 9 | 7 | 4
Postdoc + Student | 0 | 3 | 8 | 4 | 10 | 6 | 0 | 16 | 3 | 5
Total Sum | 5 | 4 | 18 | 5 | 19 | 11 | 1 | 25 | 10 | 9
The headcounts are not to the FTE
Some staffs are shared by multiple projects, while postdocs / students are dedicated to the projects

## Slide 36
  HV-CMOS pixel sensor:
  Sensor size: 20 mm 20 mm
  Pixel size: 34 m 150 m (spatial resolution: 8 m 40 m)
  Module:
  14 sensors (2 rows 7 columns)
  Module dimensions: 140.6 mm 40.1 mm
  Stave length: 986.6 mm (ITKB1), 1,409.6 mm (ITKB2), and 1973.2 mm (ITKB3)
  Barrel radii: 235 mm (ITKB1), 345 mm (ITKB2), and 555.6 mm (ITKB3)
The designed 3 ITK barrel layers has a total surface area of 13.3 m², including 33,264 sensor chips, with a power consumption of ~26.6 kW.
ITK Barrel Design with HV-CMOS Pixels

## Slide 37: Summary of FEE power
 | Vertex | Pix(ITKB) | Strip (ITKE) | OTKB | OTKE | TPC | ECAL-B | ECAL-E | HCAL-B | HCAL-E | Muon
Channels per chip | 512*1024 Pixelized | 512*128 | 1024 | 128 |  | 128 | 8~16 @common SiPM ASIC |  |  |  | 
Technology | 65nm CIS | 55nm HVCMOS | 55nm HVCMOS | 55nm CMOS |  | 65 CMOS | 55nm CMOS (or 180 CMOS?) |  |  |  | 
Power Supply Voltage (for DC-DC) (V) | 1.2 | 1.2 | 1.2 | 1.2 |  | 1.2 | 1.2 (or 1.8?) |  |  |  | 
Power@chip | 40mW/cm2 200mW/chip | 200mW/cm2 800mW/chip | 200mW/cm2 800mW/chip | 20mW/chn 2.56W/chip |  | 280μW/chn 35mW/chip 100mW/cm2 | 15mW/chn 240mW/chip |  |  |  | 
Max chips@module | 29 | 14 | 14 | 22 | 22 | 1115 | 64 | 120 | 8 | 92 | 167
Power@module (W) | 5.8 | 11.2 | 11.2 | 27.6 | 27.6 | 32.2 | 30 | 30 | 9 | 11 | 4.7

## Slide 38: The Counting room
Minimum crates from current MDI
  107 data crates, 227 power crates, 78 Det-HV crates, 20 Trigger crates
Minimum racks from current MDI
  37 data racks, 24 power racks, 23 Det-HV racks, 10 trigger racks (94 in total)
  More 2 racks for AC-DC power for all the above racks
  96 racks in total
Racks Size: 0.5m × 0.5m
Side clearance 1.5m for heat, face clearance 2m for cabling & heat
  Very rough estimation: 20% more power will be consumed due to the crate efficiency
Total room: 500m2×2floor = 25m × 20m × 2floor
  10 × 10 × 2=200 racks capacity
  Necessary redundancy for future upgrade
See Quan Ji’s talk on Mechanics

## Slide 39: VTX-Data Link
VTX scheme: Inner 4 layers stitching, with 1 typical double-sided ladder (layer 5&6)
Bkgrd rate @50MW @Higgs with safety factor 1.5
Assume RSU@stitching = ladder chip = 1024*512 matrix, then data rate for the innermost layer for a “chip” is 2Gbps, other layers according the bkgrd ratio
Inner 2 layers needs 2 fiber chns for each row, due to the high data rate
  possible to merge into less optical MTX interfaces
In total 88 fibers = 6 BEE Brd = 1 Data Crate
Layer | Comment | Data Rate/chip | Chips/Row | Data rate/row | Rows | Links@10Gbps
1 | Stitching | 2Gbps | 8 | 16G | 2*2=4 | 2*4=8（2 fiber chns）
2 | Stitching | 1.3Gbps | 12 | 15.6G | 3*2=6 | 2*6=12（2 fiber chns）
3 | Stitching | 0.27Gbps | 16 | 4.3G | 4*2=8 | 1*8=8
4 | Stitching | 0.25Gbps | 20 | 5G | 5*2=10 | 1*10=10
5 | Ladder-side0 | 0.16Gbps | 29 | 4.64G | 25 | 1*25=25
6 | Ladder-side1 | 0.16Gbps | 29 | 4.64G | 25 | 1*25=25
  From Zhijun