## Slide 1
A Low-Level Radio Frequency (LLRF) Control System for Multiple Superconducting Cavities Based on MicroTCA.4*
Wenbin Gao1,2, Nan Gan†1,2, Zusheng Zhou1,2, Jiyuan Zhai1,2, Xinpeng Ma1
Institute of High Energy Physics, Chinese Academy of Sciences, Beijing 100049, China1
University of Chinese Academy of Sciences, Beijing 100049, China2
This poster presents a domestically developed LLRF control system for simultaneously driving six superconducting cavities with a single klystron. Based on a fully domestic MicroTCA.4 platform, the system employs vector-sum control, IQ sampling, and feedforward-feedback techniques. It ultimately achieves high-precision amplitude, phase, and frequency control for the six cavities, validating a key step for the CEPC project.
[1] Schilcher, T., Schmueser, P., & Gamp, A. (1998). Vector sum control of pulsed accelerating fields in Lorentz force detuned superconducting cavities.
[2] Brandt, A. (2007). Development of a finite state machine for the automated operation of the LLRF control at FLASH (DESY-THESIS--2007-024). Germany
[3] Hoffmann, Matthias (2008). Development of a multichannel RF field detector for the low-level RF control of the free-electron laser at Hamburg (DESY-THESIS--2008-028). Germany
[4] I. Rutkowski, K. Czuba, D. Makowski, A. Mielczarek, H. Schlarb and F. Ludwig, "Vector Modulator Card for MTCA-Based LLRF Control System for Linear Accelerators," in IEEE Transactions on Nuclear Science, vol. 60, no. 5, pp. 3609-3614, Oct. 2013, doi: 10.1109/TNS.2013.2278372.
[5] Gao, J.(2024). CEPC Technical Design Report: Accelerator. Radiat Detect Technol Methods 8, 1–1105. https://doi.org/10.1007/s41605-024-00463-y
CEPC 650 MHz 6×2-cell superconducting module LLRF system design scheme
Each of the three board cards handles the complete processing for two cavities, including signal demodulation, local vector summation, tuning, and quench detection. These local vector sums are then sent to the main board, which consolidates them into a global vector sum and generates the final feedback signals.
In Progress Firmware integration and testing, calibration module development, upper-layer driver optimization, and EPICS applications are currently underway.
Future Plans By June 2026, a horizontal test platform will be established in Huairou, Beijing for the installation and debugging of the LLRF control system.
* This work was supported by the National Key Program for ST Research and Development (Grant NO. 2024YFA1610602), Yifang Wang's Science Studio of the Ten Thousand Talents Project, the IHEP Innovation Grant and the National Natural Science Foundation of China (Grant No. 12005240)
† email address: gann@ihep.ac.cn
The Vector Sum Control Principle
The 2025 International Workshop on the High Energy Circular Electron Positron Collider (CEPC2025), Guangzhou, China, Nov 05-10, 2025
ABSTRACT
VECTOR-SUM CONTROL PRINCIPLE
The system operates in a master-slave architecture, utilizing a unified vector-sum setpoint for global control, which eliminates per-cavity feedback loops to reduce cost and complexity. The tuning of individual cavities is achieved through a combination of feedforward and feedback control, ensuring precise adjustment.
FIRMWARE OF THE LLRF
OVERVIEW OF THE LLRF FOR MULTI-CAVITY
Firmware Architecture Diagram
Chart: Half bandwidth Fitting
Chart: Detuning Fitting
DETUNING-CALCULATION FIRMWARE VERIFICATION
REFERENCES
SOFTWARE AND HARDWARE PLATFORM
PROGRESS
Poster ID: A13