## Slide 1
工作进展
2025-03-17

## Slide 2
Overleaf——Ref-TDR机械部分
章节 | 完成状态
1.Overall layout of detectors machinery | √
2.Overall design requirement | 
Yoke design | √
Design of connection structures （magnet、barrel HCAL、barrel ECAL、TPC） | √
Design of connection structures （ITK、beampipe、end ECAL、end HCAL） | 
3.Installation design of each sub detector | 
Overall installation design | 
Detailed installation design | 
4.Design of detector auxiliary facilities | 
Water cooling and air cooling system | 
Cryogenic system | 
Electronics system | √
Service system | 
章节 | 完成状态
5.Design of underground experimental hall | 
Vertical shaft design | 
Multi-degree-of-freedom robot | 
Alignment | 
6.Design of auxiliary hall | 
Vertical shaft design | 
Equipment layout for water cooling and air cooling systems | 
Layout of cryogenic system equipment | 
Layout of electronics equipment | √
Service system equipment layout | 
7.Cost | 
8.Summary | 
报告截止时间：3月底
评审时间：4月14日

## Slide 3
Ref-TDR机械部分
整体可靠性和安全性评估
参与模拟的部件：
桶轭
桶部Muon
超导磁体
桶部HCAL
端部HCAL
桶部ECAL
端部ECAL
其余的子探测器及水管电缆
重量较轻，模拟时进行了忽略
桶轭
1560t
桶部muon
58t
超导磁体
290t
桶部HCAL
960t
桶部ECAL
130t
端部ECAL
25t✖2
端部HCAL
350t✖2
桶轭承载总重量：2188t

## Slide 4
Ref-TDR机械部分
桶轭
1560t
桶部Muon
58t
桶轭
简化：模块简化为整体
内部留出muon探测器的安装空间
接触：模块与端部法兰
模块之间、支撑架与桶轭
均为绑定接触
桶部Muon
简化：因为探测板过多，不便于模拟
将其简化为在桶轭上施加58t的力
等效替代桶部Muon的重力
桶部Muon
重力作用

## Slide 5
Ref-TDR机械部分
超导磁体
简化：内部线圈部分简化为实体
通过八个圆柱与端部连接
内外桶和端板保留
采用等效密度
等效弹性模量
接触：超导与桶轭为摩擦接触
桶部HCAL
简化：桶部简化为实体
采用等效密度
等效弹性模量
接触：连接结构与桶部HCAL
、连接结构与桶轭之间均为绑定接触
超导螺线管磁体
290t
桶部HCAL
960t
桶部ECAL
130t
桶部ECAL
简化：桶部简化为实体
采用等效密度
等效弹性模量
接触：连接结构均为绑定接触

## Slide 6
Ref-TDR机械部分
端部ECAL
25t✖2
端部HCAL
350t✖2
端部HCAL
简化：简化为实体
采用等效密度
等效弹性模量
接触：连接环为绑定接触
斜铁之间为摩擦接触
桶部ECAL
简化：简化为实体
采用等效密度
等效弹性模量
接触：连接结构均为绑定接触
固定支撑
桶轭底部固定支撑

## Slide 7
Ref-TDR机械部分
自重模拟
探测器总体
最大变形
10.427mm
最大等效应力
377.24MPa
排除异常点
整体的应力分布较为均匀
安装
内部各子探测器后
探测器总体模拟结果
最大等效应力
应力奇异点

## Slide 8
Ref-TDR机械部分
自重模拟
桶轭
最大变形
1.1092mm
最大等效应力
78.567MPa
最大变形
0.67166mm
最大等效应力
50.259MPa
空载状态
桶轭模拟结果
安装
内部各子探测器后
桶轭模拟结果
安装内部子探测器后，桶轭自重变形增大，超过了1mm。
因此提出新的变形设计要求。

## Slide 9
Ref-TDR机械部分
自重模拟
探测器总体
最大变形
1.5058mm
最大等效应力
94.327MPa
安装
内部各子探测器后
桶轭模拟结果
参与模拟的部件：
桶轭
重力加速度取9.8
桶部Muon 58t
等效力A=568400 N
超导磁体 290t
桶部HCAL 960t
端部HCAL 700t
桶部ECAL 130t
端部ECAL 50t
内部其他探测器与管线 10t
等效力B=20972000 N