## Slide 1: Progress of the Muonium-to-Antimuonium Conversion Experiment (MACE)
赵诗涵 on behalf of the MACE working group
zhaoshh7@mail2.sysu.edu.cn
第四届高能物理理论与实验融合发展研讨会，2025，大连
2025-09-20
Ai-Yu Bai, Hanjie Cai, Chang-Lin Chen, Siyuan Chen, Xurong Chen, Yu Chen, Weibin Cheng, Ling-Yun Dai, Rui-Rui Fan, Li Gong, Zihao Guo, Yuan He, Zhilong Hou, Yinyuan Huang, Huan Jia, Hao Jiang, Han-Tao Jing, Xiaoshen Kang, Kim-Siang Khaw, Hai-Bo Li, Jincheng Li, Yang Li, Shulin Liu, Guihao Lu, Han Miao, Yunsong Ning, Jianwei Niu, Huaxing Peng, Alexey A. Petrov, Yuanshuai Qin, Mingchen Sun, Jian Tang, Jing-Yu Tang, Ye Tian, Rong Wang, Xiaodong Wang, Zhichao Wang, Chen Wu, Tian-Yu Xing, Weizhi Xiong, Yu Xu, Baojun Yan, De-Liang Yao, Tao Yu, Ye Yuan, Yi Yuan, Jian Zhang, Yao Zhang, Yongchao Zhang, Zhilv Zhang, Guang Zhao, Shihan Zhao
(MACE working group)
[arXiv:2410.18817] Conceptual Design of the Muonium-to-Antimuonium Conversion Experiment (MACE), accepted by Nuclear Science and Techniques

## Slide 2: Contents
Motivations
MACE conceptual design
Proposal of MACE Phase-I
MACE offline software
Summary

## Slide 3: Contents
Motivations
MACE conceptual design
Proposal of MACE Phase-I
MACE offline software
Summary

## Slide 4: Symmetries of SM
The Standard Model (SM) gauge symmetry:
The absence of right-handed neutrino leads to lepton flavor symmetry:
Lepton flavor is always conserved in the Standard Model, however…
QCD
Electroweak
Baryon number conservation
Lepton flavor conservation
 | +1 | 0 | 0 | -1 | 0 | 0
 | 0 | +1 | 0 | 0 | -1 | 0
 | 0 | 0 | +1 | 0 | 0 | -1
 | +1 | 0 | 0 | -1 | 0 | 0
 | 0 | +1 | 0 | 0 | -1 | 0
 | 0 | 0 | +1 | 0 | 0 | -1

## Slide 5: Charged lepton flavor violation (cLFV): a portal of new physics
    Lepton flavor is not conserved in the real world.
      Neutrinos have mass and mixing.
      So cLFV should exist, but it hasn't been seen yet...
    Many new physics model beyond SM predict scalable cLFV.
    cLFV is forbidden in SM, free of SM background.
    A clear evidence of new physic if observed!
Why muon?
Lightest massive unstable charged lepton.
Reasonably long 2.2-μs lifetime.
Almost free from QCD corrections.
MEGII (PSI)
Mu3e (PSI)
Mu2e (Fermilab)
COMET (J-PARC)
MACE (China)

## Slide 6: 1940s till now: a cLFV odyssey
MEGII
(PSI)
Mu3e
(PSI)
Mu2e (Fermilab)
COMET
(J-PARC)
MACS, 1999
Crystal Box, 1986
MACE (China)
MEGII
COMET
Mu2e
Mu3e
Towards new muon cLFV experiments
Construction of intense muon beamlines in China
Development of particle detection technology
sensitivity!
MACE
Notes: The figure above shows the reported charged lepton flavor violation searching in the history
We aim at sensitivity
Decay and conversion
Improvement compared to

## Slide 7: Muonium science and application
缪子素是前沿科学研究的理想探针
缪子素在前沿科学研究中有重要价值
缪子素是精确检验基础物理定律的重要体系
  精确测量缪子素能级 → 精确检验量子电动力学
  寻找正反缪子素转化过程 → 寻找超越标准模型的新物理
  测量缪子素重力 → 研究反物质重力及检验广义相对论
缪子素是交叉学科前沿的重要窗口
  缪子素自旋谱学 → 研究材料内禀磁学性质
  缪子素化学 → 研究化学反应机理
缪子素 态的 Breit-Rabi 能级
Tanaka K S, Iwasaki M, Kamigaito O, et al. PTEP, 2021, 2021(5): 053C01.
正反缪子素转化实验
缪子素研究铁氢酶催化机理
缪子素示意图
缪子素
由正缪子（和电子（组成的原子，基本性质类似氢原子，但质量较轻且会自发衰变。
缪子素重力测量实验
Ai-Yu Bai et al (MACE working group). Conceptual Design of the Muonium-to-Antimuonium Conversion Experiment (MACE). arXiv: 2410.18817, 2024.
Anna Soter and Andreas Knecht, Development of a cold atomic muonium beam for next generation atomic physics and gravity experiments, SciPost Phys.Proc. 5, 031, 2021
Joseph A. Wright. Muonium Chemistry at Diiron Subsite Analogues of [FeFe]-Hydrogenase. Angewandte Chemie International Edition, 55, 47, 14471, 2016

## Slide 8: Muonium conversion
Muonium (): a leptonic isotope of hydrogen
1957, B. Pontecorvo first suggested process.
1960, V.W. Hughes et al. first observed the muonium directly.
1961, G. Feinberg and S. Weinberg published a research on .
Muonium
Antimuonium
: an process
In SMEFT: operators different from processes
(μ → eγ, μ → eee, μN → eN)
can be possible even if is suppressed.
Complementary to process searches.
Phys.Lett.B 852 (2024) 138621
Phys.Rev.D 105 (2022) 1, 015026
Current bound:
< 8.3×10-11
in 0.1T field, 90% C.L.
Phys. Rev. Lett. 82 (1999), 49-52.
Notes: Let’s move on to the muonium
Complementary
comparable
Trace back
push

## Slide 9: Contents
Motivations
MACE conceptual design
Proposal of MACE Phase-I
MACE offline software
Summary

## Slide 10: Signal and background
Coincidence of a fast and a slow
Common vertex (by selecting e+/e- track DCA)
  Select of e+
  Reject accidental e-
Time coincidence (by selecting e+ TOF)
  Select of e+
  Reject e+ from IC decay or Bhabha scattering
Charge identification (by e- track & e+ annihilation)
e+
(13.5eV avg.)
e- (26MeV avg.)
ν
ν
M
μ+
e+
e-
ν
ν
μ+
e+ (miss)
μ+
M
e+
e-
ν
ν
1. Internal conv. (IC) decay
Signal:
fast + slow
2. Final state scattering
3. Accidental bkg.
Scattering/conv. e-
Misreconstruction
Cosmic ray, etc.
e+
e-
ν
ν
μ+
Excellent vertex resolution
  e+/e- spatial resolution
  Precise e+ transport in EM field
Excellent time resolution
  e+/e- time resolution
Target

## Slide 11
Status of muon sources
CSNS, Dongguan, China
HIAF & CiADS, Huizhou, China
(under construction)
Global facilities: PSI (Switzerland), J-PARC (Japan), ISIS (UK), TRIUMF (Canada), FNAL (USA).
First high-intensity muon source in China, to be built in the Greater Bay Area: CSNS/CiADS/HIAF.
Notes: The UK, Switzerland,.. have all built their own muon beamlines, and became important centers of muon physics.
On the other hand
Three major
Guangdong

## Slide 12: Muon beamline of CiADS
A surface muon beamline is under way at China Initiative Accelerator Driven System (CiADS)
Exploring cutting-edge research with high muon flux?
25 kW: 500MeV & 50μA
  Accelerator construction
  Proton beam commissioning
2025～2026
H. -J Cai et al. PRAB 27 (2024) 2, 023403
  Beam stability test
  Muon beam commissioning
  One target station, two beamlines
2026～2027
250 kW: 500MeV & 500μA
  2.5 MW commissioning
  2.5 MW long-term run
  Two target station, four beamlines
  Muon physics and applications
2027~2030
3 MW: 600MeV & 5mA
Beam power | Target | Target | Intensity（s-1） | Spin pol. | background
300 kW | Graphite | Full-solenoid |  | ~94% | <0.1%
 |  | Mixing |  | >99% | 
3 MW | Lithium jet | Full-solenoid |  | ~94% | 
 |  | Mixing |  | >99% | 
Beam power | Target | Target | Intensity（s-1） | Spin pol. | background
300 kW | Graphite | Full-solenoid |  | ~94% | <0.1%
 |  | Mixing |  | >99% | 
3 MW | Lithium jet | Full-solenoid |  | ~94% | 
 |  | Mixing |  | >99% | 
Notes: As we can see here the figure below shows the timeline of the construction and upgrade plans of the accelerator and muon target stations
Considerable parameters
focus
What can we do
answer

## Slide 13: Conceptual design of MACE detector system

## Slide 14: Conceptual design of MACE detector system
Surface muon stop in target → muonium
M diffuse into vacuum & convert to
Decay in a vacuum:
CDC detects Michel track
Triple coincidence:
MMS + MCP + ECAL
Atomic
Michel
Transport atomic to MCP (conserving transverse position)
MCP detects position
annihilates on MCP
ECAL detects 2 back-to-back annihilation
MMS:
CDC: tracking
TTC: Trigger, timing
PTS:
Accelerate and transport atomic
PDS:
MCP: atomic transverse position
ECAL: identification

## Slide 15: Sensitivity estimation
single event sensitivity is expected:
Summary of simulation results:
Notes: We estimated the sensitivity of MACE by detailed simulations
Left side table: each type of backgrounds and their levels
Right side table: the detailed efficiency of each subdetectors
For the muonium to antimuonium conversion, we can expect a single event sensitivity of

## Slide 16: Muonium production target
The simulation is validated by muonium yield data measured in TRIUMF.
Optimize in perforated bulk target by scanning parameters, it can achieve
  Max , with 2mm hole depth, and .
Intensity of in-vacuum muonium source:
can be improved by utilizing porous materials, ideally perforated silica aerogel.
A simulation method is developed to accurately simulate muonium production and diffusion.
Zhao, Shihan, and Jian Tang. "Optimization of muonium yield in perforated silica aerogel." Physical Review D 109.7 (2024): 072012.
2 times larger than the yield in 1999
J. Beare et al., PTEP. 2020, 123C01 (2020)

## Slide 17: Positron transport system
The component of positron transport system (PTS)
  I. Electrostatic accelerator
  II. Solenoid system
  1. MMS solenoid
  2. TS solenoid
  3. ECAL solenoid
PTS performance
I. Transmission efficiency: 65.8%.
II. Flight time: 322 ns.
III. Flight time FWHM: 6.9 ns.
IV. Spatial resolution: 0.088 mm 0.102 mm
Lu, Guihao, et al. "Positron Transport System for Muonium-to-Antimuonium Conversion Experiment." arXiv preprint arXiv:2508.07922 (2025).
Suppress the IC decay bkg. by a level of

## Slide 18: PTS prototyping progress
PTS validation
  Testing with TS solenoids and accelerator module
Accelerator module prototype
  Multi-layer PCB
  High voltage > 2 kV
Ionization Vacuum Gauge
Thermocouple Vacuum Gauge
Particle Source
Molecular Pump
Dry Mechanical Pump
Roughing Valve
Foreline Valve
High Vacuum Gate Valve
Venting Valve
Detector Chamber
Validation
prototype
Credit: Guihao Lu

## Slide 19: Tiled timing counter (TTC)
Tilt design, signal track hits 2-3 scintillator tiles.
Azimuth spacing , tilt angle .
Full simulation result:
  Geometry efficiency:
  Detection efficiency (amp. > 3 p.e.):
Test with cosmic-ray muons:
Fitted time resolution:
  Double-tile:
  Single-tile:
Credit: Hao Jiang

## Slide 20: Contents
Motivations
MACE conceptual design
Proposal of MACE Phase-I
MACE offline software
Summary

## Slide 21: Proposal of MACE Phase-I
Test of the Standard Model
Muon cLFV decay modes
  annihilation：
  Neutrinoless decay：
  New particles: DM, ALP, Familon, …
Crystal Box、MEG
, 1959
, 1988
PRL, 1959, 3: 288-291
PRD 38 (1988) 2077
EPJC 80 (2020) 9, 858
, 2004
, 2015
PIONEER CDR, 2022
EPJC 76 (2016) 3, 108
Int.J.Mod.Phys.A 20 (2005) 472-481
PRL. 115 (2015) 7, 071801
arXiv:2203.01981
Crystal Box:
…
MeV, 2016
MEG:
How to improve the sensitivity?

## Slide 22: MACE Phase-I detector
Phase-I requirements：
High-intensity muon beam —— improvement of statistics
Detectors with fast response —— “pileup” rejection
tracking and timing, discrimination
High acceptance and granularity, good resolution
Challenge：
No magnetic field applied.
High background rate.

## Slide 23: Tracker System
Precise timing and tracking ability
Low material budget
Low cost
discrimination
  High active area
  High detection efficiency
  Low detection efficiency
Plastic scintillators
325.4 mm
SciFi baseline design:
Crossing fiber arrangement
2360 channels
Single-end readout by SiPM
Spatial resolution ~1 mm
Timing resolution ~800 ps
Credit: Yinyuan Huang

## Slide 24: Tracker System
ECAL
SciFi
TTC
Tiled timing counter (TTC)
  108 tiles of plastic scintillator in total
  Double-end readout by SiPM
  Good timing resolution, ~ ps
  Providing timing information to ECAL, e/γ discrimination
Plastic scintillator
PCB
Credit: Hao Jiang

## Slide 25: Electromagnetic Calorimeter
Design scheme：
High acceptance and granularity
Symmetrical structure
Class-I GP(8,0) Goldberg polyhedron
Crystal scintillators coupled with SiPM arrays
Sensors 19 (2019) 2, 308
PEN detector
pCsI + PMT
BGO
8000 ph/MeV
300 ns
Not hygroscopic
Emits at 480 nm
CNY ￥100/cm3
LYSO
30000 ph/MeV
40 ns
Radiation hard
Not hygroscopic
Emits at 420 nm
CNY ￥300/cm3
Pure CsI
3500 ph/MeV
40 ns
Slight hygroscopic
Emits at 310 nm
Adopted by Mu2e and PIBETA
CNY ￥30/cm3
MACE ECAL
pCsI + SiPM
NUV SiPM readout
Baseline design

## Slide 26: Sensitivity estimation of
Signal:
Triple coplanar tracks
and two s
Background:
Double radiative muon decay
BR upper limit estimation: (90% C.L.)
in 1988
PRD 38 (1988) 2077
SciPost Phys. 9, 027 (2020)
Calculated by McMule
Event selection criteria:
Time coincidence
One track in tracker, two tracks in ECAL
Select missing energy

## Slide 27: Sensitivity estimation of
M
μ+
Target
γ
γ
M
μ+
Target
e+
μ+
e+
Signal: Double collinear 53 MeV gamma-rays
Background: Accidental coincidence of “pileup” positrons
No response in Tracker
Double tracks reconstructed by ECAL
Positron → gamma misidentification
Two accidental coincidence misidentified tracks at same vertex
BR upper limit estimation: (90% C.L.)
in 1959
PRL, 1959, 3: 288-291
More background simulations and refined data analyses to be updated!

## Slide 28: Contents
Motivations
MACE conceptual design
Proposal of MACE Phase-I
MACE offline software
Summary

## Slide 29: MACE offline software
Experiment design stage: simulation-guided detector design optimization.
Engineering stage: detector alignment and detector-response simulation.
Data-taking stage: bridges experimental data to physics results.
Tasks:
  Event generation
  Simulation: detector, DAQ…
  Reconstruction & analysis
  Visualization: event, track, detector geometry…
Software quality control:
  Framework and architecture
  Continuous integration
  Validation

## Slide 30: Software Architecture
Mustard framework:
  A modern, distributed, high-performance architecture for particle physics experiments.
High-performance design:
  Distributed executor for simulation and analysis.
  Based on C++20, template-rich design for zero-overhead abstraction and flexibility.
Key components:
  Distributed computing framework
  Unified geometry interfaces
  High-level data model abstractions and IO
  Utilities for simulation, reconstruction, analysis...

## Slide 31: Continuous Integration
Challenges in Parallel Development
  Merge conflicts
  Tedious code review
  Hidden risks
Practice of Continuous Integration
  Frequently integrate code into a shared repository.
  Each integration is verified via automated builds and tests.
CI/CD
  Configure pipeline via config file.
  Runners execute automated test scripts.
  Regression tests.

## Slide 32: Contents
Motivations
MACE conceptual design
Recent progress and prototyping
MACE offline software
Summary

## Slide 33: Breakthrough point for fundamental research
The latest result was obtained by MACS in 1999, with a muon flux of .
Requirement: China domestic accelerator muon source to provide surface muon.
Over 20 years, significant advances in detector technology.
China’s accelerator and particle detection technology have made great strides.
The new generation of experiments is expected to improve sensitivity by over two orders of magnitude compared to the 1999 PSI results!
Thanks!
Acknowledgements:
We express our gratitude to Yoshitaka Kuno, Klaus Jungmann, Lorenzo Calibbi, Ce Zhang, Tsutomu Mibe, Yuichi Uesaka, Yu Bao, Ningqiang Song and
many other colleagues for their insights and expertise during discussions. We also appreciate the professional and constructive comments provided by Xin Chen, Kim-Siang Khaw, Teng Li, Yi Liao, Yong Liu and Xiang Xiao in reviewing the MACE conceptual design report.

## Slide 35: Muonium production target
Proposed design: Tilted single-layer silica aerogel.
Improves the muon emmision efficiency while keeping the muon stopping power.
Simulation in progress.

## Slide 36: Key components
Distributed executor & scheduler
  Based on Message Passing Interface (MPI)
  Pure message passing model (nice speedup and reduced technical complexity).
Event Data Model
  Statically typed data model built by C++ template metaprogramming.
  Interface enables:
    Compile-time type checking.
    Zero-overhead tuple mapping.
    Consistency with actual data object.
Detector Geometry & Field
Separates human-readable parameters (Description) from detailed geometry construction (Definition).
Supports reusable EM field definitions and interpolation from field maps.
Unifies interface for simulation and reconstruction processes