## Slide 1
CEPC Fast Luminosity Monitor Introduction
2025.07.16 RASER Workshop 2025
李雁鹏

## Slide 2
OUTLINE
CEPC Introduction
Fast Lumi Monitor Project of CEPC
RASER Simulation

## Slide 3
CEPC Introduction
Circular Electron Positron Collider
Higgs factory
Circumference: 100 km
Symmetric circular electron-positron collider
4 run mode: Higgs(240GeV), Z boson(91GeV), W boson(160GeV), tt^{bar}(360GeV)(c.m.s)
High luminosity(~ )

## Slide 4
CEPC Introduction
Beijing Electron Positron Collider II(BEPCII, China)
Physic goal: τ-charm(2~5GeV c.m.s)
Symmetric circular electron-positron collider
Peak luminosity( )

## Slide 5
CEPC Introduction
SuperKEKB(Japan)
Physic goal: B meson decay and CP violation
Asymmetric circular electron-positron collider(:4GeV, :7GeV)
Nanobeam collision scheme (+ crab waist)
High luminosity( )

## Slide 6
CEPC Introduction
Higher and Wider energy region
Higher luminosity
More physic targets

## Slide 7
Fast Lumi Monitor Project of CEPC
For horizontal IP orbit feedback: Luminosity-driven with a dithering system
weak beam deflection
Based on SuperKEKB fast luminosity project design
Due to various reasons (e.g., GM), the two colliding bunches failed to align properly.
😃
🙁

## Slide 8
Monitor based on radiative Bhabha at zero degree
Large cross section
Fast Lumi Monitor Project of CEPC

## Slide 9
Fast Lumi Monitor Project of CEPC
Where to detect radiative Bhabha electrons?

## Slide 10
Fast Lumi Monitor Project of CEPC
Monitor candidates: Si, diamond and SiC
4H-SiC
Stronger radiative tolerance()
Lower leakage current(~pA)
Excellent time resolution(~100ps)
Higher thermal conductivity(RT~500℃)
Cost less
5mm×5mm PIN-type detector developed by NJU and IHEP
94ps

## Slide 11
RASER Simulation
Secondary particle distribution
Vertival: 0mm
Beam direction: 230mm
Detector placement postion:
P1=(-31mm, 0, 230mm)
P2=(31mm, 0, 230mm)
Whthin coordinate

## Slide 12
RASER Simulation
Vertical length: 3cm
Beam direction length: 1cm
2*12 pixel
1uA threshold for each channel
Design plan:
2*12 channel

## Slide 13
RASER Simulation
How to use RASER to simulate CFLM project?
Example: Simulation for secondary particle distribution
setting/g4experiment/cflm_spd.json
"par_type": "gamma"
"par_type": "e-"
mkdir src/raser/lumi/figs
mkdir src/raser/lumi/input
mkdir src/raser/lumi/output/
Upload input file to src/raser/lumi/input
Setup RASER environment
raser lumi spd_dis
raser lumi spd_dis_plot
About 1h

## Slide 14
Backup

## Slide 15
Primary electron distribution