## Slide 1
Construction and testing of the LLRF test platform for the 1.0 GeV linear accelerator of Wuhan Advanced Light Source Research Center
Presenter: Yue Hongwei
Supervisor: Nie Yuancun
Wuhan Advanced Light Source Research Center

## Slide 2
Contents
1 Introduction of 1.0 GeV Linear Accelerator
2 Overall Design of LLRF Test Platform
3.1 S-band Solid-state Amplifier Test
3.2 Low Level RF Control System Test
3.3 Timing and Signal Distribution System Test
4 Summary and Prospect of LLRF Test Platform

## Slide 3
1 Introduction of 1.0 GeV Linear Accelerator
Advanced Materials Modification
1.0GeV LINAC
Medical Applications，FLASH
High-Energy Electron Imaging
Advanced Acceleration
Laser Inverse Compton Scattering
Motivation: multipurpose 1.0 GeV electron beam application research platform / future 1.5 GeV injector of the WALS（high-energy electron beams have many potential applications）
Extensive efforts have been made in physical design, technical study, and the mass production of 1.0 GeV components (with an investment exceeding 100 million RMB)
1.0GeV LINAC
The Starting Point of the Light Source
Application Platform
Gun
LINAC
Storage Ring

## Slide 4
1 Introduction of 1.0 GeV Linear Accelerator
Conceptual design
LINAC tunnel
Parameters | Values
Energy | 1.0 GeV
Energy Spread（RMS） | ≤1%
Normalized Emittance（RMS） | ≤50 mm·mrad
Bunch Charge | 1-2 nC
Macro Pulse Repetition Frequency | 10 Hz
Micro-pulse Repetition Frequency | 500 MHz
From 2021 to 2023, the physical design, the project CDR (conceptual design report) and TDR (technical design report) were completed successively.

## Slide 5
1 Introduction of 1.0 GeV Linear Accelerator
科技创新，点亮武汉
RF gun
Photocathode production
Driver laser
Dual-feed accelerator tube
Thermionic components
High-voltage pulse modulator
LLRF test platform
High-power klystron
Technical support for facility performance
Electron Gun: 10^-8 Pa high vacuum, replaceable photocathode.
Accelerator Tube: New type of dual-feed traveling wave tube, segmented external water cooling design.
Klystron: Domestic 50MW
LLRF: Long-term amplitude and phase stability better than 0.04% and 0.02°.
Microwave elements

## Slide 6
2 Overall Design of LLRF Test Platform
Design goal
A LLRF test platform for Wuhan Light Source 1.0 GeV linear accelerator is built.
Verify the performance of key subsystems ( solid state amplifier, low level control system, timing and signal distribution system ).
Provide technical support for subsequent engineering construction and optimization.
Timing system
Low level RF controller
Signal distribution system
Solid-state amplifier
LLRF test platform
Design of LLRF test platform

## Slide 7
3.1 S-band Solid-state Amplifier Test
Parameters | Values
Operating Frequency | 2997.924 MHz±3 MHz
Output Power | 50-1280W
Amplitude Stability(RMS) | ≤0.02%
Phase Stability(RMS) | ≤0.02°
Pulse Width | 1-10μs
Pulse Repetition Frequency | 1-100Hz
Rising and Failing Edge | ≤0.05us
Pulse Leading Edge Jitter | ≤0.3ns
Input and Output Isolation | ≥85dBc
S-band Solid-state
Function : The solid-state amplifier is the driver stage of the klystron, which needs to provide stable and low-noise RF power input.
Performance : The output power and phase need to have high stability and consistency.
Test : The key indicators of the solid-state amplifier are systematically tested.
Solid-state amplifier physical diagram

## Slide 8
3.1 S-band Solid-state Amplifier Test
Especially, the amplitude and phase stability ( RMS value ) of the solid-state amplifier is better than 0.02 % and 0.02 °.
Pulse leading edge jitter
Input and output isolation
Rising and failing edge
Output power
Pulse repetition frequency
Amplitude and phase stability
Pulse width

## Slide 9
3.2 Low Level RF Control System Test
Parameters | Values
Operating Frequency | 2997.924 MHz
Output Power | ≥10dBm
Amplitude Measurement Resolution(rms) | ≤0.02%
Phase Amplitude Measurement Resolution(rms) | ≤0.02°
Amplitude Stability with Solid-state Amplifier(rms) | ≤0.02%
Phase Stability with Solid-state Amplifier(rms) | ≤0.02°
Timing Trigger Adjustment Resolution | ≤6ns
Reflection Protection Response Time | ≤1us
Channel Isolation Degree | ≥60dB
Low Level RF Control System
Function : Be responsible for the real-time stable control of the amplitude and phase of the acceleration cavity.
Performance :
  The resolution of amplitude and phase measurement is better than 0.02 % and 0.02 °;
  Support open-loop and closed-loop feedback control mode ;
  Support internal and external trigger mode ;
  Have the ability of temperature drift compensation and suppression.
Test : Open-loop closed-loop test with solid-state amplifier and timing device.
Low level controllers produced

## Slide 10
3.2 Low Level RF Control System Test
Amplitude and phase measurement resolution(RMS)
Output Power
Operating Frequency
Amplitude and Phase stability with solid-state amplifier(RMS)
Reflection protection response time
Timing trigger adjustment resolution
Channel isolation degree

## Slide 11
3.3 Timing and Signal Distribution System Test
Parameters | Values
Shake Of Timing Output Signal Relative To Rf Reference Input Signal | ≤7ps
Timing Output Signal Rising Edge | ≤0.7ns
5ps Delay Time Precision Adjustment | √
1 / 20 Event Clock Precision Adjustment | √
Event Clock Precision Adjustment | √
The Phase Jitter Of The Output Of The Signal Distribution Receiver | ≤0.01°
Phase Drift Of Signal Distribution Receiver Output | ≤0.7°
Timing and Signal Distribution System
Function : Provides a unified clock reference and trigger signal for linear accelerators.
Performance :
  The timing device has low signal jitter, stable rising edge, 5 ps delay time accuracy adjustment, 1 / 20 event clock accuracy adjustment and event clock accuracy adjustment;
  The signal distribution system needs to ensure low phase jitter and low drift performance.
Test : Timing and signal distribution devices have been cross-tested and meet the design requirements.
Timing and signal distribution system diagram

## Slide 12
3.3 Timing and Signal Distribution System Test
1 / 20 event clock precision adjustment
5ps delay time precision adjustment
Timing device phase jitter and rising edge
Phase drift of signal distribution receiver output
The phase jitter of the output of the signal distribution receiver
Event clock precision adjustment

## Slide 13
4 Summary and Prospect of LLRF Test Platform
The test platform has been successfully built, and the individual and joint tests of S-band solid-state amplifier, low-level control system and timing and signal distribution system have been completed.
The system construction, debugging and optimization methods have been mastered, and it has the ability to support the subsequent accelerator operation.
Summary
Upgrade the test platform to achieve joint debugging and performance verification with the klystron ;
Optimize and upgrade the hardware and software of the platform ;
It provides a reliable experimental verification platform for linear accelerator and free electron laser LLRF systems.
Prospect

## Slide 14
Thanks for your attention!