## Slide 1
in accordance to Revision 3.0 of MTCA.0 Standard
New MTCA.4 Crate
Alphonso Liu | 刘扬
2025-9-17

## Slide 2: The Challenge of the Measurement & Control System in Large Science
Managing unprecedented data volumes & rates
Extreme timing & synchronization requirements (nanoseconds)
Reliable operation in harsh environments radiation, EM interference, unstable temperature, vibration etc
The need for modularity and scalability over decades-long project lifecycles
Multiple industrial computer platforms

## Slide 3: Modular Industrial Computer Platform - Started From Versa Module Eurocard
16-bit asynchronous
Motorola 68000
Intel 8088---- IBM ISA
1992
Intel PCI

## Slide 4: What is xTCA?
Advanced Telecom Computing Architecture
xTCA
ATCA
MTCA
Micro Telecom Computing Architecture
AMC
Advanced
Mezzanine
Card

## Slide 5: What is MTCA.4?
MicroTCA Specification Family Tree
MTCA.0
MTCA.4
Micro Telecommunications Computing Architecture Base Specification
MTCA.2
MTCA.3
AMC.0
MTCA.1
Air Cooled Rugged MicroTCA Specification
Hardened Conduction Cooled MicroTCA Specification
MicroTCA Enhancements for Rear I/O and Precision Timing
Advanced Mezzanine Card Base Specification
Hardened Air Cooled MicroTCA Specification

## Slide 6: Typical MTCA.4 Crate
1 Upper Cooling Unit (CU1)
2 Lower Cooling
3 Air filter
4 ESD Wrist Strap Terminal
5 Cable Tray Unit (CU2)
6 Backplane
7 Card cage
8 Rear card cage
9 Cable Tray
10 Ground Terminal

## Slide 7: nVent Schroff MTCA.4 Crates
nVent SCHROFF
MTCA.4 Crates

## Slide 8: NEW MTCA.0 Rev 3.0 compliant backplane
Signal Integrity, compatibility and differences

## Slide 9: Next Generation MicroTCA
MTCA.0 Rev 3.0
NEW FEATURES
Supports PCI Express Gen 4 & 5
Supports 100 Gb Ethernet (100GBASE-KR4)
MCH with new management features
MCH slot gets 110 W of power to support 100 GbE or PCIe Gen 4 / 5 switches
Power Module with 110 W channels for MCH and CU

## Slide 10: New Backplane Design
Connectors changed from Press Fit to Surface Mount to minimize the losses in the through holes
Connectors are downward compatible
Low loss material and new routing strategy for pcb to improve the signal integrity
Data transmission channel from PCI-SIG and IEEE divided into sections, with limits defined for MCH, AMC and Backplane
The backplane in the NEW nVent SCHROFF MTCA.4 crate meets the requirements of the MTCA.0 Rev. 3.0 Standard for PCIe Gen 4 & (5) and 100GBASE-KR4
Rx/Tx Chip
Tx/Rx Chip
transmission channel

## Slide 11: Similar Backplane Topology BUT different physical AMC locations
New MCH location required new optimized routing strategy
NEW AMC module order is (from left to right):
old topology
NEW topology

## Slide 12: Cooling Unit update

## Slide 13: Current nVent SCHROFF Cooling Unit
MTCA.0 Rev3: Cooling Unit Power Channel enhancement: 80 W -> 110 W
  Already using the strongest 120 mm, 12 V DC fans available in the front
  Rear fans are upgraded to improve air flow in the RTM section
  No cooling improvement of front card cage possible with current System architecture
New Cooling Unit Manager:
  The Cooling Unit Manager has been redesigned, now using the STMicro STM 32 controller

## Slide 14: Increases in Computer Power – More Heat

## Slide 15: Cooling MTCA Crates Inside the Cabinet
COOLING SOLUTIONS FOR ALL REQUIREMTS
COMPLETE PORTFOLIO
Row Aisle Containment
(Active w/IRC)
Row Aisle Containment (Passive)
Server Rack
Server Rack w/Fans
Server Rack w/AC
2-4 kW
8-12 kW
15-25 kW
4-6 kW
6-8 kW
25-55 kW
300 mm
600 mm
30-75 kW
per cooler
10-25 kW
10-25 kW
40-800+
kW
40-800+
kW
Rack w/Integrated LX Cooling (MicroEdge)
In Row Cooling – LX
Rear Door Cooling (Passive/Active)
Chassis Level Immersion Cooling
Row and Rack Coolant Distribution Unit (CDU) & Rack Manifolds
3.2 kW per chassis
AIR AND LIQUID COOLING SOLUTIONS
15
Notes: Marc/Stefan Djuranec

## Slide 16: Thank You!