## Slide 1: Development of RPC detector for ATLAS Muon Phase-II upgrade -- progress report
Yongjie Sun (孙勇杰)
On behalf of the ATLAS China Muon team
University of Science and Technology of China

## Slide 2: Introduction – towards HL-LHC
LHC will upgrade to HL-LHC with 5 - 7.5 times higher luminosity.
ATLAS will collect 90% of its physics data during the HL-LHC period
 Unprecedented opportunities to search for new physics at energy frontier and measurement of the SM, e.g. Higgs boson properties
ATLAS detector is undergoing Phase-II upgrades accordingly.
Run-1
2009-2012
LS-1
2013-2014
Run-2
2015-2018
LHC construction
1998-2008
Higgs. discovery
7,8 TeV
30 fb-1
13 TeV
190 fb-1
Run-3
2022-2026
LS-3
2026-2029
Run-4，5
2030-2040
LS-2
2019-2021
13.6 TeV
450 fb-1
13.6-14 TeV
3000-4000 fb-1
*Latest schedule released in Oct. 2024

## Slide 3: Upgrade of the ATLAS detector
Phase-II upgrade
Silicon Inner Tracking system
Phase-II upgrade
High Granularity Timing Detector HGTD
Phase-I upgrade
New Small Wheel (NSW)
Phase-II upgrade
Thin-gap RPC (barrel muon trigger, very crucial for physics) ,
sMDT, electronics
Phase-II upgrade
Trigger and Data Acquisition - TDAQ
Main goals:
Higher radiation hardness/rate capability
Higher spatial/time resolution
Faster response time
Higher data acquisition rate

## Slide 4: The Phase-II Upgrade of Muon RPC
L=7.5×1034cm-2s-1@13TeV
Current RPC system and its limitation
  The limited rate capability: ~ 100 Hz/cm2  1 kHz/cm2
  Reaching the lifetime of 10 years @ LHC  lower efficiency
  The acceptance holes due to support structures
The desire for additional BI layers for HL-LHC
  Three layers of new RPC in the BI region
  Thin-gap design with higher rate capability and longevity
  Fix most of the acceptance holes

## Slide 5: Advantages of the BI RPC Upgrade
The new BI RPC fixed most of the acceptance holes.
Flexible trigger logic increases the trigger efficiency: 70%  90%
Improved muon coverage important for offline analysis for physics with muon signature
High time resolution (order of 1 ns) with thin gas gap can be exploited for new physics searches
Expected trigger eff. with BI upgrade ~ 90%
Current trigger eff. ~ 70%

## Slide 6: Technical design: Thin-gap RPC
Thinner bakelite:
  Less voltage drop in bakelite  improve the rate capability, larger induced signals
Thinner gas gap:
  Less charge produced per event  improve rate capability and longevity
  Higher field  better time resolution
Improved readout panel
  Better mechanics flatness and hardness  better signal transmission and spatial resolution.
New generation FE electronic:
  Higher amplification factor and high S/N ratio to compensate the lost gas amplification.
Readout panel
Bakelite electrode
Gas gap
Copper strip/GND
Low εr filler
Bakelite: 2 mm1.5 mm
Gap size: 2 mm1 mm
Specifications:
High rate capability:  kHz/cm2
Longer longevity: >10 years@HL-LHC
Higher spatial resolution: <1 cm
Higher time resolution: ~ 0.5 ns
 First application in large scale experiment

## Slide 7: Tasks of the Chinese team
Gas gap: 72 (~10%)
Readout panel: 912 (~50%)
Singlet: 360 (~50%)
FE board: 5000 (>50%)
Installation & commissioning
China contributions
We are here

## Slide 8: The thin gas gap production
The largest gaseous detector with strict requirements on structure precision
  Length / thickness = 2500 / 1
  Spacer: 1 mm ± 10 μm
  Frames: 1 mm ± 30 μm
  Gap size: 1 mm ± 100 μm in 7×7 cm
Typical BIL: 2500 x 680 mm
Size: ~1.7m2
Typical BIS: 1700 x 1100 mm
Size: ~1.9 m2

## Slide 9: China gas gap production site
Spacer gluing platform
Graphite painting machine
Spacers placed
Finished gas gap
Full production line established
8 prototypes produced
  Size = 1300 x 680 mm2
Procedures are under optimization
Getting ready for mass production
HV electrode
Details can be found in Dongshuo’s talk

## Slide 10: Aging test of gas gaps at GIF++
Chart: HV (V)
| 1000 | 2000 | 3000 | 4000 | 4500 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000
gap 1 | 0.4 | 0.86 | 1.6 | 1.85 | 2.3 | 2.8 | 3.2 | 3.7 | 4.4 | 5.3 | 6.8
gap 2
gap 3 | 0.55 | 1.2 | 1.9 | 2.5 | 3 | 3.8 | 4.3 | 5.2 | 6.3 | 7.8 | 10.3
gap 4 | 0.53 | 1.1 | 1.8 | 2.8 | 3.5 | 4.7 | 5.5 | 6.7 | 8.1 | 10 | 13
gap 5 | 0.32 | 1.6 | 1.5 | 2.4 | 2 | 3.5 | 2.7 | 3.3 | 3.5 | 4 | 4.3
gap 6 | 0.1 | 0.45 | 0.4 | 0.73 | 0.65 | 0.93 | 0.95 | 1.1 | 1.2 | 1.65 | 2
Chart: 
| 4500 | 4600 | 4700 | 4800 | 4900 | 5000 | 5100 | 5200 | 5300 | 5400
GTE1 | 1.236 | 2.54 | 5.194 | 9.87 | 16.874 | 26.528 | 37.986 | 50.892 | 64.992 | 80.024
GTE2 | 1.3 | 2.784 | 5.442 | 10.112 | 17.12 | 26.606 | 37.934 | 50.9 | 64.824 | 79.654
USTC1 | 0.304 | 0.716 | 1.474 | 2.706 | 4.682 | 7.22 | 10.514 | 14.254 | 18.452 | 22.956
USTC2 | 0.614 | 1.234 | 2.356 | 4.046 | 6.386 | 9.372 | 13.032 | 17.276 | 21.948 | 26.908
USTC3 | 0.876 | 1.46 | 2.33 | 3.492 | 4.86 | 6.68 | 8.578 | 10.894 | 13.338 | 16.094
USTC4 | 0.61 | 1.2 | 2.016 | 3.174 | 4.558 | 6.424 | 8.382 | 10.558 | 12.944 | 15.506
Prototypes are under aging test at GIF++
Very low current observed
Normal behavior under irradiation
First scan at CERN
First scan at GIF++ with full source
Scan with different filters
S=OFF
S=10
S=33
S=100

## Slide 11: The readout panel production
Large size PCB  BIS = 1705 x 1072 mm
Flatness control  ± 100 μm in 7×7 cm
Developed vacuum bag production method
Qualification method  400 measurement points/panel
All BIS panel production finished (~580 panels).
1.1m
1.7m
Large size PCB
Vacuum bag pressing
Automatic thickness scan
Details can be found in Dongshuo’s talk

## Slide 12: The singlet assembly and qualification
Technical challenge of building large & thin Barrel Inner RPC singlet
The basic functional unit of RPC, Quality Assurance needed
  gas tightness
  electrical connectivity
  leakage current
  efficiency
RPC singlet assembly
Large area, large quantity, systematic test
large-scale multi-layer test station and data acquisition system
Joined the training at CERN for singlet assembly. (18 BIS-1 singlet built with good qualities.)
RPC singlet test station
Details can be found in Francois’s talk

## Slide 13: DAQ system for FEE test and for singlet qualification
Initially designed for the New front-end electronics (FEE) with a specialized Manchester encoding for data transmission (“the baseline solution”)
Quickly modified to the TDC mode for the test of “the backup solution”
DAQ functions：
  Provide 40MHz clock for FEE
  144 channels decode or TDC
  Trigger mode: External/self/master-slave
  Data package & upload
Made significant contribution to the test of the FEE boards.
Details can be found in Jiaxuan’s talk

## Slide 14: Issue addressing
Quality of gas gaps produced in Italy company (GTE)
  Issue: gas leak  refurbishment produced gaps & modification of the gap design
  Issue: current drifting  pre-washing and re-oiling, bakelite inspections, etc., still under investigation.
The FEE
  Delay of the board design and test  USTC offered an FPGA readout system for FEE test
  Restrictions of chips to USTC  FE board procured by USTC & chip bonding by HK
  Pre-production of 500 FE boards started.
The singlet
  Restrictions of FE boards with chips, singlet with electronics can not be assembled and tested in USTC
   Move the BIS singlet assembly line to MPI

## Slide 15: Decision made in MPI
Infrastructure and production
MPI tasks
  BIS triplets
  assembly equipment
  power supplies
  Oiling station
USTC tasks
  BIS singlets
  Monitoring instrumentation
  Data acquisition system
Schedule
June/July: Preparation of the assembly lines
September: Start of the singlet assembly
Singlet assembly
Triplet assembly
and test stands
Intermediate storage
Oiling station

## Slide 16: Timeline and milestones
RPC gas gap prototype construction and test – Done
BIS readout panel production and qualification – Done
Qualification method of the FEE – Done
FEE production and qualification – 500 boards submitted.
  Mass production will start after the Review in June.
BIS singlet assembly – delayed
  Mass production planned from September
Cosmic ray test station – under design
BOM/BOR panel design – in progress

## Slide 17: Summary
RPC gas gap prototypes (130 x 68 cm2) built successfully in USTC
Mass production and qualification of BIS readout panels (580 pieces) finished
Singlets (without FEE) assembly and test at CERN
An FPGA-based readout system developed for FEE test and singlet qualification
Getting ready for mass production and commissioning.
Chinese team covers most parts of the RPC production and makes significant contributions to ATLAS Muon upgrade
Chinese team makes necessary adjustments to fulfill the project

## Slide 18
BIS
BOM/BOR
BIL