## Slide 1: RCS BPM Re-Mapping: Motivation and strategy
R. Yang
20/05/2025

## Slide 2: Motivation
Abnormal offset of the RCS BPM has been pointed out this February
The possible error sources: calibration system, BPM electronics (timing window, baseline, channel unbalanced, … (Naïve)
M. Huang, March 04, 2025

## Slide 3: BPM calibration system 1/3
Machine accuracy: ±0.05 mm (achieved)
Components
  Wire: cupper, 0.26 mm, 35 N
  Dummy pipe between pickup and pulley
  Network analyser to apply sin wave and measure transmission coefficients
Work temperature: 20-21 C (same to tunnel temperature) IMPORTANT!!!
* K. Hanamura et al., PASJ meeting (2006)
** T. Miura et al., PASJ meeting (2006)
*** Y. Hashimoto et al., PASJ meeting (2007)
XY stage tilt
XY stage tilt w/ different Δx/Δy
Wire position error
pickup position error
calibration data repeatability
Calibration accuracy ≤0.05 mm

## Slide 4: BPM calibration system 2/3
The measured beam/wire position could be expressed as
where and are the measured beam/wire positions, and characterize the position sensitivities, and electrode rotation errors, and real beam/wire positions, and the electrical center offsets. and are given by
and and are half-aperture, and are the lengths of the extensions of L/R and U/D electrodes, as

## Slide 5: BPM calibration system 3/3
Calibration results
  Pickup electrode rotation + Electrical center offset + Gain error
  Comments: correction coef. from the mapping data should includes all these errors !?
* K. Hanamura et al., PASJ meeting (2006)
** T. Miura et al., PASJ meeting (2006)
*** Y. Hashimoto et al., PASJ meeting (2007)
1. Both correction coef. and electrical center are correlated to the freq.
2. Measured wire position varies versus BPM tempurature~0.15 mm/ °C (d130 mm BPM)
 How about the CSNS BPM??
Comments:
Electrical center offsets seems reasonable, <0.3 mm (rms.) !! The differences between pickups is ~0.1 mm  calibration every pickup to approach the goal ±0.1 mm accuracy requirement

## Slide 6: Lessons learnt at J-Parc MR
cable order
trigger timing
poor contact
beam duct step error
Taper
Small aper.
Large aper.
Large aper.
Small aper.
Result large offsets and gain errors!
Resolution measurement@4x1011 ppp, 3 GeV
shot by shot resolution (TbT): ~350 μm (hor., synchrotron oscillation) and ~100 μm (ver.)
Averaged position resolution (1000 shots, COD): ≤30 μm
=> position accuracy is still to be quantified
* T. Toyama et al., PASJ2009