## Slide 1
Recent progress on CEPC Accelerator studies
段哲
On behalf of the CEPC Accelerator Study Group
30 Oct - 02 Nov, 2025, CLHC 2025, email: zhe.duan@ihep.ac.cn
Circular Electron Positron Collider
Courtesy of Jie Gao, Dou Wang, Yuan Zhang, Dazhang Li, Yingshun Zhu for their help in preparing the slides.
Institute of High Energy Physics, CAS
See Jie Gao’s plenary talk “Overview of the CEPC Project” at 10:30 Nov 2nd (Sunday)

## Slide 2: A brief introduction of CEPC
Circular Electron-Positron Collider (CEPC) as a Higgs (Z / W / ) factory in China
  Higgs Factory (>1M Higgs, ~1% precision)
  Z Factory (~Tera Z)
  The W+W- pair and then pair production thresholds
  Higgs, EW, flavor physics & QCD, probe to new physics up to 10 TeV
Possible pp collider (SppC) of ~ 125 TeV (TDR spec.) in the far future.
CEPC Operation Plan and Goals
Anticipated accuracy on Higgs properties at CEPC versus at LHC/HL-LHC
Covered energy scales of NP

## Slide 3: Accelerator Considerations in TDR
3
Baseline: 100 km, 30 MW; Upgradable to 50 MW, High Lumi Z, ttbar
S+C-band 30 GeV linac
Accelerator Complex
H/tt-bar
W and Z
Seamless mode switch for Higgs/Z/W/(ttbar)
CEPC Collider Ring
Machine Detector Interface
Common tunnel for booster/collider & SppC
Circular collider: Higher luminosity than a linear collider
100km circumference: Optimal total cost
Shared tunnel: Compatible design for CEPC and SppC
Seamless switchable operation: Higgs/W/Z/(ttbar)
Accelerator complex comprised of a 30 GeV Linac, a 100 km booster and a double-ring e+/e- collider with two IPs
High energy & high flux synchrotron light source provides γ-ray up to 300 MeV, critical for multi-disciplinary sciences

## Slide 4: Hardware R&D progress in the TDR
4
Specification Met
Prototype Manufactured
  Key technology R&D spans all component lists in CEPC TDR
representative Key Technologies for the CEPC
Fraction

## Slide 5: Key technologies demonstrated in BEPCII
BEPCII has achieved a peak luminosity > 1.01033cm-2s-1 & stable operation of ~1A beam current in 2023, mastering key technologies of high intensity, high luminosity e+e- collider
BEPCII has been upgraded in 2024-2025, to achieve 3X increase of luminosity at 2.35 GeV, and energy reach up to 2.8 GeV
  Home-developed superconducting final focus quadrupoles in routine operation
BEPC Il luminosity design goal attained routinely in 2023
1.01033cm-2s-1
Home-developed Superducting quadrupole with serpentine coils

## Slide 6: Successful commissioning of High Energy Photon Source
Passed the performance acceptance organized by CAS yesterday, with high peer appraisal https://mp.weixin.qq.com/template/article/1761783531/index.html
Relevance to CEPC
  Demonstration of many shared key technologies
  A team trained with rich experiences in design, construction and commissioning of state of the art accelerator facility

## Slide 7: CEPC Accelerator EDR
Accelerator physics study
  Design
    Refinery of accelerator design & key parameters with engineering considerations
    Beam loss mechanism and management
    MDI
  Research
    Simulation code development: APES
    Combined influence of various effects: beam-beam, impedance, SR, ion effects, space-charge, nonlinearity, polarization
    Beam commissioning and luminosity tuning procedures
  Collaborative studies on SuperKEKB
    injection, beam-beam, instability etc
Key technology R&D
  More prototypes
    SRF
    Klystron
  More detailed design and planning
    MDI
    Control and Timing
    Alignment and Installation Plan
    Tunnel Mockup for installation
  Mass production preparation
    Magnets’ Automatic Production Lines
    Massive Production Line of NEG Coating Vacuum Chamber
  Experimental studies for advanced accelerator physics topics
    Plasma wakefield accelerator test facility @ BEPCII
    Polarized beam

## Slide 8: Accelerator Physics Emulation Studio （APES）
To meet the requirements of beam dynamics study in CEPC
Flexible modeling of complicated accelerators
Self-consistent simulation of combined effects
Application of new IT technology: GPU acceleration etc
8
More accurate, powerful and faster
Machine Modeling
Single Particle Dynamics
Optics function
Analysis of Nonlinear Dynamics
Combined Effects
Analysis
of Collective Instability
Online Commission
Detector Background
Modeling of SuperKEKB
Simulation of Swap-out injection (Higgs)
- with element-by-element tracking and beam-beam
Spin
Weibin Liu et al., IPAC24.
Yuan Zhang, CEPC workshop, Jun.16-19 2025,Barcelona.
Zhiyuan Li etal., NIMA 1064 (2024) 169386

## Slide 9: CEPC Booster automatic production line
Thanks for your attention
~15000 dipole magnets in the CEPC booster
4 booster magnets fabricated per day
3 production lines with 5 years
Status： construction started, the first workstation to be completed in 2025

## Slide 10: CEPC vacuum chamber NEG coating automiatc production line
Thanks for your attention
Cleaning
Spraying heating film
Assembling for NEG coating
NEG coating
Layout of production line
Status：construction started, commissioning scheduled in 2026
兼顾NEG镀膜和喷涂
5年完成真空盒制造
total length of vacuum chamber ~ 190km in CEPC collider rings

## Slide 11: CEPC 650MHz full-size cryomodule prototype
The collider Higgs mode for 30 MW SR power per beam will use 32 units of 11 m-long cryomodules each contain six 650 MHz 2-cell cavities, a full size 650 MHz cryomodule will be developed in EDR
CEPC collider ring 650MHz 2*cell short test module has been completed in TDR phase
mid-temp backing high Q, high gradient
低温、机械设计考虑CEPC自身要求

## Slide 12: CEPC high efficiency klystron
Klystron R&D
C band 5720MHz 80MW Klystron
CEPC collider ring 650MHz klystron development in TDR/EDR phase
Parameters | Value
Frequency | 5720 MHz
Output Power | 80MW
Pulsed width | 2.5us
Repetition rate | 100Hz
Gain | 54 dB
Efficiency | 47%
bandwith | ±5MHz
Beam voltage | 420 kV
Beam current | 403 A
Focusing field | 0.28 T
Parameters | Value
Frequency | 5720 MHz
Output Power | 80MW
Pulsed width | 2.5us
Repetition rate | 100Hz
Gain | 54 dB
Efficiency | 47%
 | ±5MHz
Beam voltage | 420 kV
Beam current | 403 A
Focusing field | 0.28 T
C band 5720MHz 80MW
Klystron design completed
Technical assessment has been done
on August 12, 2024, construction
started , high-power test starts soon
78.5%@803kW CW in 2024
in Fabrication.
1拖4

## Slide 13: CEPC 650MHz energy recovery klystron R&D
Parameter | Value
Operating frequency | 650 MHz
Beam Voltage | 113 kV
Efficiency | 77.5%
Output power | 800 kW
Beam perveance | 0.25 μP
Beam current | 9.5A
Efficiency (one-stage depressed collector) | 85%
4200mm
The 4th Klystron (Energy recovery, one stage) ：machining will start soon

## Slide 14: CEPC C-band microwave beam test platform
CEPC EDR will establish the C-band test bench and test the components. With pulsed compressor, waveguides, directional couplers, loads, bend and straight waveguides, etc. as a basic unit of CEPC C-band linac
The C-band test bench is equipped with a CEPC 5720MHz 80MW power source
The CEPC C-band test bench will be completed in 2026
BJ48
Waveguide taper
Match section
Regular section
End cavity
C band 5720MHz 80MW Klystron design completed, and fabrication will be completed in 2025
The deformation caused by temperature variation
Cavity shape
CEPC C-band linac test platform will be completed in 2026

## Slide 15: CEPC tunnel model and installation verification
Demonstrate alignment and installation procedure, highlighting the installation of the booster on the roof
A 60 m long tunnel mockup, including parts of arc section and part of RF section
Booster magnets installation
Collider ring magnets supports
Plan：to be completed in 2026

## Slide 16: Green technology and sustainability study
HEPS experiences
  solar panel of 10 MW -> 10% saving
  permanent dipole magnet: 5.6M kWh saving/yr
  Cooling water for heating 13 MW@42oC
CEPC approach
  High Q SRF: 60M kWh saving/yr
  High E klystron (80%): 160M kWh saving/yr
  shared coils in dual aperture magnets
  liquid helium recovery system
  permanent magnets in damping ring/transfer lines
CEPC carbon footprint study
  lowest carbon emission/Higgs
Publication: Dou Wang; Jie Gao; Yuhui Li; Jinshu Huang; Song Jin; Manqi Ruan; Mingshui Chen; Shanzhen Chen,
"The carbon footprint and CO2 reduction optimization of CEPC“, RDMT, https://doi.org/10.1007/s41605-025-00535-7 (2025).

## Slide 17: Plasma-based Acceleration: >103 increase in Eacc
RF cavity：< 100MeV/m
Drive Beam:
laser pulse
e- bunch
proton beam
…………
Table-top X/γ sources
High Energy colliders
HEDP platforms
Plasma：1-100 GeV/m
SACLA, 750 m, 8 GeV
SACLA, 750 m, 8 GeV
LBNL, 20 cm, 7.8 GeV
High power laser facilities (2020)
SLAC
ANL
BNL
CERN
LNF
DESY
THU/IHEP
THU/SINAP

## Slide 18: CEPC Plasma injector study
Replace the 100km booster by a PWFA accelerator, promising significant cost reduction
  Key issues identified for experimental justification

## Slide 19: PWFA test facility @BEPCII

## Slide 20: Timeline and progress

## Slide 21: Beam polarization study
Motivation
  Precision beam energy calibration @ Z, W (~100keV), w/ resonant depolarization
  Longitudinal polarization at Z-pole and beyond, for weaking mixing angle measurement, CPV etc.
Design
  Polarized beam injector
  ~70% longitudinal polarization at Z-pole
  Potential to attain polarization at Higgs
W. Xia et al., Investigation of spin rotators in CEPC at the Z-pole,
Radiat. Det. Tech. Meth. 6:490 (2022).
T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).

## Slide 22: Polarization R&D in the EDR phase
CEPC requirements, R&D items,
and required experiment demonstration
R&D, beam tests, and foreseen experimental demonstration at IHEP accelerator facilities
These activities will set the basis for polarized beam applications @ CEPC.

## Slide 23: Compton polarimeter @ BEPCII
CEPC vertex detector prototype
Laser optics & detector layout
Attempt first beam polarization measurement before end of 2025
Resonant Depolarization experiment in 2026

## Slide 24: Other polarization R&D
Polarized electron source
  First superlattice GaAs cathode under test @ JGU Mainz
  Beam test of the polarized e- beamline in 2027
Superconducting solenoid spin rotator under design.
E- longitudinal polarization @ BEPCII under study.
Polarized e- source beamline
YBCO superconducting solenoid
e- longitudinal polarization scheme for BEPCII

## Slide 25: Other CEPC Accelerator EDR Activities

## Slide 26: Summary
CEPC accelerators are in the phase of Engineering Design Report
Some R&D highlights are reviewed
Experiences of BEPCII & HEPS set steady basis for the success of CEPC
Thank you for your attention!