## Slide 1: Status of RPC Muon trigger detector for ATLAS Phase-II upgrade
Yongjie Sun
On behalf of the ATLAS China Muon team
University of Science and Technology of China
CLHCP 2025, Nov. 1st, Xinxiang

## Slide 2: Upgrade of the ATLAS detector
Phase-II upgrade
Thin-gap RPC (barrel muon trigger, very crucial for physics) ,
sMDT, electronics
Phase-II upgrade
Silicon Inner Tracking system
Phase-II upgrade
High Granularity Timing Detector HGTD
Phase-I upgrade
New Small Wheel (NSW)
Phase-II upgrade
Trigger and Data Acquisition - TDAQ
Main goals:
Higher radiation hardness/rate capability
Higher spatial/time resolution
Faster response time
Higher data acquisition rate

## Slide 3: Muon RPC upgrade for Phase-II
Limitations of current RPC system
  Rate capability: ~ 100 Hz/cm2
  Lifetime: 10 years @ LHC  lower efficiency
  The acceptance holes due to support structures
Phase-II upgrade for HL-LHC
  Three layers of RPC in BI region
  Thin-gap design with higher rate capability and longevity
  Fix most of the acceptance holes
  Increase redundancy and flexibility
678 singlets，1054m2 effective area
~70,000 electronics channels
触发效率：70%  90%
BOMBOR

## Slide 4: The contribution from China
~50% of the detector components and related assembly and QA/QC
Cover full chain of RPC production
  288 BIS singlets and readout panel
  120 BOMBOR singlets and readout panel
  72 RPC gas gaps
  5000 FE boards
  LV and HV power supply
Readout panel
Gas gap
FE board
singlet

## Slide 5: Technical scheme of thin-gap RPC detector
Readout panel
Bakelite electrode
Gas gap
Copper strip/GND
Low εr filler
Bakelite: 2 mm1.5 mm
Gap size: 2 mm1 mm
Specifications：
  Rate：>1 kHz/cm2
  Longevity：>10y@HL-LHC
  Spatial resolution：<1 cm
  Time resolution：~ 0.5 ns
Thinner bakelite:
  Less voltage drop in bakelite  improve the rate capability, larger induced signals
Thinner gas gap:
  Less charge produced per event  improve rate capability and longevity
New generation FE electronic:
  Higher amplification factor and high S/N ratio to compensate the lost gas amplification.
Honeycomb readout panel
  Better mechanics flatness and hardness  better signal transmission and spatial resolution.
Notes: 高能物理实验中的首次大面积应用

## Slide 6: Gas gap production
Automatic distribution gantry
  Spacer positioning, glue drop/line distribution
Precision machining of spacers, bars
  Customized process and tooling for strict uniformity and tolerance
Gas tight, linseed oiling, graphite painting, thermal laminating
6 gaps under aging test at GIF++
Full production chain established in China
Spacers placed
HV electrode

## Slide 7: Profit the mass production in Italy company
The early production of ~160 gas gaps suffered gas leak problem
Weak point addressed based on the experience in our prototype production
Problem solved with mechanical modifications
  Gas leak problem
3.1mm
0.7mm
1.4mm
4.5mm
PET
Policarbonate
1.0mm
Hole
2.0 mm
Slot
Hole + slot with steps

## Slide 8: Profit the mass production in Italy company
More than half of ~290 gas gaps (till Sep. 2025) were tested with drifting current
Many measures taken to improve the quality.
  Pre-wash before oiling, extend drying time, Ar training, improve gluing quality … Most based on our experience
The recent batch has a yield of 15/16
  The drift current problem
Chart: USTC gas gaps
| 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 4500 | 5000 | 5500 | 5800 | 6000
gas gap 2 before | 0 | 4.3 | 8 | 12.1 | 17.3 | 21.2 | 25.6 | 31.8 | 39.4 | 49 | 64.2 | 88.5 | 101.5 | 132
gas gap 2 after | -2.3 | -1.8 | 0 | 4.1 | 7.8 | 10.4 | 13.6 | 18.4 | 23.2 | 30.2 | 43.4 | 54.1 | 69
gas gap 3 before | 0 | 3.1 | 6 | 8.8 | 12.3 | 15.2 | 18.3 | 22.2 | 26.7 | 32 | 42.8 | 55.4 | 66.1 | 84
gas gap 3 after | -1.8 | -0.3 | 2.6 | 5.3 | 7.9 | 10 | 12.4 | 15.1 | 18.8 | 22 | 26 | 34.7 | 41.8
Chart: Italy gas gap
| 1000 | 2000 | 3000 | 4000 | 4500 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800
11 | 0 | 0.0008 | 0.0052 | 0.0334 | 0.0288 | 0.0752 | 0.0872 | 0.1298 | 0.151 | 0.1896 | 0.2606
12 | 0.0456 | 0.109 | 0.1688 | 0.2854 | 0.4808 | 0.781 | 1.185 | 1.7198 | 2.6038 | 3.561 | 4.8136
13 | 0.0956 | 0.1642 | 0.2294 | 0.3458 | 0.5314 | 0.7486 | 0.9576 | 1.2722 | 1.5566 | 2.0554 | 2.6318
14 | 0.048 | 0.0724 | 0.1292 | 0.2108 | 0.28 | 0.4252 | 0.5782 | 0.9642 | 1.4536 | 1.9118 | 2.3842
15 | 0 | 0.0134 | 0.051 | 0.1268 | 0.2666 | 0.4196 | 0.6222 | 0.8832 | 1.1582 | 1.4862 | 1.9508
16 | 0.006 | 0.03 | 0.0416 | 0.0526 | 0.0618 | 0.0898 | 0.107 | 0.138 | 0.1446 | 0.1546 | 0.2038
17 | 0.019 | 0.059 | 0.0854 | 0.1338 | 0.1748 | 0.2508 | 0.4226 | 0.5522 | 0.7294 | 1.0404 | 1.5612

## Slide 9: Readout panel production
The sole manufactory for large size PCB
The vacuum bag method for honeycomb panel production
The automatic scan system for panel qualification
All 576 BIS panels qualified
1.1m
1.7m
Large size PCB
Vacuum bag pressing
Automatic thickness scan
  All BIS panels produced and qualified

## Slide 10: The singlet assembly at CERN
Participate the joint singlet assembly training at CERN
21 BIS singlet assembled in July 2025
QA/QC procedures applied and qualified
Gas-tight refurbish
Singlet finishing
HV test
Dimensions and thickness checks
Triplet prototyping
  Assembly and QA/QC procedures established

## Slide 11: BIS singlet production line in MPI
USTC on the US. “entities list”, singlet assembly can not carry out in USTC
Multiple solutions discussed together with upgrade management.
Warmly welcome from MPI with strong support promised
After on-site discussion in April, the cooperation decided
  MPI takes care of all the necessary facilities, tools, gas, HV system
  China team sets up the production line together with a cosmic ray test station

## Slide 12: FPGA-based TDC system
288 channels capacity sufficient for one test station
100 ps time resolution on leading and trailing edge
Flexible trigger mode：external/self/master-slave
Broad potential application field
  A crucial solution for performance test in mass production

## Slide 13: The delays and solutions
Delay of the gas gap production in GTE
  The gas leak problem
  Solved by mechanical optimization
  Produced leak gap: all refurbished
  Drifting current problem
  Improved by multiple optimization in production
  Produced drifting gaps: re-oiling, Ar-training, etc. on going
Delay of the electronics system
  Supports from other institutions injected
  Several pre-productions in China
  The situation improved a lot to catch up with the plan

## Slide 14: The plan
RPC gas gap production: preparing the material
BIS singlet assembly：
  2025.11-2025.12：setting up the production line in MPI
  2026.1-2026.6：BIS singlet assembly in MPI
BIS singlet qualification：
  2025.11-2025.12：setting up the cosmic test station in MPI
  2026.1-2026.12：BIS singlet qualification test
Join the installation and commissioning

## Slide 15: Summary
Huge efforts towards the mass production in 2025, especially with main issues addressed and solved.
The main progresses
  RPC gas gap prototypes produced with all manufacture procedures
  Finished the BIS readout panel production and qualification
  Established the singlet assembly and qualification procedures
  Developed the read out system for performance test station
Close cooperation with all the sub-tasks and institutions, making the project progress smoothly and successfully.
Thanks!

## Slide 16: backup
backup