## Slide 1: Comparison of CGEM Data Integration Schemes
Tingxuan Zeng 2025/06/30
IHEP DAQ Group

## Slide 2: Background
CGEM data is currently stored separately and merged offline.
With improved system stability and higher analysis demands, more efficient integration methods are needed.
This report compares three options and offers recommendations.

## Slide 3: Option 1: DAQ Readout Module Receives CGEM Data in Real Time from GUFI
✅ Pros：
  Data integration is completed at the readout stage
  Simplifies backend processing and enables unified handling
  GUFI handles the hardware configuration, save commissioning time
⚠️ Cons：
  Needs GUFI developers to add a real-time data sending module

## Slide 4: Option 2: DAQ Reads Files Stored by GUFI
✅ Pros：
  Same as Option 1
⚠️ Cons：
  Synchronization between concurrent file read and write operations must be ensured.

## Slide 5: Option 3: DAQ Reads Data from VME-DC Board
✅ Pros：
  A VME-based readout program has already been developed.
  Easy to maintain, with good real-time performance
⚠️ Cons：
  The debugging efficiency of the DC board is low, and interrupt issues still need to be resolved.
  The hardware configuration program needs to be re-integrated and commissioned.

## Slide 6: Option 4: DAQ Reads Data from GEMROCs
✅ Pros：
  Easy to maintain, with good real-time performance
⚠️Cons：
  The hardware configuration program needs to be re-integrated and commissioned.
  An UDP data acquisition program requires to developed and commissioned together with the hardware team.

## Slide 7: Options Comparison Table
Options | 1（read from GUFI） | 2（Read from file） | 3（read from VME-DC） | 4（read from GEMROCs）
Development Effort | ✅moderate | ✅ moderate | ⚠️significant | ⚠️significant
Real-time Performance | ✅ good | ⚠️ has Latency | ✅ good | ✅ good
Maintainability | ✅ good | ✅ good | ✅ good | ✅ good