## Slide 1: CEPC control system EDR design and development status
Dapeng Jin
Institute of High Energy Physics, CAS, Beijing
18 July, 2025
环形正负电子对撞机
Circular Electron Positron Collider

## Slide 2: Outline
Part of the main tasks & development
Next to do
Summary

## Slide 3
Part of the main tasks & development

## Slide 4: Fiber routing & radiation experiment
Fiber routing in tunnel with IP3 as the center.
Radiation hardness & cost.
~3000km 48-core opt. fiber needed.
Overall
IP3

## Slide 5: Fiber routing & radiation experiment
Rad. Exp.
Total dose:
354Gy@HCF，268Gy@RRF，195Gy@G652
1550nm
Joint fiber radiation experiment among YOFC, CSNS & IHEP.
Neutron radiation experiment done at ANIS of CSNS.
Ge doped fiber is very radiation sensitive.
Even F doped fiber is not suitable for accelerator.
HCF is much better with a price ~50RMB/core/m at present.
Further experiment planned.

## Slide 6: System monitoring & DAQ
AI related issues
AI is essential for the large & complex facility.
High perform. computing
High speed DAQ
High quality data
High perform. actuator
High bandwidth
Open loop applications
Closed loop applications
High Performance applications
Digital twin
Slow control & monitoring
…
Other applications

## Slide 7: System monitoring & DAQ
Joint design
Joint design of control, DAQ/AI-related applications and network.
Network traffic localized as much as possible.
Distributed data acquisition, storage & services.
Services with only local data deployed on distribution servers.
Services with multi-region data deployed on central servers .
Physical separation of control & DAQ network.

## Slide 8: System monitoring & DAQ
Logic structure of DAQ
Preliminary logic structure of data acquisition, storage, distribution & analysis

## Slide 9: System monitoring & DAQ
Dataflow & tools
Dataflow & tools of data acquisition, storage, distribution & analysis
Data format & tools, HDF5?
Design & development of Kafka servers.
Note: Referenced to documents of Sinong Cheng, from APS-U and Apache Software Foundation.
Fault tolerance & recovery.

## Slide 10: System monitoring & DAQ
Component & cable database
Indirect connection of devices through cable
Direct connection of devices : housing

## Slide 11: System monitoring & DAQ
Component & cable database
Data from users
用户数据
Dictionary data managed by administrator
管理员管理的字典数据

## Slide 12: Timing system & reference line
Motivation: To achieve high-precision global clock transmission, and timing synchronization
  Within a 100 km range through wireless transmission
  Reducing the need of radiation-hard optical fibers
  Providing a backup technical solution.
Research
  Long-distance free space optical wireless transmission system
  Data transmission and clock synchronization technology
  Large scale, multi-cascaded clock synchronization technology
Structure of cascaded clock synchronization system
Main node
Timing system with wireless transmission
Schematic of long-distance FSO transmission

## Slide 13: Timing system & reference line
Timing system with wireless transmission
Progress
  Long-distance Free Space Optical wireless transmission system.
    A 1 km distance laser wireless transmission system has been designed and tested.
    Data transmission and clock synchronization tests have been conducted with a bit error rate of less than 1E-13 and a synchronization accuracy of 20 ps (without optimizition).
  Point-to-point data transmission and clock synchronization technology
    A new high-precision clock synchronization hardware node has been designed and tested.
    With fiber, the TIE jitter of receive clock is 2.28 ps, the clock synchronization accuracy is 3.33 ps.
  Large scale, multi-cascaded clock synchronization technology
    A machine learning-based approach is proposed to gather multi-node information and dynamically adjust the phase of all nodes to alleviate long-term clock drift caused by cascading.
    A small system with 7 nodes is scheduled, aiming for a timing accuracy of better than 10 ps across all nodes.

## Slide 14: Timing system & reference line
Timing system with wireless transmission
High-precision clock synchronization hardware node
Test setup of 1 km FSO Equipment in HEPS
TIE jitter of receive clock
RMS=2.28ps
RMS=3.33ps
Clock synchronization

## Slide 15: Next to do
Further radiation experiment of optical fibers focusing on HCF.
DAQ design and implementation, applied first in BEPCII.
Further development of component-cable database and application in BEPCII & PWFA.
Long-distance & long time test of reference line.
Larger system integration & test of wireless transmission based timing system.
Further design of fast orbit feedback system & fast protection system.
Further design of network.

## Slide 16: Summary
Key issues of control system go forward steadily.
Much work will be done with manpower limited.
Thanks for your attention!