## Slide 1: Time-stamping photons with sub-nanosecond resolution for quantum imaging and telescopy
Andrei Nomerotski
Florida International U & Czech Technical U
7.7.2025 IHEP Beijing seminar

## Slide 2: Types of fast Imaging
“normal” cameras: 0.1 ms  10 ms
Burst mode cameras: 1 ms  10 ns
Data-driven cameras: 10  0.01 nsec
Streak cameras: 1 psec
Repetitive “pump/probe cameras” : fsec
10-4 sec
10-9 sec
10-14 sec
10-6 sec
10-12 sec

## Slide 3: Modern CMOS Imagers
Ever increasing complexity and data rate
One example (ix-cameras.com)
  2048x1536: 8 kfps  26 Gpix/sec
BUT: Not fast enough! 100000 nsec  1 nsec

## Slide 4: Imaging with photon counting
Low occupancy
Integrated image
Photons appear as standalone objects  data driven readout
Has parallels with x-ray imaging and particle detection

## Slide 5: Timepix Optical Cameras

## Slide 6: Hybrid pixel detectors
Lukas Tlustos and Erik H. M. Heijne, Performance and limitations of high granularity single photon processing X-ray imaging detectors, in CERN proceedings (2005)
Decouple readout chip and sensor
  optimize technologies for chip and sensor separately
Use different sensors with same readout, versatile approach for x-rays (Si, CZT)
 we will use OPTICAL sensors
credit: IZM
Have roots in R&D for LEP/LHC vertex detectors

## Slide 7: Photon absorption in silicon
Blue photons are absorbed near the surface (~0.25 um for 430 nm, P47 max emission)
Longer wavelengths penetrate deeper (~1 um for 500 nm, ~10 um for 800 nm)
d, m
l, nm

## Slide 8: Thin window optical sensors
Developed at BNL, first produced at CNM (Barcelona) in 2015
Surface preparation is very important, inspired by astronomical CCDs (LSST)
High QE
Nomerotski et al, Characterization of TimepixCam, a fast imager for the time- stamping of optical photons,
Journal of Instrumentation 12 (01) (2017) C01017.
M. Fisher-Levine, A. Nomerotski, Timepixcam: a fast optical imager with time-stamping,
Journal of Instrumentation 11 (03) (2016) C03016.
Backside illuminated optical sensors
Anti-reflective coating, thickness 300 um

## Slide 9: TimepixCam

## Slide 10: Timepix3 Camera  Tpx3Cam
Camera = sensor + ASIC + readout
Timepix3 ASIC:
256 x 256 array, 55 x 55 micron pixel
  14 mm x 14 mm active area
1.56 ns timing resolution
Data-driven readout, 600 e min threshold, 80 Mpix/sec, no deadtime
each pixel measures time and flux, ~1ms pixel deadtime when hit
Sensor is bump-bonded to chip
Use existing x-ray readouts:
SPIDR (Nikhef & ASI)
www.amscins.com
Zhao et al, Coincidence velocity map imaging using Tpx3Cam, a time stamping optical camera with 1.5 ns timing resolution,
Review of Scientific Instruments 88 (11) (2017) 113104.
T. Poikela et al, Timepix3: a 65k channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout,
Journal of Instrumentation 9 (05) (2014) C05013.

## Slide 11: Advantages of optical approach
Outside of vacuum
  Decoupled from setup
  No cooling in vacuum
  No HV close to electronics
Power of optics
  lens & mirrors
  magnification/ demagnification, flexible mapping between scintillator screen and sensor
“Hybrid” approach
  Use same camera for different applications
  Easily upgradable: different cameras with same setup
  Use different photocathodes/ intensifiers with same camera

## Slide 12
TPX3Cam @ ASI
SPIDR readout for Timepix3 (Nikhef, ASI)
Use existing readouts of x-ray detectors:
J. Visser et al, SPIDR: a readout system for Medipix3 and Timepix3, Journal of Instrumentation 10 (12) (2015) C12028.

## Slide 13: Applications & Results

## Slide 14: Ion Imaging
Google Scholar 134 citations

## Slide 15
Ions in TimepixCam

## Slide 16
FLASH data, paper submitted to Journal of Synchrotron Radiation

## Slide 17: TimepixCam
First results were presented at IWORID in June 2015, paper published in 2016

## Slide 18: ToT vs ToF: timewalk

## Slide 19: Single (optical) photons

## Slide 20: Correction of time walk
before TOT correction
after TOT correction

## Slide 21: Intensified camera: use off-the-shelf image intensifier
Image intensifier (Photonis PP0360EG)
Cricket@
Intensifier
Intensified cameras are common:
  iCCD
  iCMOS cameras

## Slide 22: Photocathodes
GaAs
Photonis photocathodes
Can choose any wavelength!

## Slide 23: Single Photons in Tpx3Cam
Tpx3Cam + intensifier by Photonis
data taken by J. Long (ASI)
1 ms slice of data
1.5ns time-stamping
TOA
TOT
TOT

## Slide 24
TOA
TOT
Each photon is a cluster of pixels
3D (x,y,t) centoiding
Spatial resolution: 0.1 pixel / photon
Time resolution: < 1 ns / photon

## Slide 25: Imaging capable of 1 Mhits/s and 30ps timing
32 ps timing resolution from MCP+digitizer
  0.7 ns deadtime
Imaging of electrons with 1Mhit/sec rate: Tpx3Cam
  Improved from few kHz rate
D.Debrah , G.Stewart, G.Basnayake, A.Nomerotski , P.Svihra , S.K.Lee, and Wen Li Developing a camera-based 3D momentum imaging system capable of 1 Mhits/s Rev. Sci. Instrum. 91, 023316 (2020)
Electron spectroscopy at WSU

## Slide 26: Other applications
HEP: TPC optical readout
Neutron imaging
X-ray imaging
Lifetime imaging

## Slide 27: Optical readout for LAr TPC
Image light from avalanches in gas phase
hep.ph.liv.ac.uk/ariadne/index.html
Kostas Mavrokoridis, Adam Roberts et al
Tpx3Cam can measure drift time
 converts 2D to 3D

## Slide 28
5.5 MeV alphas in CF4 gas
Using Tpx3Cam in Oct 2018
Color = TOA
Color = TOT
First demonstration of 3D optical readout of a TPC using a single photon sensitive Timepix3 based camera, A Roberts, P Svihra,
A Al-Refaie, H Graafsma, J Küpper, K Majumdar, A.Nomerotski ….
Journal of Instrumentation 14 (06), P06001

## Slide 29
TPX3Cam on ARIADNE 1-ton dual phase Liquid argon TPC
LAr Cosmic Muons (10msec slice)
A. Roberts et al., 2019 First demonstration of 3D optical readout of a TPC using a single photon sensitive Timepix3 based camera JINST 14 P06001
D. Hollywood et al, 2020 ARIADNE—A novel optical LArTPC: technical design report and initial characterisation using a secondary beam from the CERN PS and cosmic muons JINST 15 P03003
Image light from avalanches in gas phase in THGEM
hep.ph.liv.ac.uk/ariadne/index.html
Kostas Mavrokoridis et al

## Slide 30: More ideas
Scintillator flashes are imaged by intensified Tpx3Cam
Alphas, hard x–rays, neutrons, …
Thin fast scintillator
Difficulty: light collection efficiency (but it’s single photon sensitive)
Advantage: outside of the beam, around the corner (with mirrors)

## Slide 31: Optical detection of x-rays
25 keV x-rays converted to light in thin LYSO, ASP (Argonne NL), tested in 2019
image of foam target
Time-resolved beam structure
beam
Intensified Tpx3Cam
Jeph Wang (LANL)
Advantage: efficiency to high energy (> 20 keV) x-ray where silicon is inefficient
Difficulty: high rates, MCP saturation and slow recovery

## Slide 32: Alphas in LYSO in Tpx3Cam
Am241 5.5 MeV alphas
LYSO 0.5 mm thickness
Alpha hits in Tpx3Cam
Occupancy map
TOT
TOA
TOA, ns
LYSO decay 40ns
Single alpha hit
G. D'Amen et al JINST 16 P02006, Feb 2021

## Slide 33: Neutron detection with Tpx3Cam
6Li-based scintillator
Neutrons produce alphas
Time resolved
Material characterization with Bragg edges
J.Yang et al, A novel energy resolved neutron imaging detector based on a time stamping optical camera for the CSNS, NIM A, volume 1000, 165222, Apr 2021
Losko, A. S. et al. New perspectives for neutron imaging through advanced event-mode data acquisition. Sci. Reports 11, 21360, Nov 2021
Tpx3Cam neutron event display

## Slide 34: Lifetime imaging with oxygen sensors
Sensor lifetime depends on oxygen concentration  in-vivo monitoring of oxygen in tissues
Biomedical Optics Express 11 (1), 77-88 (2020)

## Slide 35: telescopes

## Slide 36: Astronomy picture of the decade
2019 ApJL 875
Black hole in the center of M87 imaged at 1.3mm
Achieved by radio interferometry with ~10000 km baselines
sensitive to features
on angular scale
dime at Moon: 5 arcsec

## Slide 37: Classical interferometery

## Slide 38
Radio
Optical
Can literally record entire waveform, over some band, separately at each receiver station and interfere later offline
One photon at a time! Need to bring paths to common point in real time
Need path length compensated to better than c/bandwidth
Need path length stabilized to better than
Accuracy ~ 1 mas
Max baselines to ~ 100 m
mode population
mode population

## Slide 39: Two-photon techniques

## Slide 40
Measure photon quantum state at one station  teleport the sky photon to 2nd station
Correlation of counters are sensitive to sky photon phase  direction
Need to transfer the photon quantum state  can use quantum networks, this will allow long distances
Verified experimentally in quantum optics settings: M Brown et al, PRL 131, 210801 (2023)
Second photon for quantum assist

## Slide 41: Quantum Network
Attenuation in fibers  need quantum repeater to reproduce qubits
  Simple amplification will not conserve the quantum state
Qubit teleportation: produce entangled photons and send them to two locations
Bell State Measurement (BSM) on one photon will collapse the wave function of the other one (or swap entanglement, or teleport photon)
A.Zeilinger

## Slide 42: Hanbury Brown - Twiss effect
If points are close enough two options of photons paths are coherent = photon phases not so different and they interfere
Interference produces photon bunching or HBT effect
visibility = S/B = 46%

## Slide 43: Stellar Intensity Interferometry
renewed interest due to progress in fast detectors!

## Slide 44
New ideas extending original proposal
Extensions of Stellar Intensity Interferometry bridging to quantum-enhanced ideas
Perfect to start exploring this approach
arxiv.org/abs/2010.09100

## Slide 45: Possible impact on astrophysics and cosmology
offers orders of magnitude better astrometry with major impact
Parallax: improved distance ladder - sensitive to Dark Energy
Proper star motions - sensitive to Dark Matter
Microlensing, see shape changes
Black hole accretion disk imaging
Gravitational waves through coherent motions of stars - microHz range
Exoplanets etc
https://arxiv.org/abs/2010.09100

## Slide 46: Requirements for detectors
Fast imaging techniques are the key
  Promising technologies: SPADs, SNSPDs
  Target 1-100 ps resolution
Spectral binning: diffraction gratings, echelle spectrometers
High photon detection efficiency
Fast spectrometers at Heisenberg limit
Photons must be indistinguishable so close enough in frequency and time to interfere  temporal & spectral binning : need ~ 10 pm * 10 ps

## Slide 47: Benchtop Verification
SPAD and SNSPD readout
arxiv.org/abs/2301.07042 published in Optics Express

## Slide 48
HBT and HOM Cancellation
HBT and HOM Cancellation
arxiv.org/abs/2301.07042

## Slide 49: Phase dependence
Population of HBT peaks as function of phase = phase oscillations
arxiv.org/abs/2301.07042

## Slide 50: Next step: spectral binning

## Slide 51: Spectral binning
Two beams of thermal photons  diffraction grating
Based on intensified Tpx3Cam, ns time resolution
spectral resolution for Ar lines ~0.15 nm
Ar spectrum
A.Nomerotski et al. Intensified Tpx3Cam, a fast data-driven optical camera with nanosecond timing resolution for single photon detection in quantum applications, arxiv.org/abs/2210.13713, published in JINST

## Slide 52: Next step: faster spectrometer based on LinoSPAD2
Diffracted photon stripe projected on to linear array
Spectrometer time resolution: 5 ns 100 ps

## Slide 53: Possible technologies: SPAD
512 x 1 pixels
24 x 24 micron pixels
Max PDE (with microlenses) ~ 30%
50 ps resolution
Developed in EPFL (Switzerland)
AQUA group (E.Charbon)
SPAD = single photon avalanche device Semiconductor device: p-n junction with amplification
LinoSPAD2
C. Bruschini et al, Linospad2: a 512x1 linear spad camera, in Quantum Sensing and Nano Electronics and Photonics XIX, vol. 12430, pp. 126–135, SPIE, 2023.

## Slide 54: SPAD arrays with 50 ps resolution
time difference, s=57 ps
Two beams from SPDC source
Coincidence of two single photons
arxiv.org/abs/2304.11999

## Slide 55: SPAD arrays with 50 ps resolution
Two beams from Ar lamp + polarizer after
beamsplitter
HBT peak
Next step: HBT in spectral bins for broadband light
time difference, s=110 ps
visibility = 50%
arxiv.org/abs/2406.15323
arxiv.org/abs/2406.13959

## Slide 56
Spectrometer with LinoSPAD2
Used Ar lamp coupled to SM fiber
Ar spectral lines
arxiv.org/abs/2304.11999
spectral resolution 0.04 nm
Achieved 0.04 nm spectral and 40 ps timing resolution
only x10 more than
arxiv.org/abs/2304.11999

## Slide 57: Colored HBT peaks in LinoSPAD2
dual spectrometer in Prague
time difference, s=70 ps
visibility = 3.8%
HBT peak in two spectral bins
S.Kulkov, L.Rademacherova
unpublished, work in progress

## Slide 58: Colored HBT peaks in LinoSPAD2

## Slide 59: telescopes

## Slide 60: On-sky measurements
Need to couple to single mode fiber
Need adaptive optics
Both are difficult tasks

## Slide 61: Quantum Optics applications with time stamping of single photons
Some examples how nanosecond scale resolution is used in Quantum Optics

## Slide 62: Quantum photon sources - spontaneous parametric down-conversion (SPDC) sources
Produce two photons correlated (sometimes entangled) in
  Time
  Position
  Energy

## Slide 63: Multidimensional Quantum Illumination
In collaboration with NRC (Ottawa) D.England, Y.Zhang et al
Y Zhang, D England, A Nomerotski, P Svihra et al, Multidimensional quantum-enhanced target detection via spectrotemporal-correlation measurements, Physical Review A 101 (5), 053808
P Svihra et al, Multivariate Discrimination in Quantum Target Detection, Appl. Phys. Lett. 117, 044001 (2020)
Pump photon wavelength vs time difference
dl*dt ~ 5 ns * 0.5 nm

## Slide 64: Quantum light-field microscope
Ottawa NRC group
Use one photon for position and one photon for angle information
This allows refocussing at arbitrary distance

## Slide 65: 1- and 2-D ion crystals
RF 18 MHz
Paul trap
Ba ions
50-100 ns micromotion period

## Slide 66: Down-conversion of x-rays
first imaging of x-ray cone
record rate of pair detection ~ few Hz
arxiv.org/abs/2310.13078
NSLS-II @ BNL

## Slide 67: Detected simultaneously 3 types of correlations: time, spatial & energy
Motivation: x-ray detectors with good timing and energy resolutions
Scope: entanglement studies for x-rays
TOT correlation
poor resolution
18 ns resolution due to
variation of conversion depth

## Slide 68: Sensor R&D
Ideas for 2d imaging sensors which can provide 20 ps resolution

## Slide 69
X. Llopart
by Medipix4 collaboration

## Slide 70: First Tpx4 measurements
Optical sensor + Tpx4, no intensifier
Tested with 450 nm laser, pulse width 90 ps
Silicon sensor bias 60 V
272 ps
TOF vs TOT

## Slide 71: First Tpx4 measurements
Single photon sensitive (intensified) optical Tpx4 camera
hi-QE-blue Photonis intensifier
Tested with attenuated 450 nm laser, pulse width 90 ps
Silicon sensor bias 20 - 70 V
TOF vs TOT
resolution 827 ps @ 70 V

## Slide 72: Direct detection after MCP in Timepix
Has been implemented before with Timepix3
Limitation: photocathode QE ~ 35%
External amplification in MCP

## Slide 73: Hybrid SPADs: 20 ps timing
20 ps timing is needed for next round of CERN experiments in 10 years, there will be lots of investment in fast ASICs
example: Timespot1 chip
  32 x 32
  50 ps
  55 micron pitch
Hybrid detector: SPAD + 20 ps chip
ASIC
SPAD sensor

## Slide 74: Main points to take home
Quantum-assisted two-photon interferometry dramatically enhance astrometric precision with great impact on astro science
Requires single photon cameras with 10 ps scale resolution
Broad program in quantum-assisted optical interferometry ahead, efforts underway to develop new timing technologies
This will be useful in many fields including the quantum
Entangled x-rays motivate pixels with ns timing resolution and good energy resolution

## Slide 75
“The great advances in science usually result from new tools rather than from new doctrines”
Freeman Dyson (1923-2020)

## Slide 76: Acknowledgements
Eden Figueroa
Paul Stankus
Tom Tsang
Justine Haupt
Mael Flament
Guodong Cui
Sonali Gera
Dimitros Katramatos
Michael Keach
Steven Paci
Alex Parsells
Jonathan Schiff
Denis Dolzhenko
Stepan Vintskevich
Anze Slosar
Zhi Chen
Jesse Crawford
Aaron Mueninghoff
Jingming Long
Erik Hogenbirk
Martin van Beuzekom
Bram Bouwens
Erik Maddox
Jord Prangsma
Duncan England
Yingwen Zhang
Boris Blinov
Mila Zhukas
Maverick Millican
Alex Kato
Peter Svihra
Michal Marcisovsky
Sergei Kulkov
Jakub Jirsa
Raphael Abrahao
Brianna Farella
Ryan Mahon
Edoardo Charbon
Tommaso Milanese
Ermanno Bernasconi
Claudio Bruschini
interns