## Slide 1: ITK power cabling report
Yihan Zhang 2025.07.25

## Slide 2: CEPC ITK stave design
Stave support
Cooling plate
Sensors
12V to 1.2V DC-DC
48V to 12V DC-DC
Data aggregation chip
Each chip responsible to 14 sensors
Data link chip
Connect to 5-7 modules and optical fiber module.
There were 7 Data link chips in old design, now reduced to only one.
Optical module
The supported data rate per sensor is up to 693.33 Mbit/s, corresponding to a maximum hit rate of Hz/, which is ∼ 334 times larger than the estimated maximum.
The estimated hit rates for ITK barrel is Hz/. Each fired pixel generates 42 bits. For maximum estimated hit rate, each module generates 11.4Mbits/s.

## Slide 3: CEPC ITK stave design
Stave support
Cooling plate
Sensors
12V to 1.2V DC-DC
48V to 12V DC-DC
Data aggregation chip
Each chip responsible to 14 sensors
Data link chip
Connect to 5-7 modules and optical fiber module.
The primary low-voltage (LV) input is 48 V, which is delivered to the secondary data aggregation board via power cable .The DC-DC module in the secondary data aggregation board converts the voltage from 48V to 12V. The DC-DC module on each module convert the voltage from 12V to 1.2V
The total power comsumption is 100W.
Optical module