## Slide 1
Design of Muon Detector
Xiaolong Wang
Fudan University
July 29th, 2025

## Slide 2: The Muon Detector
Designed for Muon ID. Furthermore,
  Trigger signal,
  Pion veto,
  Search for LLPs,
  Detect the leakage of HCAL.

## Slide 3: Geometry and main parameters
Endcap
Barrel

## Slide 4: Detector channel (PSU)
PSU: Plastic Scintillator (PS) detector Unit
  A PS bar with cross section:
  A WLS fiber with diameter of or
    1.2mm for PSU < 3m, 2.0mm for PSU > 3m
  A SiPM with a sensitive area of
Thickness of reflection layer on PS bar
  TiO2: 0.07-0.1mm
  Teflon: 0.05mm
Coupling component:
  Hold the one terminal of fiber in a long PS bar
  Ensure a fixed alignment between SiPM and fiber
  Coupling between SiPM and fiber is critical for photon collection.
5m PSU at FDU

## Slide 5: Newest test on 5m PSU
Efficiency: >95%
Time resolution: ~1ns
We are testing on new WLS fiber.

## Slide 6: Electronic system
SiPM Tile:
SiPM+PCB of each PSU
FEB (uFB):
Front-End Electronics Board;
A module design integrating 32 readout channels.
MB (uMB):
Management Board;
Central node for multiple functions.

## Slide 7: Internal structure of barrel module
The largest module:
Two perpendicular layers of PSUs.
  Step 1: long PSUs at bottom layer, 3cm between PSUs and frame border for cables. Length of PSU: ~459 cm
  Step 2: mount FEBs for long PSUs at short frame border.
  Step 3: short PSUs at the top layers, 3cm between PSUs and frame border for cables. Length of PSU: ~343cm
  Step 4: mount FEBs for short PSUs at the long frame boarder.
  Step 5: arrange the cables from FEBs to an MB through the window at the long border.
FEB: thickness less than 2cm
  each connect to 32 PSUs and the position near their center.
  All FEBs are above the bottom layer, at a similar height of as the top layer. PS bars conflicting FEBs are reduced by 2cm in length further.
In one layer, the PS bars are close to each other. They are hold together by glue to form a robust module.
Thickness of module is 3.5 cm, which the thickness of PSU layers is 2.0cm. The spare 1.5cm for aluminum covers, mechanical enhancement, FEBs, and cables from FEBs to the cable window.
Near the middle of barrel
Near the endcap
Cable window

## Slide 8: Positions of SiPMs and FEBs
The SiPMs and FEBs are new the endcap or the barrel’s outer edge, minimizing the radiation damage.

## Slide 9: Cabling from module to MB in barrel
Commercial composite cable for connection between FEBs and MB.
All the cables for one module is combined to one bunch.
Each sector (1/12 of the barrel, one side) has one MB.

## Slide 10: Inner module in endcap
Similar procedure in arranging the PSUs and FEBs.
Bottom layer for horizontal PSUs, and top layer for vertical PSUs.
FEBS are mounted on the outer arc border.
FEBs for the two layers of PSUs may have the same position, especially at the middle of the arc border. In this case, shift their positions to avoid their confliction.
The area close to the beam pipe is fully covered by PS bars and WLS fibers, enhancing the detection coverage.
Rate capability (kHz/cm2) of PSU is well above the beam induced bkgs (<5 Hz/cm2).
SiPMs and FEBs are far away from the beam pipe, minimizing the radiation damage.
Cable window

## Slide 11: Outer module in endcap
Do it similarly for the outer module.
Inner module
Outer module
Cable window

## Slide 12: Cabling for endcaps
After rotating the inner and outer modules inside a detector, 5cm from the detector modules and the vertical surface of the iron structure should be assigned for cabling, i.e., a tunnel with a cross section inside the gap between iron plates.
MB at top
MB at bottom
This one is not necessary, very difficult for cabling.

## Slide 13: Regarding the simulation
The geometry in the simulation is according to the design, except the very small space between PSUs and module frame borders for cables.
However, there are questions in defining the MuID.
Our suggestion: number of layers with hits of a charged track.
In TDR chapter 9:
In TDR chapter for software?
In TDR chapter for performance?
The new software group of the Muon Group is trying to understand the MuID.

## Slide 14: Geometry simulation
In TDR for barrel module:
For endcap module:
Bottom layer
Bottom layer

## Slide 15
Thank you for your attention!
Oct. 21st, 2024, CEPC Detector Ref-TDR Review

## Slide 16
Detector module
  Superlayer with perpendicular channels
  Carriers for preamps held at the frame
  Space between PS bars and aluminum layer is allowed for long cables.
  All the electronics should be integrated into the module.
Module and electronics
superlayer
Micro-coaxial cable
High Density electronic board,
Data output via fibers
Board at corner
Hole for 1-2 cables and2-4 fibers
Module
Electronic board
An example

## Slide 17: Improvements on the scint. strip
Simulation for single channel
  Fiber embedding: groove  hole,
  Diameter of fiber:  ,
Very new R&D, like the production in Fermilab.
Fiber embedding: Groove  hole
No new fiber available yet, we use three fibers.
Optical glue can increase the by 25-30%. Tested!
Use NDL EQR15
new scint with diameter hole
New scintillator provided by GNKD, with our R&D!
Scintillator production at Fermilab
Very positive to the design of long module ().
Trigger at middle
Without optical glue

## Slide 18: And the chimneys for magnetics

## Slide 19: SiPM mini power
Study on mini power to be integrated into the FEE.
Temperature sensor
DC Power supply
USB-C communicate
SiPM POWER | BIAS-2-14/70 @NDL | C14156 @Hamamatsu | MAX5026 @Fudan
Voltage (V) Output Range | 14~70 | 0~80 | 0~71
Current (mA) Output Range | 0.5 | 2 | 2
Number of SiPMs driven | 100 | 400 | 400
Power consumption (mW) | 250 | 100 | 200
Ripple noise (mV/Vpp) | 5.2 | 0.1 | 2
Price (¥) | ~2000 | 500 | 30
Ripple noise @ OUTPUT:45V
NDL
NDL
CAEN
CAEN
HAMAMATSU
HAMAMATSU
500ns/div
20ms/div
1$ = 7¥