## Slide 1
Feedback of 2025 IDRC Review Report

## Slide 2: Outline
Chapter 3 Machine Detector Interface and Luminosity Measurement
Chapter 4 Vertex Detector
Chapter 5 Silicon Trackers
Chapter 6 Gaseous Tracker
Chapter 7 Electromagnetic calorimeter
Chapter 8 Hadron calorimeter
Chapter 9 Muon detector
Chapter 10 Superconducting solenoid
Chapter 11 Readout Electronics
Chapter 12 Trigger and Data Acquisition
Chapter 13 Offline software and computing
Chapter 14 Mechanics and integration
Chapter 15 Detector and physics performance
Chapter 16 Overall construction cost and timeline

## Slide 3: Machine Detector Interface

## Slide 4: Findings
F-A-3-1: A layout of the interaction region—including the anti-solenoid, final focus quadrupoles, IP beam pipe, and Luminosity Monitor—has been presented. Although not yet final, it is sufficiently advanced to proceed with detailed component design.
The Be beam pipe has an inner diameter of 10 mm and a length of 220 mm. It consists of an inner Be layer 0.2 mm thick and an outer Be layer 0.15 mm thick, separated by a 0.2 mm gap, which seems quite aggressive. The default coolant is water, with paraffin as a backup. The cooling technology is well-established, and the cost estimates are considered reliable. The coolant flow remains in the stable laminar regime. Mechanical analyses for cantilever support during installation have been performed, and no issues have been found. With an inlet water temperature of 15°C, the Be pipe temperature remains below 20°C, which is within acceptable limits.
F-A-3-2: Beam background sources—including synchrotron radiation (SR) photons, pairs, and off-energy particles—have been studied in detail, along with other minor contributions. For SR photons, important interactions such as the photoelectric effect and Rayleigh scattering have been simulated. It was found critically important to employ high-Z SR masks to protect the IP beam pipe region. Pair backgrounds are mitigated by designing the IP beam pipe to stay outside the high- density region. The hit rate on the first layer of the vertex detector (VTX) is estimated to be around 1 hit per cm² per bunch crossing. Backgrounds from off-energy particles are suppressed by placing collimators at strategic points around the ring and heavy metal masks near the IP to absorb secondary showers.
F-A-3-3: Experience from BESIII was presented, showing that real background levels were about 1/5 of those predicted by simulation.
F-A-3-4: An updated design of the LumiCal, using a silicon detector and LYSO crystals for pile-up event veto, is included in the Reference TDR. Mechanical design and optimization are complete, and construction of a large prototype is planned for the EDR phase. The selected technology appears feasible, although achieving the required luminosity precision will demand electron impact position measurements at the level of better than ten microns.
Machine Detector Interface

## Slide 5: Comments
C-A-3-1: From the presentations and draft Ref-TDR, it is unclear whether a gold (Au) coating is applied to the inside of the Be beam pipe, and if so, what thickness is used. Further study on this issue may be necessary.
Answer: The 10um Au coating is implemented, as indicated in Ref-TDR MDI Chapter: “The gold coating on the inner surface of the central beryllium pipe has a thickness of 10 𝜇m .”
C-A-3-2: The current SR mask configurations require further study. In particular, changes in beam or bit— such as during commissioning—must be considered to ensure continued protection of the Be beam pipe region.
Answer: Sure. Currently, only the ideal beam with some tail has been studied. The changes in beam orbit will be studied in future together with accelerator colleagues to figure out the working scenarios and the parameters.
C-A-3-3: While heavy metal masks can effectively reduce backgrounds from off-energy particles, they may also generate secondary backgrounds. This study suggests the effect is moderate, but further investigation is needed, especially concerning the tungsten (W) masks near the IP.
Answer: The secondaries has been studied. We also realize that the SR masks in the -1.9m may also increase the other sources of beam induced backgrounds. We are optimizing our design of the SR masks, by introducing some dedicated SR collimators relatively far away from the IP, the decrease the height of the SR mask to mitigate the secondaries introduced by it. These work is still on going.
Machine Detector Interface

## Slide 6: Comments
C-A-3-4: The discrepancy between real background measurements and simulations observed at BESIII is a significant concern. Although the energy scales differ between BESIII and CEPC, understanding this discrepancy is critical for evaluating the reliability of CEPC background predictions.
Answer: The previous study already decreased the discrepancy as shown in the text, and we will perform more dedicated study in future when we have machine times.
C-A-3-5: Although background rates (after shielding) are presented, detailed histograms and numerical data characterizing these backgrounds (e.g., energy spectra, multiplicity, polar and azimuthal angle distributions) are often missing. Such information is essential to assess the impact on the entire apparatus, particularly on the first layers of the vertex detector and LumiCal.
Answer: We have those information, and all these information have been given to the subdetector designers as indicated in MDI Chapter. Further optimization for LumiCal is also needed, and the study taking the beam induced background at LumiCal is still on going.
Machine Detector Interface

## Slide 7: Recommendations
R-A-3-1: Conduct studies to finalize the decision on the Au coating inside the Be beam pipe, including its thickness and the possibility of omitting it.
Answer: The 10um Au coating is implemented, as indicated in Ref-TDR MDI Chapter: “The gold coating on the inner surface of the central beryllium pipe has a thickness of 10 𝜇m.”
R-A-3-2: Continue detailed studies of SR mask configurations and materials, considering the effects of beam orbit steering in collaboration with the accelerator group.
Answer: Currently, only the ideal beam has been studied. The changes in beam orbit will be studied in future together with our accelerator colleagues when they have the results of the orbit corrections and the parameters and designs used for the commissioning phase.
R-A-3-3: Further investigate the role of heavy metal masks in absorbing particle backgrounds, including the possibility of operating without them.
Answer: The secondaries has been studied. We also realize that the SR masks in the -1.9m may also increase the other sources of beam induced backgrounds. We are optimizing our design of the SR masks, by introducing some dedicated SR collimators relatively far away from the IP, the decrease the height of the SR mask to mitigate the secondaries introduced by it. These work is still on going.
Machine Detector Interface

## Slide 8: Recommendations
R-A-3-4: Pursue deeper studies of BESIII backgrounds to understand the discrepancy between simulation and data.
Answer: The previous study already decreased the discrepancy as indicated in MDI Chapter: ”Such discrepancy was mainly due to the incomplete particle tracking and insufficiently modeled interactions involving complex components in IR in the simulation and was already decreased from more than 10^4 to current level by the improving of the geometry and adding the study on tip-scattering on the collimators”, and we will perform more dedicated study in future. We are working on the analysis of the data currently taking from BEPCIIU, and plan to perform this years dedicated beam induced backgrounds study and experiments at BEPCII when possible.
R-A-3-5: Continue dedicated studies on LumiCal readout electronics at high rates, followed by beam tests with detector prototypes at later stages.
R-A-3-6: Study the effects of beam backgrounds on LumiCal reconstruction for realistic configurations.
Answer: The shielding optimization and further mitigation of the beam induced background at LumiCal is still ongoing. Current beam induced background level is high at LumiCal, therefore the dedicated optimization must be performed to control the level and let the LumiCal works better. Also the bhabha and Radiative bhabha scattering needs to consider the beam-beam deflection, which is not considered yet. The data rate due to the beam induced backgrounds are already considered when design the electronics of the LumiCal. Such studies are ongoing at the same time to give us an idea how the situation would be. We are currently invistigating the generator guinea-pig++, and plan to implemented it with APES.
Machine Detector Interface

## Slide 9: Vertex Detector

## Slide 10: Findings
F-A-4-1: The design and technology choice for the vertex detector is highly ambitious and at the forefront of technological innovation. The baseline option—thin, bendable silicon CMOS sensors that can be stitched together to create a large, lightweight vertex detector—is certainly a very challenging yet promising approach. The backup solution, which also employs thin CMOS sensors mounted on ladders, remains technologically advanced. The project has made significant progress since the last review.
F-A-4-2: The vertex detector is expected to operate for 10 years during Higgs and low-luminosity Z running, after which it will need to be replaced for high-luminosity Z, WW, and tt̄ operations. The ability to run at high-luminosity Z mode imposes additional demands on an already extremely challenging design (e.g., larger data rate capabilities, shorter charge collection times, lower noise, and tighter power consumption constraints).
F-A-4-3: There are several major challenges for the vertex detector. Achieving the desired position resolution has been demonstrated with the TaichuPix-3 chip in TJ180 nm technology. However, this process has limitations, particularly its high-power consumption (>100 mW/cm²), which is too high for air cooling. Transitioning to the TPSCo65 process is a way forward, reducing power consumption to approximately 40 mW/cm². The required position resolution and uniform hit efficiency have already been demonstrated in this new process.
F-A-4-4: The real challenge now lies in the development of large-area stitched sensors of ~40 μm thickness that can be bent to radii as small as 11 mm, achieving a material budget of just 0.06% X₀. Successful bending of dummy 40 μm wafers has been demonstrated, but bending fully processed wafers (including metal layers for data and power lines) remains to be achieved. Securing access to TPSCo65 technology, including a modified process optimized for particle detection, is crucial. An alternative approach under early exploration is the HLMC 55 nm technology, although it has yet to be demonstrated.
F-A-4-5: The mechanical design is quite advanced for this stage, with many demonstrators and mock-up parts already tested, including a full ladder demonstrator. The simulations shown for mechanical and thermal performance, efficiency coverage, and background hit rates are detailed and of high quality. The impact of background hit rates on physics performance has been found to be negligible. The planned laser alignment system is a very positive development, but its effective operation must still be demonstrated.
F-A-4-6: The fifth double layer of the vertex detector employs a more conventional ladder design, achieving approximately 0.25% X₀. At the larger radius of the fifth layer, this becomes necessary but also requires parallel development. Importantly, this ladder design offers a reliable fallback option in case insurmountable problems arise with the stitched sensor technology for the inner layers.
However, adopting this backup would come at the cost of a slightly higher material budget, and thus a somewhat degraded pₜ resolution at lower energies.
Vertex Detector

## Slide 11: Comments
C-A-4-1: The chapter in the TDR is very long and detailed. In sections covering previously published R&D, the level of detail could be reduced. However, we found it very positive that past efforts from various groups were acknowledged, and that valuable experience and knowledge have been incorporated into the current vertex detector design.
  This section has been reduced from ~60 pages to 40 pages
C-A-4-2: Although pursuing the HLMC 55 nm process could dilute focus and resources, it remains a worthwhile avenue, especially if difficulties arise in securing access to TPSCo65.
C-A-4-3: While the mechanical design, simulations, and testing are advanced for this stage, maintaining mechanical stability and achieving efficient cooling remain significant challenges.
C-A-4-4: The foreseen cost of sensors (~4.0 MCHF) appears reasonable. The relatively higher cost per unit area compared to other silicon detectors likely reflects the fact that the baseline sensor producer is not domestic.
C-A-4-5: The estimated costs for mechanics, electronics, and the alignment system are of the correct order of magnitude but constitute only a fraction of the sensor cost
Vertex Detector

## Slide 12: Recommendations
R-A-4-1: Re-evaluate the required performance specifications, focusing on operation during ZH and low-luminosity Z runs over the first 10 years.
Answer: the new result of hit rate with latest simulation is updated in Sec 4.1.3.
Add figure readout frequency vs power consumption
R-A-4-2: We reiterate our previous recommendation to expand the current manpower dedicated to design and R&D efforts. A close collaboration with ALICE-ITS3 on stitched sensor development is strongly encouraged.
Answer: start having meeting with CERN team on ALICE3 upgrade, potential collaborate on HLMC55nm
R-A-4-3: Explore constructing a mock-up with dummy heaters for thermal performance tests, to be used also for simulation validation.
Answer: has added this suggestion into future plan section in vertex chapter sec. 4.8. ‘The plan begins with exploring the construction of a mock-up featuring dummy heaters for thermal performance testing. Results will also validate thermal simulation models.’
R-A-4-4: While pixel functionalities are similar for the ladder and stitched sensor options, significant differences in chip-to-chip (RSU-to-RSU) connectivity could impact performance. Address potential challenges (e.g., power and data distribution across large, stitched sensors) as early as possible through simulation studies
Answer: will perform simulation on stitching design when we are about to tape out the next version of sensor by the end of 2025. Most of this potential challenges can be simulated with design kits when the stitching design is in shape.
Vertex Detector

## Slide 13: Comments on Draft v0.4.1
C-B-4-1:
Daniela’s comment:
I read the tracker section and found that the structure of the reference TDR has improved.
Nonetheless, the Barcelona version still needs substantial editing. In addition, some figure captions — for example, Figure 4.8: “For we could not completely handle high-lumi 𝑍 mode now, as well as the major difference between high-lumi 𝑍 with 𝑍 mode is luminosity which means their hit rate distribution is similar, the hit rate distribution of high-lumi 𝑍 would not be shown here.” — indicate that there is still an unresolved issue with the high-lumi 𝑍 mode.
This should be addressed carefully.
Answer:
We added this statement in Section 4.2 “The readout architecture can accommodate the data rates in both the Higgs factory mode and the low-luminosity 𝑍 boson factory mode during the first ten years of operation. A replacement of the VTX with upgraded technology is foreseen thereafter, with the readout architecture for the high-luminosity 𝑍 boson factory mode discussed in Chapter 11.2.”
“The process involves: buffering detector signals and background data on the front-end chip; the trigger system generating fast trigger arbitration information quickly and sending it to the front-end chip via a dedicated channel; the front-end chip comparing buffered data with the fast trigger information and transmitting preliminarily arbitrated data to the BEE.”
Vertex Detector

## Slide 14: Comments on Draft v0.4.1
Gregor:
General observation:
C-B-4-2: The Chapter has improved significantly from the April draft in terms of length, restriction to important information and clarity. The length is appropriate and some unnecessary details from the first draft are left out.
C-B-4-3: Alignment and laser alignment monitoring system are adequately addressed.
C-B-4-4: Rich and at that stage advanced R&D is in a separate section which is positive. It is difficult in part to disentangle different objectives of JadePix and TaichuPix
ANSWER -->we rephase the first part of Section 4.5 (R & D section): The JadePix project focuses on optimizing the charge collection diode design and the analog front-end circuitry, with particular emphasis on achieving low power consumption in the analog domain. In contrast, the TaichuPix project is dedicated to developing a fully functional digital architecture, incorporating in-pixel logic and a data-driven, column-drain readout scheme. This design is specifically tailored to meet the stringent timing and data throughput requirements of the high-luminosity CEPC environment, particularly during the low-luminosity Z-pole operation with high event rates.
C-B-4-5: The cost estimate from April was already reasonable and wasn’t touched in the review.
Vertex Detector

## Slide 15: Comments on Draft v0.4.1
C-B-4-6: Is the Layer 5,6 the exactly the same design/concept as L1,2 and L3,4 of the backup design? The stitching concept is very attractive, but also very innovative and unproven which poses a significant risk. Given the development of the backup (baseline for L5,6) will have to go hand in hand with stitched-chip design it may be worth presenting the impact of using conventional design on performance (not only d0,z as in 4.6 but maybe a subset of physics channels) . Also a possible lack of technology access or resources may force you to abandon stitched-MAPS part baseline option. If you are confident in stitched-chip technology wouldn’t it be worth finding the way to use it also in L5,6?
 Yes, Layer 5,6 in baseline layout the exactly the same design/concept as L1,2 and L3,4 of the backup layout.
Due to wafer size limitation and the yield issue, we still don’t have a good solution for stitched-chip technology in Layer 5/6 yet.
C-B-4-7: VTX design for for high lumi Zmode which only comes after 10 y is super challenging. Relaxing design parameters for longer BX may lead to more robust design. VTX is not very large and a better design for high lumi Zpole running may emerge with time.
 We optimized the VTX for the first 10 year operation including Higgs and low-lumi Z, the design parameters already related. More dedicated design for high-lumi Z pole runs is expected to be performed for the VTX replacement before high-lumi Z runs.

## Slide 16: Comments on Draft v0.4.1
C-B-4-8: Background studies from ee and synchrotron radiation are crucial for understanding the background. Mixing the tables and plots with/without different background contributions is difficult to follow and evaluate.
 The dominated component of background contribution is pair production. That is the reason why we did not talk further about the contribution from different component. Detailed information about different background is mentioned in section 3.
C-B-4-9: Laser alignment is an important tool and if implemented will reveal many unknowns about the mechanical stability of such objects not demonstrated in real experiment before. However, illuminations at shallow angles on almost entirely metalized surfaces are much more complicated that for e.g. strip detectors. Understanding all reflections and ways to induce signals will be a challenge.
 more study with illuminations at shallow angles on prototype sensors will be performance in a short time scale.
We will investigate laser alignment with infrared laser shotting at backside (without metal) of the MAPS. In this way, the reflection can be reduced.
In longer time scale, the laser alignment method will be checked with vertex detector prototype with stitched sensors

## Slide 17: Comments on Draft v0.4.1
C-B-4-10: Remarks/questions and editorial comments:
C-B-4-10-1: L2444 - dead zone -> inefficient region (all over the text) ->Done
C-B-4-10-2: L2479 - 65 nm or 55 nm (SMIC) - maybe it would be better not to limit yourself ->Added more info about alternative technology on 65/55nm
C-B-4-10-3: Table 4.1 - time stamp precision should be without +/- ->Removed
C-B-4-10-4: L2505 - using the word chip can be confusing as people use it for reticle size objects -> stitched-chip would make it clearer all over the text
C-B-4-10-5: L2506 - to satisfy the coverage from 8.1-90 deg ->Corrected as |cos (theta)|<0.991
C-B-4-10-6: Figure 4.2 : CMOS, MAPS used here imply as CMOS and MAPS are different detector technologies. Maybe planar CMOS sensors -> “single reticle MAPS” and “stitched MAPS” is a better terminology.  we now unify the wording stitched layer and planar layer
C-B-4-10-7: Figure 4.6 - please put “not to scale” in the caption. ->Done
C-B-4-10-8: Figure 4.7 - Please mention that the cell in this case is a single chip, for easier reading. The legend (Layer 1 and Layer 2 labels should be larger. The colour coding of the plots is not the most convenient. I would advise you to use the same scale on both plots! ->Corrected
C-B-4-10-9: L2626 - remove Tower from the TPSCo ->removed.
C-B-4-10-10: Table 4.7 and also in the text put the fill factor (sensitive area) of the RSU
   Table 4.7 (area for each functional block in MAPS) has been removed, since the design has not been finished yet. We will try to keep a highest possible fill factor during the design process.

## Slide 18: Comments on Draft v0.4.1
C-B-4-10-11: Figure 4.9 it is unclear to what the data interface part if the middle x~10 mm is stitched to (or "stitched" can be omitted)? For 1D stitching of RSU as I understand reticles are stitched along the z axis.
   stitching direction is along the z axis, we now indicated the stitching direction in Figure 4.3 and also in the text.

## Slide 19: Comments on Draft v0.4.1
C-B-4-10-12: L2699 - What about the n-spray implant (modified process) to find optimum between collection efficiency and position resolution.  we now added some tex to mention n-spray implant
C-B-4-10-13: L2679 - “the leakage current should be controlled in 5 times of TaichuPix” - this doesn‘t read well. ->Removed
C-B-4-10-14: L2840 – although some studies show that that bending of silicon to 11 mm is doable, this is far from certain and surprises may appear.  Thanks, we will keep that in mind.
C-B-4-10-15: L2847-2849 – this needs a rewrite for easier reading. ->Rewrote
C-B-4-10-16: L2876 – with our previous prototyped vertex design -> with an earlier prototype design. -> done
C-B-4-10-17: L2906 – 300 mW/cm2 cooling with airflow needs a reference and also at what conditions. This may lead a reader to a false believe that around an order of magnitude less is trivial to cool. A fee more sentences are needed here: what flow was simulated (laminar/turbulent), if all obstacles were correctly accounted for. Have the thermal gradients along the flow been taken into consideration?  the simulation results indicated it is a turbulent flow. The thermal gradients along the flow has been considered, Not all the obstacles accounted for. We now added more information about the cooling simulation in the text. “To evaluate the performance of the cooling system, simulations were performed under various airflow speeds, as shown in Figure 4.18. The results indicate a turbulent pattern under the current geometry and flow conditions. “

## Slide 20: Comments on Draft v0.4.1
4.4.1 looks a generic wish list. It is clear that presently the level of details known or needed is not large, but a bit more refined information would be welcome. added more detailed “During the assembly phase of the CVTX layers, the thickness and curvature of the stitched sensors will be inspected. In later stages, the layer-to-layer coaxiality and 𝜙-stagger across layers will also be checked and recorded. “
4.4.2./3 The alignment is critical and level of distortions at 3.5 m/s airflow which may change/oscillate with time is a big challenge for the first 4 layers.  In longer time scale, we will check the laser alignment in vertex prototype with stitched sensor.
Figure 4.19: Please use (a), (b) and ( c) so that the figure captions are coherent across the text.  done
L3131 - Better wording would be lateral and more uniform depletion ->Rewrote as suggested
4.5.2.3 Prototype of a stitching CMOS detector - It is not clear what is the state of that prototype or the results from it. It is a very important piece of information of e.g. of LDOs performance … A few sentences summarizing the state of functional tests would be welcome.  added one paragraph in 4.5.2.3 of the function tests results.
4.6.1 - Genantino studies are well described, but it is not clear on how much the physics performance would degrade if e.g. fraction of hits=4 increases to say 1% and hits=5,6,7 are reduced.  More detailed will be done. According to Section 4.7.3, the performance degradation is limited when we turned off some fraction of the sensors.
L3283 - I would replace "domestic" with "Chinese" or omit it, unless you want the TDR to be biased.  we omitted it.

## Slide 21: Inner Tracker (ITK)

## Slide 22: Findings
F-A-5-1: The Inner Tracker (ITK) of the CEPC silicon tracking system adopts a baseline technology based on HV-CMOS monolithic active pixel sensors (SMIC 55), offering excellent spatial resolution (pixel size: 34 μm × 150 μm), moderate time resolution (3–5 ns), and low material per layer (<1% X₀). As an alternative for the endcap, a HV-CMOS strip sensor technology is also under development.
F-A-5-2: Since the last review in October 2024, the project has made notable progress in ASIC development. The COFFEE3 chip (SMIC 55 nm)—the second-generation HV-CMOS prototype— was successfully submitted for fabrication in January 2025 and is expected to be delivered for testing in May 2025. COFFEE3 integrates two readout architectures, supports in-pixel time stamping, and includes significant improvements in power optimization and data-driven readout. In parallel, the CSC1 chip, which integrates a passive CMOS strip sensor and an analog front- end placed in the periphery (CMSC 180 nm process), is scheduled for tape-out in April 2025. Together, these developments demonstrate strong and steady progress in the ITK technology program.
F-A-5-3: Significant system-level advancements have also been achieved, particularly in mechanical design, cooling, and thermal management. The ITK now incorporates a well-defined multi-loop water-cooling system capable of maintaining stable operation at a power density of ~200 mW/cm², with thermal gradients controlled below 4°C. Updated mechanical simulations confirm the structural integrity of staves and validate the mechanical design for integration and prototyping.
ITK

## Slide 23: Comments
C-A-5-1: The alternative ITK endcap technology based on CMOS strips, while offering slightly better intrinsic spatial resolution (~4 μm), presents greater challenges compared to the HVCMOS pixel baseline. Achieving 3D tracking requires stereo configurations, increasing the material budget and mechanical complexity. Furthermore, the integration of a CMOS readout circuit in the strip sensor periphery, although innovative, may introduce additional design and integration risks.
C-A-5-2: The COFFEE3 chip successfully consolidates the sensor, analog front-end, coarse-fine TDC for time-of-arrival and time-over-threshold measurements, and data-driven digital readout into a single device. Achieving these capabilities within a power density of ~200 mW/cm² is an impressive technical goal. A successful validation of COFFEE3 would represent a major milestone, demonstrating the technological feasibility of the CEPC ITK concept
ITK

## Slide 24: Recommendations
R-A-5-1: Given the limited resources available for R&D and the increased complexity associated with the CMOS strip-based solution for the ITK endcap, we recommend a careful evaluation of the merit and timing of continuing this development. The CMOS strip approach remains a promising technological direction; however, it may be appropriate to continue work at a lower priority to preserve long-term potential, while focusing current resources on advancing the baseline HV-CMOS pixel system.
In our previous Ref-TDR draft, the CMOS strip was presented as a backup or alternative approach with low R&D priority. Following the Referee’s comment , we have removed all content related to CMOS strip from the current Ref-TDR to better focus on HV-CMOS baseline.
R-A-5-2: We strongly encourage prioritizing the COFFEE3 validation campaign. As a comprehensive integration of position sensing and timing capabilities within a monolithic HV-CMOS technology, successful testing of COFFEE3 would constitute a critical milestone for the CEPC silicon tracking system, helping to de-risk the ITK concept and validate the soundness of the baseline detector design.
The latest COFFEE3 sensor was received at the end of May, and the sensor test campaign was lunched immediately upon receipt. The test setup is fully prepared, and testing is currently underway. We are committed to completing the critical validation promptly, as it represents one of the most important milestones for the ITK.
ITK

## Slide 25
  COFFEE3 incorporates two readout architectures, both featuring nearly a complete ASIC readout framework. This solution can be extended to final chip.
Architecture 1: An optimized design framework based on the current process conditions (Triple-well process)；
Architecture 2: An improved solution that requires process modification (Deep P-well required) to fully utilize the advantages of the 55 nm process node.
Architecture 1
Architecture 2
Passive diodes
PLL
Array：48 row 12 column
Pixel：40 μm×145 μm
Array：32 row 12 column
Pixel：40 μm×100 μm
DLL
LVDS driver/receiver
Left and Right Matrix Test Board
Test Board (TB) designs for left and right matrix separately
COFFEE3 left matrix is under test: laser, responce scan, SPI communication...

## Slide 26: Outer Tracker(OTK)

## Slide 27: Findings
F-A-5-4: The Outer Tracker (OTK) of the CEPC is a large area tracking system designed to provide precision timing and position measurements, complementing the inner tracking systems and the central Time Projection Chamber (TPC). It plays a critical role in improving momentum resolution for high-momentum tracks and mitigating performance degradation of the TPC in high-luminosity operations, where ion backflow-induced space charge can distort the drift field and impair tracking accuracy. The OTK is based on AC-coupled Low-Gain Avalanche Detectors (AC-LGADs) arranged as microstrip sensors, capable of delivering ~10 μm spatial and ~50 ps timing resolution, covering approximately 85 m² across the barrel and endcap sections.
F-A-5-5: Since the October 2024 IDRC review, the CEPC OTK system has made significant progress in response to the committee’s recommendations. The AC-LGAD sensor design was updated, reducing the baseline size from approximately 8 × 5 cm² to 4 × 5 cm² to improve timing performance and manage higher particle rates. A new prototype sensor layout was submitted for tape-out in February 2025, featuring a variety of strip lengths, pitches, and electrode widths to optimize capacitance, noise, and spatial resolution. In parallel, the LATRIC readout ASIC was finalized and submitted for tape-out in April 2025, integrating all main functionalities. Mechanical and thermal simulations were also updated, confirming stable operation under a heat flux of 300 mW/cm².
OTK

## Slide 28: Comments
C-A-5-3: The latest submission of the redesigned AC-LGAD sensor marks a key step toward determining the optimal strip geometry and layout for the OTK system. By systematically varying strip length, p-well doping, electrode width, pitch, and implementing isolation structures (e.g., trenches) to reduce capacitance, this prototype will provide crucial data to balance timing resolution, position resolution, power dissipation, and occupancy, ensuring the final design meets the stringent performance and rate requirements of the CEPC detector.
C-A-5-4: The LATRIC ASIC is a critical demonstrator, consolidating all essential functionalities required in the OTK readout chain into a single chip. It includes a low-jitter analog frontend, clock generation via PLL, coarse-fine TDCs, internal calibration circuits, and a data readout architecture with serializer and control interfaces. Its successful validation will be essential to confirm the feasibility of a compact, low-power, fully integrated readout solution for the AC-LGAD-based OTK system
OTK

## Slide 29: Recommendations
R-A-5-3: To fully exploit the potential of this design iteration, it is strongly recommended to conduct exhaustive performance characterization of the newly submitted AC-LGAD sensors in test beams. These studies are critical to experimentally validate the effects of strip length, pitch, electrode width, n⁺-well doping, and isolation structures on timing and position resolution, power dissipation, and occupancy. Given the importance of timely feedback 9 and the current unavailability of the LATRIC ASIC, it is advised to perform these measurements using fast discrete amplifiers until the LATRIC ASIC becomes available.
Following the submission of the new AC-LGAD prototype in March 2025, we are actively preparing the test setup for comprehensive sensor characterization. Once the sensors are received from tape-out, we will perform a series of measurements using radioactive sources and laser systems. To fully evaluate sensor performance, our dedicated team has a plan to carry out thorough assessments, including test beam studies.
OTK
4-channels readout boards has been fabricated for AC-LGAD testing
2-stage amplifiers, Gain~70
Signal shape has significantly improved, showing no oscillations.

## Slide 30: Recommendations
R-A-5-4: The collaboration should continue evaluating other LGAD sensor options and should closely follow novel developments, particularly the trench-isolated DC-LGADs currently under investigation by the team.
We are open to exploring various LGAD sensor options to achieve high performance through the optimization of spatial resolution, timing resolution, and power efficiency. Trench-isolated LGADs are particularly important, as the isolation structure reduces sensor capacitance and thus lowers power consumption. In addition to the LGAD prototype submitted in March, as previously reported, we are currently preparing another tape-out that includes trench-isolated designs with both DC- and AC-coupled variants. We will continue to closely follow ongoing developments and conduct detailed evaluations to identify the most suitable sensor technology for our application.
OTK

## Slide 31: Recommendations
R-A-5-5: It is recommended to ensure that the LATRIC ASIC is made available for sensor bonding as early as possible to enable realistic and fully representative characterization of the AC-LGAD sensor performance. Integrating the final readout ASIC with the sensor is crucial to obtaining accurate estimates of timing, position resolution, and power consumption. Given the critical role of the OTK in correcting space charge distortions in the TPC, it is essential that the OTK be robustly designed with service granularity in mind, exploring all known failure modes and developing strategies to mitigate them.
We are fully aware of the critical importance of the LATRIC ASIC, as it is essential to the success of the OTK. Our ASIC team, which includes several senior designers, has made substantial efforts to ensure the reliable and timely delivery of functional chips. The development process is carefully planned and regularly reviewed, with ongoing technical discussions to track progress and resolve challenges. All efforts are focused on accelerating the design and verification phases, so that the ASIC can be made available in a timely manner for sensor bonding and realistic performance characterization.
OTK

## Slide 32: Comments from Ivan on Draft v0.4
C-B-5-1: Concerning the chapter organization, this is significantly improved, facilitating the reading. The ITK and OTK dedicated sections now share the same subsection structure (design,electronics, mechanics, sensor technology and ASIC, and future plans); they also cover the important aspects of alignment, background estimations, and performance. As mentioned, the removal of the alternative sensor technologies for ITK and OTK has greatly improved the draft’s readability.
Your suggestions have greatly improved the clarity and organization of our paper. We appreciate your positive feedback on the chapter structure and the revisions implemented.

## Slide 33: Comments from Ivan on Draft v0.4
C-B-5-2: The remaining content is very similar to the previous version; I noticed that the background hit rates are now lower than those presented in April’s version, and the major missing part remains the definition of an approach to tackle the TPC performance degradation due to ion back-flow, but this will likely require considerably more time to address.
We are actively studying and improving the shielding design to reduce beam induced background. Since the last review, we have updated the MDI shielding design, which has enabled us to achieve a further reduction in background levels. In response to the referee’s suggestion, we have added Section 6.3.2 (Ion back flow suppression), which outlines our proposed approach to mitigate ion back-flow effects in the TPC.

## Slide 34: TPC

## Slide 35: Findings
The Time Projection Chamber (TPC) with pixelated micro-pattern gaseous detector readout has been chosen as the baseline for the central tracker. It offers continuous 3D tracking with minimal material budget over a large volume and provides particle identification (PID) capabilities. This is a solid and well-justified choice for the Reference TDR, building on extensive past TPC experience at lepton colliders and more recent developments from ALICE, the LCTPC, and DRD1 collaborations. Several technological advances have recently been achieved; notably, a novel ultra-light QM55 carbon fiber material is now used to construct the TPC cylinder.
However, realizing the TPC as the tracker will require further significant efforts, particularly in mechanical design, structural integrity, and achieving uniform magnetic field conditions (see also the comments and recommendations in the Magnet chapter). Full simulation and digitization tools, based on the software framework and reconstruction algorithms, have been developed and must now be used to produce an updated set of performance plots (e.g., separation power plots).
The possibility of using a drift chamber as an alternative tracking option is also presented in the TDR.
TPC

## Slide 36: Finding on Draft v0.4.1
The Barcelona version of the TPC chapter shows clear progress in terms of section organization and clarity compared to the previous drafts:
  The overall structure is improved, with more logical sub-sections and better-defined description flow;
  The mechanical design aspects (inner/outer cylinders and support structures) are more consistently described;
  There is a better introductory explanation of the role of the TPC as the central tracking detector and its importance for the PID performance;
  Prototype development efforts are more explicitly referenced, including pad readout, based on micro-pattern gas detector studies;
These editorial and content enhancements are really appreciated and help to bring the chapter into more advanced stage. However, several technical issues raised in the previous review remain (partially) unresolved or are addressed only qualitatively.

## Slide 37: Comments
Since the IDRC 2024 review, significant progress has been made in the simulation of space charge distortions. For CEPC Higgs and low-luminosity Z runs, the maximum distortions after 3 meters of drift were found to be approximately 10 μm and 150 μm, respectively. Nevertheless, these figures require further verification, and careful evaluation of beam-related background effects must continue. In the longer term, dedicated simulation efforts are needed to develop and refine a "data driven" approach for extracting space-charge corrections, based on the alignment and correction models developed for the ALICE TPC
Clarify target performance: For each open topic (e.g., ion backflow, pad size), provide the expected performance goals (e.g., maximum tolerable distortion, acceptable ion backflow level, target spatial resolution) that guide the ongoing design effort;
The simulations and analysis of beam-induced background in the TPC have been continued with some collaboration (KEK, DESY). The low-energy photons (MeV) are the main source of positive ions in the TPC, both in the Higgs and low luminosity Z modes. The space charge density in the CEPC TPC is only about 1/60 of the ALICE TPC in the Higgs mode if the ion-backflow (IBF) can be suppressed to the primary ion level. Some optimization strategies are proposed to further reduce the backgrounds.
  Reducing the beam lost rate.
  Added shielding after the lumiCal.
  Added a dedicated distortion correction in the section of Calibration and Alignment
TPC

## Slide 38: Comments
TPC

## Slide 39: Comments
TPC

## Slide 40: Comments on Draft v0.4.1
Space-Charge Distortion and Ion Backflow
The chapter still lacks a quantitative description of space-charge distortion and its impact on tracking;
The description of space-charge distortion and its impact on tracking have been added in the subsection of 6.3.2.4 (TPC space distortions estimation). The detailed R&D of its impact on tracking will do in next steps.
There is no indication or explanation of how correction strategies (e.g., ALICE-like data-driven approaches) can be implemented, at least qualitatively;
The brief description of the correction strategies have been added in the subsection (Calibration and alignment).

## Slide 41: Comments
TPC
https://doi.org/10.1051/epjconf/202024501003

## Slide 42: Comments
The choice of the pixel readout chip (TEPIX) with a 500 × 500 μm² pixel size is currently driven by power consumption considerations. A TPC module prototype with 10 × 300 readout channels (using 24 TEPIX chips) has been developed and is planned for beam testing at DESY in 2025. Larger prototypes will need to be developed and tested during the EDR phase. Optimization of pad size and gas mixture must be finalized, clearly distinguishing between the digital pixel readout case and the pad readout case. These two approaches lead to distinctly different electronics requirements, particularly regarding the need for analog-todigital conversion in the pad case.
Within the framework of the LCTPC and CERN DRD1 international collaboration, our research group has booked a beam test at the DESY Institute in Hamburg, Germany, scheduled for November 2025. We will use a 5 GeV electron beam to test the performance of a TPC prototype, providing solid experimental evidence for the existing pixelated readout, The functions of the analog-to digital conversion and digital readout mode have been started to do R&D in our collaboration group. The full size prototype will be considered also.
TPC

## Slide 43: Comments
TPC

## Slide 44: Comments
TPC
Study of the TPC prototype assembled with seven modules using UV laser and cosmic rays, the module size is same as the TPC module in TDR (Left). The prototype of the 2.9m full-length TPC is primarily designed to study the electric field and the electron drift (Right).

## Slide 45: Comments
If the alternative drift chamber option is pursued, it will be necessary to identify a hydrocarbon free gas mixture that maintains the required performance characteristics
Thank you for the suggestion. Some updated simulations and optimizations of the gas mixture will be carried out beyond the TDR of CEPC , and the recycle gases system will be considered.
TPC

## Slide 46: Recommendations
The structure of the TDR chapter needs better definition and further consolidation; some figures presented during the review must be updated in the document. The structure and content of Chapter 06 have been updated within the CEPC community. The new version has been updated in the document.
TPC

## Slide 47: Recommendations
The updated results of FEA have been added in the document.
TPC

## Slide 48: Recommendations
The updated figures of the field cage and detector module have been added in the document.
TPC

## Slide 49: Recommendations
The updated water cooling of the detector module and endplate have been added in the document.
TPC

## Slide 50: Recommendations
Ion backflow during operation in low-luminosity Z-mode remains the primary concern. Further simulations of TPC space-charge distortions induced by beam-related backgrounds are necessary to optimize the Machine-Detector Interface (MDI). New module prototypes implementing advanced ion suppression techniques (e.g., double-grid structures or graphene layer coatings) should be studied. Mitigation strategies (e.g., double GEMs, gating grids, graphene coating) are mentioned, but not developed or prioritized for future studies;
Acknowledge open issues: clearly define which aspects of the TPC design (e.g., ion backflow mitigation, space-charge correction, gas mixture optimization) are still under investigation, and describe the R&D or simulation path that will be followed to finalize these aspects at the next stage;
The description of the IBF strategies has been added in the subsection 6.3.1.2 (Ion back flow suppression).
In the design, the double mesh Micromegas has been designed as the baseline.
After detailed discussions with Prof. Imad, we have explored the potential of graphene technology to control positive ion feedback. This exploration involved researching graphene membrane conversion technology and engaging with various institutions. Specifically, we have initiated collaborative research efforts with Shandong University, CEA-Saclay, Lyon University, the University of Bern, and CERN. These collaborations aim to leverage the unique properties of graphene to mitigate positive ion feedback, thereby enhancing the performance and reliability of our detectors.
TPC

## Slide 51: Recommendations
TPC
The updated double meshes Micromegas of the detector module have been added in the document.

## Slide 52: Comments on Draft v0.4.1
Gas Mixture and Ion Backflow Suppression
No clear indication about choice of gas mixture is presented. Therefore, the interplay between gas properties, backflow suppression, and long-term stability cannot be sufficiently discussed.
The detector baseline operating gas is the T2K mixture, chosen for its high drift velocity and low diffusion.
Next R&D stage, we will carry out gas-mixture optimization, circulation-system design, and long-term stability studies.

## Slide 53: Recommendations
TPC
The updated graphene R&D of the detector module have been added in the document.

## Slide 54: Comments on Draft v0.4.1
Tracking Performance and Simulation
There is no significant update on spatial or momentum resolution, dE/dx performance, tracking efficiency, or fake rate studies;
Simulation plans: Summarize how future simulations will validate TPC performance in full physics conditions (e.g., displaced vertices, Z-mode operation), if feasible;
The update description on spatial or momentum resolution, dE/dx performance and tracking efficiency has been added in the subsection 6.4.3 (Spatial resolution and momentum resolution).
Particle-identification research based on machine learning has already begun.

## Slide 55: Comments on Draft v0.4.1
Performance plots, especially in conjunction with the ITK/VTX system, are missing or remain in a preliminary stage;
The update description of the performance plots in conjunction with the ITK/VTX system has been added in TDR document.

## Slide 56: Comments on Draft v0.4.1
Pad Size and Readout Architecture
We understand that the choice between pad and digital pixel readout can not be finalized at this stage and remains uncertain. Still, some comments about the implications in terms of electronics complexity, data volume, and reconstruction performance would be beneficial; The absence of a baseline readout definition introduces uncertainty in downstream systems (DAQ, reconstruction).
The TEPIX ASIC has undergone performance tests, and the resulting data are considered reliable for reference. Based on the current detector channel count and expected data volume, a complementary description has been added in the DAQ chapter.
Detector-module R&D is now underway, the next step will use beam-test results to further refine the design and reduce readout-related uncertainties.

## Slide 57: Comments on Draft v0.4.1
Pad Size and Readout Architecture
Readout architecture: While a final decision may not be ready, describe the criteria that will drive the selection of the readout scheme and how each option will be validated. Summarize the impact of this choice on reconstruction, electronics design, and system integration. Clarify what is called a pixel TPC (digital readout) and a pad TPC with ADCs. Quantify power consumption in the two cases and document cluster counting for a digital readout;
In the studies on TPC module and prototype, the pad readout TPC has been developed using 1mm*6mm pad size. Also a low-power readout ASIC with integrated ADC functionality has already been developed under the WASA chips. In TDR, the readout module is pixel readout detector module.

## Slide 58: Recommendations on Draft v0.4.1
Editorial additions
Include a concise summary table linking current detector parameters and technologies to physics requirements. This will help contextualize the design and highlight where validation is still pending;
Some revision have been updated in this new version chapter. The concise summary table has been updated in the overall detector chapter.

## Slide 59: Recommendations on Draft v0.4.1
Streamline English and revise references;
The updated document has been polished.

## Slide 60: Comments from Ivan on Draft v0.4
Anyhow, we may recommend including a subsection in the chapter mentioning the TPC response degradation issue, along with an overall strategy to mitigate it. This addition would send the message to the reader that they are aware of the importance of the issue and are actively working on how to resolve it. This section could be also fit in the TPC chapter, though.
As previously mentioned, we have added Section 6.3.2 (Ion back flow suppression), which outlines our proposed approach to mitigate ion back-flow effects in the TPC. This section explicitly addresses the TPC response degradation issue and our overall mitigation strategy.

## Slide 61: ELECTROMAGNETIC CALORIMETER

## Slide 62: Findings
The high-granularity crystal ECAL is a recently proposed concept designed to be compatible with particle flow algorithm (PFA) reconstruction of jet energy within a homogeneous structure. The calorimeter is modular, with the fundamental detection units consisting of long orthogonal BGO crystal bars, read out at both ends by SiPMs.
Achieving high granularity at an affordable cost requires making strategic choices and compromises, guided by specific performance benchmarks. The team has made steady progress in understanding the performance and optimizing the performance-cost balance, using the ECAL standalone energy resolution and PFA jet resolution as primary benchmarks.
The baseline granularity was recently updated to 1.5×1.5×40 cm³, resulting in a significant reduction in the number of readout channels and associated power needs. Simulations indicate that, even with this updated configuration, the calorimeter meets the target requirements for boson-mass resolution and standalone electromagnetic energy resolution. The overall performance remains excellent, despite some degradation in π⁰/γ identification and two-photon separation; the latter may potentially be recovered through improvements in offline reconstruction methods.
A full-scale prototype with the updated granularity is planned. Current simulation studies and experimental results from similar granularities provide confidence that the ECAL performance and component requirements are sufficiently understood, despite limitations in previous test beams due to electron beam spread. The team is also aware of the need for further progress beyond the reference TDR, particularly in defining QA/QC aspects for the components.

## Slide 63: Recommendations
Continue developing a full-scale prototype with the final geometry (using existing readout ASICs) and aim to confirm performance in an electron beam with low momentum spread.
Further refine calibration strategies to ensure that necessary stability in transparency, linearity, and uniformity can be achieved in situ, without relying on a dedicated monitoring system.
Advance preliminary engineering of the gaps between modules and fully assess their impact on reconstruction performance.

## Slide 64: Feedback to IDRC Recommendations (1)
Continue developing a full-scale prototype with the final geometry (using existing readout ASICs) and aim to confirm performance in an electron beam with low momentum spread.
  Developing a full-scale prototype with the final geometry is planned for near future, by integrating crystals, readout boards (embedded with SiPMs and ASICs), light-weighted mechanics and cooling
    Covered in Chapter 16 “Timeline and Plans” (Section 16.2, page 615)
  International Collaboration in DRD-Calo (DRD6): subtask of WP3 (i.e. WP3.1.1 HGCCAL)
  Electron beams with low momentum spreads: a stringent requirement for test beam facilities
    First ECAL prototype shows EM resolution better than 2%, which requires beam momentum spread to be controlled well below 1% (or can be measured by tracker + dipole magnet)
  Test beam facilities
    CERN PS-T09 is the primary option (with best knowledge and hands-on experiences). Due to the Long-Shutdown 3 (LS3), we will also consider and investigate other options.
    Options in China: need to investigate synchrotron radiation light sources (e.g. HEPS)
    Option in Japan: 1-6 GeV electrons at KEK (momentum spreads appear significant, comparable to DESY)
      DESY 1-6 GeV electron beams: momentum spread measured on the order of 10% at 1 GeV

## Slide 65: Feedback to IDRC Recommendations (2)
Further refine calibration strategies to ensure that necessary stability in transparency, linearity, and uniformity can be achieved in situ, without relying on a dedicated monitoring system.
  Covered in Chapter 7 (Section 7.2.6, page 231-234) and in Chapter 15 (Section 15.3.3, page 606)
  Updates in Section 7.2.6 “Calibration and Monitoring”
    On-detector calibration: (1) pedestals and noises, (2) SiPM non-linearity, (3) channel-wise calibration per ASIC, (4) Beam-Induced Backgrounds
    Collision data calibration: (1) Bhabha scatterings, (2) decays, (3) decays, (4) MIPs from muons and “punch-through” hadrons, (5) other decays: , ,
    Calibration precision studies in simulation (Section 7.2.6.3)
    Detailed calibration scheme on SiPM non-linearity (next page)

## Slide 66: Feedback to IDRC Recommendations (2)
Detailed calibration scheme on SiPM non-linearity effects
  Updates in Section 7.2.6 “Calibration and Monitoring”
  SiPM non-linearity effects are studied by including SiPM pixel recovery during the relatively slow BGO scintillation time (typ. 300 ns), which further increases the effective number of SiPM pixels (i.e. many pixels can be fired multiple times during this scintillation process)
  Calibration is first done in an off-detector way, by extracting key parameters related to the SiPM non-linearity effects via the SiPM QA/QC database (e.g. breakdown voltage, interpixel crosstalk, etc.)
  Apply these parameters to all SiPMs in ECAL after detector assembly and use them for commissioning
  Use Bhabha events as an in-situ calibration source to monitor and calibrate SiPM non-linearity
Plans beyond Ref-TDR scope
  To validate the SiPM non-linearity simulation model either using laser or in beam tests
  To test batches of SiPMs for non-linearity calibrations: to extract QA/QC parameters and to validate the proposed scheme mentioned above

## Slide 67: Feedback to IDRC Recommendations (3)
Advance preliminary engineering of the gaps between modules and fully assess their impact on reconstruction performance.
  Engineering designs have been significantly updated in Section 7.2.5 (page 224-230), including readout boards, mechanical structures, cooling pipes and plates
  EM performance have been updated in Section 7.3.4 (page 238-239)
    An energy-correction algorithm has been developed to correct cluster energy loss in module gaps
    Incident photons are uniformly distributed around ECAL modules including module gap regions

## Slide 68: Feedback to IDRC comments in April (1)
The ECAL standalone energy reconstruction requires an energy threshold of 0.1 MIPs (as shown in Fig. 7.17), whereas the PFA jet reconstruction, based on fast simulation, adopts a higher threshold (Fig. 8.2). The ECAL team acknowledges the need to further develop and refine particle flow algorithms, photon identification at low energies, and π⁰/γ separation to fully exploit the calorimeter’s potential.
Feedback
  Updated CyberPFA for photon reconstruction
    Descriptions are updated in Section 7.3.2 (page 236)
    Achieved significant performance improvement, esp.
    in low-energy regions
  π⁰/γ separation: updates in Section 7.5.1 (page 255)
Figure 7.21 (a)

## Slide 69: Feedback to IDRC comments in April (2)
The timing specification of 0.5 ns for MIPs was not strongly motivated. This corresponds approximately to the time spread across a full bar and is insufficient to provide significant benefits for event reconstruction. Additionally, the current time resolution analysis appears suboptimal. The team acknowledges that a deeper understanding of timing response and its potential use is needed, although this is not a priority at this stage.
  Updates in Section 7.2.1 (page 219)
  A good timing resolution was initially motivated by the positioning precision to resolve ambiguities due to the arrangement crossed crystals. But test-beam results of long BGO crystal bars indicate that the timing resolution can not satisfy the positioning precision requirement.
  Good timing performance (e.g. 0.2ns in EM shower cores) can also be motivated for better performance of PFA clustering, which requires further quantitative studies in PFA.

## Slide 70: Feedback to IDRC comments in April (3)
Crystal transparency variations are significant. While progress has been made toward developing a calibration plan using collision events, a quantitative demonstration that the precision and event rates are sufficient for monitoring response evolution across the detector is still missing.
  Updates in Section 7.4.5.2 (page 251)
  BGO crystal transparency variations along with the TID dose was briefly discussed and a reference on TID-transparency measurements was added
  Further quantitative studies will be performed in simulation and dedicated irradiation R&D studies.
The non-linearity of the SiPMs poses a potential risk to the constant term in the energy resolution. Although compact photon detectors with more linear responses (such as APDs) were noted, SiPMs are preferred for cost and design uniformity reasons. However, SiPMs will require per-channel calibration, and possibly sorting during construction, along with continuous in-situ monitoring and corrections.
  Updates in Section 7.2.6.1 (page 231)
  Key parameters of the SiPM non-linearity curve will be extracted from QA/QC protocols and recorded in database, along with in-situ monitored and corrections using collision data (e.g. Bhabha events).

## Slide 71: Feedback to IDRC comments in April (4)
Prototyping with close-to-final components is essential to confirm performance. Using existing readout ASICs can help decouple detector characterization from electronics debugging and allow parallel progress rather than sequential steps.
  Details in the Feedback to Recommendation 1
  New: beam tests of the first crystal ECAL prototype were performed at CERN during June-July in 2025, using existing readout ASICs, also with minimum possible materials in upstream at PS-T09 beamline
The committee was pleased to see a substantial effort in understanding the impact of gaps between modules. However, the mechanical design and service layout within the gaps remains sketchy, and some components, such as the cooling plates, could be prone to underperformance.
  EM performance updated in Section 7.3.4 (page 238-239)
  Details in the Feedback to Recommendation 3 (updated engineering designs and performance results)
From a stylistic perspective, the TDR would benefit from an upfront presentation of the key performance benchmarks and detector specifications, followed by a focused discussion of the performance-cost optimization supported by R&D and simulation evidence. The detailed discussion of alternative options currently in Section 7.2 could be summarized briefly and moved to an appendix.
  Updates in Section 7.6 (page 257-258) : completely restructured, following up the IDRC suggestion

## Slide 72: Feedback to IDRC Comments on Draft v0.4.1
General comment
  There is no mention of separation of showers or individual particle depositions. The parameters mentioned are energy resolutions without mentioning the segmentation (granularity) needed to achieve particle flow performance. We suggest adding mention of needed segmentation or granularity.
Feedback: Updates in Section 7.2.2 (page 219-220) and 7.3.2 (page 236-237)
  The two-particle separation performance (separation efficiency)
  The required granularity of 15x15 mm is added in the updated version.

## Slide 73: Feedback to IDRC Comments on Draft v0.4.1
Detailed comment
  The MIP requirement for the MIP light output has been raised from 200 to 300 p.e./MIP. While this makes the 0.1 MIP threshold for signal-to-noise ratio easier to achieve, it makes the requirement for the linearity up to 3000 MIPs (set by the maximum energy deposition from e showers for the CEPC operated at 360 GeV) more difficult to be met. Additionally, tests with prototypes show that the light yield of bars in the baseline bar configuration (1.5x1.5 x 40 cm3) are 400 pe/MIP (L.6527), thereby requiring linearity up to 106 pe and beyond. Simulation studies show that the linearity requirements are met (Section 7.3.5). However, these studies assume the nominal 300 pe/MIP and not the measured output of 400 pe/MIP for the baseline design choice for the BGO bars. Additionally, the study is limited to photons from the H → γγ decay for operation at 240 GeV, which have an energy deposition up to about 1500 MIPs (Fig. 7.5b). The SiPM dynamic range is further discussed in Section 7.4.2.2, with numbers that appear inconsistent with other parts of the TDR. For example, it is stated (L.6586) that a maximum deposition per bar of 45 GeV corresponds to 5x105 pe. However, at L.5984 it is stated that the MPV for a MIP is 13.3 MeV, which converts into 3383 MIPs for a 45 GeV energy deposition. At 300 pe/MIP, this gives already 106 pe. At 400 pe/MIP this is above 1.3x106. In summary, the effect of non linearity over the full range and up to 106 p.e. (or beyond) with SiPMs having 250k pixels does not appear to be sufficiently documented.
Feedback
  Updates in Section 7.4.1 (page 242) on the MIP Energy Response measurements with beam particles
  Beam-test data: 307 p.e./MIP for 1x1x40cm BGO crystal bar rescaled with the target SiPM and the signal integration time of 300ns

## Slide 74: Feedback to IDRC Comments on Draft v0.4.1
Detailed comment
  The specification about radiation hardness requirements has been dropped from the list (Table 7.1). A statement on the response stability of the BGO vs the ionization dose is needed in the section where the crystal choice is discussed, even if this is not translated into a specification.
Feedback
  Total Ionization Dose (TID) for BGO crystals: a reference and conclusions are added in Section 7.4.5.2 (page 251)
Detailed comment
  There are a few inconsistencies in the requirements about energy resolution. At line 5932 it is "𝜎𝐸/𝐸 ≤ 2%/root(E)" while at L.1501 it is required an "energy resolution of <3%/root(E)". In other places the energy resolution is required to be less than 3% (Table 7.1) without specifying any energy dependency. Then there are instances where both the stochastic and the constant term are indicated (L. 6851 and L.1321, again with some inconsistency between 2% and 3%). Please clarify and distinguish clearly between the requirement and what is achieved. For example at L.6851, if the requirement is 3% and you achieve <2%, you can simply state that the requirement of <=3% is achieved.
Feedback
  Thorough updates in Chapter 7: descriptions of the EM energy resolution requirement () are upated for consistency in the whole chapter

## Slide 75: Feedback to IDRC Comments on Draft v0.4.1
Detailed comment
  The discussion about timing performance (Section 7.4.3) remains confusing. The time resolution is defined as “the standard deviation of the time difference of the time stamps of SiPM signals from the two ends of a crystal”. This quantity is not independent of the hit position and does not correctly quantify the precision with which the position of a deposition can be reconstructed. A deposition in the centre of the bar, would give a Δt = 0 with an RMS from the resolution of the device. A deposition near the ends of the bar would give a distribution with the same RMS centered at Δt = +/- L/2v, where L is the bar length and v the velocity of the light in the crystal. For a uniform hit distribution, the RMS will therefore get a contribution from the propagation path of L/(v sqrt(12)) ~ 0.6 ns for L=40 cm, v = 1.5c. This should be added in quadrature to the genuine time resolution from the detector and readout. In Fig. 7.31 at L=40 cm, the resolution is 0.7 ns, which is consistent with 0.6 ns from propagation (+) 0.4 ns intrinsic to the detector, which you can read from the measurement with L=2 cm crystals. At L=60 cm, your measured resolution is almost 1 ns, which is again consistent with an L/(v sqrt(12)) ~ 0.9 ns (+) 0.4 ns. So, while your data show the expected behaviour, your interpretation of the results is different. At L 6602, you conclude that at L=40 cm, the resolution is 700 ps (500 ps per end), while your data indicate a resolution is 400 ps/MIP (280 ps per end), which would scale to a resolution of 100 ps already at 200 MeV (per crystal). A better measure of the time resolution is provided by the RMS of the sum of the two timestamps, because the sum of the two propagation times is independent of the hit position. A plot of this quantity should clarify what is the actual resolution. You may still have some dependence on the bar length, because the light output is lower for longer bars.
Feedback
  Updates in Section 7.4.3 (page 245-246)
  We have thoroughly re-analyzed the testbeam data using the definition in TDR (i.e. T1-T2) and the alternative definition suggested in the IDRC review (T1+T2). Plots are presented in the next page (also in the reference cited by the TDR).
  Conclusions: (1) the 1-MIP timing resolution along the crystal length is uniform; (2) the 1-MIP timing resolutions using two definitions mentioned above are mostly the same.

## Slide 76: Feedback to IDRC Comments on Draft v0.4.1
40cm BGO scan (testbeam data)
Two definitions of timing resolution compared: similar performance
T1-T2 used in Ref-TDR
T1+T2 suggested by IDRC: to eliminate position dependence
Timing Resolution vs Hit Position in BGO (testbeam data)
ΔT=T1-T2: used in Ref-TDR
Uniform sigma(ΔT) with hit positions

## Slide 77: Feedback to IDRC Comments on Draft v0.4.1
Line by line comments:
  line 1475, 1481: - reference to just LEP for last gen e+e-. Suggest "LEP and SLD at SLC"
  line 1490: "the key ingredient" I suggest "a key ingredient"
  lines 1493-1494: We suggest expanding the sentence to "We propose to use BGO crystals as full absorption ECAL which will significantly improve energy resolution, which is essential for optimal H-> gamma gamma detection, for example."
  line 1496: "18 longitudinal layers providing 24 radiation lengths" → "providing 24 or more radiation lengths", since there are more than 24 radiation lengths. for much of the barrel
  line 1499: "fully contain electromagnetic showers." → "maximize containment of electromagnetic showers.", because, strictly speaking, there is still some leakage.
  line 1524: "typical" would be better as "the typical" and "result" should be plural "results".
Feedback
  Changes were implemented in Chapter 2 by Haijun Yang (Editor of Chapter 2), which correspond to the lines mentioned above

## Slide 78: Feedback to IDRC Comments on Draft v0.4.1
Line by line comments (not exhaustive):
  -line 5914 - "It also detects neutral pions 𝜋0 ...." → "It detects neutral pions 𝜋0 ...." The current formulation (with “also”) is a bit strange to me since it actually detects the gammas from neutral pions and those were already mentioned in the previous lines.
  -line 5920 - "Moliere Radius" → "Moliere radius"
  -line 5935 - "at two ends." slightly better would be "at both ends."
  -line 5939+ and Fig 7.1: "contains over 400 long crystal bars”. It would be helpful here to re-state number of crystals in depth (18 specified much earlier on line 1496)
  -line 5963 - "ers.`necessitating" looks like a typo ".`" should be ", "
  -Figure 7.1: Here the "module" is shown as a "supercell". This is the first use of the term "supercell". Supercell is later referred to in section 12, but not until then. A clarification of these two different references should be added.
  -Table 7.1 "EM energy resolution < 3%". Shouldn't this be energy dependent? Perhaps, add <3% above xx GeV.
  -lines 6009 - 6010: "A typical 40 × 40 cm2 module employs 1.5 × 1.5 × 40 cm3 crystal bars". It would be helpful here to state there are 18 layers.
  -lines 6861-6863: "∼ 285,000 crystals" "571,000 SiPMs". As there are two SiPMs per crystal by design, make the two figures a factor two: either ~285,000 and ~570,000 or 285,500 and 571,000.
  -line 6851 "to achieve an EM energy resolution of 𝜎𝐸/𝐸 ≤2%/root(GeV) ⊕1%" should be root(E(GeV)). Please correct also the requirement on line 1321 "𝜎𝐸/𝐸 ≤ 3%/ root( 𝐸( GeV)) ⊕ 1%," (and make them consistent)
  -lines 11299-11301: "The ECAL supercells, mentioned in Section 7.2, are used for the preliminary trigger studies.". We don’t find mention of supercells in section 7.2, where discussion of ECAL elements are modules. If the ECAL supercells are identical to "modules" the terminology used in Section 7, it would be helpful to state that here.
Feedback
  Changes were implemented in Chapter 7 accordingly

## Slide 79: HADRONIC CALORIMETER

## Slide 80: Findings
A key innovative feature of the Hadronic Calorimeter (HCAL) is the large sampling fraction achieved through the use of heavy scintillating glasses (GS). The proposed layout offers the potential to significantly improve the PFA resolution by enhancing the stochastic term of the single-particle energy resolution. The committee acknowledges that the team is highly motivated and is making steady progress toward this ambitious design.
HCAL

## Slide 81: Findings
HCAL
The proposal is reasonable but aggressive. Detector specifications and performance benchmarks are clearly defined; however, considerable work is needed to bring the GS-HCAL baseline choice from its current R&D phase to a full-scale detector.
--The primary objective of this section is to validate that the GS-HCAL design meets the CEPC physics program’s core performance criteria. Leveraging extensive simulation studies in the absence of prototype data, we demonstrate the design’s compliance with these requirements. In the new version in Section 8.5 ( simulation and performance).
The estimated energy resolution of 𝜎𝐸 /𝐸 = 29.8%/√𝐸 ⊕ 6.5% and an energy linearity within 2% before calibration, outperforms the stochastic term of traditional HCALs.

## Slide 82: Findings
HCAL
For instance, during the review, the team was uncertain about the origin of the constant term observed in the hadronic energy resolution, a result obtained from idealized simulations with only limited hardware effects included.
--To verify the hypothesis that longitudinal leakage was the cause of the observed discrepancy, we increased the depth of the GS-HCAL from 48 layers (6 𝜆𝐼 ) to 80 layers (10 𝜆𝐼 ) in Section 8.5.2 Hadron Energy Resolution. When the calorimeter depth was extended to 80 layers, this tail decreased significantly, and the constant term dropped to around 2.9%. The significant improvement in the constant term upon increasing the depth of the GS-HCAL supported the hypothesis that shower leakage, rather than an intrinsic design flaw.

## Slide 83: Findings
The committee is pleased to note that the next step is the construction of a large-scale prototype.
--Yes, in the new version of the HCAL-TDR, the new design of the prototype has already described, as in the Section 8.4.8. The construction and testing program proceeds in phases. A 3×3×7 mini-prototype is currently under construction for initial beam tests at CERN in October 2025. The full 8112-channel prototype is scheduled for completion by end-2026.
HCAL

## Slide 84: Findings
In this prototype, each tile will be read out by four SiPMs, whereas in the final detector only one SiPM per tile is foreseen for cost reasons.
--It is clear that there is only one SiPM for tile for the design and cost, as show in Figure 8.2, and detialed describe could be found in section 8.2.1 (Single layer structure). In the Section 8.4.5 (Measurements of GS with SiPM), it is shown the performance test result of the 4cm*4cm*1cm glass cell coupling with 1 piece of 3mm*3mm SiPM.
HCAL

## Slide 85: Findings
In this prototype, each tile will be read out by four SiPMs, whereas in the final detector only one SiPM per tile is foreseen for cost reasons.
--It is clear that there is only one SiPM for tile for the design and cost, as show in Figure 8.2, and detialed describe could be found in section 8.2.1 (Single layer structure). In the Section 8.4.5 (Measurements of GS with SiPM), it is shown the performance test result of the 4cm*4cm*1cm glass cell coupling with 1 piece of 3mm*3mm SiPM.
HCAL
Cosmic ray test results of the GS tile measured using single SiPM.
(a) The measurement using Hamamatsu S13360-3050PE SiPM, resulting a light output of 64 p.e./MIP.
(b)The measured result is about 160 p.e./MIP using a Hamamatsu S13360-6025CS SiPM. The two results are consistent.
The difference is due to the different sizes of the SiPMs, and different PDEs.

## Slide 86: Findings
Regarding costs, the committee notes that the current cost estimate does not include the cost of PCBs, which experience shows can become a significant item for granular calorimeters due to the complexity of design and production.
--the cost of PCBs has already included in the electronics part.
HCAL

## Slide 87: Findings
It was also acknowledged that a sampling calorimeter based on plastic scintillator (PS-AHCAL), which is more mature and better understood, remains a viable fallback option. The committee encourages the team to continue pursuing the GS-HCAL option, while maintaining the PS-HCAL as a backup.
--Yes, the GS-HCAL and PS-HCAL are both the options of the HCAL. the size of the GS or PS tile are the same as 4cm*4cm, has the same photon readout SiPM and the electrinics, the same size Box and Prototypes. If the GS R&D was falled, it will be easy go back to the PS-HCAL design. There is also a special Section 8.6 (Alternative HCAL options) introduce the R&D results of the RPC-SDHCAL and PS-HCAL.
HCAL
RPC-SDHCAL
PS-HCAL

## Slide 88: Comments
Scintillating glasses represent new territory for hadronic calorimetry. The material properties, such as radiation length and hadronic interaction length, are not yet fully characterized. Although the decision to adopt this technology is well justified, it carries significant risk. Therefore, extensive prototyping and simulation studies are mandatory to validate the concept.
--Yes, the study of the GS-HCAL option is only start in two years ago, and choise to be the baseline option on Aug.2024, there are lots studies need to do. And the new design of the prototype has already described, as in the Section 8.4.8.
HCAL

## Slide 89: Comments
A deep understanding of the response to hadrons is essential, including clarification of the constant term origin, study of the e/h ratio (software compensation), validation of GEANT4 physics lists, and accurate characterization of material properties such as quenching (Birks' law).
--The new version of the TDR ahs already update the simulation work and the group also did more study for the design. In Section 8.5 simulation and performance. The energy linearity and resolution of the GS-HCAL are estimated using Geant4 simulation within the CEPC Software (CEPCSW) framework.
HCAL
The estimated energy resolution of 𝜎𝐸 /𝐸 = 29.8%/√𝐸 ⊕ 6.5% and an energy linearity within 2% before calibration, outperforms the stochastic term of traditional HCALs.

## Slide 90: Comments
The introduction of the TDR currently lacks references to important developments such as the CALICE AHCAL, built by German, Czech, and Japanese groups, which served as a foundation for the scintillator section of the CMS HGCAL.
--The refs has already marked in the new version. Especially in the Section 8.6 (Alternative HCAL options), it is introduced the developments of different option for HCAL. Multiple technological approaches of the CEPC calorimeters have been investigated to achieve the required jet energy resolution. These include gaseous detector-based approaches like the Digital HCAL (DHCAL) [29, 30] and SDHCAL [5, 31], as well as plastic scintillator tile designs (AHCAL) [10–13].
HCAL
RPC-SDHCAL
PS-HCAL

## Slide 91: Comments
The process of down-selecting technology options should be better explained in the text. Statements such as "excessive power consumption" should be supported with quantitative arguments for clarity and transparency.
--The quality of the language has already improved a lot in the new version. In this new version, only one person (Li Hengne) represents the whole HCAL team to write documents and hold discussions with others, maintaining the uniqueness of the writing style.
HCAL

## Slide 92: Recommendations
Develop a detailed plan to validate the choice of GS-HCAL technology in a timely manner. This plan should include the development of glass samples with reproducible and controlled quality, along with a detailed understanding of single-particle and jet energy resolution.
--Yes, in the new version, there is a new section 8.4 (Technology R&D to demonstrate technologies and prototypes) introduced the technology of HCAL as GS, SiPM, Simulation and Calibration. To verify the performance stability of the GS, a batch of 150 glass samples were produced, and corresponding performance tests were conducted.
In Section 8.5.2 （Hadron Energy Resolution）introduce the energy linearity and energy resolution of GS-HCAL with the digitization model.
HCAL

## Slide 93: Recommendations
Prioritize the construction of a full-scale prototype. This prototype should incorporate the preliminary selection of glass tiles and ideally include a first version of both the readout ASIC and the PCB. Decide early on the final configuration regarding the number of SiPMs per tile and implement this choice in the prototype.
--The final prototype will use the GS,ASIC and PCBs, which will be used in the HCAL-CEPC in the future. A 3×3×7 mini-prototype is currently under construction for initial beam tests at CERN in October 2025. This mini-prototype will use the DT5202 from CAEN (https://www.caen.it/products/dt5202/ )for electronics. But the full 8112-channel prototype scheduled for completion by end-2026, with include the readout ASIC and the PCB by our electronics group in CEPC. The full 8112-channel prototype is scheduled for completion by end-2026, with cosmic ray tests planned at IHEP and subsequent beam tests preferably at CERN in 2027. This prototype implements a steel-scintillator sandwich structure in a compact 0.6 m3 volume (52 cm × 52 cm × 130.6 cm).
Organize the group’s work such that the prototype is simultaneously implemented into the simulation framework, including a complete digitization chain, to enable rapid feedback from test beam campaigns.
--Yes, These will be the next steps to focus on.
HCAL

## Slide 94: Comments in backup
The authors are encouraged to make the text more concise where possible, while still providing sufficient detail where necessary.
  o Captions such as that for Fig. 8.12 ("The real AHCAL prototype") are inadequate and should be made more informative.
  --the outline of the HCAL in new version has changed, this types of pictures were deleted.
  o The authors should carefully review the text to ensure that all figures are properly motivated, and that the overall argumentation is logical and coherent.
  --the outline of the HCAL in new version has changed.
  o For example, it is unclear why the emission spectrum shown in Fig. 8.52 is included—is it representative or used for digitization? This should be explicitly explained.
  --this figure was deleted. Totally about 91 figures aere deleted, and all the figures in the new version TDR were modfied with high quality.
HCAL
Fig. 8.12 in old version
Fig. 8.52 in old version

## Slide 95: Comments in backup
The authors are encouraged to make the text more concise where possible, while still providing sufficient detail where necessary.
As with other sections, the presentation was significantly better than the corresponding document and should serve as a guideline for revising the written material.
-- the old version of the HCAL TDR has about 122 pictures and 70 pages, after the IDRC review, we have rewrite the new version with only 30 pictures and 40 pages without the reference.
HCAL

## Slide 96: Comments in backup
Section 8.5 contains an extended discussion of SiPMs, mixing general background information with results from the collaboration’s own R&D. This section should be streamlined to separate general background from specific experimental achievements.--.
--this part was deleted in HCAL. The introduction of SiPM could be find in ECAL part. In the new version part, there is small subsection 8.4.3 (Photon detector) about the SiPM, as other key technologies include in the Secion 8.4 (Technology R&D to demonstrate technologies and prototypes).
Since SiPMs are used extensively across the calorimeter and muon systems, it would be more effective to consolidate the discussion of SiPM R&D into a single section. This would avoid redundancy and present a more coherent overview of the topic.
--this part was deleted in HCAL. It could be find in ECAL part Section 7.4.2 SiPM.
HCAL

## Slide 97: Comments in backup
Mechanical integration aspects, currently occupying much of Section 8.7, could be better placed within a general "Detector Integration" section. The authors should use their judgment to decide which integration details are most relevant to retain in the specific HCAL section, while moving broader topics to a centralized discussion.
--there is the new section about the mechanical part at the begin of the HCAL as 8.2 Design part. The Outline of the HCAL part are the same an other Detector, first the design, then the Key technologies, both the major challenges and the R&D results. Then the simulation and performance. The Alternative HCAL options are to be a special section to overview the other group's work for the HCAL.
HCAL

## Slide 98: Comments on Draft v0.4
General comment
Let us first congratulate them for the huge amount of interesting work that is presented. As already observed for the Eca part also the HCal part has been restructured. It also presents directly the design choice and comments on alternatives at the end of the chapter, meeting therefore a comment made during the review in April. In the following a few high level comments and a non-exhaustive list of line-by-line comments. An annotated pdf file of the HCal put has been put at the disposal of the project members.
HCAL

## Slide 99: Comments on Draft v0.4
High-level comments
Still the main problem is that a technology is proposed that is at the very beginning of the R&D cycle
  From our point of view It will take at least five years with full resources before this calorimeter will reach the TDR level
  We note however that the authors show awareness of this (major) shortcoming
  The project matches perfectly a strategic R&D topic in DRD Calo but is too early for a TDR.
--The answer from Imad.
1）several components of the is technology are similar to ones used in the AHCAL technology like SiPM and readout systems as well as calibration techniques. All this is integrated in the new technology
2）although future extensive tests will confirm it, the simulation used to produce the TDR results seems to be corroborated by the first beam tests and cosmic benches.
3) the strong collaboration with local industries allow us to be confident that new generation of scintillanting glass will provide even higher performances in terms of light yield and attenuation length leading to even much better performances than the ones put in the TDR.
--The answer from Hengne & Sen.
Agree. In deed we well accept this glass scintillator technoligy is still at its early stage . however, given it's valuable potential (e.g. cheap, easy modeling, etc.) we chooose to boost it in the future CEPC HCAL application. For this reason We did the following updates in the text accordingly:
1.Updated the preamble part before "Overview" Section, explicitly mention that we fully aware the GS technology is at its early stage and still need at least 5 years of R&D to be a TDR-Level technology.
2.Update corresponding sections, to clearly present what R&D have been done, what haven't yet. And trying to make a clear and solid plan towards a mature technology at the time scale of 5 - 10 years, i.e. before the construction of the CPEC detector.
HCAL

## Slide 100: Comments on Draft v0.4
High-level comments
  How critical is the non availability of CERN (i.e. a high energetic hadron beam) between the middle of 2026 and ~2029.
  ---May be in KEK or the Proton beam in CSNS in China.
  -- A clear proposal of using CERN high energy hadron test beams for the R&D of the GS-HCAL is presented.
The document lacks a clear plan toward construction
--please see the section 8.4.8 Prototype, the section 8.7 Summary and Future Plan.
HCAL

## Slide 101: Comments on Draft v0.4
High-level comments
What are design parameters (on e.g. cell S/N) of the system?
-- we are expecting a 10% of MIP value as the S/N cut threshold.
At the moment only a handful of tiles have been tested
  How to ensure mass production?
  In this context how to ensure homogenous tiles and what are the criteria?
  --No matter what. We must trust the production capabilities and quality control of Chinese enterprises.
  --the successfull example is the 20 inch MCP-PMT for JUNO. We get the small number of prototypes at Lab in 2015, and the factory setup the mass production line in 2016, and start the mass production from 2017 to 2020, finished 15000 pics 20 inch MCP-PMTs for JUNO.
  --for the Glass Scintiallator and SiPM, the situation right now are really much better than the PMTs at that time. When the CEPC will be supported by the goverment, the factories will do the mass production by themeslves.
  --for the SiPM, the chinese company ZJGD (www.zjgd.com.cn) has already finished the mass production line on June 2025, and produce the SiPM with 40% PDE and acceptiable price. The news will be publish in The Innovation will introduce it.
HCAL

## Slide 102: Comments on Draft v0.4
In the draft we don't see the results of all the (few) tiles that have been e.g. tested beam or in the cosmic stand
--In Fact， in the Section 8.4.2 Glass Scintillator, the Figure 8.12: the transmission and XEL spectra of large GFO glass, the Energy spectra of GFO GS and the Scintillation decay curve of the GFO.
there is the new version for the 8.4.5 Measurements part, the Figure 8.17: Measurement results of the GS cell with SiPM readout, using 137Cs radiation source and Cosmic ray.
HCAL

## Slide 103: Comments on Draft v0.4
There are inconsistencies; examples (non exhaustive)
  All SiPM tests in 8.4.4 were carried out with HPK SiPMs however for the prototype NDL SiPMs will be used
  --all changed, not fix the SiPM for HCAL.
  Is the pre-amp tested in Sec. 8.4.6 the same that will be used in SIPAC?
  --not yet. The pre-amp was combined in ASIC, which has not designed for using right now.
On Page 290 the authors raise concerns about the radiation hardness.
  The tiles will not withstand 10 years of operation. Is this a fundamental problem and if yes how will this be systematically addressed?
  -- radiation section is removed. it is not an issue. According to the existing TDR data, during the 10-year Higgs run (with a luminosity of 8×10³⁴ cm⁻²s⁻¹), the irradiation dose reaches 100 Gy.For the Z run, the luminosity is 192×10³⁴ cm⁻²s⁻¹, so a rough estimate suggests that 1 year of Z running would result in an irradiation dose of 240 Gy. However, since the Z-peak energy is 91 GeV (lower than the Higgs production energy), the actual dose is expected to be somewhat lower.
  indeed, you correctly pointed out adiation hardnes is not a fundamental problem. Previously we spent many text discussing radiation damage but in fact it is not really an issue. We have receved comments from several experts that the radiation damage is actually not an issue in electron-positrom machine such as CEPC, we agree on that and re-evaluated the situation, we deceided to remove a large fraction of the radiation damage discussion.
  --8.4.2.3 Radiation Tolerance
HCAL

## Slide 104: Comments on Draft v0.4
The description of the cooling system (Page 279) is insufficient.
-- agree, adding more text and a figure to better describe the cooling system. More detialed could be seen in Section 8.2.2 Barrel and Section 8.2.3 Endcap.
HCAL

## Slide 105: Comments on Draft v0.4
Think to shorten the introduction to 8.4
--The Part 8.4 have to change as follows:
keep the 8.4.1 Historical review; 8.4.3 Photon detector; 8.4.4 Simulation Study of Attenuation Length
8.4.6 Calibration;8.4.7 Readout electronics for R&D; 8.4.8 Prototype
rename 8.4.5 Measurements of GS with SiPM as 8.4.5 Measurements
rewrite the 8.4.2 Glass scintillator;
8.4.2.1 Light Yield,
8.4.2.2 Light Attenuation Length;
8.4.2.3 Radiation Tolerance
HCAL

## Slide 106
rewrite the 8.4.2 Glass scintillator; (1) light yied,
delate the result of the electron beam result;
remove cosmic ray test result to 8.4.5 Measurement
HCAL

## Slide 107
rewrite the 8.4.2 Glass scintillator; (2) Light attenuation length,
delate the test result of the data by the light output in our lab published in Ref[18];
retest the samples by the transmittance data and give the new results and also the ref.23
R. Y. Zhu et al. “A Study on the properties of lead tungstate crystals”. Nucl. Instrum. Meth. A 376 7517 (1996), pp. 319–334..
HCAL

## Slide 108
rewrite the 8.4.2 Glass scintillator; (3) Radiation resistance ,
just delate this part and give the result in (1) Light Yield part. and ref the papaer published in NIMA about this result right now (suggested by Imad).
Ref「22」S.H. Yin et al. “Radiation resistance study of Gd-Al-B-Si-Ce3+ glass scintillators using 80MeV proton beam irradiation”. Nucl. Instrum. Meth. A 1081 (2026), p. 170869. issn: 0168-9002.
HCAL

## Slide 109: Comments on Draft v0.4
The constant term is still an issue.
  Line 7867: "Both approaches led to a reduction in the fitted constant term". What was the fraction of the events that were selected?
  it is less than 20%, the selection requires the shower starts in the first 60mm, curresponding to the first two layers, about 0.25 nulcear interaction length, which agrees with the calculation usign the simplified formula P = 1-exp(-0.25) ~ 0.2 . Attached is the eff. (fraction of starting showin in first two layers) vs each energy points in the simulation.
  the text modified to be "The other required the hadrons to initiate their first interaction within the first two layers of the \gls{GS-HCAL} (corresponding to the initial $0.25\lambda_\mathrm{I}$), though such events constituted less than 20\% of the total sample."
HCAL

## Slide 110: Comments on Draft v0.4
The constant term is still an issue.
  We propose to show the linearity in addition to the resolution
  --As shown in Fig. 8.24, conparing linearity and resolution between with and without digitisation, the linearity does not show a apparent issue, i.e. the leackage, or the hadronic shower longitudinal profile is not expected to depend on the energy of the incident hadrons, e..g.
  accroding to some previous studies such as [Y.A. Kulchitsky, V.B. Vinogradov/Nucl. Instr. and Meth. in Phys. Res. A 413 (1998) 484—486], where Longitudinal profiles of the hadron showers of 20 GeV (crosses), 50 GeV (squares), 100 GeV (open circles) and 140 GeV (triangles) energies as a function of the longitudinal coordinate x in units j I for the conventional iron-scintillator calorimeter do not show apparent difference in the shape.
HCAL

## Slide 111: Comments on Draft v0.4
The constant term is still an issue.
  Please comment on the expected e/h ratio
  --We added a new subsection based on previous samples describing e/h results " 8.5.3 Energy Response e/h Studies."
  By fitting the energy responses of electron and pion, kion...etc, the e/h is derived to be from 1.02 to 1.14, exhibits a non-compensation at the level of 9–14%,
  We understand "all inner sub-detectors are removed" in this study.
  -- indeed, added this information in the following setence in the pretty beginning of this section. :
  “In initial studies of the \gls{GS-HCAL}, the energy resolution yielded a constant term ($b$) of approximately 5–6\% based on Geant4 full simulations with all inner sub-detectors (e.g., \gls{ECAL}) removed. ”
HCAL

## Slide 112: Comments on Draft v0.4
The constant term is still an issue.
  Since there will be an ECAL before the HCAL in the actual experiment, the effective depth of calorimetry will be larger and the selection and constant term (with and without selection) will be different. It is also interesting to investigate how the different responses in the ECAL and the HCAL will impact the constant term in the integrated detector.
  -- Indeed, agree, with the ECAL infront of HCAL the overall ECAL+HCAL PFA results will largely reduce the impact of the leagage, and therefore smaller constent term. A through study is needed as the next step after TDR, but we already added this point here:
  "As mentioned before, the leakage studies were performed with \gls{HCAL}-only. In the full \gls{CEPC} detector configuration, the \gls{ECAL} with about $1.2\lambda_\mathrm{I}$ will cause approximately 70\% of hadrons to initiate showers before reaching the \gls{GS-HCAL}.
  This upstream shower development is expected to significantly reduce leakage effects and consequently lower the constant term in the combined \gls{ECAL} and \gls{HCAL} system."
  The AHCAL prototype discussed in Sec. 8.6.2 has a depth (from memory) of 4-5 interaction lengths but a constant term of only 2.59%. Thus, the depth cannot be the only reason for the large constant term of the GS HCAL
  --After verify this point we learned that the beam test results onf the AHCAL prototype showing 2.59% constant term is after a selection of events showing interactions (with energy deposition) in the first several layers to keep sufficient containment in the AHCAL, and avoid leakage from the back.
HCAL

## Slide 113: Comments on Draft v0.4
Line-by-Line Comments
Line 6952 - "The HCAL is a key component in achieving the jet energy resolution". One may could argue it is THE key component
--agree, indeed, Re-written the beginning of the chapter, and provided justification and discussion why HCAL is "THE key component", e.g. HCAL is responsible for the reconstruction of >70% of jet energy....etc.
Lines 6962-6964 "plastic scintillators and gaseous detectors, with readout based on SiPMs or other photon sensors.”. This is confusing. Maybe "plastic scintillators, with readout based on SiPMs or other photon sensors, and gaseous detectors."?
--agree, fixed, Re-written the beginning of the chapter.
Line 6983 "𝑊and 𝑍decays" - spaces missing - "𝑊 and 𝑍 decays"
--agree, fixed, re-written the beginning of the chapter.
Lines 7042-7043: "851.34 mm" and "1367.56mm" are unnecessarily precise (10 microns). Could this be rounded off to mm? --agree, fixed.
Figure 8.3: "851.34 mm" and "1367.56mm" are unnecessarily precise (10 microns). Could this be rounded off to mm? --agree, fixed.
Lines 7570-7574: Could some example distributions be shown? --Added.
Line 8066 "measure hadronic jets energy" I believe jet should be singular. "measure hadronic jet energy" line 8068 "GS and SiPMs'. We suggest spelling these out again when first mentioned in the summary ----agree, fixed.
Line 8082 "This can be achieved" -> may be achieved? -> "This may be achieved" -----agree, fixed.
---Agree, the pointed out parts have already update in the new version.
HCAL

## Slide 114: Comments on Draft v0.4.1 from Roman
The comments from Roman on 29th.July. 2025.
----all the comments are replayed one by one within the PDF file.
<CEPC_Ref_TDR_v0.4.1_BarcelonaEdition-Roman_reply.pdf>
HCAL

## Slide 115: Comments on Draft v0.4.1 from Roman
Origin of four emission lines in GFO spectrum (is the multiline structure a problem?
----no, it's not the background noice, it is the usefull signals. They are the ADC pedestal,
the 32keV peak,
the 180keV peak,
and the 662keV full-energy peak.
HCAL

## Slide 116: MUON

## Slide 117: Findings
F-A-9-1: The TDR presents a baseline design for the Muon Detector based on extruded plastic scintillator (PS) bars, coupled with WLS fibers and SiPMs. This approach is cost-effective, and the primary objective is to demonstrate that the system can meet stringent performance requirements across the detector’s large active area.
F-A-9-2: The Muon Detector will consist of six superlayers in both the barrel and endcap regions. It uses long scintillator strips, 4 cm wide, with lengths exceeding 4 meters. Due to WLS fiber routing, effective optical lengths can be even longer, making attenuation length a critical parameter, directly impacting timing resolution and detection efficiency. Enhanced light collection strategies are thus essential.
F-A-9-3: The readout system adapts designs from the ECAL and HCAL and includes uSiPMs, front-end boards (uFEBs), and management boards (uMBs), tailored specifically for the Muon Detector. 14 Background studies show a maximum hit rate of ~2 Hz/cm², comfortably below the system’s rate capability.
F-A-9-4: The Muon Detector supports trigger functionalities, including tagging long-lived particles (LLPs), although integration into the full CEPC TDAQ system remains preliminary. RPC technology, using environmentally friendly gases, is also under consideration via the DRD1 collaboration.
MUON

## Slide 118: Comments
The TDR chapter and the review presentation show significant technical progress with clear physics motivation and encouraging prototype results. However, several areas need further development:
C-A-9-1: Testing of full-length bars (4.2–5 m) must be completed, fully implementing optimized light collection methods.
C-A-9-2: Standardized procedures for optical glue application (thickness, curing time) and validation of coating quality at scale are still required. A detailed system-level comparison between NDL and MPPC SiPMs is lacking. Given the Muon Detector’s lower light yield and tighter timing requirements compared to calorimeters, selecting the optimal SiPM is critical.
C-A-9-3: Consolidated detector specifications (spatial and time resolutions) must be validated through simulations and trigger performance studies
MUON

## Slide 119: Comments
C-A-9-4: Testing of full-length bars (4.2–5 m) must be completed, fully implementing optimized light collection methods.
  Prototypes incorporating 5m long PS bars have been successfully developed and tested, as depicted in Fig. 9.12 of the TDR v0.6.0. These new PS bars exhibit a 50% enhancement in fluorescence yield. The prototypes utilize WLS fibers with a diameter of 2.0 mm, and the coupling between the WLS fibers and the sensitive area of the SiPMs being improved. However, due to the technical challenges associated with applying optical glue uniformly along the 5m PS bars, no optical glue was used to optimize the coupling between the PS bars and the WLS fibers. Testing of the 5-meter prototypes at their far ends demonstrated an average nPE of ~35, a time resolution of ~1 ns, and an efficiency of ~97% at an nPE threshold of 15. The prototypes achieved the required performance without the use of fill glue within the PS strip's hole, validating the design's effectiveness under these conditions. Filling optical glue in a 5m bar to enhance the light collection is implemented into the future R&D.
MUON

## Slide 120: Comments
C-A-9-5: Standardized procedures for optical glue application (thickness, curing time) and validation of coating quality at scale are still required. A detailed system-level comparison between NDL and MPPC SiPMs is lacking. Given the Muon Detector’s lower light yield and tighter timing requirements compared to calorimeters, selecting the optimal SiPM is critical.
  The primary challenge in optical glue application lies in uniformly filling the glue in PS bars exceeding 4m in length. This process remains under a further R&D, and we are collaborating with the company to establish a test procedure for validating the quality of the coating.
  We have completed a system-level comparison between NDL and MPPC SiPMs, and the results have been documented in the TDR, as illustrated in Fig. 9.11 of v0.6.0. The NDL SiPMs demonstrate consistent quality and stability in mass production. Testing of a 5m prototype yielded an average nPE of approximately 35 at the far end, with the nPE consistently exceeding the threshold of 15 for signals from MIPs in cosmic ray tests. Although the NDL SiPMs exhibit lower gain, DCR, and increased cross-talk compared to MPPC SiPMs, both types perform equally in terms of efficiency and time resolution. NDL SiPM has a large advantage in cost.
  Additionally, we have identified a new WLS fiber from Kuraray, which features a significantly shorter decay time. This fiber is currently under evaluation, and we anticipate improved performance in time resolution as a result of its enhanced characteristics.
MUON

## Slide 121: Comments
C-A-9-6: Consolidated detector specifications (spatial and time resolutions) must be validated through simulations and trigger performance studies
  Currently, the software and simulation focus on standalone muon identification and pion fake rate analysis. The spatial and time resolutions depend on standalone track reconstruction within the muon detector, which has not yet been implemented. This will be addressed in the next step, along with the trigger performance study.
MUON

## Slide 122: Recommendations
R-A-9-1: Complete comprehensive tests on full-length bars using final SiPM configurations and 2.0 mm WLS fibers, measuring timing, light yield, and efficiency.
Prototypes utilizing 5-meter-long plastic scintillator bars, 2.0 mm-diameter wavelength-shifting (WLS) fibers, and EQR-20 SiPMs have been tested. The results demonstrate a time resolution of 1 ns, an average nPE of approximately 35, and an efficiency of 97% at a threshold of 15 photoelectrons.
R-A-9-2: Define standard application procedures and conduct studies addressing mechanical stability, aging, radiation resistance, and refractive index.
We have outlined the standard procedure for assembling a plastic scintillator unit (PSU), constructing a detector module, and installing the module into the muon detector in the TDR. The process is designed to minimize mechanical complications. In the near future, we plan to build detector modules to evaluate mechanical stability.
We recently completed research and development for 5-meter-long scintillator bars, focusing on enhancing fluorescence. Using these new samples, we will soon conduct studies on mechanical stability, aging, radiation resistance, and refractive index.
MUON

## Slide 123: Recommendations
R-A-9-3: Systematically assess MPPC and NDL SiPMs (including new 20 μm pixel versions), focusing on gain, DCR, cross-talk, and operating thresholds under realistic conditions.
We conducted a systematic comparison between MPPC and NDL SiPMs, specifically the MPPC S14160-3050 and the NDL ERQ20-11-3030. The results are detailed in Section 9.3.1 and Figure 9.11 of the TDR v0.6.1. The tests focused on key parameters such as gain, DCR, cross-talk, and breakdown voltage.
R-A-9-4: Expand simulation studies to include full event samples, especially displaced vertex signatures, to validate and refine time resolution requirements.
This study has not yet been conducted, as the current focus remains on muon identification and reducing the pion fake rate. We plan to carry out the recommended analysis in the near future. Achieving excellent time resolution is critical, as it not only facilitates the identification of signals from displaced vertices but also enhances background suppression, eliminates ghost tracks in cases of multiple tracks within a detector sector, and improves the search capabilities for LLPs. For these purposes, we aim for the best possible time resolution.
R-A-9-5: Clearly state detector performance requirements linked to physics goals. Move Muon ID algorithm discussions to the global TDR Performance chapter and focus this chapter on local and standalone performance. Ensure consistent technical terminology and improve figure referencing.
In accordance with the recommendation, we have moved the discussion on the overall muon ID algorithm from the TDR. The current discussion now focuses on the standalone muon ID for the muon detector. Additionally, we have updated the figures in Section 9.4 of the TDR v0.6.1.
MUON

## Slide 124: Findings on Draft v0.4.1
The updated Muon Detector chapter in the CEPC Reference TDR (Barcelona version) shows clear improvements over the previous iteration:
The chapter is better structured and easier to navigate.
A performance summary table is now included early in the chapter.
Key technologies—such as SiPMs, long scintillator strips, and optical coupling—are described more clearly.
The new EQR-20 SiPM (20 μm pixel, higher gain, lower DCR) is introduced, and preliminary test results are presented.
Initial prototype results for long strips (up to 4–5 m) are now included.
These updates are welcome and demonstrate tangible progress. However, several important technical and editorial issues remain only partially addressed or unresolved.

## Slide 125: Comments on Draft v0.4.1
1. Long-bar prototype test results
C-B-9-1-1: The inclusion of tests for 4–5 m strips is a positive step, but the presented information lacks clarity and context.
C-B-9-1-2: Figures (e.g., Fig. 9.12) are not well integrated into the text and sometimes captions are confusing.
C-B-9-1-3: The intended target threshold remains undefined, despite reporting signal yields at various p.e. levels.
C-B-9-1-4: Results from IHEP and Fudan differ in setup (SiPM type, fiber), and the comparison lacks explanation.
C-B-9-1-5: Dual-ended readout is briefly mentioned but not quantified or discussed.
The long-bar prototype test was incomplete in Draft v0.4.1, as the results from both IHEP and Fudan did not align with the design of the plastic scintillator unit. We have since completed the test using new prototypes, which feature 5m-long plastic scintillator bars, NDL EQR20 SiPMs, and 2.0mm-diameter WLS fibers. Additionally, there was the test conducted with dual-ended readout. All new results are presented in Section 9.3.3 and Fig. 9.12.

## Slide 126: Comments on Draft v0.4.1
2. SiPM characterization (NDL vs. MPPC)
C-B-9-2-1: While pixel size and gain differences are noted, the comparison remains superficial.
C-B-9-2-2: Critical performance aspects—such as timing, noise, cross-talk, and behavior under temperature or radiation—are not evaluated.
C-B-9-2-3: There is no final decision or validation plan for SiPM selection.
We conducted a systematic comparison between MPPC S14160-3050 and NDL EQR20-11-3030 SiPMs. While the MPPC demonstrates advantages in gain, dark count rate (DCR), and cross-talk, these characteristics do not significantly enhance performance in the PSU application. On the other hand, the NDL EQR20 offers benefits in terms of operating voltage and cost. Based on these findings, we clearly state that the NDL SiPM is the preferred option.

## Slide 127: Comments on Draft v0.4.1
3. Readout architecture and threshold definition
C-B-9-3-1: The readout chain is inherited from ECAL/HCAL but lacks justification for its use in the Muon Detector.
C-B-9-3-2: Lower light yield and tighter timing constraints raise concerns about its suitability.
C-B-9-3-3: Thresholds shown in figures are not linked to a defined operating point or noise model.
(Difficult to answer from muon group.)
4. Trigger strategy
C-B-9-4-1: Trigger concepts are mentioned (e.g., LLP tagging), but no logic, architecture, or latency assessment is included.
C-B-9-4-2: No integration plan with the CEPC trigger system is presented.
(Difficult to answer from muon group.)

## Slide 128: Comments on Draft v0.4.1
5. Simulation studies and background
C-B-9-5-1: Beam background simulations are provided and show manageable occupancies.
C-B-9-5-2: Section 9.4.3 suffers from language issues (tense shifts, awkward phrasing).
C-B-9-5-3: No physics-driven simulation studies (e.g., low-pT muons, displaced vertices) are presented.
C-B-9-5-4: Detector performance specs (e.g., timing, granularity) are not explicitly linked to physics goals.
We have revise the section for simulation studies and backgrounds. As discussed before, we need more studies on software and simulation.

## Slide 129: Comments on Draft v0.4.1
6. Structure and editorial issues
C-B-9-6-1: Figure referencing is sometimes incomplete.
C-B-9-6-2: Section 9.3.3: The last paragraph of this section is duplicated, likely due to a copy-paste error. This repetition should be removed. In addition, the text would benefit from a general language revision to fix grammatical issues (e.g., subject-verb agreement, article usage) and improve clarity.
C-B-9-6-3: Section 9.4.3: The background paragraph conveys relevant information, but the English requires significant improvement. Verb tenses are inconsistent, and some expressions are unclear or incorrect. A thorough revision is needed to improve clarity and readability.
C-B-9-6-4: Terminology and language quality vary across the chapter and require final editorial revision.
We have made extensive revisions to the structure, figures, and language, as detailed in TDR v0.6.1.

## Slide 130: Recommendations on Draft v0.4.1
Considering that the TDR is near completion, we do not expect extensive new studies. Nonetheless, to improve clarity and completeness, we recommend:
R-B-9-1: Clarify prototype study objectives
Explicitly state the performance targets (e.g., threshold, signal yield, efficiency, timing) for long-strip tests and explain how the results support detector requirements. Threshold and noise strategy Even if a final threshold is not yet fixed, describe the criteria and expected noise level. Justify the thresholds used in figures and explain how they relate to realistic detector conditions.
In a realistic detector condition, the threshold can be adjusted according to the background level. Typically, the threshold is nPE~8.

## Slide 131: Recommendations on Draft v0.4.1
R-B-9-2: Readout chain evaluation
Acknowledge the differences between the Muon and ECAL/HCAL environments. Outline how the current electronics will be validated or adapted to meet the Muon Detector’s demands.
We will add the related discussion in the next version of the TDR.
R-B-9-3: SiPM selection process
Describe the performance metrics which will drive SiPM selection (e.g., dark noise, gain, radiation tolerance) and outline upcoming R&D needed for final validation.
To date, the tests have demonstrated that both the MPPC and NDL SiPMs meet the required performance specifications for the muon detector.

## Slide 132: Recommendations on Draft v0.4.1
R-B-9-4: Trigger implementation
Provide at least a minimal scheme and indicate how integration with the CEPC trigger system will be assessed.
(Difficult to answer from muon group. It may require a standardalone track reconstruction, which has not been done.)
R-B-9-5: Simulation roadmap
Include plans to simulate full physics events and connect detector specs to the physics motivation (e.g., LLP, muon ID performance).
We will add this into the research plan in the TDR.
R-B-9-6: Final editorial revision
Ensure all figures are referenced in the text, remove the duplicated paragraph in Section 9.3.3, and revise language in Section 9.4.3 for clarity.
This has been done, see TDR v0.6.1.

## Slide 133: SUPERCONDUCTING SOLENOID

## Slide 134: Findings
F-A-10-1: The CEPC Ref-TDR superconducting solenoid design has made significant progress. The solenoid provides a central magnetic field of 3T (for tt ̄, Higgs, and W runs) and 2–3T (for Z runs), with an inner bore diameter of 7.07 m and a cryostat/yoke half-length of 4.53 m. It is enclosed within an iron yoke that also houses the muon detector. The variation of the solenoid magnetic field in the central tracker (TPC) region is currently calculated to be approximately 10%.
F-A-10-2: The solenoid coil design is based on four layers of Al-stabilized superconductor, supported by an aluminum-alloy outer support cylinder and cooled using a two-phase helium thermosiphon system. This general design concept is well established, drawing on the reliable design experience of the CERN-LHC CMS detector.
F-A-10-3: A key technology development effort focuses on Al-stabilized superconductors, with two approaches to mechanical reinforcement:
  Option A: Double-layered, two-step co-extrusion process.
  Option B: Single extrusion with micro-alloying for reinforcement, followed by a cold-work process.
F-A-10-4: Further R&D is planned for 2025.
F-A-10-5: The maximum von Mises stress on the Al-stabilizer during magnet excitation is evaluated at 96 MPa, which is close to the current yield strength of the Al-stabilizer material (105 MPa). Further mechanical evaluation is necessary to ensure an adequate safety margin, including the mechanical integrity of the NbTi/Cu superconductor itself.
F-A-10-6: Remaining technical challenges primarily concern the production of large-scale, high-strength Alstabilized superconductors, as well as ensuring the reliability of the numerous aluminum-pipe welds required in the thermosiphon cooling system
SYSTEM MAGNET

## Slide 135: Comments
C-A-10-1: Field uniformity in the TPC region is a fundamental boundary condition for detector performance. The current 10% field variation must be carefully assessed to ensure it is acceptable for the required TPC performance. It is important to note that the ALICE detector has a different configuration, and that the ALICE magnet is much larger resulting in significantly better field quality in its TPC region compared to CEPC.
SYSTEM MAGNET
Impact on tracking:
It is impossible to achieve a uniform magnetic field in the experiment. Fortunately, the impact of non-uniform magnetic field on the momentum measurement can be minimized if the track fitting algorithm (i.e. Kalman filter) can deal with the non-uniform magnetic field with the measured magnetic field map.
The key issue is whether we use a right field map in software. Two requirements
Measurement precision of the magnetic field map is good enough.
Gradient of the field small enough (The map is smooth, without big fluctuation within small area)
CEPC magnetic field gradient of the TPC region:
  The gradient of TPC region is around 5.4*10-5 T/mm, which is small enough and meets the requirement
Measurement precision:
  If the measurement precision is 10-3 (i.e., position error during measurement is around 1mm), the deviation of B is around 5.4*10-5 T according the gradient, which meets the requirement of momentum resolution (~0.1%)
An example of BESIII
NUMF in BESIII is 5%, and measurement error of B is around 0.3%
The momentum resolution is good as the expected after the track fit with Kalman filter and track-based calibration. No significant impact from NUMF is observed.

## Slide 136: Comments
C-A-10-2: The committee recognizes the remarkable progress achieved in developing Al-stabilized superconductors, achieving a yield strength of 105 MPa at 4.2 K using micro-alloying (Ni + Be). However, further R&D is required to demonstrate the full mechanical performance of the conductor and the successful fabrication of full-scale Al-stabilized superconductor segments.
C-A-10-3: It is critical to demonstrate that the full conductor (NbTi/Cu + Al-stabilizer) can withstand mechanical stress up to 135 MPa. This threshold is about 50% higher than the maximum von Mises stress (~90 MPa) expected during operation at 3T. If achieving this mechanical strength proves difficult, increasing the thickness of the support cylinder could be considered, although this would be undesirable. As a last resort, if necessary, a reduction in the operating field strength may need to be discussed.
SYSTEM MAGNET
The stress issue can be addressed by either increasing the cross-sectional area of the aluminum stabilizer or enhancing the yield strength of its material. However, due to the current limitations in the size of the aluminum coating equipment and the overall design dimensions of the detector, it is relatively difficult to increase the cross-sectional area of the aluminum stabilizer. We made certain progress in the development of Box type conductor, which has a better mechanical performance. We will continue to do the R&D of high strength and RRR value aluminum stabilizer.
Secondary co-extrusion Box type Cable size and structure: 56mm*22mm (Box type)

## Slide 137: Comments
C-A-10-4: Developing a scaled model coil, including full cooling and excitation tests, will be an important step. Without such a demonstrator, confidence in the readiness of the solenoid technology for CEPC will be limited.
Establishing a scaled model coil is really a necessary step before the processing of the detector magnet, and we will take this important process into consideration in our subsequent planning.
C-A-10-5: Two cooling channel designs are under consideration:
  Vertical Al-pipe channels, as used in CMS.
  Sloped or tilted serpentine channels, which may reduce the number of welds and save cryostat space.
The latter option could be advantageous for construction reliability
We will optimize the cooling system from two aspects: Design and Welding Technology
We will consider doing the design of the sloped serpentine cooling path, on one hand, meets the requirements of temperature distribution, and on the other hand, reduces the number of welds.
Regarding the welding of aluminum tubes, we had experience in welding small model coils, but we have not yet had experience in welding such a large number of pipes in a large-scale cooling structure. We will conduct verification experiments in the near future.
SYSTEM MAGNET

## Slide 138: Recommendations
R-A-10-1: Carefully verify that the magnetic field uniformity of the CEPC Ref-TDR solenoid meets the TPC performance requirements without introducing unacceptable distortions to particle drift paths. If the current configuration proves insufficient, consider alternative design modifications—such as the addition of compensation windings in the forward and backward regions, as explored in ILD studies, or adjustments to the shape and configuration of the magnetic iron poles.
We will carefully verify the magnetic field uniformity with TPC collogues, put the simulated magnetic field distribution into TPC simulation software.
R-A-10-2: Maintain the highest priority for the R&D of the Al-stabilized superconductor, aiming to demonstrate full-scale conductor fabrication, production of sufficient lengths, and mechanical performance that meets the required safety margins.
The full-scale conductor is very important. We will develop the full-scale conductor with sufficient length in the year 2025 which meets the requirements of CEPC.
SYSTEM MAGNET

## Slide 139: Recommendations
R-A-10-3: Develop a detailed plan for the construction and testing of a superconducting model coil, including demonstrations of cooling and excitation. Achieving this milestone is essential for progressing toward full-scale magnet construction.
Establishing a scaled model coil is really a necessary step before the processing of the detector magnet, and we will take this important process into consideration in our subsequent planning.
R-A-10-4: Finalize the cooling system design based on the thermosiphon concept, with particular attention to the reliability and quality assurance of aluminum-pipe welding procedures during construction
We will optimize the design of the cooling system. While we have experience in welding small model coils, we have not yet tackled the welding of such a large number of pipes in a large-scale cooling structure. We plan to conduct verification experiments in the near future to ensure reliability and quality assurance.
SYSTEM MAGNET

## Slide 140: Finding and comments on Draft v0.4.1
C-B-10-1: The superconducting (SC) solenoid design for the CEPC Reference Detector Technical Design Report (Ref-TDR) has significantly progressed. Congratulations!
C-B-10-2: The solenoid provides a central magnetic field of 3T (for tt̄, Higgs, and W runs) and 2–3T (for Z runs), within an inner bore diameter of 7.07 m and a cryostat/yoke length of 9.06 m. As a fundamental number, the SC magnet stored energy (E) is 1.5 GJ with the coil mass (M) of 145 tons with E/M = ~ 10 kJ/kg. It is assembled with an iron yoke, helically assembled, also with muon detectors. The profile and uniformity of the solenoid magnetic field in the central tracker (TPC) region is expected to be approximately 7%. It would be OK, if the TPC may accept this field variation.
C-B-10-3: The solenoid coil is composed with four layers coils wound with Al-stabilized superconductor, supported by an outer support cylinder made of Al-alloy and cooled by using a two-phase helium natural convection flow with a thermo-siphon scheme. This design concept has been well experienced and established with previous collider detector programs, such as the CERN-LHC CMS detector and others.
C-B-10-4: The ‘box-type Al-stabilized superconductor’ with two step co-extrusion has been uniquely proposed, and the development is in progress. It is expected to successfully demonstrate the full-scale box-type conductor within 2025. It shall be a very important milestone and strongly encouraged. However, it is also important to keep backup solutions to be prepared for the box-type conductor development not to be successful.
This aligns with our development roadmap: the box-type conductor remains the primary focus, with parallel R&D on backup solutions.
SYSTEM MAGNET

## Slide 141: Finding and comments on Draft v0.4.1
C-B-10-5: The mechanical stress analysis is advanced. However, the results have not been clear enough and the mechanical safety design has not been clearly described. It would be very important to determine necessary mechanical strength of the Al-stabilized superconductor with the box-type design and to be consistent with the performance test results from the conductor development. It must be critically evaluated.
We have updated the coil stress-analysis results and added the average stresses for every component within the cable. The peak stresses in all cable parts are now under control, each carrying a one-third safety margin. Mechanical safety: A full-scale conductor mechanical test campaign is underway; results will update the FEA model and be documented in 2025.
C-B-10-6: The SC coil winding design with a four-layer coil is to be wound by using an ‘inner coil winding technology’, and it sounds reasonable and promising. The demonstration by using a dummy conductor has been successfully made in cooperation with industry. It needs to be recognized as a preparation step for a SC model coil to be developed and SC performance to be demonstrated.
Establishing a scaled model coil is really a necessary step before the processing of the detector magnet, and we will take this important process into consideration in our subsequent planning using 100 m full-scale conductor.
C-B-10-7: The quench protection and safety design is based on two technologies of ‘partial energy extraction’ by using an external dump resister and ‘quench back’ inductively induced by the external support cylinder, functioning a single-turn secondary circuit. On the other hand, an expected energy extraction fraction of > 80% may need to be confirmed or updated. If the coil temperature would be increased to ~ 60 K on average after switching off the circuit, a half of the stored energy might be already dumped in the coil. The energy extraction ration would be more reasonable with a level of ~ 50%. The quench protection study may be further improved.
We will optimize the quench-protection system and refine the simulation process to confirm the reliability of the results. At the same time, we will adjust the quench protection in line with the progress of conductor development.
SYSTEM MAGNET

## Slide 142: Recommendation on Draft v0.4.1
C-B-10-8: Proceed the ‘box-type’ Al-stabilized superconductor as the highest priority, aiming to demonstrate full-scale conductor fabrication, and to verify the superconducting and mechanical performance that meets the required safety margins. It will be important to demonstrate a sufficiently continuous length, at least, enabling to realize a superconducting model coil to be fabricated and the superconducting magnet performance demonstration. In parallel, backup solutions shall be continued to prepare for the case of the ‘box-type’ not to be practical.
This aligns with our development roadmap: the box-type conductor remains the primary focus, with parallel R&D on backup solutions.
C-B-10-9: Advance/improve the quench protection and safety study that reach a reasonable estimate for a balance of the coil temperature rise after the quench and the energy extraction ratio. It is a fundamental balance to be well understood.
We will optimize the quench-protection system and refine the simulation process to confirm the reliability of the results. At the same time, we will adjust the quench protection in line with the progress of conductor development.
SYSTEM MAGNET

## Slide 143: ELECTRONICS

## Slide 144: Findings
F-A-11-1: The reference TDR provides a clear and accurate description of all on-detector and off-detector electronic systems required for the readout of the various detectors, along with their associated 17 requirements—many of which are critical to the overall experiment performance. Since the last committee meeting, several important decisions have been taken, most notably the adoption of full data transmission (streamed readout), which is now firmly established.
F-A-11-2: The nine different ASICs, currently at various stages of development, are clearly summarized, with an assessment of their maturity ranging from level 2 (initial design) to level 4 (prototyped) on a 1-to-5 scale. Three of these are common service ASICs used for power distribution and data transmission. The required manpower for the ASIC developments and future steps is well detailed and appears realistic.
F-A-11-3: The shared back-end architecture and power distribution scheme are also well described, building upon the solid experience gained from large-scale operational experiments such as JUNO.
ELECTRONICS

## Slide 145: Comments
The committee is very impressed with the progress made and the thorough implementation of previous recommendations. In particular, the decision to adopt a data streaming readout is a major step forward, significantly impacting the ASIC architecture. The handling of data rates and the application of safety margins are well managed.
C-A-11-1: The ASICs are well documented, and several key building blocks have already been successfully prototyped, demonstrating the strength and efficiency of the teams involved. The progress is remarkable; however, as the complexity of the chips increases, substantial work still lies ahead. It would be helpful for each ASIC to clearly identify the lead responsible person(s) and the contributors to the various blocks and development tasks.
  The responsible persons have been assigned for each new chip.
  Data Link: FEDA, FEDI, OAT – Di Guo (CCNU)
  Power: PAL – Jia Wang (NPU)
  SiPM – SIPAC (ECAL, HCAL, MUON): Huaishen Li (IHEP)
  OTK – LATRIC: Xiongbo Yan (IHEP)
  For existing chips, development will follow with the current team:
  VTX - Taichupix: Wei Wei (IHEP)
  TPC – TEPIX: Zhi Deng (THU)
ELECTRONICS

## Slide 146: Comments
C-A-11-2: Verification of the ASICs is critical, especially for large chips that include substantial digital logic (e.g., tracking ASICs). Verification should be conducted by individuals independent of the design teams and should use state-of-the-art tools and methodologies.
C-A-11-3: Testing of ASICs can never be too extensive: it should involve not only the designers but also multiple user teams wherever possible. Chips should be characterized across a range of temperatures and supply voltages to detect weaknesses early. As larger volumes become available, systematic analysis of failing or underperforming chips (“bad chips”) will be essential.
  Part of the verification has been done during the design phase by the design team. However, more verification work should be done while lack of manpower
  Independent verification work will be done during the test phase by independent teams, for which it is not so high-level tech required
C-A-11-4: From a stylistic standpoint, the SIPAC chip (common to three detectors) is extensively described within this chapter, while other ASICs are detailed within each detector’s respective section. For improved readability, it may be preferable to move the SIPAC description to the calorimeter section, retaining in the electronics chapter only a general overview of all ASICs and a detailed view of the shared service chips (e.g., for power and data transmission). For the front-end ASICs, detailed schematics could be reduced in favour of presenting more relevant simulation results, such as pulse shapes or noise versus input capacitance.
  We have done exactly as suggested.
  SIPAC part has been moved into the ECAL chapter, and shrunk for the length and details, only the main specs and scheme were kept.
ELECTRONICS

## Slide 147: Comments
C-A-11-5: The back-end electronics are comprehensively described and benefit from the team's previous experience with large-scale systems. However, the availability of high-performance FPGAs could pose a risk. Maintaining a dual-source strategy for critical components would be a prudent mitigation measure.
  Yes, that is also our current idea. We have kept eyes on backup resources for the key components. Almost all of them have found extra vendors or substitutes.
C-A-11-6: Identify the teams responsible for testing each ASIC, ensuring they are different from the design teams. Bugs are often discovered late in development, and broader involvement in chip evaluation improves characterization and helps uncover potential weaknesses.
  See the answer for the comment 1.
  We have assigned the teams and responsible persons for each chip.
C-A-11-7: Begin detector testing with available “sister chips” where feasible. This parallel approach can advance both detector and chip development and provide valuable benchmarks for comparison.
  This is the idea during previous R&D for detector prototypes, like for the ECAL.
  We will follow this way for the future R&D for the early prototypes for sub-detectors. “Sister chips” (like the ROC chip series) will be evaluated to make the chip development in parallel (to some extent) with the detector R&D.
ELECTRONICS

## Slide 148: Recommendations
R-A-11-1: Minimize power dissipation at every stage. Each milliwatt of consumption should be justified by a specific performance requirement.
  We are continuing optimize the scheme.
  Currently we have several consideration:
    Optimize the OTK detector design, so that the power may be saved.
    Optimize the electronics design for HCAL, according to the new design from the detector side. Channels will be saved, and frontend will be reconsidered with less dynamic requirements.
R-A-11-2: Proceed with system development in parallel with chip development. System-level issues can often be addressed early at the chip design stage if identified promptly.
  We will keep that in mind.
  Actually we already have a prototype design of the common backend board, which works well and has been verified. We will optimize the design for the following prototypes of sub-detector R&D.
ELECTRONICS

## Slide 149: Comments on Draft v0.4
C-B-11-1: However, I regret that the overview of the ASICs has also been removed and it only figures as the "next steps" in section 11.10, squeezed in a table which is actually difficult to read. The previous version which was detailing the different ASICs, their number, number of channels, level of maturity, existence of a "sister chip"... was very important and helpful. As in many experiments, they are likely to be a corner stone of the project and they should not become stumble stones !
  We have added this table in the Ref-TDR, to describe the maturity of all related ASICs and similar chips. The table can be found below:
ELECTRONICS

## Slide 150: TDAQ

## Slide 151: Findings
F-A-12-1: The TDAQ system is based on the full transmission of data from the front-end electronics to the back-end electronics (BEE), with the trigger operating at the BEE level. Data rates from each subsystem are provided for the different CEPC operational scenarios; however, the underlying assumptions behind these estimates should be discussed more explicitly in some cases.
F-A-12-2: The TPC represents a special case due to its long drift time, and a more detailed discussion of the implications of this extended integration time is necessary.
F-A-12-3: The first stage of the trigger is planned to operate on the BEE boards, generating trigger primitives from the calorimeter and muon systems, with the possible addition of primitives for a track trigger. The trigger architecture has evolved to include BEE-resident primitive algorithms alongside a three-layer L1 hardware system. The CEPC team has demonstrated that simple requirements on calorimeter and muon primitives effectively reduce background rates while preserving high efficiency for the primary physics processes of interest, addressing a key recommendation from the previous review.
F-A-12-4: It was noted that some exploratory work on a fast-track trigger has been conducted, though no results were presented. A silicon-based fast track trigger remains of high interest, as it would complement calorimeter and muon primitives and provide stronger separation between collision and non-collision backgrounds.
F-A-12-5: This review focuses primarily on the ZH production and low-luminosity Z-pole running planned for the first ~10 years of CEPC operations. Nevertheless, the overall TDAQ design appears appropriate for other planned running modes as well.
F-A-12-6: The Ref-TDR chapter should first describe the proposed baseline trigger system before presenting proof-of-concept studies for the trigger primitive algorithms.
TDAQ

## Slide 152: Comments
C-A-12-1: The background event rate and event size are critical inputs to defining the TDAQ system dataflow requirements. Assumptions used should be explicitly stated and consistently referenced across all relevant chapters (some inconsistencies were noted in the current draft).
>>The detail information for the event rate and event size are summarized in table 12.3 and 12.4. The event size is calculated based on the information from the electronic chapter, and the time windows for each sub-detector.
TDAQ

## Slide 153: Comments
C-A-12-2: The safety factors applied in system design should be made explicit, clearly motivated, and documented to allow for easy updates and assessment of their impact on different subsystems.
>>A safety factor "1.5" is applied when estimating the event size, mentioned in section 11.2: "During the calculation, a safety factor of 1.5 was considered for the background rate.". Another safety factor "10" is applied when estimating the trigger efficiency, as mentioned in section 12.4.1: "For both the Higgs and the Z mode, each beam background event includes 10 bunch crossings, corresponding to a safety factor of 10.“
C-A-12-3: Section 12.4 should be moved after Section 12.6 to improve the logical flow of the chapter.
>>Done.
TDAQ

## Slide 154: Recommendations
R-A-12-1: Clearly motivate the data bandwidth requirements into the L1 trigger, between trigger layers, and specify the number of links needed. Provide details on the expected trigger primitives from each BEE type and the associated data volumes. Similarly, describe the output products of the local trigger layers and provide data bandwidth estimates into the global trigger layer.
R-A-12-2: Update the design of the common trigger board—particularly the bandwidth and input link capacities from the BEEs—to reflect the information presented. Explain the rationale behind the estimated number of trigger boards required at each of the three L1 levels.
TDAQ
>> These part is added in "resource estimation" section as following. In the resource estimation, the trigger primitives for ITK, OTK, ECAL and HCAL are cluster information, which includes cluster position, size, energy information and time information; The muon detector provides hit counting information, including hits number, hit position and timing information. For TPC detector participating in trigger further research is needed. Currently only preliminary estimates are made based on its’ data volume. The estimation of global trigger part of each detector is based on the divisions of sector. All trigger primitives information is obtained from off detector electronics. Trigger primitive transmission to trigger system from back end electronics is based on 10Gbps line rate, 8Gbps bandwidth removing the encoding overhead of 8B/10B. In the Level-1 trigger system, 16 channels of optical will be used for connection with off-detector electronic boards or previous level trigger boards. Based on the data volume of trigger information which calculated based on background simulation of each detector, trigger optical links to each detector’s sub-trigger and number of trigger boards can be estimated. In trigger system installation, one ATCA crate can install up to 10 trigger boards and at least one DCTD board. According to this calculation approach, a rough scale of trigger system was estimated as shown in table 12.5.

## Slide 155: Recommendations
R-A-12-3: Provide a detailed description of how the TPC data stream will be handled, especially considering its long drift times.
>>A new paragraph for the TPC data stream detail information is added in section 12.1.2. It can still utilize L1 to pack TPC data whatever all raw data need be read out with more than 30 kHz L1. Data is packed in blocks by multiple Trigger ID for parallel processing. TPC data is easily located via Trigger ID, enabling joint analysis with other detectors sharing the same trigger.
R-A-12-4: Continue exploring the development of a fast-track trigger, emphasizing its potential to reduce background rates and ease the load on the HLT.
>>A preliminary track trigger study is added in Section 12.4.2.1. The current results doesn't improvement the trigger selection, further study need be done in future.
TDAQ

## Slide 156: Recommendations
R-A-12-5: Demonstrate the necessity for RDMA technology in transferring data from the BEE to the HLT, including a justification based on system performance needs.
>> Currently, CEPC's baseline design is to use the traditional TCP protocol for data transfer from the BEE to the HLT, while RDMA is primarily being considered as a research direction. This consideration is mainly based on the following points:
  1.RDMA supports direct memory access, significantly reducing CPU utilization during data transfer. This helps to overcome the performance bottlenecks of traditional protocols and meet the demands of future high-throughput data transmission (e.g., for high-luminosity Z mode).
  2.Validating RDMA on the existing readout electronics platform in advance can prevent large-scale hardware upgrades triggered by data volume growth, thereby lowering the cost and technical risks of future system upgrades.
  3.Applying RDMA in the high-level trigger system can reduce CPU load and interrupt overhead during data transmission, improve the efficiency of trigger algorithms, and lay the technical foundation for future one-to-many data distribution and real-time event assembly.
In summary, although the current TCP-based solution can already meet present requirements, early research into RDMA is a forward-looking strategy that can meet the demands of future experiments for high-performance data transmission, aligning with the development trends of leading international particle physics projects.
TDAQ

## Slide 157: Recommendations
R-A-12-6: Describe the system’s strategy for handling data flow in the event of full buffers to avoid data loss or system instability.
>> This added in 12.2.4. BEE should generate full signal when buffer full and feedback to TCDS, TCDS will mask the L1 signal until full or error signals cleared to avoid data overwriting in data packing buffer in DAQ readout.
R-A-12-7: Evaluate whether the L1 trigger hierarchy could be simplified, for example by collapsing it into a multiplexer layer feeding directly into boards handling full global trigger primitives.
>> Fast trigger and Gobal trigger are combined as one layer according to the suggestion, see the Fig12.2. Trigger primitive generation is divided into local and global two layers one reason is that it is restricted by common trigger board IO number and FPGA resources we can purchase. Structure maybe optimized with the development of FPGA IO and resources we can buy in the future.
R-A-12-8: Categorize the event rates into physics signals (e.g., ZH production, two- and four-fermion processes, Bhabha scattering), gamma-gamma interactions, beam-related backgrounds. The first category aims at full trigger efficiency, the second one is potentially of some interest but with lower priority and the last one must be reduced as much as possible.
>>In table 12.1 and 12.2, the physical processes are categorized into two group "high priority" and "low priority". All the gamma-gamma interactions are under "low priority".
TDAQ

## Slide 158: Recommendations
TDAQ
R-A-12-9: Analyze the beam background distributions as functions of energy, multiplicity, and polar/azimuthal angle to optimize background suppression algorithms. In particular, investigate the origin of background peaks such as the one observed at ~7 GeV in the ECAL endcap.
>>We studied the beam background energy distribution as function of polar/azimuthal angle and the background component(Beam-Gas Bremsstrahlung, Beam-Gas Coulomb, Pair Production...), and notice that the background peak is attributed to significant energy deposition in the supercells adjacent to the beam pipe in the endcap region from the Pair Production.
The first figure presents the average energy deposition across ECal Endcap modules for 10,000 beam background events. The second plot illustrates the average energy deposition per Endcap supercell across distinct θ (polar angle). As shown in the first plot, about 6 GeV energy deposition is observed in the supercells around the center.
To enhance background suppression, an angle-dependent energy thresholds will be explored in the R&D with better understanding of the beam background simulation.

## Slide 159: Comments from Bob on Draft v0.4
C-B-12-1: It would help the reader to have stated early in the chapter the timelines associated with different decisions. For example, at lines 10835-10837 additional R&D is listed as being necessary. By when does this R&D need to be completed? Similar comment for lines 10875-10876. This arises again at lines 10944-10947. There is some discussion of timelines at the end of the chapter (lines 11836-11838); I suggest this timeline is referred to earlier.
  This version of ref-TDR is aiming at Higgs and low lumi-Z modes. Current there is no technical bottleneck for CEPC Phase-I TDAQ. High lumi-Z mode is Phase-II of CEPC. The requirement of technical for High lumi-Z is not included in this version.
C-B-12-2: In fact, it might be good to start the chapter with the summary and then give the details.
  Add a summary section in overview
TDAQ

## Slide 160: Comments from Bob on Draft v0.4
C-B-12-3: Some minor things I noticed as I read:
C-B-12-3 -1: 10849-10852: not sure what is being said here
->In the high luminosity Z mode, the data volume of the detector will be significantly increased. The \gls{TDAQ} system should have scalability to cope with such situations.
C-B-12-3 -2: 10890-10893: not sure what is being said here
->Most of the \gls{L1} trigger algorithm will be running on \gls{FPGA} farm, which has the advantage of low latency and real time. As the principle of trigger is to keep all the good events and reduce the background events to acceptable level of \gls{DAQ} readout, it is challenging to maintain the data purity.
C-B-12-3 -3: 10897-10900: repeated sentence.
Deleted the repeat sentence
C-B-12-3 -4: 10916-10917: trails = tracks?
trails -> tracks
C-B-12-3 -5: 10922-10924: not sure what is being said here
->The combination of these physical objects can be used to reconstruct the particle flow object and further suppress the background process.
C-B-12-3 -6: 11090-11091: meaning unclear
Global trigger resource allocations for each subsystem employ sector-based segmentation as the foundational calculation method. For global track trigger, Calorimeter track finding, and Global trigger, 60° will be defined as a sector. For the energy trigger of the calorimeter, 120° will be defined as a sector.
C-B-12-3 -7: 11813-11814: text is garbled, not clear what is meant
->Following the recent update results of sub-detector design and simulation, significant progress in the technical development of the \gls{TDAQ} and online systems has been achieved.
TDAQ

## Slide 161: SOFTWARE AND COMPUTING

## Slide 162: Findings
F-A-13-1: The review team acknowledges the very good progress made in software and computing since the last report. Almost all previous recommendations have been successfully addressed by the collaboration. The current status and advancements are thoroughly documented in the Ref-TDR and were presented and discussed during a dedicated session at this review. Overall, the Offline Software and Computing activities are in a strong position, the outlined approach appears highly feasible, and no significant challenges or showstoppers have been identified.
F-A-13-2: The offline software, CEPCSW, is based on the international Key4hep project, which is used by all future collider projects. CEPC is making significant and well-aligned contributions to this effort within the global community. In terms of computing, CEPC leverages established tools and methodologies developed for the LHC. The current computing model follows the traditional Tier structure, though a transition to a more efficient model is envisaged, aligned with broader community developments.
F-A-13-3: A detailed simulation model of the reference detector has been implemented. For track reconstruction, the collaboration is currently adapting tools and algorithms from the linear collider community while also developing more advanced techniques. A new particle flow algorithm, CyberPFA, has been developed, particularly to meet the challenges posed by the novel crystal ECAL design. This builds on prior work from the HCal side and has been successfully integrated into CyberPFA. The full simulation and reconstruction framework has been employed to produce a comprehensive set of technical performance plots, demonstrating that the detector concept, combined with sophisticated algorithms, can meet the required physics performance targets.
F-A-13-4: The offline software has also been used to estimate the computing needs, based on reasonable— though not highly refined—assumptions regarding data rates, data volumes, processing schedules, and methodologies. However, the estimates also assume optimistic developments in CPU performance and cost trends over the next decade.
SOFTWARE AND COMPUTING

## Slide 163: Comments
C-A-13-1: The corresponding Ref-TDR chapter would benefit from some revisions: reducing the length of more general descriptive sections and expanding technical details where appropriate.
The total number of pages has been reduced from 62 to 41, plus an additional 4 pages for citations.
  C-A-13-2: Some important aspects of the planned computing model remain insufficiently detailed, such as the structure for user analyses, data distribution strategies, open data policies, and long-term data preservation plans.
  Structure for user analyses, data distribution strategies:
  Line 1064-1071: An efficient data distribution strategy within the data model is essential for optimizing data storage, access, and processing. Raw data will reside in central storage, while reconstructed data (RecData), simulation data (SimData), and analysis data (AnaData) will be distributed across Tier-1 storage. These datasets will be accessible on demand through a tiered storage and caching system, ensuring streamlined availability for various sites. A progressive reduction of the data format for user analysis, coupled with corresponding analysis facilities in \gls{Grid} and non-\gls{Grid} resources, creates a robust structure that enables fast and reliable user analyses.
  Open data policies: A new section of 13.8 Open data was added.
  Long-term data preservation plans: A new section of 13.9 Long term data preservation was added.
C-A-13-3: The development of CyberPFA is a significant achievement and positions the collaboration as a leader in custom in-house algorithm development. However, the degree of reliance on existing tools like PandoraPFA and ArborPFA needs to be better explained and justified.
Line 533-536: The experience of clustering in high granularity calorimeter and integrating track and calorimeter information from \pandorapfa and Arbor are also adopted in \cyberpfa for the reconstruction in traditional high granularity \gls{HCAL} and optimal performance.
SOFTWARE AND COMPUTING

## Slide 164: Comments
C-A-13-4: While the event data model (EDM4hep) is well established, more detailed data formats for reduced, compact data levels (e.g., various stages of AODs) are not yet clearly defined.
Line 981-984:
\item AnaData (analysis data): which is a summary of the reconstructed event, and contains sufficient information for common analyses
\item TagData (event tag): summary of some general features of the event, allowing rapid access to the events and performing fast selection
Line 988-990:
AnaData and TagData are expected to be relatively smaller in scale compared to RecData. Given their importance for data analysis, they will be defined as soon as event-level reconstruction, following data reconstruction in sub-detectors, becomes available.
SOFTWARE AND COMPUTING

## Slide 165: Comments
C-A-13-5: The costs associated with the required computing infrastructure—such as whether a new data center will be necessary—are not discussed in the Ref-TDR.
Described in 13.10.4 Smart data center infrastructure
C-A-13-6: While future technologies such as quantum computing, machine learning, and AI are mentioned, their potential roles and the motivation for pursuing them should be more clearly articulated, with better-defined staging scenarios
Line 723-736:
The trend in computing hardware is shifting toward increased CPU cores and more diverse architectures, including \gls{GPU}, FPGAs, and other accelerators. Machine learning plays a crucial role in high-energy physics experiments. Consequently, the development of software capable of efficiently handling simultaneous computations and leveraging machine learning techniques to enhance data processing and analysis has become an increasingly important topic.During $Z$-pole operation at CEPC, computing demands are expected to reach the exabyte scale, posing technical challenges comparable to those encountered at the High-Luminosity Large Hadron Collider. Advances in artificial intelligence, along with the integration of concurrent and heterogeneous computing, will form the operational backbone of future collider experiments. Meanwhile, quantum computing and its associated algorithmic frameworks present a potential paradigm shift in addressing these challenges, offering a promising—though ambitious—solution for the CEPC initiative.This section will present relevant research efforts exploring these advancements.
SOFTWARE AND COMPUTING

## Slide 166: Recommendations
R-A-13-1: Further develop and consolidate the detailed simulation model and reconstruction framework, with particular attention to:
  R-A-13-1-1: Adding realistic estimates for detector imperfections, such as gaps or insensitive material from cables and services, to the simulation model.
  Line 163-167:
  \ddhep can also be used to represent more realistic geometry, rather than idealized models, by integrating alignment and calibration data. Misalignment corrections can be applied to reflect actual detector shifts, and calibration constants are included to ensure accurate detector responses. By incorporating these elements, DD4hep offers a comprehensive and precise detector description for the experiment.
  R-A-13-1-2: Performing detailed studies of the CyberPFA performance, including jet energy resolution for light-quark dijet events, single particle responses, neutral hadrons, and neutrino energy measurements in b-decays.
  presented in Chapter 15
  R-A-13-1-3: Studying the impact of misalignment on tracking performance.
  discussed in Chapter 15
R-A-13-2: Develop a systematic performance monitoring framework, organized around a set of benchmark figures and analyses that qualify simulation and reconstruction quality. Each sub-detector should define its own "detector performance" plots, while a standard set of global physics performance plots should be maintained to validate software improvements.
Line 217-219:
\item Release validation: Large-scale data production is manually triggered using predefined workflows, which are submitted to local or distributed computing systems. Key physical quantities are then compared against standard distributions, providing a clear reference for evaluating detector performance.
SOFTWARE AND COMPUTING

## Slide 167: Recommendations
R-A-13-3: Once consolidated, establish a clear reference for detector performance within the RefTDR, ensuring that future detector and physics performance studies use consistent versions and conditions (e.g., ensuring that jet resolution and b-tagging results are presented with the same software version and setup).
  Performance studies will be conducted using a fixed software release, as agreed upon with the physics group.
  R-A-13-4: Develop a more detailed and phased estimate of computing needs during the R&D and preparation phases, for example by organizing a sequence of increasingly challenging "data challenges." These would also serve as benchmarks for assessing the maturity of the offline software and computing infrastructure.
  Line 1023-1027: The allocation of computational and storage resources is divided into three distinct phases: 2\% during the TDR phase, 10\% during the construction phase, and 100\% during the data-taking phase. The detailed estimate of computing resources will be obtained through a series of increasingly complex data challenges, tailored specifically for the experiment.
SOFTWARE AND COMPUTING

## Slide 168: Comments on Draft v0.4.1
C-B-13-1: The Offline Software and Computing section of the TDR has been significantly improved wrt. version from the April review meeting at IHEP. Manyn of the comments have been well addressed, e.g. the overall length is reduced with replacing more general sections with technical descriptions, open data policies and long term data preservation plans have been added, the relation of CyberPFA to PandoraPFA is clarified.
C-B-13-2: The CEPC Software and Computing group has also started to address the recommendations made in the previous review, e.g. by developing a more detailed and phased computing resource needs and the planing of dedicated computing challenges to monitor the progeress.
A detailed data challenge plan has been incorporated into Section 13.6.2:
  “Detailed estimates of computing resource requirements will be obtained through a series of Data Challenges—large-scale Monte Carlo productions designed to validate computational needs before building the final system. These challenges will be conducted in multiple rounds, each increasing in complexity and data volume to more accurately simulate future CEPC operational conditions. Early stages will focus on prototype tests of offline software, profiling CPU, memory and storage demands for core algorithms, followed by full-chain processing from simulation to reconstruction, with particular emphasis on bottleneck and performance of key workflows. As the Data Challenges progress, later rounds will emphasize the generation of approximately 1 million Higgs events, complemented by inclusive Monte Carlo datasets that simulate one month of low-luminosity Z data collection. Those rounds will incorporate Grid computing integration, significantly enhancing the realism of both data processing workflows and analysis pipelines.
  The final phase of the program will feature collaborative efforts with the CEPC international sites, coordinated through a Common Computing Readiness Test. This structured approach ensures comprehensive validation of the computing model, overall operational readiness, paving the way for the full-scale deployment of the CEPC.“
SOFTWARE AND COMPUTING

## Slide 169: Comments on Draft v0.4.1
C-B-13-3: At the same time a number of recommendations have not yet been addressed, e.g. performing detailed studies of the CyberPFA performance, including jet energy resolution for light-quark dijet events etc. We encourage the group to continue to pursue these recommendations, well aware that not all will be possible before handing in the TDR.
we have already completed the jet energy resolution study of light-quark jet events from e+e-->ZH process, the dependence of JER on energy, costheta and phi are provided. Now we are working on the processes of e+e--> di-quark jets, and other single particles are IDRC recommended.
SOFTWARE AND COMPUTING

## Slide 170: MECHANICAL INTEGRATION

## Slide 171: Findings
F-A-14-1: Significant progress has been made since the last review in the mechanical design of the CEPC reference detector. The weight and boundary dimensions of each sub-detector are now well defined in the Ref-TDR. Clearances between sub-detectors are typically around 10 mm, which appears adequate to ensure a seamless installation sequence. However, in the critical interface between the integrated beam-pipe/vertex detector assembly and the ITK, the clearance is reduced to just 2 mm.
F-A-14-2: The issue of sagging of the magnet yoke under its own weight has been effectively addressed. The introduction of end-flanges satisfactorily mitigates the problem, reducing the sagging from about 13 mm to within the required limit of less than 1 mm.
F-A-14-3: The installation sequence has been carefully developed. The core shaft designed for the installation of the barrel HCAL and ECAL detectors appears adequate, as does the cantilever system proposed for installing the TPC, ITK, and beam-pipe assembly (including the Vertex and LumiCal detectors). The animations presented clearly illustrated the feasibility and logic of the installation process.
MECHANICAL INTEGRATION

## Slide 172: Comments
C-A-14-1: The mechanical connection structures between sub-detectors are well designed, considering the specific requirements of each system. However, the methods by which these structures will achieve the precise alignment of the sub-detectors are only briefly described in the current Ref- TDR. Reference is made to an alignment control network that would provide positional benchmarks, but further details would strengthen the documentation.
We have further optimized the connection structures between sub-detectors to ensure reliable mechanical connections while minimizing deformation that could affect installation accuracy. The relevant details and FEA have been added in the updated TDR documentation. Additionally, Section 14.4.1 Configuration of the experimental hall introduces the plan of the survey network in the experimental hall. During detector installation, in addition to relying on survey devices for positioning, we will also implement measures in the installation tooling and connection structures to enhance positioning accuracy and assembly efficiency. These aspects will be further refined and elaborated in next work.
C-A-14-2: Significant progress has also been made in designing the auxiliary facilities, which include the air- conditioning system for the experimental hall, gas and cooling systems for the various sub- detectors, power distribution and electronics systems, the cryogenic system for the superconducting magnet, and the hydraulic pump station used to move the detector to the collision point.
Next we will proceed with optimizing the spatial layout of the main hall and auxiliary halls, as well as the routing of pipeline systems, to ensure clear coordination with the accelerator in terms of space and facility usage. The layout and utilization of the ground hall will also be taken into consideration in next-stage planning.
MECHANICAL INTEGRATION

## Slide 173: Recommendations
R-A-14-1: Further refine the routing plans for cables and services, especially in the critical interface areas between sub-detectors and through the barrel-to-endcap transitions to the outside of the detector and the auxiliary facilities.
We have supplemented the service section 14.3.2, describes the external service routing of sub-detectors. These services are still being finalized and optimized. The routing scheme has been studied, and we have checked and verified that the allocated space is sufficient. Preliminary interconnection schemes have been studied for cable routing from the yoke to the electronics room.
R-A-14-2: Pay particular attention to the air-cooling and service routing for the vertex detector, where space within the beam-pipe assembly is extremely limited. It is essential to verify that sufficient space is available to ensure the proper functionality of the air-cooling system, without compromising reliability or maintenance access.
Internal cabling and piping of sub-detectors have been studied, with the simulation and testing results presented in their dedicated chapters.
C-A-14-3: Regarding refrigerant choice for the other sub-detectors:
  C-A-14-3-1: Supercritical CO₂ (sCO₂) could be considered as an alternative to water. As a single-phase refrigerant, it is user-friendly for complex, multi-branch systems. Like water, it is non-toxic, non-flammable, and readily available; unlike water, it is dielectric and harmless to electronics in case of leaks. While sCO₂ brings operational advantages, these must be weighed against some disadvantages (see appendix for details).
  C-A-14-3-2: Boiling CO₂ (subcritical, operating around 20–25 °C) is also simpler than twophase CO₂ systems, which require more complex design, maintenance, and expert operation. Thus, unless two-phase cooling is clearly necessary, a simple and efficient single-phase refrigerant (such as water or supercritical CO₂) is preferable
We are fully aware of the technical complexity of this option. Preliminary research has been initiated for some sub-detectors, while further in-depth studies and tests will be planed to demonstrate both the feasibility and safety of it.
MECHANICAL INTEGRATION

## Slide 174: Comments in backup
Detailed Considerations on the Advantages and Disadvantages of a Refrigeration System Based on Supercritical CO₂ (sCO₂) Compared to Water.
Advantages of sCO₂ Refrigeration:
sCO₂ is fully dielectric, making it inherently safer for use near sensitive electronics.
sCO₂ requires much smaller piping for the same flow rates due to its lower viscosity and higher operating pressure.
It has a higher heat transfer coefficient, provided that operational conditions (temperature and pressure) are well optimized.
The high fluid pressure allows for larger acceptable pressure drops in the heat exchanger (e.g., in the detector stave’s tubes). With optimized heat exchanger design, it is theoretically possible to induce the necessary pressure drops to maintain nearly isothermal conditions—achieving single-phase flow with the same inlet and outlet temperatures while efficiently removing heat.
Experience shows that low-pressure circuits tend to develop leaks over time due to lower quality construction standards, while high-pressure systems, requiring stricter quality controls, are more robust. This leads to lower long-term maintenance costs (both financial and operational).
Disadvantages of sCO₂ Refrigeration:
High-pressure systems are generally estimated to be 15–20% more expensive than equivalent low-pressure systems.
Operation at 30–35 °C might impact surrounding systems and needs to be considered during integration.
A dedicated pressure control component ("bladder" or similar device) is required to maintain stable system pressure.
Depending on the system volume, there are potential safety issues (especially personnel safety) associated with storing large quantities of CO₂ in confined underground spaces.
The combined effects of all parameters (temperature, pressure, flow rates) on the thermal fluidic behaviour of supercritical CO₂ are not yet fully understood. However, significant research and development work in this area is currently ongoing
MECHANICAL INTEGRATION

## Slide 175: Comments on Draft v0.4.1
C-B-14-1: However, unless I have overlooked something, the two main recommendations we made in April the 2nd review in April have been addressed yet:
  C-B-14-1-1: Refine the routing plans for cables and services, especially in the critical interface areas between sub-detectors and through the barrel-to-endcap transitions to the outside of the detector and the auxiliary facilities.
  C-B-14-1-2: Pay particular attention to the air-cooling and service routing for the vertex detector, where space within the beam-pipe assembly is extremely limited. It is essential to verify that sufficient space is available to ensure the proper functionality of the air-cooling system, without compromising reliability or maintenance access.
C-B-14-2: They might not have had the time to do so yet, but I regret that in the to-do list at the beginning of the document it only says:
  C-B-14-2-1: Mechanics and integration is mostly done, but requires improvements to the text, and cross references, and minor changes to increase plot sizes. No new studies are planned to be added.
C-B-14-3: It would be important that they take at least note of the comment and indicate how they intend to address the topic in the future. If they could make at least an estimation that routing and cables and services works on paper, it would already be good.
I have no line comments to provide yet and would prefer to do so only at a later stage, when the document has undergone further editing.
  We have studied the routing and service, and added the section 14.3.2 service in the new TDR version. These services are still being finalized and optimized. The routing scheme has been studied, and we have checked and verified that the allocated space is sufficient. The Internal cabling and piping of sub-detectors are presented in their dedicated chapters.
MECHANICAL INTEGRATION

## Slide 176: DETECTOR PEREORMANCE

## Slide 177: Findings
Although further improvements are possible and recommended, the collaboration’s response to the previous evaluation has been excellent and deserves recognition. The detector software, particularly the simulation component, now enables comprehensive studies of detector performance and physics benchmarks. Several design decisions have been made based on both detector and physics performance criteria. This progress has allowed the definition of a baseline detector concept. While still perfectible and requiring further detailed investigation, this is a significant and commendable step forward. The scope of physics performance studies has broadened considerably since the last assessment. The range of channels explored and the methodologies employed respond well to previous recommendations and collectively address key detector areas and primary physics topics.
DETECTOR PEREORMANCE

## Slide 178: Comments
The Ref-TDR text could be improved and shortened by presenting certain aspects (e.g., particle identification, jet studies) more concisely, while still ensuring that the algorithms are described clearly and transparently. shortened and reorganized
Many additional physics analyses are planned. Their presentation and motivation should be aligned with the main purpose of this document: demonstrating the feasibility and physics potential of the reference detector. several more analyses implemented and included since last review
Algorithms for particle identification, jet tagging, etc., are mentioned in multiple places and are still evolving. A systematic approach should be adopted to define and refer to these algorithms consistently across the document. restructured, and referencing properly done.
DETECTOR PEREORMANCE

## Slide 179: Recommendations
The studies encompass both physics benchmarks and detector performance metrics. A clearer distinction between these two aspects would be beneficial. The editorial team is encouraged to organize the content into:
    Sub-detector technical performance — technical performance figures (used for sub-detector configuration decisions) should be placed in the relevant sub-detector chapters.
      Single photon reconstruction efficiency and resolutions now only shown in ECAL chapter
      Tracker impact parameters now appear only in Vertex chapter
    Physics-related performance — to demonstrate baseline detector capabilities for physics analyses (e.g., particle identification, global variables like ETmiss), and to present the physics analyses themselves. This should be the main focus of the performance chapter.
      Full system tracking, PID (TPC+TOF) are also in Silicon chapter: duplicated plots removed in perf. chapter
The physics benchmarks listed in Table 15.3 are intended to demonstrate the performance of the reference detector. Each listed study should be discussed explicitly, explaining the role of the detector performance in achieving the result. Currently, only a subset (e.g., Higgs recoil mass, Higgs branching ratios, weak mixing angle from Z→μμ) are covered. Other channels (exotic Higgs decays, LLPs, CVP in D-meson decays) should also be summarized, possibly in a summary table. More channels (being) added
The technical improvements planned for more detailed simulation (noise, event overlap, misalignments, calibration effects) should be pursued, and their impact on physics performance carefully demonstrated.
  Noise checked (negligible), event overlap evaluated on tracking (5% worse resolution) Studies of event overlap in calo, misalignment effects underway
DETECTOR PEREORMANCE

## Slide 180: Recommendations
Several specific technical issues should be clarified and potentially improved:
The photon efficiency behaviour around E = 1 GeV appears unusual and should be either justified or corrected, as it could impact EM/hadronic separation in PFA and influence missing energy and mass resolution. discussed in ECAL chapter
Jet energy resolution for light quarks should be studied more systematically and used as a benchmark metric.
Missing energy reconstruction should be further investigated, particularly in b- and c-jet events with tagged leptons and in BSM channels with large ETmiss. done, a section on missing E/M added
(Longer term) Tracking performance should be tested in exotic scenarios, such as long-lived particles.
(If possible) Include photon conversions in tracking studies as a material probe and describe their treatment in PFA. added material budget plot and conversion rate vs. cos(theta)
Particle identification needs further organization and development:
  Currently, simple cuts are applied; more sophisticated algorithms (including ML-based methods) should be considered, balancing the ambition against available time and resources. A simpler multivariate approach could serve as an intermediate step. XGBoost is default now
  Different working points ("tight" for high purity, "loose" for high efficiency) should be defined and used consistently across analyses (e.g., Figure 15.7, where a 90% WP for muon/electron ID is mentioned). Coherence with PFA must be ensured (avoiding double-counting residual energy, etc.) BEST WP used now
DETECTOR PEREORMANCE
Ongoing
Beyond TDR

## Slide 181: Recommendations
The description of jet flavor identification needs to be streamlined. Currently, information is dispersed across sections (vertexing, tracking, PFA). A concise but complete description should be provided in one place restructured
  A brief overview of standard Jet Flavour Tagging (JFT) is given in Section15.2.6, while Jet Origin Identification (JOI) is discussed in 15.2.7. However, it is unclear what performance gains are achieved by moving from JFT to JOI. JFT vs JOI shown for b/c tagging eff and mis-id rates
  Benchmark comparisons (b/c-tagging efficiency versus misidentification rates at Z-pole and ZH 240 GeV) should be provided to evaluate performance systematically.
The offline software environment is evolving rapidly. Performance studies should be conducted with synchronized and version-controlled frameworks, especially as CyberPFA depends critically on tracking, particle ID, calibration, and alignment inputs. yes
A centralized database tracking the produced samples and their statistics should be maintained and updated (extending Table 15.4). Technical samples (e.g., single electrons, muons, decaying kaons for PFA studies) should be included and documented similarly for use in detector performance validation.
a centralized database created and maintained with IHEP gitlab service (in CEPCSW code repository)
DETECTOR PEREORMANCE

## Slide 182: Recommendations
Longer-Term Considerations (for post-TDR development)
  Consider a dedicated chapter for jet flavour tagging, especially given the comprehensive nature of JOI (which involves many sub-detectors). Comparative studies between "ideal" and "compromised" performance would also help derive systematic uncertainties in the AI-based approach.
  The confusion matrix (Fig. 15.22) suggests JOI could distinguish quarks from antiquarks. If validated, this could significantly improve flavour-specific AFB measurements. Physics benchmarks involving b/c-quark AFB (or even strange quarks) should be added if feasible.
  Organizing "data challenges," as mentioned in the "Offline Software and Computing" section, could be valuable. These would serve both as benchmarks for detector performance and stress tests for computing models (through massive production, analysis, and quality checks)
  Plan discussed to have another round of data production with a final TDR SW release in July-September
  * based on detector design/geometry in June 15 * TDR SW release June 30 for internal test
  * SW validation/fixes by July 30 - final TDR release
  * August 1st - data production ~ 1 month
  * all results updated in September
DETECTOR PEREORMANCE

## Slide 183: Comments on Draft v0.4.1
  - The particle ID section 15.1 are now readable and well structured It would be nice if the section 15.1 ends up with a conclusion summarizing the salient performance features observed in these studies. I suggest a table of this type.
Particle Id. | Physics channel/sample considered | Performance exemple
Missing Energy | e+e-HZ, 𝑍 → 𝜇𝜇, 𝑒𝑒 or 𝑞𝑞 𝐻 → 𝑍𝑍∗ → 4𝜈 | deltaM (𝑍 → 𝜇𝜇)=0.288 GeV deltaM (𝑍 → ee)=0.40 GeV
Jets JOI | 𝜈𝜈.𝐻 production with 𝐻 → qq and Ecm= 240 GeV | b-jet tagging efficiency of 95%with a misidentification rate of only 0.1% for light quark jets. ….
A subsection is added to summarize the performance with a table with objects ordered consistently with the subsection structure.
DETECTOR PEREORMANCE

## Slide 184: Comments on Draft v0.4.1
The physics benchmarks in section 15.2 should be listed by physics domain and in the same order as introduced in table 15.3
  We have updated the table based on the physics domain and center-of-mass energies. The subsections are ordered consistently now.
in table 15.3 W fusion appears out of order (the domain is “Higgs”). Maybe move it up together with “Higgs”.
  We have decided to remove the W fusion, as the analysis did not converge on time & is unlikely to do so in a short time scale.
DETECTOR PEREORMANCE

## Slide 185: Comments on Draft v0.4.1
15.2 please make sure that each analysis presented have 1-2 phrases at the end to compare with a reference analysis (for instance present state of the art, limits from LHC or previous LEP results etc) This exists in some places but not everywhere.
  Sentences are added at the end of each
  analysis subsections.
-This is not necessarily for this document, but on a few benchmarks items (MHiggs, MTop etc.) it would be good to have a direct comparison with FCCee studies. (and good answers if significant differences are observed)  We didn’t included in the document, but a direct comparison to FCCee is as below:
Mhiggs
MTop
DETECTOR PEREORMANCE

## Slide 186: Comments on Draft v0.4.1
Table 15.18: maybe having the cell limits would help readability?
  Added a vertical line and made a few minor cosmetic changes (e.g. avoided merging cells)
-Figure 15.33 : are the contours right? They seem to be confined at the right of the figure and are not readable.
  The contours are correct, but indeed were
  not readable. We zoomed in the figure.
  The left side of the contours are fully
  excluded.
V0.4.1
New
V0.4.1
New
DETECTOR PEREORMANCE

## Slide 187: Comments on Draft v0.4.1
- The section 15.3 : I suggest to move the subsection 15.3.4 as a part of the final section, to be renamed as “Summary and future plans”.
- I suggest to rename the section 15.3 as: “Further performance aspects”
  The new structure is as below.
-I suggest a proof reading, there are a few editorial minute errors left in the text. (make the references uniform etc.) But in general the text is OK.
  We went through the chapter again and made detailed updates to improve readability.
V0.4.1
New
DETECTOR PEREORMANCE

## Slide 188: OVERALL CONSTRUCTION COST AND TIMELINE

## Slide 189: Findings
The cost estimation is provided as an ancillary table outside the Ref-TDR, following a standard Work Breakdown Structure (WBS). Only summary tables for the baseline detector option are included within the TDR text itself. Costs are primarily based on raw material prices (by volume, weight, or area), projected over the next 5 to 10 years, and multiplied by a fabrication factor.
Currently, only a very rough timeline for detector construction is presented in Chapter 16 of the TDR.

## Slide 190: Comments (1)
For future, more informed cost reviews, it would be beneficial to provide the full WBS information, with a breakdown of:
  Raw material costs
  Production costs (including fabrication losses)
  Labour costs
  Integration costs
Additionally, for each item, the following should be clearly specified:
  Unit description (clearly linked to the detector design)
  Unit cost (in original currency)
  Basis of the estimate (e.g., vendor quote, internal prototype, previous projects, catalogue pricing)
  Quantity required for the detector
  Quantity including yield loss
  Total quantity and total cost
It should be explicitly stated whether the current costs include allowances for yield loss.
A structured, consistent table format for each major cost item would greatly improve clarity and traceability.
All these are good suggestions, which require dedicated cost reviews and redesign of the WBS
As we are not going to include detail cost estimation in the TDR, only a summary table will be kept.
We plan for an internal cost review for each system after the TDR is released. An international cost review is under consideration.

## Slide 191: Comments (2)
Regarding the detector construction timeline, the information currently provided is too limited to allow for a meaningful assessment.
A detailed timeline will be worked out in the detector EDR stage.
Concerning computing costs: while the extrapolations appear reasonable, the model could be further refined by considering data size, number of re-processing, number of data copies, and data accumulation schedules. Even a small additional effort to refine or document these factors would be valuable.
The resource modeling and extrapolations account for the following parameters:
Raw data size: 306 KB (DAQ system estimate)
MC data size: 1 MB (offline software estimate)
Reprocessing: Both MC simulation and reconstruction data are generated in 2 versions
The resources are allocated for a 5-year period: four years of Higgs data collection and one year of low-energy Z data collection. The low-energy Z data is acquired in 2-month intervals annually, distributed across the 5-year Higgs data-taking period.
Currently, we have only accounted for baseline requirements and assumed a single copy for all data types.

## Slide 192: Comments (3)
The projections for hardware performance and price evolution over 10 years seem somewhat optimistic, as they combine assumptions of improved CPU performance per core with reductions in cost per core.
The projection of a 50% reduction in average cost per CPU core over the next ten years is based on two key estimations:
Advances in semiconductor manufacturing: The transition from 7nm to 3nm and even 2nm process nodes enables significantly more transistors per core, enhancing both speed and energy efficiency. AMD’s upcoming Zen 6 “Medusa” architecture, expected around 2026–2027, may deliver up to 30% higher single-core performance compared to Zen 3, driven by improved core design and interconnect technology.
Industry cost trends: According to Future Market Insights, the average cost per core in data center CPUs is projected to decline by 30–50% over the next decade, particularly in mid-range and high-volume deployments. (www.futuremarketinsights.com)
HDD storage costs are projected to decline by up to 50% over the next decade:
HDDs are evolving from traditional Perpendicular Magnetic Recording (PMR) to advanced methods like Heat-Assisted Magnetic Recording (HAMR) and Microwave-Assisted Magnetic Recording (MAMR). These technologies dramatically increase areal density, allowing more data to be stored per platter and reducing cost per terabyte.

## Slide 193: ECAL BGO Crystals (1)
The cost of BGO crystals significantly impacts the overall budget. The table presented dates back to 2019. We recommend engaging with multiple vendors to ensure the required quality, production rate (given the enormous volume), and lowest possible price.
Before and after the review, we visited three suppliers of BGO, and received new quotes
50% higher price compared to 2019, mainly due to increased GeO2 price (next page)
Xiamen Tungsten and Boya are developing new methods to produce long (40 cm) BGO
Supplier | SIC | Boya | Xiamen Tungsten
Production method | Bridgman | Czochralski | Kyropoulos
Available BGO samples | 40 cm | 20 cm | 20 cm
Quote ($/cc) | 7 (2019)→10.6 (2025) | 10.6 | Production costs could be lower
Raw material cost fraction | ~60% | 51% | N/A
Production ability | 1/3-1/2 of the total BGO volume in 5 years |  | 
Thank Prof. Renyuan Zhu to help get new quotes

## Slide 194: ECAL BGO Crystals (2)
We also visited the research institute of the Aluminum Corporation of China (Chinalco) and its subsidiary, Yunnan Chihong Germanium International Co., Ltd.
  Production capacity fully meets CEPC’s requirement (~50 ton GeO2)
  GeO2 price increased by a factor of 2-3 since 2020, hard to predict the future trend
  Action: potential collaboration with Chinalco through a high-level channel.
Alternative option: BSO
  SIC is able to produce 40 cm BSO bars, quality to be studied
Keep BGO and current cost estimation ($5/cc) as the target price. Looking for reduction of GeO2 cost and developing BSO.

## Slide 195: SiPM Packaging Costs
The cost of packaging could be as high as 50% or more. It should be clarified whether packaging costs are included in the quoted SiPM price, and this should be explicitly reflected in the WBS. The current estimate of 1.25 CHF (10 RMB) per channel may be optimistic.
  TAO uses SiPM 6×12 mm2, 8 times larger than CEPC SiPM 3×3 mm2
  Assuming the cost packaging for CEPC is 50%, and for TAO is 25%, the new estimation is 20 RMB/piece, twice of our expectation.
  Obtained new quotes from three suppliers (including Hamamatsu), two of them below 20 RMB/piece including packaging. Further reduction expected in the next 5-10 years.
 | TAO | Extrapolated to CEPC
Material | 10 RMB | 10 RMB
Packaging | 3 RMB | 10 RMB
Price of SiPM per 3×3 mm2 based on TAO’s experience
Extrapolation from TAO is consistent with new quotes: ~20 RMB/piece

## Slide 196: HCAL Cost Estimates
Currently, the lowest informal offer is used for the cost of glass plates. Until it is confirmed that the lowest bidder meets the required specifications, it would be more prudent to use the average of the three quotes.
The average price is 0.8 CHF/cc, 40% higher than our expectation (~0.5 CHF/cc). After careful comparison, we found vendor 2 has very high labor cost, power and depreciation; vendor 3 has very high cost for manufacturing and management. For now, we choose the lowest as our target and will work with all vendors to further understand their differences.
Some cost uncertainty reflecting the outcome of ongoing R&D should be included.
Considering the “unreasonable” items introduced before, the difference between each vendor is largely reduced, which should be cover by 20%-30% uncertainty assumed for each system.
Additionally, the cost estimate assumes one SiPM per glass plate, whereas the detector design currently requires four SiPMs per plate for viability.
In the new version of the TDR, the baseline design has been changed to one SiPM per glass plate.

## Slide 197: Muon Detector Electronics
The cost book reports 43,000 ASICs, 43,000 FEE units, and 43,000 Readout FEE units. However, the readout architecture has recently been updated to a three-stage system, and the number of FEE boards (uFEBs) should be significantly lower than the number of SiPM channels. The cost estimate should be updated to reflect this new architecture.
In the WBS, 43,000 is the number of channels, instead of ASICs or units. The cost estimation has already converted the total cost of ASICs, FEE boards into the cost per single channel.
Additionally, the TDR mentions the need for 72 Management Boards for slow control and DAQ interfacing—these boards are currently missing from the cost book and should be added.
Management boards are part of the on-detector FEE. They are also converted into the cost per single channel and are already included in the cost estimation.
Notes: Muon detector needs about 43,000 SiPMs, 1,662 Front-end Electronics Boards (uFEB), and 80 Management Boards (uMB). These quantities have been updated based on the most recent detector layout and the revised architecture of the readout chip. The estimation reflects the number of modules required to fully instrument the detector, taking into account the current design of module segmentation, including barrel parts and end-cap parts, and readout chain configuration. These figures are the result of close coordination with the detector integration team to ensure alignment with the latest system design and performance requirements.

## Slide 198: Magnet Cost Comparison
The TDR quotes a magnet cost of about 22 MCHF, compared to around 130 MCHF for the more complex ILD system (which includes the yoke). A cross-check should be performed to understand and justify the difference between these two estimates.
The total cost of magnet and yoke is 36 MCHF, 1/3.6 compared to ILD, reasonable considering lower price of material and labor cost in China, and different complexity. The cost estimation is based on quotations of major components.
No public cost budget of ILD magnet, contacted ILD experts, waiting for reply.

## Slide 199: TPC Cost Comparison
Similarly, the TPC cost is estimated at 5 MCHF, whereas the ILD TPC estimate was 36 MCHF. This discrepancy should be investigated and explained.
  Including backend electronics, CEPC TPC cost 5223 + 1094 = 6317 (6.3 MCHF)
  36 MCHF is the sum of two readout options (Micromegas 15.4 MCHF, GEM 19.1 MCHF) in ILD
  Comparing Micromegas readout, the ILD is 2.5 times higher (15.4 VS 6.3)
Items | Pixelated reaout TPC @CEPC (kCHF) | Micromega TPC @ILD (KCHF) | Comments
Fieldcage: Hanging, damping and shipping | 0 | 468 | 230kCHF should be added refer to mechanical
mesh and DLC | 0 | 524 | 350kCHF should be added refer to USTC/KEK
Laser system | 0 | 505 | 325kCHF should be added refer to IHEP R&D
Assembly on site | 0 | 2023 | Labor cost (w.o.)
Management | 0 | 56 | Labor cost (w.o.)
Three missing items added: +905 kCHF
Labor cost not included in the project cost

## Slide 200: TPC cost update
Three missing items in mechanics suggested by IDRC: +905 kCHF
Optimized design of carbon fiber barrel: -260 kCHF
Optimized design of electronics cooling: +290 kCHF
 | April | August | Difference
Common Mechanics | 1998 | 2640 | +642
Readout | 518 | 518 | 0
Electronics (FEE) | 2149 | 2435 | +286
HV/Gas system/Calibration | 407 | 407 | 0
Installation (3%) | 152 | 180 | +28
Sum | 5223 | 6179 | +956
Unit: kCHF