## Slide 1
COFFEE3 tests
Left Array
48 row 12 col
40 145
Right Array
32 row 12 col
40 100
Passive diodes
PLL
Passive diode array: validation of sensor performance; test result consistent with COFFEE2:
Breakdown voltage: -71V
Responsive to - and X-rays

## Slide 2
COFFEE3 tests
Left Array
48 row 12 col
40 145
Right Array
32 row 12 col
40 100
Passive diodes
PLL
PLL: new module for clock synchronization.
Test result consistent with simulation up to 320MHz output with 40MHz input Module validated!
320 MHz clock output with 40 MHz input
simulated 320 MHz output

## Slide 3
COFFEE3 tests
Left Array
48 row 12 col
40 145
Right Array
32 row 12 col
40 100
Passive diodes
PLL
Left pixel array: readout architecture fully exploiting 55nm process potential, with in-pixel TDC etc. Need an extra deep p well
Right pixel array: architecture optimized for current Triple-well process, NMOS-only in pixel
Testing goals:
Pixel response to charge injection
TDC performance
LVDS driver
Column readout validation
…
Dedicated test PCB + CariBou readout board in place; SPI config successful
Test PCB designed; Current test focusing on left array
Readout performance (time resolution, power, …) to be compared with left array