## Slide 1
Stereo crystal ECAL for CEPC
Lianyou Shan, Han Wang, Chaochen Yuan,
Huaqiao Zhang, Xiao Zhao, Shengsen Sun(IHEP, Beijing)
Lei Guo, Yang Liu (SYSU)

## Slide 2: Requirement of a CEPC PFA calorimeter
CEPC Physics requirements
  Precision measurements with Higgs and Z/W
  Jet energy resolution (dEjet/Ejet- 3~4%)
PFA based Calorimeter (CEPC)
  Good Shower separation
    Small Moliere radius (Dense detector)
    High lateral granularity (~Moliere radius)
  Good Energy resolution
    Critical in some special process
  Sophisticate algorithm
    Multi-million channels(energy and timing)
    Multi-Dimensional information
Overlap removal

## Slide 3: Available options for CEPC ECal
Silicon tungsten ECal
Scintillator sampling ECal
Dual readout calorimeter
Homogenous Crystal ECal: long bar, Stereo
Stereo Crystal ECal: Try to get 3D shower with 2D readout in simplified way
Long bar Crystal ECal
SiW ECal
Sc ECal

## Slide 4: Stereo Crystal Electromagnetic Calorimeter: Basic idea
Traditional Crystal Ecal （CMS/BES…):
  Crystal long bar pointing to interaction point (IP)
  Slight twist to avoid escape of particles
Stereo Crystal ECal:
  Crystal long bar not pointing to IP
    Angle between Crystal long bar and det. radius is 𝛼
      -90 <= 𝛼 <= 90 degrees
      𝛼 = 0; pointing to Z axis  traditional
      𝛼 != 0: obtain sampling on R
  Number of sampling can be optimized
  Single-end readout on the outer surface w.r.t. IP
  Form circular structure with trapezoid crystal without gap
Sampling 1
Sampling 2
Sampling 3
Sampling 4
readout
Cylindrical coordinate

## Slide 5: Stereo Crystal Electromagnetic Calorimeter: Design
To improve the 3D position resolution
  Pointing angle of even layers alone Z: 𝛼
  Pointing angle of odd layers alone Z： 𝛼’= -𝛼
Left eye
Right eye
Traditional Crystal Ecal
SCEcal
Not proportional to real angle/size
Even layer
Odd layer

## Slide 6: Analytical optimization of SCECal geometry
3 degree of freedom for a given inner and outer radius of barrel
  Pointing angle:
    Correlated with the crystal length:
    Correlate with the crystal size(typically ~1cm) along :
  Crystal size along Z : (typically 1 cm)
Even layer
Odd layer
Form stereo structure
Form a super layer of 30 cm thick along Z
Super layer form the full barrel
Readout at outer surface
Only one freedom left, or longitudinal sampling
One trapezoid shape

## Slide 7: Demo for Mechanics and cooling
TSAIW值为0.3
Shaojing Hou
Z
Jingfan Chang
phi

## Slide 8: Design of Endcap SCECal
Shelf like structure
Each Super layer consistent of 30 layers of crystals
Crystal pointing angle w.r.t. Z axis（beam）
  One variant of crystal shape: Parallelagon
  Even layers: 𝛼; Odd layers: -𝛼
Readout electronics at outer Z w.r.t. IP
Super layer

## Slide 9: SCECal simulation using BGO crystal
Simulation and reconstruction done using CEPCSW
  Ideal Geometry implemented
  Crystals（BGO） without wrapper/gap etc. (ideal situation)
  Simulation readout using carloStep info (no digitization)
    Threshold of readout energy is applied
Energy, position resolution and separation of photon/pion:
  Different R segmentations tested: 5/10/14 layers
    10 layers turn out to be the best
  Different recontruction method:
    Simplified reconstruction
    End-to-End Machine learning
The following study based on 10 layers segmentation on R
  r1=1.9 m, r2=2.2m, Z=6.7 m; endcap not included yet. 26.7 X0 BGO
  Crystal size: = [8.8-8.9]mm; =10mm; =316 mm
  Pointing angle: 𝛼=20º

## Slide 10: Simplified Reco method for isolated particle
Find a 2D Cluster, energy is the sum of crystals about 2 MeV
Hit (red points): The cross point of two nearby cluster crystal
  Geometric center of hit define its z, phi, R
  Assign hit energy as sum of the two crossed crystals
  Renormalize the total energy to the Energy of 2D cluster
Cluster Phi/Z/R: energy weighted phi/Z/R of all hits
R [mm]
2D cluster
3D hits projection

## Slide 11: Performance of 3D positioning resolution
Particle gun used: check resolutions as function of γ energy
For 5GeV γ, phi: 0~360°, theta: 90°
  Z resolution ~ 0.84 mm; Phi resolution ~ 1.9 mm
  R resolution ~ 7.6 mm;
R resolution
Z resolution
Phi resolution
Gain resolution along R 
Good Z/phi resolution

## Slide 12: Closer look at Photon cluster/energy reconstruction
Typical photon shower in the home-made clustering algorithm
a=0.65%

## Slide 13: Boson mass resolution in H γγ
H γγ mass resolution use clustering algorithm
BMR = 0.25%

## Slide 14: Separation between two 5 GeV photons
Two 5 GeV photons, vary distance along phi between them
Success reconstruction: 2 neutral particles, 3.3GeV<Eγ<6.6GeV for each photon
Threshold: 2MeV
two γ from IP

## Slide 15: Separation between γ/π
5 GeV γ/10GeV π, vary distance along phi between them
Success reconstruction: 3.3GeV<Eγ<6.6GeV
Different π/γ separation power: pointing angle / magnetic field
Threshold: 2MeV
π+
γ
π-
γ
γ
π-
γ
π+

## Slide 16: γ/γ performance using CLUE algorithm
CLUE (CLUstering of Energy):
  Input parameters to determine cluster seeds, outliers and follower hits
  the cut-off distance in the calculation of local energy density (dc);
  the minimum density to promote a hit as a seed or the maximum density to demote a hit as an outlier (ρc);
  the maximum distance for a hit to be linked to a nearest higher point (δo);
  the minimum distance for a local high density hit to be promoted as a seed (δc).
[1] https://cds.cern.ch/record/2802590/files/CR2022_027.pdf
Separate the raw data into odd and even modules
CLUE clustering algorithm
Merge odd/even sub-Clusters
Current CMS HGCal reco. alg.
γ/γ separation
even dc :1 rho: 2 delta_c: 2 delta_o:3
odd dc :1 rho: 0.2 delta_c: 2 delta_o: 2
higgs->
BMR: 0.35%
Consistent with simplified method, further tunning possible
science.1242072

## Slide 17: Particle separation using ML
End-to-End method is used
  2 steps, one for classification, one for energy regression(max 2 obj. now)
More complex NN is under investigation
  Regression of 2D energy hit map of individual particle
  Regression of 3D energy hit map of individual particle
  Clustering
  PID
  Jet energy
Calor only
With information from tracker and helps of PFA
CMS reconstruction of merged photons paper
PRD 108，052002（2023）

## Slide 18: Separation between two 5 GeV photons: ML regression
Trained with 2 γ with energy(0-10] GeV and distances varis
Significant improvement than simple clustering
  100% eff. After 20 mm distance
Prob. of 1 γ reco as 2 γs (1->2)
100% eff when 2 γ distance >20 mm
Longitudinal separation, 1->2, conversion
2 γ have diff. shower start

## Slide 19: Separation between γ/π: Calor only ML
Trained with a sample of 1-10GeV γ, 2-20GeV π +, distance @calorimeter variated around 20 mm
Applied to separate 5 GeV photon and 10 GeV π +
  ~100% efficiency when > 100 mm distance
γ+π
γ only
π only

## Slide 20: Reconstruct of jets: event display
Clear V-Parten seen in the 2D energy map (1 crystal  1 pixel)
Jet energy map
jet

## Slide 21: 1st try: Reconstruction of charged muons in Stereo ECal
Fit the intersection of the two adjacent layers
Obtained Pt consistent with truth
Encouraging, Still way to do full jet reco.
Pt=0.855/sin(β)
∠1=∠4=β
P_initial / GeV | β° | Pt-recon/ GeV | Pt-truth/ GeV | Relative Diff.
2 | 37.21 | 1.41 | 1.41 | -0.02%
4 | 17.65 | 2.82 | 2.83 | -0.31%
5 | 14.00 | 3.53 | 3.54 | -0.06%
6 | 11.64 | 4.24 | 4.24 | -0.10%
8 | 8.78 | 5.60 | 5.66 | -1.01%
10 | 6.99 | 7.03 | 7.07 | -0.63%
Θ=45°
Could help on Charge particle cluster matching

## Slide 22: Summary
A new configuration of Homogenous Crystal Ecal is presented
  Long crystal bar with 2D readout at outer end of ECal
  Use stereo structure to obtain measurement on the 3rd dimension
    Only one free parameter: easy to optimize
    Only one variant of crystal, very uniform in phi, Z, and R
    minimal dead regions, minimal ghost hits,
    Friendly to cooling, radiation shielding …
Working principle is demonstrated with preliminary simulation
  Good energy resolution on EM objects including H γγ
  Good separation between γ/γ and γ/π with Machine learning
    100% eff. @ 20 mm for γ/γ and @100mm for γ/π
  PFA/ML jet boson mass resolution study is ongoing
Optimization of crystal/readout
  Starting from existing CEPC crystal Ecal R&D: BGO+SiPM
  Further optimization to consider the large signal size

## Slide 23: Backup

## Slide 24: Ghost hits
Confusion of red hit with yellow ones
  Happens only in small phi/R range
    R-range: 0-30CM
    Phi-range: -4.5 cm - +4.5 cm (10 layer)
Large probability have hits in middle shower depth, small chance to have hits in small or large shower depth
Big energy deposited in middle shower depth hit, small in inner/outer depth
If ghost hits happens
  largest change of phi: ~4.5 cm,
  Largest change of R: ~15cm
R
Phi
Phi range
Ghost hit in Z*phi plane: 1cm * 9cm
Ghost hit in R*phi plane: 30cm * 9cm
Ghost hit happens within this Parallelogram area
SCEcal unit ghost hits area： ～32/2*32/2*sin（2*𝛼） =160cm2；
Long bar Ecal unit ghost hits area： 40*40 = 1600 cm2

## Slide 25: Analytical formular for SCECal geometry
3 degree of freedom for a given inner and outer radius of barrel
  Pointing angle:
    Correlated with the crystal length:
    Correlate with the crystal size(typically ~1cm) along :
  Crystal size along Z : (typically 1 cm)
Crystal bar open angle along :
Total number of crystals along
Shower depth(Sn) and along R at nth sampling:

## Slide 26: Configuration of 5/10/14 layers along R
Taget: change layers along R, keep similar Z/phi segmentation
  5 layers: 𝛼=10º; crystal size: [9]*10*304 mm3, n = 1309 * 671;
  10 layers: 𝛼=20º; crystal size: [8.8-8.9]*10*316 mm3, n = 1276 * 671
  14 layers: 𝛼=30º; crystal size: [9.1-9.4]*10*339 mm3, n = 1141 * 671
Simulated 30 GeV photon pointing at theta = 90, phi = [0-360]
Simpler clustering algorithm with threshold of 1 MeV
Energy/Z resolution do not change for different layers along R
E std. dev. ~0.5%@30GeV
5 layer
10 layer
14 layer

## Slide 27: Boson mass resolution in H γγ
Sample: ZH->2neutrinos + γγ at 240 GeV
Energy, position reconstruction and separation using simplified reconstruction method described above
Crystal energy threshold: 2 MeV/50MeV
BMR = 0.33%
BMR = 1.3%
Threshold: 2MeV
Threshold: 50MeV
Good BMR，more realistic simulation will give more reliable results
Very optimistic simulation
Very optimistic simulation

## Slide 28: Event display for shower seperation
Two 5 GeV photon, 66 mm distance
Two 5 GeV photon, 165 mm distance
5 GeV photon and 10 GeV pi-, 195mm
5 GeV photon and 10 GeV pi-, 66mm

## Slide 29: Simplified Reco method for 2 particle separation
Cluster splitting
  For each layer (along Z): Find two locations with maximum energy deposition and separate them by the min. value between them
  Merge clusters in individual layers use layer matching alg.
    Criteria on delta phi according to its point angle direction
Phi
Z
Two 5GeV γ
γ1
γ2

## Slide 30: Stereo ECal: muon momentum reconstruction
∠ 1
∠ 2
∠ 1
∠ 3
∠ 4= β
Origin info：
  Single 5GeV μ
  Θ=45°
  Φ=100°
Geometric info：
  ∠1=∠4=β
  OA=1.9 m
  ρ=1.9/2sin(β)
Particles move in a magnetic field
  P=mv=RBq
  Pt=0.3ZBρ
    Z=1 for charge
    B=3 T for magnetic field
    Pt for GeV/c
    ρ for m
   Pt=0.855/sin(β)
O
A
ρ
ρ
O’

## Slide 31: Strategy
The fitted plot is as follows, with the green line being made by fitting the intersection of each of the two adjacent layers (odd/even)
Take the φ that fits the first intersection in the lower left corner
The deviation Angle β is obtained by differentiating the φ_ fitted with the φ_ initial
The β Angle is added to the Pt calculation formula and compared with truth

## Slide 32: Results
event | Pt-recon/ GeV | Pt-truth/ GeV | Uncert.
0 | 3.53 | 3.54 | -0.06%
1 | 3.51 | 3.54 | -0.78%
2 | 3.53 | 3.54 | -0.02%
3 | 3.53 | 3.54 | -0.11%
4 | 3.54 | 3.54 | 0.02%
  Single 5GeV μ
  Θ=45°
  Φ=100°
  Energy threshold 2MeV
  Five cases were examined and the results are as follows: （Keep to two significant decimal places）
3.77%
-2.95%