## Slide 1: 2025.12.05 group meeting
陈伟文

## Slide 2: Feedback placement location
The horizontal kicker and tune BPM cable is connected to Zone R2
The Vertical kicker and R4RFBPM cable is connected to Zone R4
Horizontal Tune BPM
Horizontal kicker
Vertical kicker
Libra-BPM
(R4RFBPM)
 | Horizontal | Vertical
 | Horizontal | Vertical
Power amplifier
BPM
?

## Slide 3: Power amplifier
Output waveform requirements
  Feedback applied to the Kicker needs to be constant over the length of the bunch
  Corresponding to amplifier needs
  The limitation of the amplifier's low-frequency bandwidth -> output square wave signal will be drop
  Considering that the output droop is less than 10%, the lower limit of the amplifier bandwidth requirement is 10 kHz (Simulation is needed to further quantify the impact)
  The upper limit of the bandwidth -> rising and falling edge response of the output waveform
[2] accelconf.web.cern.ch/HB2014/talks/tho3ab01_talk
BxB
Intra-bunch
Low frequency cut-off
High frequency cut-off
J-PARC MR feedback
Duty =90%

## Slide 4: Power amplifier test
Power amplifier test
Bandwidth 5 kHz-148 MHz
ENA
input
output
Power amplifier
Attenuator
（DTS2000 40 dB）

## Slide 5: Power amplifier test
Lower bandwidth ≈ 3.14 kHz
The output power of P-1 dB = 63 dB = 2000 W and a maximum output power of 2300 W
Output inversion, delay 110 ns, 1 us top drop <7%(corresponding to actual bandwidth ≈3 kHz)
Oscilloscope
(DSOX3034T)
input
output
Power amplifier
Attenuator
（DTS2000 40 dB）
Source
(AFG 31000)
Power amplifier test
single pulse response
Power and Linearity

## Slide 6: Simulated feedback output
There will be a low-frequency baseline drift superimposed on the subsequent pulses when continuous unipolar pulses generate a DC component
We can decrease the DC component by applying a contrast pulse in feedback off in one bucket without beam
a
b
Ratio = a/b

## Slide 7: Feedback output test
Feedback simulated output generated by AFG31000 was input to power amplifier
The ratio = 1 mean that DC component ≈ 0
ratio = 0.5
ratio = 1
ratio = 0

## Slide 8: Kicker
Stripline kicker
Shunt impendence
Voltage
Frequency
220 mm

## Slide 9: Kicker
Kicker cable TDR
Delay about 444.5 ns(Hor.)，382.5 ns(Ver.)
Characteristic impedance
 | Horizontal electrode 1 | Horizontal electrode 2 | Vertical electrode 1 | Vertical electrode 2
(Ω) | 46.6 | 46.6 | 45.7 | 46.0
(Ω) | 46.4 | 46.9 | 45.5 | 45.8
 | Horizontal electrode 1 | Horizontal electrode 2 | Vertical electrode 1 | Vertical electrode 2
 | 46.6 | 46.6 | 45.7 | 46.0
 | 46.4 | 46.9 | 45.5 | 45.8
R2 -> Hor. kicker
R4 -> Ver. kicker
88.9 m
76.5 m

## Slide 10: Kicker time response
Single square wave input test
Horizontal Kicker bandwidth < 5.15 MHz, vertical kicker bandwidth < 5.83 MHz
Hor.
Ver.
Simulation of 1 μs, 90% duty cycle module square wave time response
Frequency range limited to 4 kHz – 5 MHz
No obvious issues for bunch-by-bunch feedback

## Slide 11: Kicker port test
Kicker S11
Seem no good.

## Slide 12: Beam instability generate
Initial bunch parameter
Particle intensity:
Particle distribution: KV distribution
RMS bunch length
RMS momentum spread
Without wake fields
M_BtoK =
[[-1.12446315e+00, 4.35257954e+00, -4.64024432e-24, 1.10417008e-23, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[-1.66915475e-01, -2.43215735e-01, -9.65655416e-25, -1.06680597e-24, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[ 0.00000000e+00, 0.00000000e+00, -7.66843433e-01, 3.89955830e+00, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[ 0.00000000e+00, 0.00000000e+00, -1.78175096e-01, -3.97989749e-01, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[ 0.00000000e+00, 0.00000000e+00, -2.01150785e-23, 1.22458415e-23, 1.00000000e+00, 8.30464432e+01, 7.70548583e-15],
[ 0.00000000e+00, 0.00000000e+00, -9.64876874e-34, -4.50128356e-33, -5.98502761e-21, 9.99999835e-01, 2.04788238e-16]]
M_KtoB =
[[-7.51147889e-01, 2.93674690e+00, -2.89970864e-23, 3.25704876e-23, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[-1.05658648e-02, -1.28998543e+00, 1.80541107e-24, -3.32138783e-23, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[ 0.00000000e+00, 0.00000000e+00, -1.08435573e+00, 3.34106103e-01, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[ 0.00000000e+00, 0.00000000e+00, 3.27397833e-02, -9.32294062e-01, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00],
[-4.41097632e-02, -4.49815175e+00, -2.74344292e-23, -8.17048356e-23, 9.99269350e-01, 1.10691441e+03, -9.39237536e-06],
[ 0.00000000e+00, 0.00000000e+00, 8.42882527e-30, -1.28715529e-28, -1.87469423e-06, 9.98652672e-01, -2.40988566e-08],
[ 0.00000000e+00, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00, 0.00000000e+00, 1.00000000e+00]]
])

## Slide 13: Beam instability tracking
Condition :
Without consider space charge
Without consider energy ramping by RF
Instability caused by wake field
No obvious other frequency
No gauss
FB: Change the with a fixed ratio correlated to

## Slide 14: FPGA signal processing
Laboratory tests
Test protocol
Stage results
In electronics, the feedback signal can be generate, by have some problem in output from DAC
Modulated rf signal
(BPM signal)
RF signal generator
arbitrary signal generator
RTM(SIS8900)
示波器
Square wave signal
(RF window signal)
Pulse signal
(T0 signal)
DAC output
SIS8300KU
MTCA4 electronics
Ideal signal processing process
GUI
PCIE
The ideal is a sequence of square wave pulses with a duty cycle of 80%

## Slide 15: Other and next plan
Feedback simulation
  Add the BPM, electronic and kicker effect step by step
Finish the other power amplifier test
MTCA4 develops feedback electronic
  Resolve PCIe connection issues
  Implement PCIe transmission of control signals (based on existing API)
  Debug DAC output to achieve normal feedback waveforms(before can also do the feedback in DC mode)