## Slide 1
Direct observation of the Migdal effect induced by neutron bombardment
米格达尔(Migdal)效应的直接观测
刘 倩
MigdAl pRocess Validation by nEutruaL scattering (中性散射中的Migdal过程验证)
中国科学院大学
（代表 MARVEL 合作组团队）
Nature 649, 580 (2026)

## Slide 2: 从卢瑟福散射实验说起
Au
He
He

## Slide 3: Dark matter
Galactic rotation curve
Gravitational Lens
Galaxy mergers
Dark matter makes up most of the mass in galaxies and galaxy clusters.
Current evidence comes solely from gravitational interaction.

## Slide 4: WIMP

## Slide 5: Dark matter experiments
WIMP dark matter searches, PIC-2025

## Slide 6: DM-nucleus elastic scattering
WIMP
Nucleus
Non-relativistic elastic scattering
/c2; /c2;

## Slide 7: Migdal效应
1939年由前苏联科学家Migdal预言
如何让核产生位移？

## Slide 8: Migdal效应的间接探测证据
PhysRevC.11.1740（1975）
K shake off
PhysRevLett.108.243201（2012）
衰变
衰变
电离铅核的k层电子导致能量降低
衰变中2价锂离子的核外电子产生3价锂离子
Li
Pb
J. Phys. A: Math. Theor. 55 (2022)
测量的是核子信息

## Slide 9: 中性粒子碰撞中的Migdal效应
至今已有80余年，仍未有直接观测的证据

## Slide 10: 直接探测暗物质实验

## Slide 11: 直接探测暗物质实验

## Slide 12: 利用Migdal效应直接探测暗物质实验
+…
在低动量转移情况下仍然提供可探测信号！

## Slide 13: Migdal效应的特点
不同轨道均可能产生Migdal电子
M. Ibe, JHEP03(2018)194
Migdal电子沉积能量大于核反冲能量
CDEX

## Slide 14: 轻质量暗物质区间的探测限—由Migdal效应主导
Migdal （ME）
Bremsstrahlung (Brem)
Nuclear recoil
Z.Liu, [Phd thesis], 2022
各大暗物质实验：XENON/LZ/PandaX/CDEX/DarkSide50/SuperCDMS/EDELWEISS/LUX…

## Slide 15: 国际上中性粒子Migdal效应实验
Phys. Rev. D, 109(5), L051101（2024）
Phys. Rev. D,107, 035032
测量沉积能量
测量cluster距离
Nr/Er的径迹成像

## Slide 16: Migdal事例的特征
电子径迹
核子径迹
A
B
共顶点
布拉格峰
？

## Slide 17: Migdal事例的特征
电子径迹
核子径迹
B
共顶点
布拉格峰

## Slide 18: 对探测器的要求
N+
e-
模拟结果
核心挑战:
  信号：有效信号事例率极低
  本底：本底种类繁杂，且实验中存在大量伴生光子本底。
探测器性能要求:
  能量分辨好：电子径迹~keV，核子径迹~百keV，要求大动态范围
  空间分辨高：电子径迹仅数百微米
  有时间分辨能力：通过时间关联筛选信号，压低本底
解决方案:
  主动屏蔽：设计屏蔽体压低本底
  多维度：测量中子/光子能谱、开发蒙卡模拟、事例挑选、径迹重建、顶点重建等算法

## Slide 19: MARVEL 实验装置示意
GMCP
GMCP
Topmetal-II
Topmetal-II
DD neutron source
ER
NR
Migdal topology

## Slide 20: 核心器件：GMCP
微结构气体探测器：GEM/THGEM、MicroMegas…
真空器件MCP并不能直接在气体下使用！
电荷累积在GEM孔内导致增益下降！
设计新工艺，在孔内制作阻性材料，释放电荷
运用于气体探测器（GMCP）
真空器件微通道板（MCP）

## Slide 21: 核心器件：像素芯片Topmetal
 | Topmetal-II- | Topmetal-M1/M2 | Topmetal-L
Chip Size /mm2 | 6 × 6 | 18 × 23 | 17 × 24
Pixel Array | 72 × 72 | 400 × 512 | 356 × 512
Pixel Size /um2 | 83 × 83 | 45 × 45 | 45 × 45
ENC | ~ 13.4e- | ~ 15.4e- | ~ 20.0e-
Power Consumption | ~ 1W @3.3V | ~ 4.3W @3.3V | ~ 0.8W @3.3V
Clock | 40MHz | 5MHz | 20MHz
Frame Rate | 2.5ms | 2.4ms | 0.37ms @Sentinel Readout
Readout Mode | Rolling Shutter | Rolling Shutter | Rolling Shutter /Sentinel Readout
Readout Channel | 1 | 16 | 1
Topmetal-Ⅱ

## Slide 22: Detector performance
Good linear energy response
20%-30% energy resolution(FWHM)
Energy resolution follows the relationship ~
Stable gain under different count rates(no pile up)
Good linearity in charge response
~200 m vertex resolution
@ 6.4 keV
~262 time resolution
Energy resolution
Dynamic range
Vertex resolution
Time resolution

## Slide 23
D-D neutron source
shielding
Migdal detector
Working gas:
0.8 atm @ ~300 K
40% Helium + Dimethyl ether (DME,C2H6O)
Scintillator ①
D-D source monitoring
Scintillator ③
D-D source monitoring
Scintillator ②
n/gamma spectrum meas.

## Slide 24: 中子/光子能谱测量
0.5 MeV: e+/e- annihilation
0.8 MeV: 56Fe
1.4 MeV: 40K
2.2 MeV: H in polyethylene
Neutron energy spectrum
Gamma energy spectrum
采用液闪探测器进行中子/光子能谱测量
开发波形分析算法进行中子/光子鉴别
根据模拟及标定数据得到液闪探测器的响应矩阵；开发反卷积算法得到中子/光子能谱
Notes: 环境光子流强：139.99 cts/s/cm2

## Slide 25: Neutron Flux & Detector performance monitor
neutron flux monitored by the two LS.
Gain monitored with an 55Fe.
T & P are monitored.

## Slide 26: 电子径迹与反冲核径迹
data
data

## Slide 27: 软件模拟框架
模拟探测器响应
提供MC模拟的truth信息
探测器的数字化模拟
模拟电子在探测器中的漂移、倍增及收集过程
模拟电子学对信号的采集及处理过程，并保存为与实验数据完全相同的格式输出

## Slide 28
实验与模拟的一致性检验
6.4 keV photo-electron
241Am alpha source

## Slide 29: 事例挑选
Data
Vertex cut
YOLO*1
preselection
NR
reconstruction
ER
reconstruction
Dataset |  | Train | Valid
Exp | ⁵⁵Fe | 3000 | 1493
 | D-D | 2994 | 1354
Sim | ER | 1200 | 301
 | NR | 1200 | 301
Total |  | 8394 | 3449
Training
*1 https://github.com/ultralytics/ultralytics
Labeling

## Slide 30: 事例重建
1. Search for the NR vertex through recursive iteration:
2. Fit the NR(direction, diffusion σ) and subtract it from the image.
3. Search for the electron vertex using adaptive cutting algorithm(Nucl. Sci. Tech.doi:10.1007/s41365-021-00903-0).
4. Determine whether the electron vertex is adjacent to the nucleon vertex.
Data
Vertex cut
YOLO*1
preselection
NR
reconstruction
ER
reconstruction

## Slide 31: Migdal 事例

## Slide 32: 更多的Migdal事例！

## Slide 33: 全部通过YOLO识别！

## Slide 34: 电子与核子径迹
data
data
Migdal事例中的电子与55Fe源的光电子样本区间一致；核反冲径迹与中子数据中核反冲控制样本一致！

## Slide 35
本底估计
Background Component | Description | Expectation value (5 - 10 keV) | Method
Recoil induced δ ray | δ electron near NR track origin | 0.035±0.023(stat.)±0.0068(sys.) | Data driven
Particle Induced X-ray Emission |  |  | 
X-ray emission | Photoelectron near NR track origin | 0 | 
Auger electrons | Auger electron near NR track origin | 0 | 
Bremsstrahlung processes |  |  | 
Quasi-Free Electron (QFEB) | Photoelectron near NR track origin | ≈ 0 | 
Secondary Electron (SEB) | Photoelectron near NR track origin | ≈ 0 | 
Atomic (AB) | Photoelectron near NR track origin | ≈ 0 | 
Nuclear (NB) | Photoelectron near NR track origin | ≈ 0 | 
Random track coincidences | Photo-/Compton electron near NR track | 0.180±0.022(stat.)±0.042(sys.) | Data driven
Muon induced δ ray | δ electron near NR track origin | 0.013 | MC+Data
Gas radioactivity |  |  | 
Trace contaminants | Electron from decay near NR track origin | 0.001±0.00087(sys.) | Data driven
Neutron activation | Electron from decay near NR track origin | ≈ 0 | 
Secondary nuclear recoil fork | NR track fork near track origin | ≈ 0 | 
Total background |  | 0.229±0.032(stat.)±0.043(sys.) | 

## Slide 36
Consider the selection efficiency for δ-electrons.
Finally get: 0.035±0.023(stat.)
1. Delta电子本底
H
Only H has the δ electron > 5 keV.
No δ above 5 keV were found.
Estimate by extrapolating from the exponential fit
n
N
e-
e-

## Slide 37: 2. 偶然符合本底
Method 1: 液闪测得的 n/γ 能谱代入GEANT4模拟
n
N
e-
n
N
e-
n
Neutron spectrum
Gamma spectrum
n
N*
e-
N
 | NR | Compton e- | photonEle
I | 1 |  | 
II | 1 |  | ~
III | 1 |  | 
 | NR | Compton e- | photonEle
I | 1 |  | 
II | 1 |  | 
III | 1 |  | 
三种贡献之和为: 0.16±0.01(stat.)

## Slide 38: 2. 偶然符合本底
Method 2: 数据驱动的方法
  选取实验数据中的核径迹控制样本与光电子径迹在同一帧上的事例.
  考虑偶然符合在统一顶点的几率,得到最终本底结果为： 0.180±0.022(stat.)±0.042(sys.)
方法一与方法二的结果在统计误差范围内一致。
Method 1
keV

## Slide 39: 显著度
定义概率密度函数
构造最大似然函数
假设检验
  versus
Background:0.229±0.032(stat.)±0.043(sys.)
在该本底水平下，观测到5.77个事例达到5σ

## Slide 40: 相对截面计算
最终结果:
Migdal过程截面与核反冲截面的比值:
参数:
上下限的计算方式:

## Slide 41: 总跃迁几率
41
每种元素的跃迁几率
总跃迁几率
初态为 的电子跃迁到具有 能量末态的几率.

## Slide 42: 总结
六家单位均为 BESIII 合作组成员单位。
中国科学院大学、广西大学、华中师范大学、兰州大学的相关核心教师，均具备 BESIII 等对撞机实验的科研工作经验。
项目组参与培养的马瑞廷、景新媚、黄文谦等多位学生，亦依托 BESIII 等对撞机实验完成学业与科研训练。
向 BESIII 实验组致以诚挚感谢！
谢 谢！

## Slide 43
Backup

## Slide 44: Cross section
Er [keV]
Nr [MeV]
He
Er [keV]
Nr [MeV]
Xe

## Slide 45: Migdal Effect
arXiv:1711.09906v2
/c2;
The electronic energy is much easier to detect than the nuclear recoil energy, especially in light DM region.
Nr + QF》补充quenching factor的内容

## Slide 46: DM-nucleus elastic scattering
Nucleus
Non-relativistic elastic scattering
/c2; /c2;
WIMP

## Slide 47: Migdal Effect
Nucleus
e
First predicted by Migdal in 1939-1940
Initial momentum in the CMF
final momentum in the CMF

## Slide 48: Simulation
The cross sections for nuclear interaction and electromagnetic interaction are from Geant4
The theoretical Migdal cross sections for Ar/C/F/Ge/He/Kr/Ne/Si/Xe nuclei are available.

## Slide 49: Energy distribution of recoil nuclei
Recoil kinetic energy distribution
dE/dX distribution
The recoil energy range of different nucleons is mainly in the interval of hundreds of keV to MeV.
Different nucleons exhibit differences in their distribution peak positions, and the total contribution curve shows a good fit with the experimental data.

## Slide 50
Determine the economic center of gravity and its trajectory based on ignition point and energy deposition.
Calculate the sign of, , , determine the head and tail(Bragg peak) of the trajectory
Slide a perpendicular line along the center of gravity, compute the second-order moment M2 to measure trajectory curvature, and truncate at the point of maximum M2 change for a straightened path.
Recalculate the center of gravity and its line for the truncated trajectory to identify the photoelectric interaction point and emission direction.
Incident direction
Adaptive cutting algorithm

## Slide 51: Bremsstrahlung processes
Process name | Energy Region | Mechanism
Quasi-Free Electron Bremsstrahlung, QFEB | Low | The electrons are scattered in the Coulomb field of the recoiling ion.
Secondary Electron Bremsstrahlung, SEB | Intermediate | The excited electrons interact with other atoms.
Atomic Bremsstrahlung, AB | Higher | The electrons are excited to highly bound states or the continuum and then return to their initial state.
Nuclear Bremsstrahlung, NB | Highest | The Coulomb scattering between the recoiling ion and the target atoms.
ratio of brem photons(E>5keV) and NR
Numb of photoelectron from simulation
Bremsstrahlung background is negligible.

## Slide 52: Muon induced δ ray
Adopt Local Cosmic Muon Flux Measurement Results
  The local cosmic muon flux measurement(Liu,G.,et al, 2024) in Lanzhou is used for estimation.
Set Nuclear Recoil Rate Benchmark and Calculate δ-ray Ratio
  Set the nuclear recoil rate of the D-D neutron source as 1.4 event per second, and in the 5-10 keV energy range, considering the detector's energy resolution, calculate the ratio of δ-ray production to nuclear recoil as 1.85×10-5.
Considering random track coincidence
Include detector’s muon exclusion efficiency
Normalize to the number of experimental data points and determine that δ-rays contribute 0.013 events.

## Slide 53: Trace contaminants
The detector's alpha decay count rate
The decay chain of 222Rn
Assuming:
  All alpha rays are attributed to the decay chain of 222Rn.
  The secondary nuclides with a half-life of less than 1 year have completely decayed.
  Decay process ultimately ceases at 210Pb.
β decay between 5-10 keV contributed by the 222Rn decay chain:
  (7.25 ± 0.94) × 10−7 /s
Combined with the natural abundance values of the working gas:
  (3.34 ± 2.71) × 10−6 /s
GEANT4 simulation of trace radioactivity generating 5-10 keV pseudo-Migdal events yields a selection efficiency of 11.4%
The final expectation for the background contribution from trace radioactivity is: 0.001 ± 0.001.
The working natural abundance:
  ³H:(6.38±6.38)×10-8 Bq
  ¹⁴C:(4.58 ± 4.58)×10-5 Bq
β decay between 5-10 keV:
  ³H:(2.29±2.29)×10-8 /s
  ¹⁴C:(2.59±2.59)×10-6 /s

## Slide 54: Electron momentum transfer models
a. The approximate treatment of the Original Migdal’s method
Nuclear rest frame, the electronic cloud state:
Nucleus recoil
Ionization probability :
Ionized eigenstate
Separate treatment of final-state ionization& nuclear recoil
Obscure energy-momentum & probability conservation
b. From Nuclear Recoil to Atomic Recoil (Ibe, 2023)
Nuclear scattering
Electron cloud transition
Atom scattering coherently
Manifested conservation relation
(Ibe,IBS,2017)
Notes: 这一页简单介绍电子动量/能量转移的物理模型。

## Slide 55: Ionization probability
Under Dirac-Hartree-Fock approximation:
Orthogonality:
Differential ionization probability
Notes: 这一页主要简单介绍何计算电子跃迁概率。在DHF近似中(用平均场代替电子与电子间的相互作用)，多电子原子状态被近似为一个Slater行列式,这里的Φ满足所有的量子数正交关系。

## Slide 56: Migdal cross section
Under the soft limit, the neutron migdal effect scattering cross section can be factorized into two parts:
Migdal transition probability
neutron-nucleus cross-sections
mainly elastic scattering @ 2.5MeV
Sum up for each atom
Single atom approximation for
The experiment detects the ratio of the Migdal cross-section to the neutron scattering cross-section.
Total cross section for n scattering