## Slide 1: Superconductive IDs at BINP
A.V. Bragin, S.V. Khruschev, N.A. Mezentsev,
E.G. Miginskya, I.V. Poletaev, V.A. Shkaruba, V.M. Syrovatin, V.M. Tsukanov, A.A. Volkov, K.V. Zolotarev
Budker Institute of Nuclear Physics, Novosibirsk, Russia

## Slide 2: The history of superconductive ID fabrication in the Budker INP
1979 – first in the world 3.5 Tesla superconducting 20 pole wiggler (SCW) for VEPP-3
1984 – 5 pole 8 Tesla superconducting wiggler for VEPP-2
1985 – 4.5 Tesla Superconducting Wave Length Shifter (WLS) for Siberia-1, Moscow
1992 – 6 Tesla Superbend (SB) prototype for compact storage rings
1996 - 7.5 Tesla superconducting WLS for PLS, South Korea=
1997 - 7.5 T superconducting WLS with fixed point of radiation for CAMD-LSU (USA)
2000 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2000 – 10 Tesla WLS for Spring-8, Japan
2001 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2002 – 3.5 Tesla 49 pole SCW for ELETTRA, Italy
2002 – 7 Tesla 17 pole SCW for BESSY-2, Germany
2004 – 9 Tesla Superbend for BESSY-2, Germany
2005 – 13 Tesla superconducting solenoids for VEPP-2000
2005 – 2 Tesla 63 pole SCW for CLS, Canada
2006 – 3.5 Tesla 49 pole for DLS, England
2006 – 7.5 Tesla 21 pole SCW for Siberia-2, Moscow
2007 – 4.2 Tesla 27 pole SCW for CLS, Canada
2009 – 4.2 Tesla 49 pole SCW for DLS, England
2009 – 4.1 Tesla 35 pole SCW for LNLS, Brasil
2010 - 2.1 Tesla 119 pole SCW for ALBA, Spain
2012 - 4.2 Tesla SCW for Australian Light Source
2012 – 7.5 Tesla SCW for CAMD-LSU (USA)
2013 - SCW for ANKA
2013 - SCW for ANKA & CLIC with indirect cooling
2013 – 2 SCW for Siberia-2,
BINP

## Slide 3: The history of superconductive ID fabrication in the Budker INP
1979 – first in the world 3.5 Tesla superconducting 20 pole wiggler (SCW) for VEPP-3
1984 – 5 pole 8 Tesla superconducting wiggler for VEPP-2
1985 – 4.5 Tesla Superconducting Wave Length Shifter (WLS) for Siberia-1, Moscow
1992 – 6 Tesla Superbend (SB) prototype for compact storage rings
1996 - 7.5 Tesla superconducting WLS for PLS, South Korea
1997 - 7.5 T superconducting WLS with fixed point of radiation for CAMD-LSU (USA)
2000 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2000 – 10 Tesla WLS for Spring-8, Japan
2001 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2002 – 3.5 Tesla 49 pole SCW for ELETTRA, Italy
2002 – 7 Tesla 17 pole SCW for BESSY-2, Germany
2004 – 9 Tesla Superbend for BESSY-2, Germany
2005 – 13 Tesla superconducting solenoids for VEPP-2000
2005 – 2 Tesla 63 pole SCW for CLS, Canada
2006 – 3.5 Tesla 49 pole for DLS, England
2006 – 7.5 Tesla 21 pole SCW for Siberia-2, Moscow
2007 – 4.2 Tesla 27 pole SCW for CLS, Canada
2009 – 4.2 Tesla 49 pole SCW for DLS, England
2009 – 4.1 Tesla 35 pole SCW for LNLS, Brasil
2010 - 2.1 Tesla 119 pole SCW for ALBA, Spain
2012 - 4.2 Tesla SCW for Australian Light Source
2012 – 7.5 Tesla SCW for CAMD-LSU (USA)
2013 - SCW for ANKA
2013 - SCW for ANKA & CLIC with indirect cooling
2013 – 2 SCW for Siberia-2,

## Slide 4
01.11.2012
4
Superconducting multipole wigglers
ELETTRA, Italy, 2002
49-pole 3.5 Tesla superconducting wiggler
CLS, Canada,
2004
63-pole 2 Tesla superconducting wiggler
DLS, England, 2006
49-pole 3.5 Tesla superconducting wiggler
Moscow, Siberia-2, 2007
21-pole 7.5 Tesla superconducting wiggler
BESSY, Germany, 2002
17-poles, 7 Tesla superconducting
wiggler
DLS, England, 2008
49-pole 4.2 Tesla superconducting wiggler
CLS, Canada, 2007
27- poles 4 Tesla Superconducting wiggler
LNLS, Brazil, 2009
35-pole 4.2 Tesla superconducting wiggler
ALBA, Spain, 2010
119-pole 2.1 Tesla superconducting wiggler

## Slide 5: The history of superconductive ID fabrication in the Budker INP
1979 – first in the world 3.5 Tesla superconducting 20 pole wiggler (SCW) for VEPP-3
1984 – 5 pole 8 Tesla superconducting wiggler for VEPP-2
1985 – 4.5 Tesla Superconducting Wave Length Shifter (WLS) for Siberia-1, Moscow
1992 – 6 Tesla Superbend (SB) prototype for compact storage rings
1996 - 7.5 Tesla superconducting WLS for PLS, South Korea
1997 - 7.5 T superconducting WLS with fixed point of radiation for CAMD-LSU (USA)
2000 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2000 – 10 Tesla WLS for Spring-8, Japan
2001 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2002 – 3.5 Tesla 49 pole SCW for ELETTRA, Italy
2002 – 7 Tesla 17 pole SCW for BESSY-2, Germany
2004 – 9 Tesla Superbend for BESSY-2, Germany
2005 – 13 Tesla superconducting solenoids for VEPP-2000
2005 – 2 Tesla 63 pole SCW for CLS, Canada
2006 – 3.5 Tesla 49 pole for DLS, England
2006 – 7.5 Tesla 21 pole SCW for Siberia-2, Moscow
2007 – 4.2 Tesla 27 pole SCW for CLS, Canada
2009 – 4.2 Tesla 49 pole SCW for DLS, England
2009 – 4.1 Tesla 35 pole SCW for LNLS, Brasil
2010 - 2.1 Tesla 119 pole SCW for ALBA, Spain
2012 - 4.2 Tesla SCW for Australian Light Source
2012 – 7.5 Tesla SCW for CAMD-LSU (USA)
2013 - SCW for ANKA
2013 - SCW for ANKA & CLIC with indirect cooling
2013 – 2 SCW for Siberia-2,
Long period SC multipole wigglers
(B0 =7-7.5 Tesla, 0~150-200 mm)
Medium period SC wigglers
(B0 =3.5-4.2 Tesla, 0~48-60 mm)
Short period SC wigglers
(B0 =2-2.2 Tesla, 0~30-34 mm)

## Slide 6: Vertical racetrack coils
Advantages of horizontal racetrack coil technology
Simplicity of the design
Simplicity manufacturing and testing of single coil
Lowest inductivity and stored energy
Possibility to good thermo stabilization of the coil with using Gd2O2S powder add mixture to the epoxy compound (in wet winding technology)
Disadvantage
Technology not suitable for mass production of the big number of wigglers (for ex. for CLIC DR)
Resistance of the connection 10-10- 10-13 Ohm

## Slide 7: Nested coils
1-st section
2-nd section
SC wire critical curve

## Slide 9: Current lead design
Cryocooler cold head
Brass leads
Cu plate
HTS leads
SC leads
Cryocooler 1st stage
Cryocooler 2nd stage
Sapphire insulating plate

## Slide 10: Cold mass support structure
Cold mass is hung on Kevlar strings attached to the cold mass support base on one side and to the vacuum vessel on the other.
Kevlar strings
Vertical support point
Vertical support points
Horizontal position fixing points
Horizontal position fixing points
Support system:
3 vertical support points;
4 horizontal support points;
4 transport position stoppers
Cold mass base frame
Transport position keepers

## Slide 11: The history of superconductive ID fabrication in the Budker INP
1979 – first in the world 3.5 Tesla superconducting 20 pole wiggler (SCW) for VEPP-3
1984 – 5 pole 8 Tesla superconducting wiggler for VEPP-2
1985 – 4.5 Tesla Superconducting Wave Length Shifter (WLS) for Siberia-1, Moscow
1992 – 6 Tesla Superbend (SB) prototype for compact storage rings
1996 - 7.5 Tesla superconducting WLS for PLS, South Korea
1997 - 7.5 T superconducting WLS with fixed point of radiation for CAMD-LSU (USA)
2000 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2000 – 10 Tesla WLS for Spring-8, Japan
2001 – 7 Tesla WLS with fixed radiation point for BESSY-2, Germany
2002 – 3.5 Tesla 49 pole SCW for ELETTRA, Italy
2002 – 7 Tesla 17 pole SCW for BESSY-2, Germany
2004 – 9 Tesla Superbend for BESSY-2, Germany
2005 – 13 Tesla superconducting solenoids for VEPP-2000
2005 – 2 Tesla 63 pole SCW for CLS, Canada
2006 – 3.5 Tesla 49 pole for DLS, England
2006 – 7.5 Tesla 21 pole SCW for Siberia-2, Moscow
2007 – 4.2 Tesla 27 pole SCW for CLS, Canada
2009 – 4.2 Tesla 49 pole SCW for DLS, England
2009 – 4.1 Tesla 35 pole SCW for LNLS, Brasil
2010 - 2.1 Tesla 119 pole SCW for ALBA, Spain
2012 - 4.2 Tesla SCW for Australian Light Source
2012 – 7.5 Tesla SCW for CAMD-LSU (USA)
2013 - SCW for ANKA
2013 - SCW for ANKA & CLIC with indirect cooling
2013 – 2 SCW for Siberia-2,

## Slide 12: Indirect cooling conception
LHe vessel
SC magnet
He fill/vent turret
20 K radiation shield
60 K radiation shield
Beam chamber
Beam chamber
thermal link to cryocooler
LHe piping
Direct cooled magnet (magnet in bath cryostat)
Indirect cooled magnet (magnet in isolation vacuum)
Advantages of indirect cooling
Easy access to the magnetic system and to the beam vacuum chamber
Possibility for exchanging of the elements of magnetic system (and whole system) without complex operation
Possibility for exchanging the beam vacuum chamber
Possibility for installing of the wigglers in the halls with lower ceilings
Effective using of the magnetic gap

## Slide 13
Pole gap and electron beam vertical aperture
Direct cooling magnet with liquid
helium (magnet in bath cryostat)
Indirect cooling magnet
Magnet in insulating vacuum
Pole gap= V aperture + 4 mm
Pole gap = V aperture + 1.5 mm

## Slide 14: Superconductive undulator for APS
He recondenser
60 K radiation shield
20 K radiation shield
LHe vessel
Cold mass base frame
Cryocooler
Current lead assembly

## Slide 15: CLIC Damping ring

## Slide 16: General view ANKA/CLIC wiggler
Total number of poles | 72
Number of main poles | 68
Number of additional poles | 4
Period | 51 mm
Magnetic gap | 18 mm
Peak magnetic field on the main poles | 3 T
Currents | 243 A x4
Stored energy | 60 kJ
Aperture | 13 mm x
Additional requirements
Possibility for exchanging of the magnetic system in future
Possibility for exchanging of the beam vacuum pipe
Heating vacuum pipe till 90 K
Heating vacuum pipe with power load up to 50 W (with keeping temperature about 40 K)
Possibility of activation of the NEG-coating (up to 200o C)

## Slide 17: Future plans
LHe free cooling conception wit using heat pipe
Winding technology

## Slide 18: 4th Asian Forum for Accelerators and Detectors
Accelerator and its related technologies for photon science
Accelerator and its related technologies for hadron (neutron) science
Detector Technology Development
Accelerator and its related technologies for Industrial & Medical Applications
R&D for innovative accelerators
Network & Computing
http://ssrc.inp.nsk.su/conf/AFAD2013/
25 - 26 February, 2013, BINP, Novosibirsk, Russia