## Slide 1
Injection Into Low Lifetime USRs
R. Hettel, SLAC
USR Accelerator R&D Workshop
Huairou (Beijing), China
October 31, 2012

## Slide 2
Touschek-dominated lifetime

## Slide 3
Top-up injection
  Limit change in total charge Dqtot between injections to small fraction r of total qtot :
  For a given injection charge qinj (= Dqtot), injection must occur with repetition rate fi, time interval ti = 1/fi:
for ti << t(0)

## Slide 4
Injection into PEP-X (baseline design) – case study
An “extreme” case:
h = 3492 nb = 3400 Trev = 7.336 ms t(0) = 1800 sec
itot = 1.5 A qtot = 11000 nC ibavg = 0.44 mA qbavg = 3.23 nC
Dqinj/qtot = r = 0.1%
 Dqinj = ~10 nC every 1.8 s
ti = 1.8 s

## Slide 5
Case study: injection conditions
  0.1% current constancy: must restore 10 nC in n bunches every 1.8 s.
  Want to limit the variation in bunch charge in all buckets to the < ~20%  Dqb < ~ 0.7 nC for 3.5-nC bunches.
  Top-up injection from linac or linac+booster must supply just 10 nC in n bunches every 1.8 seconds.
  Swap-out (bunch replacement) injection must restore 10 nC + the total charge remaining in n bunches (e.g. ~300 nC in a 100-bunch train).
  Injected charge from linac or linac+booster injector typically limited to <~1 nC/bunch, with up to ~10 nC total multibunch
     swap-out limited to replacing ~10 nC in ~20-bunch trains (0.5 nC/bunch)  total current limited to ~160-190 mA, depending on kicker rise/fall times and requisite gaps between trains in ring
  Injected bunch from accumulator can have higher charge/bunch and longer trains  total current of 1.5 A is possible.

## Slide 6
Case study: injection example 1
FILL PATTERN 1: top-up (or replace) each bucket sequentially @ 10 Hz, beginning with bucket 1, ending with bucket 3400, leaving a gap of 92 buckets. Total average charge constancy <0.1%.
finj = 10 Hz
qinj = 0.613 nC for top-up
decay of bunch charge before top-up every 3400 injection cycles (340 s)
bunch pattern after top-up of bunch #3400
fractional variation of bunch charge from average after top-up of bunch #3400
20%

## Slide 7
Case study: variation of injection pattern 1
a different spatial frequency spectrum

## Slide 8
Case study: injection examples
FILL PATTERN 2: fill every nb/10 (= 340) buckets in sequence
FILL PATTERN 2: variation
FILL PATTERN 3: fill every nb/68(= 50) buckets in sequence
etc….

## Slide 9
Short lifetime injection: conclusions
  Frequent injection is needed to achieve 0.1% current constancy: injection interval = 0.1% of beam lifetime. Perhaps only 1% constancy is necessary.
  Linac or linac+booster can satisfy top-up injection requirements for high current, low-lifetime machines.
  For swap-out injection, total ring charge and current is limited using linac or linac+booster (e.g. <200 mA for 1.5 km ring).
  High total current can be sustained with injection from an accumulator.
  Swap-out injection requires kickers with fast rise/fall times and extremely flat tops (not addressed here).