## Slide 1: A compact low emittance lattice with superbends for Sirius
Liu Lin （刘 琳 ）
LNLS Accelerator Physics Group

## Slide 2: A Penultimate Storage Ring lattice for Sirius
Liu Lin （刘 琳 ）
LNLS Accelerator Physics Group

## Slide 3: Why Penultimate SR ?
Not yet diffraction limited for X-rays.
  e ≈ 0.25 nm.rad
Challenging but will become reality in the near future with technology ‘available’ today at reasonable cost.
  Sirius Budget:
  building US$ 100 M
  accelerators US$ 100 M Total: US$ 320 M
  13 beamlines US$ 120 M
  Sirius Schedule:
  2009 Initial design and prototypes
  12 / 2010 Sirius receives green light from the Brazilian Federal Government
  07 / 2012 New 5BA low emittance design
  09 / 2013 Start of building construction
  09 / 2015 Start of machine installation
  05 / 2016 1st beam
l | = e
4p | 

## Slide 4: Sirius – a new Brazilian Light Source
LNLS
Campinas – São Paulo
Area | 8.5 x 106 km2 | World rank 5th
Population | 195 million people | World rank 5th
GDP | $2.48 trillion per year | World rank 6th
Source: SRS Daresbury Laboratory
About Brazil

## Slide 5: LNLS campus today
Sirius
UVX
1.37 GeV – 100 nm.rad
Designed and built in Brazil
Constructed from 1987 – 1997

## Slide 6: Sirius layout
STORAGE RING
3 GeV
LINAC
150 MeV
BOOSTER
3 GeV
Energy | 3.0 | GeV
Circumference | 518.2 | m
Emittance no IDs | 0.28 | nm.rad
Straight sections | 10 x 7-m 10 x 6-m | 

## Slide 7: The Sirius low emittance storage ring lattice
Energy: 3 GeV
20 modified 5BA cells with low field main dipoles (0.58 T)  100 dipoles.
Split central dipole to accommodate a 2 T “superbend”  longitudinal field gradient.
Use of permanent magnet technology for the dipoles  more compact lattice.
Dipoles with transverse gradient to increase Jx.
Low field dipoles  lower energy dispersion  smaller beam size.
Low field dipoles  efficient use of damping wigglers.
Straight sections: 10 x 7-m, 10 x 6-m
quadrupole
doublet
0.58 T dipole
q=16.6°
2 T dipole, q=1.4°
superbend
quadrupole
triplet
7-m SS
6-m SS

## Slide 8: Superbends: hard X-ray source
2T superbend
12 keV critical energy
Beam size @ 1% coupling |  | 
straight section | 68 x 3 | mm2
superbend | 11 x 4 | mm2
Hard X-ray dipole source with modest total energy loss
X-rays are produced only at beamline exit

## Slide 9: Superbends: longitudinal gradient
- without superbends: e = 0.31 nm.rad
with superbends: e = 0.28 nm.rad 10% reduction
  Same effect as one 5.5-m damping wiggler

## Slide 10: Permanent magnets for dipoles
Strong magnetic field (hard X-ray) only at beamline exit
  Lower radiation power from dipoles
      → Lower investments in high power RF equipment.
  → Lower investments in vacuum equipment.
  Lower operational costs (RF power generation and cooling) .
Permanent magnet dipoles
  Lower investments in power supplies and cooling systems.
  Lower operational costs.
  Higher reliability.
NdFeB
Low carbon steel
Aluminum
Field trimming
366 mm

## Slide 11: Storage ring operation modes – 1
AC20 Mode
Users want low bx sections

## Slide 12: Storage ring operation modes – 2
AC10 Mode

## Slide 13: Parameters
 | AC20 | AC10 | 
Horizontal betatron tune | 44.60 | 46.25 | 
Vertical betatron tune | 11.64 | 14.15 | 
Natural horizontal chromaticity | -108.0 | -113.2 | 
Natural vertical chromaticity | -72.8 | -80.1 | 
Momentum compaction factor | 1.74 x 10-4 | 1.74 x 10-4 | 
Touschek Lifetime @ 500 mA, 1% coupling | 5.6 | 4.9 | h
Dipole field gradient | -7.8 | -7.8 | T/m
Maximum quadrupole gradient, B’ | 33.5 | 39.6 | T/m
Maximum sextupole gradient, B”/2 | 1900 | 1800 | T/m2

## Slide 14: Non-linear optics optimization – 1
AC10 Mode
AC20 Mode
Optimization using MAD (CERN), OPA (SLS), Tracy3 (Soleil) and AT

## Slide 15: Non-linear optics optimization – 2
AC10 Mode
AC20 Mode
Dynamic aperture calculations
- Tracking for 5000 turns.
Alignment and excitation errors.
Systematic multipole errors.
Random multipole errors.
Results up to now
- Alignment errors dominate DA reduction. Optics is affected by off-centered orbit in sextupoles.
DA improves by restoring design optics.
Special care with orbit correction at sextupoles. Place BPMs close to strong sextupoles.
Still need to improve AC10 mode.

## Slide 16: Injection
For the time being we keep up the 2 possibilities:
– Local bump with 4 kickers
– Injection with pulsed multipole magnet (PMM) + on-axis kicker
PMM Injection

## Slide 17: Present challenges for Sirius
Strong magnets  small bore dadius  Small aperture for vacuum chamber  copper chambers + NEG coating
Small ring emittance  small booster emittance  in-tunnel booster
Beam stabillity  tight alignment tolerances  floor stabillity  BPM stability and accuracy  power supply stability
Injection  PMM design
Dynamic aperture optimization especially for AC10 mode, centering of the orbit at sextupoles
Effects of IDs, instabilities, IBS, ...

## Slide 18
Thank you !