## Slide 1
Development of the Muon Trigger Detector for the muEDM Experiment at PSI
Xingyun Huang
2026/07/16

## Slide 2
Motivation
01.
Muon Trigger Detector
02.
Test Beam 2025
03.
Conclusion
04.

## Slide 3: Motivation
Matter-antimatter asymmetry:
Sakharov Conditions: CP violation is necessary
In SM, CP violation mainly comes from phase of CKM matrix, far from enough to explain Matter-antimatter asymmetry
Search for EDM of muon:
CP violation also contribute to the EDMs of elementary particles
Several BSM theories give much higher EDM values compared to SM

## Slide 4: Frozen-spin technique
muEDM Experiment at PSI:
Phase 1: 28 MeV/c beam aim at a sensitivity of 10-21 e﻿⋅cm
Phase 2: 125 MeV/c beam aim at a sensitivity of 10-23 e﻿⋅cm
～mrad
FNAL/J-PARC
g-2 experiment
muEDM experiment
with frozen-spin
Frozen-Spin technique:

## Slide 5: muEDM Experiment at PSI
Animation by C. Dustov

## Slide 6: muEDM Experiment at PSI
Animation by C. Dustov
Sensitivity from the asymmetry, “PENTA”:
EDM signal

## Slide 7: Muon Trigger Detector
Only roughly 500 out of 120 kHz could be stored.
MTD is responsible for detecting the injection of the muons and distinguishing wether it could be stored.
If the muon could be stored, a TTL signal is sent to the Kicker system.
Requirements of the MTD:
Fast enough to trigger the kicker.
High coincidence and anti-coincidence efficiencies.

## Slide 8: Development of the Muon Trigger Detector
Minimal setup, decided detector options
Demonstrated anti-coincidence trigger scheme
Test beam 2022: proof-of-concept
Test beam 2024: prototype v1
Test beam 2025: prototype v2
Test in PSC solenoid w/ off-axis injection
Demonstrated fast electronics with ns
Validated detector response
Near-full muEDM experimental conditions
High B-field, 25.8 MeV/c beam
Vacuum friendly construction
Overall mechanical integration

## Slide 9: Gate scintillator
﻿Geometry constraining the scattering angle 𝜽 ≤ 𝟏. 𝟒 𝒅𝒆𝒈
0.1 mm thickness give optimal results
Decide the thickness of gate scintillators:
Too thin: no enough photon to trigger SiPMs
Too thick: strongly distrube the motion of muons
DOI: 10.1016/j.nuclphysbps.2024.05.014
DOI: 10.1007/s41605-025-00570-4

## Slide 10: Aperture scintillator
89.9%
92.5%
Study the acceptance and rejection efficiencies and optimize apertures
Phase spaces are obtained to guide the design of Aperture

## Slide 11: Electronics
Electronics sketch of the trigger detector during TB24

## Slide 12: Fast electronics
SiPM
Amplifier
Discriminator
Converter
SiPM
Amplifier
Discriminator
Converter
SiPM
Amplifier
Discriminator
Converter
SiPM
Amplifier
Discriminator
Converter
AND
AND
AND
NAND
To Coil
VCC
To DAQ
SiPM
Amplifier
Discriminator
Converter
SiPM
SiPM
SiPM
SiPM
SiPM
Gate Detector
Aperture Detector
To DAQ
DOI: 10.1109/TNS.2025.3578674

## Slide 13: Test Beam

## Slide 14: Propagation delay
Run 448
Muon beam
Anti-coincidence trigger
Time of arrival (ToA) analysis to obtain propagation delay,
Run 442
Muon beam
Gate quad coinc. trigger
TB24: ns

## Slide 15: Event topology
Storable muons
Unstorable muons
Unstorable but triggered
Storable but not triggered
No
Coincidence efficiency:
Anti-coincidence efficiency:
False anti-coincidence rate:
False coincidence rate:

## Slide 16: Event topology
Anti-coincidence efficiency derived from event topology fractions:
96.29%
DAQ Triggered by Anti-coincidence

## Slide 17: Event topology
Anti-coincidence efficiency derived from event topology fractions:
96.29%
With event selection by ToT cut*: 99.48%
Agreement with TB24 results: 99.5%
Further analysis to understand coincidence efficiency
With Muon Selection
DAQ Triggered by Anti-coincidence

## Slide 18: Conclusion
muEDM experiment aims at the sensitivity of 10-23 e·cm with frozen-spin technique.
Muon Trigger Detector is responsible for distinguishing storable muons and trigger kicker coil.
  Fast enough to store muons. tpd < 15 ns
  Very precise to increase trigger efficiencies.
Latest version was tested during Test Beam 2025 at PSI
  Propagation delay was measured to be 6.46 ns, smaller than the requirement
  Anti-coincidence was measured to be 99.48%, agree with result of TB24.
MTD upgrade
  Main functions outside of the vacuum chamber: stable environment and eazy to debug
  Hermetic veto detector and more SiPM channels
  Reliable anti-coincidence logic: Gate and Aperture arrival mismatch.

## Slide 20
Test Beam 2022
﻿Gate-exit coincidence leads to > 70% accepted events
No significant difference between beam tunes
Published: https://doi.org/10.1007/s41605-025-00570-4

## Slide 21: Test Beam 2024
Test beam 2024: prototype v1
Coincidence Logic
Anti-coincidence Logic
Key Parameters and Requirements

## Slide 22: Gate distinguishing vs
Charge distribution of Gate detector in TB24, indicating a clear separation of vs
Gate trigger threshold set to select will filter out events

## Slide 23: Sensitivity of muEDM experiment

## Slide 24: Aperture Simulation
musrSim simulation was conducted to study the acceptance and rejection efficiencies and optimize apertures
Different configurations are tested.

## Slide 25: Hermetic Veto Detector
One single aperture scintillator is not sufficient to distinguish storable muons and measure the performance of the beam.
Hermetic veto detector is needed. Electronics need to be updated.
Dimensions (mm): 5*130*80
4 channel readout
Output to discriminator (anti-coinc. TTL production): 2 ch
Dimensions (mm): 100*100*5
2 channel readout
Output to discriminator (anti-coinc. TTL production): 1 ch
Dimensions (mm): 60*5*110 per side
4 channel readout
Output to discriminator (anti-coinc. TTL production): 2 ch

## Slide 26: Upgrade MTD electronics
SiPM
Amplifier
Discriminator
Converter
SiPM
Amplifier
Discriminator
Converter
SiPM
Amplifier
Discriminator
Converter
SiPM
Amplifier
Discriminator
Converter
SiPM
SiPM
SiPM
Gate Detector
Aperture Detector
SiPM
Amplifier
Discriminator
Converter
Amplifier
Discriminator
Converter
AND
AND
AND
NOR
DS1100-20
Time Delay
AND
ToKicker
4, 8, 12, 16, 20 ns
Delay are avaliable

## Slide 27: PCBs
Coincidence Board
Gate Board
Aperture Board

## Slide 28: Propagation delay test
Propagation Delay between input and TTL signal of Coincidence Board was estimated.
SiPM.signals were replaced by function generator signals.
Cable length was controlled to be same.
tpd of Amplifiers was estimated to be 3 ~ 5 ns, while Tianqi assume to be 0.
tpd of Gate part was estimated to be 11.2 ns, tpd of Aperture part was 10.6 ns.
Amplifier
Aperture
Gate
Labels:
CH1(Yellow): Input Signal
CH2(Red): Amplified Sig
CH4(Green): TTL Signal

## Slide 29: Time match between Gate and Aperture
tpd of Gate part was estimated to be 11.2 ns, tpd of Aperture part was 10.6 ns.
If hit time of Gate and Aperture matches, the anti-coincidence logic will work properly.
CH1(Yellow): Gate signal CH2(Red): Aperture signal. CH4(Green): TTL signal
Only Gate signal
Both Gate and Aperture signals

## Slide 30: Time match between Gate and Aperture
If AA is several nanoseconds later than Gate, then a narrow TTL will be generated.
Aperture input signal was delayed for 5 ns with an extra 1 m co-axial cable.
CH1(Yellow): Gate signal CH2(Red): Aperture signal. CH4(Green): TTL signal
Only Gate signal
Both Gate and Aperture signals

## Slide 31: Time match between Gate and Aperture
Aperture input signal was delayed for 5 ns with an extra 1 m co-axial cable.
Gate was delayed for 4 ns with Time-Delay Module.
tpd of Gate reaches 16.55 ns, 30Hz/1kHz narrow TTL were output.
CH1(Yellow): Gate signal CH2(Red): Aperture signal. CH4(Green): TTL signal
Only Gate signal
Both Gate and Aperture signals

## Slide 32: Time match between Gate and Aperture
Aperture input signal was delayed for 5 ns with an extra 1 m co-axial cable.
Gate was delayed for 8 ns with Time-Delay Module.
tpd of Gate reaches 21 ns, 30Hz/1kHz narrow TTL were output.
CH1(Yellow): Gate signal CH2(Red): Aperture signal. CH4(Green): TTL signal
Only Gate signal
Both Gate and Aperture signals

## Slide 33: Time Walk Correction
Before time walk correction
After time walk correction
Timewalk correction process:
Divide ToT to several bins
For each ToT bin, calculate Avg(ToA)
Fit Avg(ToA) vs ToT curve: f(ToT)
For each hit, ToA_Corr = ToA_raw – f(ToT_raw)
Propagation delay is obtained by: tPD = ToA_TTL – ToA_Gate

## Slide 34: Propagation delay
Run 448
Muon beam
Anti-coincidence trigger
Time of arrival (ToA) analysis to obtain propagation delay,
Run 442
Muon beam
Gate quad coinc. trigger
TB24: ns
After time walk correction

## Slide 35: Inlab Propagation Delay Test
Before Time Walk Correction
After Time Walk Correction

## Slide 36: ToT cut selection