## Slide 1: ADC DAQ system firmware
Ming-Kuan Yuan
Fudan University
2026/4/17
Weekly report

## Slide 2: Hardware
Mother board
  8 RJ45 connector
  Three lvds differential pair
ADC sub-board
  RJ45
  4 ADC chip
Communication
  One lvds for slow control
  One lvds for data transfer
  One lvds for clock split
Mother board
RJ45 connection
ADC sub-board

## Slide 3: Firmware – mother board
Architecture
PC
Configure files
Events data from FPGA
Mother board
SITCP
UDP
TCP
Ethernet
RBCP REG
Packet
dataEncode
x8
To sub-board
deformat
dataDecode
x8
packet
Data form sub-board

## Slide 4: Firmware – mother board
Control data frame
Control frame to sub-board
  SOF0, SOF1, ADDR_L, ADDR_H, COM, DATA, EOF
Test
Board = 0, Reg ADDR = 20, COM = 1, DATA = 5A
Board = 0, Reg ADDR = 21, COM = 1, DATA = 5B
  SOF0 = 0x5A
  SOF1 = 0xA5
  EOF = 0xc3

## Slide 5: Firmware – sub board
Architecture
ADC sub board
ADC data collection
dataDecode
Deformat
I2C
SPI
Trigger
Packet
dataEncode
SUB_REG
Clock chip
ADC chip
ADC data
From mother board
To mother board
Next step: finish configure side on sub-board and test the communication between mother board and sub board.
byteClk = 20M
Num_byte = 4106 byte
Event rate: ~5 kHz