## Slide 1: Retrofitting CSNS Utility Controls: Transition from Commercial SCADA to EPICS
Shaoxing Liang
China Spallation Neutron Source, Institute of High Energy Physics, CAS
2026/10/28

## Slide 2
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
Originally monitored and controlled by commercial SCADA platforms

## Slide 3
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
it brings
Although commercial SCADA

## Slide 4
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
The growing number of subsystems and projects makes unified management challenging
BNCT01：Boron Neutron Capture Therapy Facility 01
SAPS_TP：Southern Advanced Photon Source Test Platform
To achieve a unified utility control system, we will implement the EPICS distributed control system in phases

## Slide 5
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
EPICS Architecture Diagram
The EPICS system upgrade comprises four modules:
1.PLC-EPICS IOC Integration,
2.Data Archiving,
3.Phoebus-based HMI Reconstruction,
4.and Alarm Management System

## Slide 6
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
Name | Version | Purpose | Status
EPICS Base | 7.0.8.1 | EPICS Core | Deployed
ASYN | 4-38 | Asynchronous communication driver support | Deployed
modbus | R2-11 | Modbus protocol, such as Inovance PLC | Deployed
s7nodave | 3.0.2 | Siemens PLC | Deployed
Common Device Support Modules :
Additional extended functions will be further deployed and refined in the future
PLC-EPICS IOC Integration
1
Current Operation Status: Good, no errors

## Slide 7
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
Name | Version | Status
Apache-tomcat | 9.0.120 | Deployed
Archappl | V2.0.10 | Deployed
Implemented based on EPICS Archiver Appliance:
Data Archiving
2
Additional extended functions will be further deployed and refined in the future
Current Operation Status: Good, no errors
Archiver Appliance Management Interface in Use

## Slide 8
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
Phoebus-based HMI Reconstruction
3
Name | Version | Status
Phoebus | 4.7.4-SNAPSHOT | Deploying
Proposed Version of CS-Studio Phoebus :
Historical Trend Interface in Use
Process Flow Interface in Use
Progress: Basic features under ongoing development

## Slide 9
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
Alarm Management System
4
Name | Version | Purpose | Status
Zookeeper | 3.8.4 | Cluster coordination & service discovery | Deployed
Apache Kafka | 2.13-3.5.1 | Alarm message streaming & buffering | Deployed
Elasticsearch | 8.11.0 | Store & query historical alarm records | Deployed
Alarm Server | 5.0.5 | Monitor EPICS PVs, manage active alarms & ack | Deployed
Alarm Logger | 5.0.5 | Consume alarm stream and persist logs | Deployed
Progress: Basic features under ongoing development
Historical Alarm Test Screen in Use

## Slide 10
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
The migration is carried out without interruption to equipment operation. Commercial SCADA and EPICS run in parallel, while O&M staff get familiar with the new workflow.
The basic functions of data acquisition, data archiving, data query and operational alarm have been initially implemented. Extended features and further improvements will be developed on this basis.

## Slide 11
This lightning talk presents the utility control system migration project at the China Spallation Neutron Source (CSNS)
That’s all for my introduction.
Thank you!