## Slide 1
Development Progress of CiADS Muon Source
Muon Science and Technology application platform at CiADS (MuST-CiADS)
Institute of Modern Physics, Chinese Academy of Sciences
Hanjie Cai, Jincheng Li
on behalf of MuST-CiADS team
MuMu Forum -- Muon Physics and Muon Technologies Innovation Academic Forum
July 12-13, 2026, Beijing, China

## Slide 2
Contents
Background
Development Progress of CiADS MuST
Summary

## Slide 3
Background

## Slide 4
Muon source applications
Condensed Matter Physics (Magnetic materials, superconductors, semiconductors, quantum spin liquid)
Particle Physics
(g-2, Mu2e, COMET, MEG, Mu3e,, MACE, muEDM, etc.)
Nuclear/Atomic Physics
(strong-field QED test, nuclear fine structure, precision atomic spectroscopy)
Elemental Analysis; Muography; Biophysics; Chemistry; Muon-Catalyzed Cold Fusion
Superconductor transition-edge calorimeter for X-ray measurement

## Slide 5
Muon sources
5 muon sources and several muon beamlines
Maximun surface muon rate ~1E8/s for both CW beam at PSI and pulsed beam at J-PARC

## Slide 6
Several muon experiments and applications have been proposed in China
Efforts are underway to develop muon facilities at CSNS,HiAF,CiADS and SHINE
Soon, we will see first muon beam in China
Future high-precision experiments and applications call for an intensity of 109~1011μ/s
1. Higher intensity
The trends
Publications related to muon source:
increases rapidly in the last decade
2. New facility

## Slide 7
Development Progress of CiADS MuST

## Slide 8: CiADS
Experimental hall for high-power beam applications
CiADS: China-initiative Accelerator-Driven Subcritical system, the world`s first megawatt-level ADS research facility
Construction Period: July 2021 – July 2027
The Superconducting Linear Accelerator
• Proton Beam Energy: 600 MeV
• Proton Beam Current: 5 mA
• Operation Mode: CW or Pulsed
CiADS
HIAF
HIAF/CiADS
Location: Huizhou city
100 kilometers
5-mA Proton Beam

## Slide 9: CiADS
The Reactor Hall
The Experiment Hall
2026.1
The Superconducting Linac

## Slide 10: Timetable of CiADS Linac
  3 MW Commissioning
  Normal operation with MW-level proton beam
2027~2030
  Accelerator stability study
  Beam to the subcritical reactor and other terminals
2026～2027
25 kW:
500MeV & 50μA
  Assembly
  Commissioning
2025～2026
250 kW:
500MeV & 500μA
3 MW:
600MeV & 5mA
Beam time of the linac
3 months for the subcritical reactor
8–9 months for other terminals, including the muon source

## Slide 11: Layout and Plan of MuST
Conceptual Layout:
Each of the two tandem target feeds two muon beamlines, approximately mirror-symmetric to each other
To deliver muon beams to 6 terminals, with the intensity varies from 107/s~1010/s
Plan with two phases：
Phase | Target | Muon beamlines |  | Applications
Phase I 2025~2029 | Tgt a （MuT-a） | up to 108μ/s @0.5mA | R1: ~30MeV/c | μSR/MACE
 |  |  | L1: to 90MeV/c | MIXE/μCF
Phase II 2029~2032 | Tgt b（MuT-b） | up to 1010μ/s@5mA | R2: to 90MeV/c | μSR/MACE
 |  |  | L2: to 120MeV/c | Muography/MIXE
Phase | Target | Muon beamlines |  | Applications
Phase I 2025~2029 | Tgt a （MuT-a） |  | R1: ~30MeV/c | μSR/MACE
 |  |  | L1: to 90MeV/c | MIXE/μCF
Phase II 2029~2032 | Tgt b（MuT-b） |  | R2: to 90MeV/c | μSR/MACE
 |  |  | L2: to 120MeV/c | Muography/MIXE
MuB-R1
Target station
MuT-a
Target stationMuT-b
Muon beam lines
Muon beam lines
Proton beam
MuB-L1
MuB-R2
MuB-L2

## Slide 12
Development of the target
The first prototype
Compact structure (Φ400mm) can operate well under a thermal power of ~25 kW.
lant angle of 20°, effective thickness of 1 cm
Current(mA) | Temperature (℃) | Thermal stress (MPa) | Deformation (mm)
0.5 | 622 | ＜8.8 | 0.50
1.0 | 1096.4 | ＜14.9 | 0.64
2.0 | 1359.3 | ＜23.8 | 0.79
slant angle of 10°, effective thickness of 2 cm
The second prototype

## Slide 13: Development of the target
Concept of the liquid lithium jet target
H.-J Cai et al, PRAB 27, 023703, 2024
Li target VS C target
Li target VS C target
  ×2 higher surface muon yield
  less radioactive nuclide and positrons background
  supporting higher beam power, free of irradiation damage

## Slide 14: Development of the target
  The liquid lithium loop operated successfully;
  The First-stage experiments have been finished;
  The electromagnetic pump need to be exchanged for a higher mass flow.
Cooperated with Zongbiao Ye, Sichuan University

## Slide 15: Development of the Collimators
The emittance will increase significantly after the beam penetrating the target: from ~1 mm·mrad to ~30 mm·mrad
A combination of collimators and quadrupole magnets is used to control the beam envelope and suppress beam loss
After optimization, the beam loss along the whole line is well below 10 W/m
Target station（MuT-b）
Target station（MuT-a）
Proton beam
Collimators
Collimators

## Slide 16: Development of the Collimators
The emittance will increase significantly after the beam penetrating the target: from ~1 mm·mrad to ~30 mm·mrad
A combination of collimators and quadrupole magnets is used to control the beam envelope and suppress beam loss
After optimization, the beam loss along the whole line is well below 10 W/m
Collimators were designed to work at 3-MW-proton beam
Thermal performance under a heat load of 32kW
Proton beam
Collimators
Collimators

## Slide 17: Development of the capture solenoid
Capture field design
To obtain a high capture efficiency
To reduce deflection effect of proton beam by fringe field
Field map of the front-end section
Armor
MgO
Copper
Water
Configs | Inner radius (mm) | Layers | Quantity | I (A) | dT (℃) | P (bar)
1 | 300 | 5 | 1 | 2130 | 22 | 5
2 | 360 | 4 | 2 |  |  | 
3 | 370 | 4 | 3 |  |  | 
4 | 380 | 4 | 3 |  |  | 
5 | 390 | 4 | 3 |  |  | 
6 | 400 | 4 | 2 |  |  | 

## Slide 18: Development of muon beam monitor
Design specifications for the monitor
Position resolution: <5mm
Time resolution: 1ns
Trigger rate: 5MHz
Electronics dead time: 1%
Electronics design
Design of the muon beam monitor Sci-Fi +SiPM
Reconstruction of the muon beam
Cooperated with Jian Tang, Sun Yat-sen University

## Slide 19: Development of MuSR Spectrometer
Objective performance
Conceptual design of a general-purpose μSR spectrometer
Cooperated with Ziwen Pan, USTC

## Slide 20: Progress of muon beamlines design
Design of muon beamline
Three dipoles to avoid a direct line-of-sight to the target
Solenoid + QM focus surface muon beam into Φ30mm for μSR experiments
Intensity: ~5.6E6 μ+/s @ 0.5mA，Polarization~96.4%，Background_rate＜0.1%, Momentum~27.0±1.0MeV
Conceptual layout of 4 beamlines
RMS envelope
Transmission
Within Φ300mm, overall efficiency of ~0.11% and intensity of ~2.1E7 μ+/s @ 0.5mA
Fucused into Φ30mm
Phase I, Line R1

## Slide 21: Progress of muon beamlines design
Design of muon beamline
Full solenoid focusing for high-intensity surface/decay muons.
Aperture of Φ300mm to be cost-effective
An overall efficiency of ~1.2% and ~3E8 μ+/s surface muons @ 0.5mA
Conceptual layout of 4 beamlines
RMS envelope
Transmission
Within Φ300mm, overall efficiency of ~1.2% and intensity of ~3E8 μ+/s @ 0.5mA
Fucused into Φ300mm
Phase I, Line L1

## Slide 22: Progress of muon beamlines design
Design of muon beamline
Solenoid aperture of Φ500mm and double Wien-filters for a high efficiency
Towards 10 billion muon rate:
Surface muon: ~1E10 μ+/s @ 5mA
Decay muon (80 MeV/c): ~3E9 μ+/s and ~5E8 μ-/s @ 5mA
Conceptual layout of 4 beamlines
RMS envelope
Transmission
Within Φ500mm, overall efficiency of ~3.9% and intensity of ~1E10 μ+/s @ 5mA
Fucused into Φ100mm
Phase II, Line L1

## Slide 23: Summary
The conceptual design of the muon beamlines has been completed. The beam parameters are very competitive.
The development of the targets, the proton beam collimators, the muon beamline components and the MuSR spectrometer is ongoing, and good progress has been achieved.
The first muon beamline has entered the TDR phase. We warmly welcome collaborations and precious advice.

## Slide 24
Thank you so much！