## Slide 1: Super-MuSR – the next generation muon spectrometer at ISIS
Rhea Stewart (rhea.stewart@stfc.ac.uk)
MELODY 2026, Dongguan
24th October 2026
Peter Baker, James Lord, Adrian Hillier & Alex Louat

## Slide 2
A note about pulsed and continuous muon sources
The MuSR instrument today
The Super-MuSR upgrade
  Main components
  Expected performance
Scientific opportunities
Technical progress
Summary and timeline
Talk Outline
Notes: To replace photo with one of your own. 1) Send the geometric shape overlay to the back – Right-Click > Send to Back > Send to Back. 2) Replace image – use the guides provided to correctly position it. 3) Send your image to the back so that the geometric overlay re-appears over the image. Please remove or amend the image credit if you are using a different image to the one provided.

## Slide 3
Types of muon source – pulsed and continuous
Continuous
Pulsed
Pulsed sources | Continuous sources
Bursts of many muons | Single muons
Frequency resolution set by pulse width (~ MHz) | Frequency resolution set by electronics (~ GHz)
Low intrinsic background | Higher intrinsic background
Flypast for small samples | Active collimation for small samples
Large detector arrays needed | Simple detector systems
Notes: Showing that muon experiments are currently possible at two types of source and that each type of source has different strengths and challenges that dictate the most appropriate instrumentation. Highlight that may experiments currently need to use both types of source but that developments at many muon facilities are working towards blurring the distinction between the sources. Perhaps show an example data set (that could be done wholly on Super-MuSR) and explain why two experiments were needed.

## Slide 4
First MuSR instrument was built in 1987 with 32 detectors
Upgraded in 2004 with 64 detectors
Mostly studies quantum magnets and superconductors
Experiments are often at very low temperatures:
  70% dilution fridge (0.05-4K)
  20% 3He cryostat (0.25-10K)
  10% 4He cryostat (1.5-300K)
  CCR, flow cryostats, and furnace barely used
MuSR at ISIS Today

## Slide 5
µ+
~ 50ns
MuSR at ISIS Today
Detectors | 64
Solid angle coverage | 40%
Count rate (MEv/h) | 70
Maximum frequency (field) | 8MHz (0.06T)
Spin rotation | None
Smallest sample (mm) | ~10×10 on Ag
Muon pulse width (ns) | ~ 50
Muon rate at sample point | ~ 105 μ+s-1
% beam used | ~ 10% (!)

## Slide 6
MuSR's current performance
Decrease muon pulse width
Increase detector coverage and segmentation

## Slide 7
Super-MuSR upgrade
Two spin rotators with up to 75° spin rotation

## Slide 8
Super-MuSR upgrade
"Pulse slicer" to provide variable 10-50ns muon bunches

## Slide 9
Super-MuSR upgrade
New spectrometer and detector design
plastic scintillator
+ PMT
+ clear long light-guide
FROM:
TO:
960 tiles
2. 32 staves
3. 1 barrel
Barrel fits inside the magnet.

## Slide 10
Super-MuSR upgrade
Digitising DAE and event mode data collection
DAQ121 is a 1 G·S·s-1 12-bit Streaming Digitiser
A bespoke development for Muon Spectrometers at ISIS
Controlled from IBEX
ISIS Status
Packet (Date-Time)
Live Grafana Monitoring

## Slide 11
Digital muon data pipeline
From detector traces to analysable instrument data files.
Positrons detected
NI DAQ 121
Signals streamed to a broker
Event formation
Event filtering to histograms
analyse as today!
Event formation can be as simple as peak finding or implement more advanced digital signal processing. Event filtering allows selection of events that are important for analysis.

## Slide 12
From MuSR to Super-MuSR
 | MuSR | Super-MuSR
Detectors | 64 | 960
Solid angle coverage (of sphere) | 40% | 80%
Count rate (MEv/h) | 70 | ~1400
Maximum frequency (field) | 8MHz (0.06T) | ~80MHz (0.6T)
Spin rotation | None | 0 to 75°
Smallest sample (mm) | ~10×10 on Ag | ~2×2 in flypast

## Slide 13
Super-MUSR's expected performance
64 ch ~ 40% coverage
960 ch ~ 80% coverage
Pulse slicing

## Slide 14
Science benefits – higher resolution
Ordered moments e.g. Na2IrO3
e.g. S.K. Choi et. al. Phys. Rev. Lett. 108, 127204 (2012)
ISIS data
PSI data

## Slide 15
Science benefits – higher resolution
Materials with fast and slow relaxations e.g. Zn Barlowite
e.g. K. Tustain et. al. npj Quantum Materials 5: 74 (2020)
ISIS data
PSI data

## Slide 16
Science benefits – higher resolution
Transverse field measurements on superconductors
Which curve
fits best?
Sometimes clearer distinction between different gap models at higher fields
Spin rotators -> anisotropic effects can be probed
Better resolution to probe coexistence of magnetism and superconductivity.
...

## Slide 17
Science benefits – higher rates
Measurements on quantum decoherence e.g. F - μ - F states
J. M Wilkinson et. al., Phys. Rev. Lett. 125, 087201 (2020)

## Slide 18
Science benefits – higher rates
Transient muon spectroscopy measurements
Battery cycling
Field scans
Temperature scans
3 days MuSR - > 12h Super-MuSR
1 day MuSR -> 4h Super-MuSR
2 days EMU - > 10h Super-MuSR

## Slide 19
Science benefits – Vector MuSR
Aligned crystalline samples
  Superconductors
  Ordered magnets
With or without spin rotator
  Apply B-fields on two axes
  Find direction of internal fields
Underexplored area to date

## Slide 20
Technical progress – beamline components
First spin rotator demonstrated to reach 192kV operating voltage.
Pulse slicer power supply soon to be delivered. Expected to exceed desired performance.
Beamline magnets undergoing testing.

## Slide 21
Technical progress – spectrometer
100% of detector tiles glued, with more than 50% fully wrapped and assembled.
Completed tiles being assembled into modules and staves.
Prototype event mode data pipeline running on HIFI and MuSR.

## Slide 22
Technical progress - event mode data
Analysis courtesy of James Lord, ISIS muon group
transient muon spectroscopy measurements on LaCuO​

## Slide 23
Summary & expected timeline
Super-MuSR pre-build
Super-MuSR install
Mar 2028 ...
Dec 2026
MuSR operation ends and strip out
User operation
Nov 2027
… Now
Commissioning and friendly users
Super-MuSR will significantly extend the capabilities of pulsed muon sources:
  20 x counting rate of instruments today OR
  10 x frequency range with existing rate
higher data rates mean existing experiments will be better performed and new experiments will be feasible.

## Slide 24
Additional slides

## Slide 25: Data handling and reduction
Retained for analysis
Temporary
Digitiser traces: ~100TB per day
Event mode data: ~100GB per day
Histograms: ~1GB per day
Lake
Erie
These data rates are upper bounds needed for planning –
the pulse slicer will reduce these when it is switched on
Today’s data files: ~30MB per day